## Slide 1
DP on 3GPP consent for applications user consent requirements and UDM consent
Ericsson, AT&T

## Slide 2: Considerations related to application consent in UDM
Dynamicity, frequency of updates as required by regulation (e.g., GDPR art.7, where user can change his consent at any time) does not fit with UDM stable/planned provisioning and permanent data approach
Amount of data to be stored for application consent can become considerable given the amount of applications. Among others, as per EU Guidance on consent sect. 3.3.1, it has to include also the purpose, the data, whom the authorization is given
Application awareness:
  UDM would need to be provisioned and maintained to keep up with all possible applications the users could use
Separation of the network and exposure/application domains
  Additional traffic load to handle Application user consent provisioning and related traffic (consent checks, consent updates) put a burden on UDM, which may impact mobile network traffic
  Consent management solutions must be 4G/5G agnostic

## Slide 3: SA Plenary LS reply to GSMA OPG
SP-241934 :
user consent in UDM is only for internal 5GC purposes (not apps)
Subscription data in UDM can only be modified via provisioning (not meant for dynamic/frequent updates)
SP-241934 :
“3GPP TSG SA Answer: see answers in Q2.
3GPP user consent framework, Annex V of TS 33.501: User Consent Subscription Data (UcSubscriptionData) is specified in 3GPP TS 29.503 as subscription data stored in the UDR. This data can be retrieved from UDR by UDM and from UDM by any other authorized NF (e.g., NWDAF, NEF). Permanent subscription data within this framework can be modified only by provisioning/administration means. User Consent Subscription Data is used by the NF which is deemed an enforcement point for user consent. The user consent parameters, which are bound to a SUPI/GPSI and purpose of data processing, include whether the user consent is granted or not. Annex V provides technical means to be used when it is required by regional regulations or operator’s local policy, not otherwise. The user consent framework as defined in TS 33.501 relates to user consent data to be used within the 5G Core”.

## Slide 4: Proposed next activities for SA6 endorsement
EDGEAPP
  Clarify that consent requirements are per application and not a generic consent for all EDGE apps
  Add a clean summary of scenarios/user data indicated throughout 23.558 to be subjected to user consent
CAPIF_ph3
  Clarify everywhere applicable that the consent is per application, user resource (and purpose)
  Add a clean summary of the scenarios/user data that is indicated throughout 23.222 to be subjected to user consent

## Slide 5: Example: SA6 EDGEAPP
EDGEAPP TS23.588 uses user consent for the edge applications
6.3.2; 8.5.2.2.: EES acts “as consent enforcing entity as specified in 3GPP TS 33.558 [23] and 3GPP TS 33.501 [32]”
7.2.6: “For user's privacy reasons, GPSI in the form of MSISDN can be used only after obtaining user's consent.”
8.3.3.2.2 in the EAS Discovery procedure: “If an e2e tunnel is used in the UE for applications (e.g. user configured tunnel service), and if the tunnel service provider and the ECSP are from the same organization and only if user grants the permission, then the EEC provides the tunnel information for the associated applications in the request to the EES considering user consent.”
8.6.5.2: “User consent aspect on sharing the AF specific UE identifier with particular EAS is described in 3GPP TS 33.558 [23].”
8.14.2.3: “NOTE 3: It is outside the scope of this release of this specification how the user or the AC can consent, e.g., to the disclosure of location information and the use of the AC ID in the signalling towards the network.”
User Consent purpose | User Data (subject to consent) 23.558 | Enforcer | User Consent storage
Generally per each AF/ app | UE Location - 8.14.2.3 | LMF, NEF (via enforcing the oAuth token scope) | Not specified, ref. to SA3
EDGEAPP (per app/AF) | GPSI (MSISDN) - 7.2.6 | EES (6.3.2; 8.5.2.2) | Not specified, ref. to SA3
EDGEAPP (per app/AF) | UE tunnel e2e info (security) - 8.3.3.2.2 | EES (6.3.2; 8.5.2.2) | Not specified, ref. to SA3
EDGEAPP (per app/AF) | AF specific UE identifier (MSISDN) - 8.6.5.2 | EES (6.3.2; 8.5.2.2) | Not specified, ref. to SA3
SA6 application consent summary
NOTE: Mismatch SA3 with SA6 33.558 also allows NEF as enforcer. 33.501 only mentions NFs (not AFs like EES)

## Slide 6: Recommendations for SA6 endorsement
General direction:
  Working assumption should be that application user consent data storage does not need to be standardized
    Storage in UDM is not an explored option for application user consent either (avoid ad-hoc updates, then dynamically and frequently maintaining application user consent data and an app list continuously expanding)