## Slide 1
NWM WA3 Way forward WA3: AIML Aspects
Moderator, Samsung, Ericsson, Lenovo
basavarajjp@samsung.com

## Slide 2: WA3: AIML Aspects
Candidate Work Task | Support to Explore (based on response to Q3) | Volunteer to provide justification | Remarks
WT3.1: Handling of scarce training data for analytics services, using synthetic data | Samsung, Ericsson | Samsung S6-254340 | 
WT3.2: AI as a service in Agentic AI era | Interdigital, ZTE, Lenovo, Samsung, Apple, Ericsson | Ericson S6-254349 | 
WT3.3: Investigating the mechanism and issues of AI based applications (current or in the future), analyzing the potential exposure requirement on 3GPP AI capabilities of 3GPP system | Interdigital, CATT, ZTE, Lenovo, MediaTek, Huawei, Ericsson | Lenovo S6-254290 | 
WT3.4: How to support more AI capabilities in application enabled layer. | CATT, ZTE | No volunteer | 
WT3.5: How to expose AI services (e.g. AI/ML model inference) to the consumers. | Interdigital, CATT, ZTE | Lenovo S6-254290 | 
WT3.6: How AI enabler can benefit for services over 6G satellite access. | CATT, MediaTek | No volunteer | 
WT3.7: Study the enablement of generative AI capabilities (e.g., AI model training data with generated data, Retrieval Augmented Generation, handling LLMs, large data) and its applications in 6G architecture. | Interdigital, Lenovo, Samsung, Huawei, Apple, Ericsson | Samsung S6-254340 | 
WT3.8: Study to understand and the support required for the traffic patterns of Generative AI | Interdigital, Samsung, Ericsson | Samsung S6-254340 | 

## Slide 3: WA3: AIML Aspects; WT3.1 (1/2)
Summary of comments
  SA2 related. Data source for SA6 needs clarification.
  What is the relation with ADAE? Can be part of ADAE.
  Can be handled in AIML_App /ADAE, not 6G.
  Looks like solution, not WT.
  Is this training data solution?
  Usage and generation of synthetic data is implementation. Needs clarification.
Justification/Clarification
  Clause 6.11 of 3GPP TR 22.870 clarifies on model trained with generated data in network)
    6G system resources (e.g. powerful computing resources) to provide the AI model training service for the third-party service provider can obtain the AI model trained with efficient data (including data generated in NW) without deploying additional the expensive HW/SW resources.
Candidate Work Task | Support | Do not support | Moderator Remarks
WT3.1: Handling of scarce training data for analytics services, using synthetic data | Samsung, Ericsson | Interdigital, CATT, Lenovo, Nokia, MediaTek, CMCC, Huawei, Apple | Need clarifications, Merge to WT3.2, Seems solution, Gap analysis, Implementation specific, Can be merged with WT3.7, SA2 scope, Not SA6 scope
S6-254340, Samsung

## Slide 4: WA3: AIML Aspects; WT3.1 (2/2)
Justification/Clarification (Contd.)
  Need to study how and when the generated data can be used /supported for AIML models.
  ADAE is potential consumer of this service.
  Also, potentially can be enhancement of ADAE or AIMLE.
  No dependency with SA2. For various ADAE analytics defined, the data sources are defined in SA6.
Way forward
  Revise the WT: “Handling of training data for efficient analytics services, using generated data”
  OR
  Merge into WT 3.7 as : Study the enablement of generative AI capabilities (e.g., AI model training data with generated data, handling of scarce training data, Retrieval Augmented Generation, handling LLMs, large data) and its applications in 6G architecture.
Example: Unavailable Edge Load Analytics due to less data
S6-254340, Samsung

## Slide 5: SUMMARY WA3: AIML; WT3.2
TEMLATE
Summary of comments
  Needs more details/too generic: Huawei, CATT, Nokia, MediaTek, CMCC
  Clarify relationship with the SA2 agentic AI discussions: Huawei, CATT, Lenovo, Nokia, CMCC, Samsung, Apple,
  Important to study due to its rapid industry adoption and understand how 6G exposure can benefit for Agent-Agent, Agent on UE –Agent in NW, Agentic FW: Interdigital, Ericsson, ZTE, Lenovo, Samsung
  Intents relationship with agents unclear, but possible: Apple
  Agent at the UE should be only considered an enabler or application layer entity: Apple, Ericsson
Justification/Clarification
  Background: TR 22.870 has 39 UCs related to AI and many of them involve AI agents. Most of the UCs are application related
  Dependency handling plan:
    Need to analyse SA1 UCs to understand the impacts to SA6 and to help determine the coordination needed with SA2
    Some correlation with WT3.7, WT3.8 (Gen AI options and Gen AI technologies like L*M, SLM, etc)
Way forward (revise wording to clarify WT)
  Further work to detail more the WT description and the understanding of how AI agents (e.g., from SA1 UCs) can be used in the Exposure aspects in SA6 for both UE and network side
  Add some information on how the WT 3.2 connects with other related WTs e.g., GenAI in WT3.7, WT3.8 and potentially WT1.10 (intent)
Candidate Work Task | Support | Do not support | Moderator Remarks
WT3.2: AI as a service in Agentic AI era | Interdigital, ZTE, Lenovo, Samsung, Apple, Ericsson | CATT, Nokia, MediaTek, CMCC, Huawei | Important, Need clarifications, Overlap with SA2/SA5, Rephrase
S6-254349, Ericsson

## Slide 6: Background – AI use cases from SA1 (TR 22.870)
  Use case on optimizing 6G infrastructure utilization via resource exposure in 6G
  Use case on end-to-end AI for connected cars
  Use case on system performance optimisation using AI
  Use case on personalized AI for health monitoring
  Use case on 6G AI agent collaboration with third-party AI using LLM
  Use case on AI-agents communication
  Use case on 6G system assisted AI agent service
  Use case on collaborative AI agents
  Use case on home robots
  Use case on built-in Intelligent Communication Assistant
  Use case on 6G System supporting AI model training service
  Use case on network knowledge as part of Retrieval Augmented Generation for Generative AI
  Use case on intelligent UAV swarms
  Use case on 6G system assisted target object detection
  Use case on energy of the system intelligent management
  Use case on intelligent communication assistant
  Use case on exposing achievable QoS to aid computational resource selection
  Use case on AI-based video analysis
  Use case on smart housekeeping
  Use case on 6G network providing on-demand networking with AI Agent
Application related UC (at initial glance)
Application related UC involving AI agents (at initial glance)
  Use case on intelligent calling services
  Use case on child health management assistant
  Use case on distributed 6G network for AI computing
  Use case on AI/ML model training and inference
  Use case on optimizing user experience for GenAI applications
  Use case on network federation for collaborative AI model training
  Use case on network-assisted video-based AI inference task offloading for mobile embodied AI
  Use case on smart home user-centirc AI service
  Use case on smart healthcare
  Use case on UE-Network collaboration with AI capabilities
  Use case on disaster rescue planning enabled by network AI Agents
  Use case on AI text-to-video generation supported by computing
  Use case on 6G computing support for AI model inference
  Use Case on 6G native AI in multi-domain convergence
  Use case on AI/ML model managed service for intelligent vehicles
  Use case on energy efficiency for AI service
  Use case on AI for disability support
  Use case on responsible AI as service criteria
  Use case on AI-driven multi-vehicle cooperative perception
S6-254349, Ericsson

## Slide 7: 6G UC example from TR 22.870 (6.5)
Short analysis
Smart City Vertical = consumer which provides their requests via AI agent, has to go via an Exposure layer that handles the request, so it needs to support such AI agent requests
  AI agents in Exposure FW and App enablement to interpret the text-based requests and process into actionable tasks
  Example actionable tasks:
    Check legitimacy of SCV AI agent (auth/authZ/registered/etc.)
    Determine sequence of SBIs to use towards the AEFs
    Discover if AI agents to process identified tasks exist and if tasks can be delegateded to them
Unclear what AI agent interfacing with 6GC is needed for this UC, all could be done via exposure layer
Assumes that private networks are merged into scope for CN (smart city traffic lights, cameras and monitoring belongs to CSP)
Considerations: proposed TR requirements
[PR 6.5.6-1] Based on operator policy, the 6G network shall be able to support secure means to expose its services to the authorised third-party AI agent based on its intent.
[PR 6.5.6-2] Based on operator policy and user consent, the 6G network shall be able to take into account information related to user mobility context, subscription information when invoking 3GPP services based on user intent(s).
Proposed conclusions
AI agents support in the Exposure layer is needed, supporting communication with AI agents in the Applications/VAL
Agentic FW is needed to keep track and control the access from the various supported AI agents (UE, NW), their capabilities, communication support, security, explainability and accountability, policies, etc. This can be handled in Exposure layer
We may need to clarify what “intent” means (if different from SA5, TM Forum definitions and models)
“[..] a third-party application (e.g. a smart city traffic management system) AI Agent sends a text-based request or query to the 6G network. The request is processed by an AI agent in the 6G network that leverages LLMs and the network's advanced capabilities (e.g. sensing, real-time data processing, telemetry, analytics, and others) to provide a response or perform an action. ”
“6G network AI agent acts as an intelligent intermediary, interpreting the text-based request, gathering necessary data, and returning a response or executing a task.” Example : "Why is the traffic congested on Highway A, and what adjustments can be made to optimize traffic flow?"
Pre-conditions:
“The third-party application (e.g. smart city traffic management system) has access to 6G network’s AI agent services.”; “The 6G network has deployed LLM-based AI agents capable of understanding and processing natural language queries.”
Use case on 6G AI agent collaboration with third-party AI using LLM
S6-254349, Ericsson

## Slide 8: 6G UC example from TR 22.870 (6.6)
Short analysis
Some existing support (PIoT, PIN elements, etc).
Connectivity can be 3GPP or non-3GPP
Non-3GPP sensing data needed (e.g., identify furniture)
Different capabilities for the AI agents on new devices belonging to a user, handled in AI agent groups (for closed group communication, privacy)
  Groups can be handled in CN or in Enablement layer
AI Agents tasks and capabilities are not related to Core Network, but to apps
Agentic FW that supports their registration, discovery, communication, authN/Z, capabilities profiles, etc is needed. Unclear why it needs to be in Core Network
Considerations: 5 proposed TR requirements to support 3rd party AI agent’s attributes
[PR 6.6.6-1] & [PR 6.6.6-3] capabilities registration and discovery: “(e.g. related users, sensing capabilities, AI capabilities, service features) to other 3rd party AI agents.”
[PR 6.6.6-2] AuthN/Z of AI agents and association with a PLMN subscriber
[PR 6.6.6-4] communication between 3rd party AI agents over a wide area in a group
[PR 6.6.6-5] secure means to expose different services, e.g. computing offloading service in Service Hosting Environment, to the authorized third-party AI agent.
Proposed conclusions
Support for consolidating sensing data (3GPP, non-3GPP) needed
Support for AI agent grouping, or temporary grouping for a task is needed. Can be supported in the agentic FW in the enablement layer, to cater to the app/task requirements
Agentic FW that can keep track of the various supported AI agents (UE, NW), their capabilities, communication support, security, explainability and accountability, policies, etc.
“[..] Communication domain could be dynamically created for users and AI agents from multiple groups to communicate with each other for a specific task during a specific time.”
Pre-conditions:
Bob has a home robot and other UEs (AI assistant, drone and intelligent vehicle, etc.). All AI agents on Bob’s UEs have been associated with Bob’s ID, except for the robot
Drones and cars connected on cellular access, rest of UEs use Wi-Fi
AI agents and their capabilities must be known to the network
Use case:
Bob, Alice, and Charlie – each have created an AI agent group with their own agents. AI agents vary in their service features, capabilities and permission, etc.
Bob’s newly purchased home robot joins the Bob AI agent group and registers its capabilities
Bob asks robot to organize a family gathering.
  Robot retrieves data (past family gatherings, list of tasks) and distributes the resulting tasks to other AI agents - e.g., cleaning robots to move furniture, AI assistant to book food catering, drone to deliver the food, AI assistant to message guests and organize pickup then tell car where and when to do guest pickups.
Use case on AI-agents communication
S6-254349, Ericsson

## Slide 9: 6G UC example from TR 22.870 (6.7)
Short analysis
Sensing information used by AI agent: 3GPP sensor results + non-3GPP sensors for different objects
AI agents on UEs can trigger various clients on UE
  e.g., send a message to robot: can be done via the SMS/RCS client on UE, or WhatsApp, etc. per user configuration of the agent
  Or, can access websites from UE to book travel, check prices for VIP deals
an Agent style UNI is not necessarily needed with 6G CN, for this UC
UC can be realized entirely via exposure/app enablement layer/applications and using existing UNI with CN and IMS
Requirements to expose to AI agents on UE: some 3GPP services like IMS voice, QoS changes – unclear why the existing IMS, QoS services exposed on the 5GA UE need to be replaced by new UNI alternatives to 6G CN.
Considerations: There are proposed requirements
[PR 6.7.6-1] Based on user consent and operator policy, the 6G system shall provide a suitable means for an AI agent application on UE to invoke some 3GPP services (e.g. IMS service).
[PR 6.7.6-2] Based on user consent, operator policy and regulatory requirements, the e.g. change of QoS) to the 6G system shall provide an efficient way to expose information (application on the UE.
[PR 6.7.6-3] Based on user consent, operator policy and regulatory requirements, the 6G network shall be able to support the message exchange between the AI agent application on different UEs, considering the diverse capabilities supported by different AI agents for these applications
Proposed conclusions
Both the robot nanny UE and the mobile phone UE own AI agents each. The UC seems to imply one AI agent per device.
AI agents in this UC are UE usability enhancers, to make human interactions simpler via free text/voice on the device. An UE Agent – NW Agent interactions can be all in app layer including also the UE Agent discovering other agents it can talk to (e.g., to make the travel booking requests, to send the package pickup request).
The UC can make use of existing UNI to interface with the NW, or can support AI agents requests in the application layer (via simplified requests).
Use case on 6G system assisted AI agent service
UC: robot nanny from vendor A and phone UE from vendor B communicate, both take User input
User’s input (as free text/speech) is processed by AI agent on robot and by the AI agent on mobile phone
  Robot nanny executes the actionable tasks identified by its AI agent e.g., books vacations checks prices, picks up package deliveries
  AI agent on Phone UE determines other actionable tasks based on user’s free style commands, so it initiates communication with robot to give tasks (e.g., package delivery pickup)
S6-254349, Ericsson

## Slide 10: Proposed way forward WT3.2
WT title renaming to: Agentic fabric and AI Agents for app enablement
WT re-wording for the two inter-dependent topics to be studied:
  This work studies the support agentic common functions (e.g., agent registration and capabilities discovery, agent communication/interaction, agent collaboration, explainability and accountability for AI agents actions), of the AI agents needed to operate in, or AI agents interacting with, the application enablement layer. NOTE: interactions with existing SA6 enablers and frameworks are considered as needed (e.g., APCOT, CAPIF, EDGEAPP)
Note: Work from WT 3.2 can be leveraged for integration with and reuse by SA6 FWs and enablers -> e.g., WT1.12, WT2.6, WT3.3
Coordination with other WGs:
  Some coordination with SA2 is needed on synergies and alignment between CN/Exposure layer
  Coordination with SA3 to study security and privacy aspects
S6-254349, Ericsson

## Slide 11: WA3: AIML Aspects; WT3.3 and WT3.5
Summary of comments
  Comments related to WT.3.3: Rephasing, relation with SA2 to be clarified, anticipating future applications shouldn’t be studied in SA6.
  Comments related to WT3.5: Clarifications w.r.t SA6 are needed since AIMLE provides already exposure related to AI and inference services. Possible merging with WT.3.3 and coordination with WA1 to ensure coherent exposure
  Proposals for rephrasing to both WTs to identify the role of SA6 considering SA2 work.
Justification/Clarification
  In 6G Stage 1, SA1 has studied numerous use cases (in TR 22.870) on AI where most of them imply some exposure of capabilities to 3rd party (either towards the ASP/ vertical server or to the application layer of the UE).
  Two main “principles” are related to AI in 6G: “Network for AI” (how the 3GPP system may support AI services), and “AI for Network” (how AI may optimize existing capabilities at the network side).
  The “exposure” related capabilities w.r.t. AI is key for “Network for AI” principle, where in the 6G notion of “network” comprises the Service Enablement layer.
  SA6 has already provided capabilities related to AI: 1) ML model related support capabilities such as model retrieval, discovery and storage, 2) ML operation related support capabilities such as VFL/ HFL and TL enablement, Split AI/ML Operation support, Data management assistance, AI/ML task transfer, FL assistance in member grouping, registration and event notification, and 3) AIMLE client related support capabilities, including AIMLE client registration, discovery, participation, monitoring, selection
  6G use cases, i.e. related to support agentic AI (considering different AI agent implementations), necessitates studying the exposure of 3GPP system capabilities, and SA6 scope should be 1) study application layer enablement exposure requirements to support 6G-related AI use cases, 2) gap analysis and study potential Enabler capabilities (AIMLE enhancements) to meet requirements related AI capability exposure, 3) study a unified service exposure framework for AI/ML considering SA2/SA5 ongoing efforts on 6G AI capabilities
Candidate Work Task | Support | Do not support | Moderator Remarks
WT3.3: Investigating the mechanism and issues of AI based applications (current or in the future), analysing the potential exposure requirement on 3GPP AI capabilities of 3GPP system | Interdigital, CATT, ZTE, Lenovo, MediaTek, Huawei, Ericsson | Nokia, CMCC, Samsung, Apple | Merge with WA3 and WA1, SA2 overlap, Merge with WT3.4, WT3.5, WT3.7 and WT3.8, Need clarification
WT3.5: How to expose AI services (e.g. AI/ML model inference) to the consumers. | Interdigital, CATT, ZTE | Lenovo, Nokia, CMCC, Samsung, Huawei, Apple, Ericsson | Merge with WA3, Gap analysis, Merge to WT3.3, Need clarification
S6-254290, Lenovo

## Slide 12: WA3: AIML Aspects; WT3.3 and WT3.5
Way forward (e.g. revised WT, merging etc)
  Proposal 1: Merging of WT 3.3 and 3.5 in one WT 3.x for “Studying AI/ML Enabler-layer Exposure Requirements and Capabilities to support 6G AI related use cases“
  Proposal 2: New WT 3.x to have the following objectives/scope:
    Objective 1: Study what application enablement exposure requirements do the identified functional enhancements require to expose AI/ML services to 3rd-party applications? (exposure requirements should be studied in coordination with WA1)
    Objective 2: Analyze the AIMLE capabilities (as in TS 23.482) and study potential new enabler capabilities (AIMLE enhancements) to meet exposure requirements related to 6G use cases on “system/network for AI”
    Objective 3: Study a unified service exposure framework for AI/ML considering SA2/SA5 ongoing efforts on 6G AI capabilities
S6-254290, Lenovo

## Slide 13: WA3: AIML Aspects; WT3.7 (1/2)
Summary of comments
  Relation SA2 WTs (3,5,6) to be clarified
  Relation with 3.2, 3.3 and 3.5 needs clarification
  What is the benefit for SA6
  Existing AIMLE can work on any model, use case examples are not clear.
  Scope not clear. Merge into 3.3.
  AI model training with generated data is application layer. RAG can be potentially studied.
Justification/Clarification
  Relation with SA2 WT3 (AI in 6G architecture): SA2 studies enabling AI for core network and SA6 can study enabling AI for vertical application layers. The mechanisms specified by SA2 can be consumed where ever applicable.
Candidate Work Task | Support | Do not support | Moderator Remarks
WT3.7: Study the enablement of generative AI capabilities (e.g., AI model training data with generated data, Retrieval Augmented Generation, handling LLMs, large data) and its applications in 6G architecture. | Interdigital, Lenovo, Samsung, Huawei, Apple, Ericsson | CATT, MediaTek, CMCC | Important, Explain benefit, Need clarification, Merge to WT3.3, relation with WT3.2, WT3.3 and WT3.5, SA2 overlap
S6-254340, Samsung

## Slide 14: WA3: AIML Aspects; WT3.7 (2/2)
Justification/Clarification (Contd.)
  Relation with SA2 WT5 (Data framework): WT 3.7 is handling large data aspects of Gen AI. Data framework capabilities can be leveraged where ever applicable.
  WT 3.3 and WT 3.5 are very generic and broadly covers about enabling AIML capabilities. This WT 3.7 is specific to Gen AI capabilities. WT 3.3 and WT 3.5 can be merged and proceed, if these WTs capture specific domain aspects of AI to be studied.
  WT 3.2 is about Agentic AI, Gen AI is a technology enabler for Agentic AI. These two can be complementing work tasks.
  Certain characteristics of Gen AI are different from the other AI mechanisms. They handle with (Large LLMs and their Large data sets), support latest paradigms like relevant predictions using RAGs. Hence, WT 3.7 has to be studied to identify any potential enhancements to AIMLE. LLM model and its large data distribution should also be studied.
Way forward
  Revise the WT : Study the benefits and enablement of generative AI for the 6G application enablement for e.g., AI model training data with generated data, handling of scarce training data, Retrieval Augmented Generation, different language models suitability for applications on UE and in the NW (e.g., SLM, LLMs and large data), traffic patterns
S6-254340, Samsung

## Slide 15: WA3: AIML Aspects; WT3.8 (1/2)
Summary of comments
  Move to WA4, with enablement of traffic pattern for all AI types.
  What is the benefit for SA6?
  Relation with existing SEALDD traffic pattern analysis.
  Merge to 3.7.
  Scope of other WGs (SA2, SA4 and RAN2)
Justification/Clarification
  This work task is specifically for Gen AI traffic. Other type of AIs can be explored, but no use cases in 3GPP TR 22.870.
  Can be related to SEALDD and may be potential enhancement based on traffic pattern analysis.
  Has dependency on 6G core network evolution.
  SA6 has to study how and what Gen AI traffic patterns of VAL layer can be enabled.
Way forward
  This work task has to be studied in SA6. Can wait for 6G core network evolution.
  Either void or Merge to 3.7 as below:
    WT3.7: Study the enablement of generative AI capabilities (e.g., AI model training data with generated data, Retrieval Augmented Generation, handling LLMs, large data), its traffic patterns and its applications in 6G architecture.
Candidate Work Task | Support | Do not support | Moderator Remarks
WT3.8: Study to understand and the support required for the traffic patterns of Generative AI | Interdigital, Samsung, Ericsson | CATT, Lenovo, MediaTek, CMCC, Huawei, Apple | Important, Explain benefit, Not in SA6 scope (may be SA2/SA4/RAN2), Need clarification, Merge to WT3.7. Move to WA4
S6-254340, Samsung

## Slide 16: Justification : Why WA3?
Broad comments on WA3 received (NWM) on clarifications of the work tasks and wait for SA2.
S6-233350 - Provides detailed analysis of use cases and requirements that are currently envisioned for shaping the 6G systems, with reference to use cases illustrated in 3GPP TR 22.870
  Various use cases illustrated in 3GPP TR 22.870, indicate AI is an important tenet for 6G system.
  This paper also indicates the use cases which are in scope of application enabler layer and have no core network dependency.).
Following AIML aspects can studied, where there is no core network dependency:
  AI at Edge: Study enhancements for EDGEAPP to enable AI tasks at Edge (Model inference, Model training).
  Intent based: Study intent based exposure of application enabler services to third party AI agents.
  AI Agents: Study the support of communication and collaboration between AI agents in vertical applications and multiple application enablers.
  Generative AI: Study the enablement of generative AI capabilities (e.g., AI model training data with generated data, Retrieval Augmented Generation, handling LLMs).
  AI tasks: Study the enhancements to AIMLE tasks (e.g. model training, model inference, model management, data transfer (model, data set, multi-modality data)) offloading and collaboration for various use cases like AI-based video analytics, home robots, AI text to video, etc.
  Responsible AI: Study the considerations of responsible AI (e.g., robustness, environment sustainability, explainability, trustworthy etc.), for AI services at application enabler layer (e.g., AIMLE, ADAE).
S6-254340, Samsung

## Slide 17: Summary
Proposals for WA3: WT3.1, WT3.7, WT3.8
Candidate Work Task (Current) | Candidate Work Task (Proposed)
WT3.1: Handling of scarce training data for analytics services, using synthetic data. | Revise the WT as: “Handling of training data for efficient analytics services, using generated data” OR Merge into WT 3.7 as : Study the enablement of generative AI capabilities (e.g., AI model training data with generated data, handling of scarce training data, Retrieval Augmented Generation, handling LLMs, large data) and its applications in 6G architecture.
WT3.7: Study the enablement of generative AI capabilities (e.g., AI model training data with generated data, Retrieval Augmented Generation, handling LLMs, large data) and its applications in 6G architecture. | Study the benefits and enablement of generative AI for the 6G application enablement for e.g., AI model training data with generated data, handling of scarce training data, Retrieval Augmented Generation, different language models suitability for applications on UE and in the NW (e.g., SLM, LLMs and large data), traffic patterns.
WT3.8: Study to understand and the support required for the traffic patterns of Generative AI | Void OR Merge into WT3.7 as: Study the enablement of generative AI capabilities (e.g., AI model training data with generated data, Retrieval Augmented Generation, handling LLMs, large data), its traffic patterns and its applications in 6G architecture.
S6-254340, Samsung

## Slide 18: Way forward (Proposed) WA3: AIML Aspects
Candidate Work Task (to NWM#1) | Candidate Work Task (Revised in SA6#69) | Volunteer | Stable or open issues? | NWM#2 or SID?
WT3.1: Handling of scarce training data for analytics services, using synthetic data | WT3.1: Void. Merged to WT3.7 | Samsung | NA | NA
WT3.2: AI as a service in Agentic AI era | WT3.2: Study the support for application related agentic common functions (e.g., agent capabilities discovery, agent interaction, agent collaboration, etc), of the application related AI agents and of the AI agents needed to operate in the application enablement layer. NOTE 1: interactions with SA6 enablers and frameworks are considered as needed (e.g., APCOT, CAPIF, EDGEAPP, SEAL). NOTE 2: Some coordination with SA2 is needed on synergies and alignment between CN and Exposure layer. Coordination with SA3 to study security, privacy, regulation aspects. | Ericsson | Revision is based on offline discussions. Seems stable. Open Issue: Discussion in relation with WT1.5 | TBD
WT3.3: Investigating the mechanism and issues of AI based applications (current or in the future), analyzing the potential exposure requirement on 3GPP AI capabilities of 3GPP system | WT.3.3.1: Study potential application enablement exposure requirements w.r.t AIML and identify functional enhancements to expose AI/ML services to 3rd-party applications. WT 3.3.2: Analyze the AIMLE capabilities (as in TS 23.482) and study potential new enabler capabilities (AIMLE enhancements) to meet exposure requirements related to 6G use cases on “network for AI” NOTE 1: Exposure requirements should be studied in coordination with WA1. NOTE 2: This WT will consider work on AI/ML related exposure from SA2/SA5, to avoid overlapping. | Lenovo | Open Issue: Remove WT3.3.2, as it is implicitly included in WT3.3.1. | TBD

## Slide 19: Way forward (Proposed) WA3: AIML Aspects
Candidate Work Task (to NWM#1) | Candidate Work Task (Revised in SA6#69) | Volunteer | Stable or open issues? | NWM#2 or SID?
WT3.4: How to support more AI capabilities in application enabled layer. | WT3.4: How to support more AI capabilities in application enabled layer. | No volunteer | NA | TBD
WT3.5: How to expose AI services (e.g. AI/ML model inference) to the consumers. | WT3.5: Void. Merged to WT3.3 | Lenovo | NA | NA
WT3.6: How AI enabler can benefit for services over 6G satellite access. | WT3.6: How AI enabler can benefit for services over 6G satellite access. | No volunteer | NA | TBD
WT3.7: Study the enablement of generative AI capabilities (e.g., AI model training data with generated data, Retrieval Augmented Generation, handling LLMs, large data) and its applications in 6G architecture. | WT3.7: Study the benefits and enablement of generative AI for the 6G application enablement for e.g., AI model training data with generated data, handling of scarce training data, Retrieval Augmented Generation, different language models suitability for applications on UE and in the NW (e.g., SLM, LLMs and large data). | Samsung | Stable. There were comments on inclusion of traffic patterns. Hence removed traffic patterns. | SID
WT3.8: Study to understand and the support required for the traffic patterns of Generative AI | WT3.8: Study to understand and the support required for the traffic patterns of Generative AI. | Samsung | Open issue: No agreement, traffic patterns is SA2 scope. | NWM#2