## Slide 1: Candidate 6G Radio Technologies 2/14/25
tdoc#: 6GWS-250043
Agenda Item: 4
Vision & priorities for next generation radio technology
(RAN Parallel Session)
3GPP workshop on 6G
Incheon, Korea, March 10-11, 2025
NSC
NSC Email Contact: nishith.tripathi@nationalspectrumconsortium.org

## Slide 2: 6G Radio Technology
Mobile-Distributed MIMO (MD-MIMO)
Spectrum Sharing
Integrated Aerial, Terrestrial, and Non-terrestrial Network (IATNN)
6G Sidelink Enhancements
6G NTN Enhancements
6G Sensing Enhancements

## Slide 3: 6G Use Cases
The NGA has identified seamless mobility as a key aspect of 6G where cell-cluster connectivity can be enabled [NGA-Radio2].
The NGA has identified the need to enhance existing device-to-device communication/ sidelink technologies to improve spectral efficiency, power efficiency, and overall user experience [NGA_Radio2].
[NGA_Radio2] Next G Alliance, “6G Radio Technology Part II: Basic Radio Technologies,” May 2024.
Other use cases such as
ubiquitous connectivity for disaster relief
capacity enhancement for crowded events
capacity enhancement and coverage extension for vehicular communications

## Slide 4: Motivation for Mobile Distributed MIMO
Existing 3GPP D-MIMO in 5G NR (e.g., multi-TRP) rely on fiber connections between radio units and digital units
  Pro: High data rate connection
  Pro: Simplified D-MIMO system design
  Con: Increased deployment/operating cost
  Con: Reduced flexibility
Enhanced D-MIMO in 6G ---- Mobile Distributed MIMO (MD-MIMO): Replacing fiber links with wireless links
  Pro: Reduced deployment/operating cost
  Pro: Increased flexibility
  Con: More complicated D-MIMO system design
UE
RU
gNB

## Slide 5: Exemplary Network Architecture for MD-MIMO
Downlink MD-MIMO (2-Phase transmission)
Phase 1:
  Information sharing: MIMO broadcast channel with common information
Phase 2:
  Data transmission: D-MIMO channel
Uplink MD-MIMO (2-Phase transmission)
Phase 1:
Phase 2:

## Slide 6: Sample Challenges
Challenge 1: Wireless links will have substantially lower capacities than fiber connections
  Design challenges for synchronization, data sharing and communication latency
Challenge 2: D-MIMO channel information acquisition
  Design and algorithm challenges for reference signal design, CSI estimation, and CSI feedback for D-MIMO

## Slide 7: Preliminary Evaluation for MD-MIMO DL
System Parameters | Values
Center Frequency | 3.5 GHz
Subcarrier Spacing | 15 kHz
Number of subcarriers | 512
gNB TX antennas | 4
UE TX/RX antennas | 2
gNB Transmit Power | 35 dBm
UE Transmit Power | 26 dBm
TX UE
TX gNB
RX UE
TX gNB
TX UE
RX UE
(RX)
3rd Generation Partnership Project (3GPP), “Study on evaluation methodology of new Vehicle-to-Everything (V2X) use cases for LTE and NR (Release 15),” in 3GPP TR 37.885, 2019
Low Mobility Medium Mobility High Mobility

## Slide 8: Network Architectures for MD-MIMO
gNB
Set 1 Devices
Packet P
Downlink D-MIMO architecture: Primary architecture discussed above. Participants in D-MIMO transmission may be either mobile or fixed, wirelessly connected to the gNB.
Set 1 Devices
Packet P
Uplink UE D-MIMO architecture: Neighboring UEs with poor gNB connectivity can collaboratively transmit to the gNB by first sharing common information between them through sidelink.
gNB
Set 1 Devices
Set 2 Devices
Packet P
Pure sidelink-based architecture: One of the “more capable” UEs may be assigned an additional responsibility of scheduling to increase spectral efficiency compared to distributed or random resource scheduling.

## Slide 9: Take-Away and Proposal
Preliminary evaluation suggests that MD-MIMO can scale system throughput substantially with flexibility in deployment
Proposal: Study the feasibility and performance improvements of enhanced D-MIMO through MD-MIMO in 6G:
  Coherent joint transmission for throughput enhancement
  Non-coherent joint transmission for coverage extension and reliability enhancement

## Slide 10: Motivation for Spectrum Sharing
Spectrum will continue to play an important role in 6G. Expected data-intensive services in 6G such as digital twins, high-fidelity holograms, and immersive video calls necessitate access to a large amount of spectrum.
Making a large amount of spectrum accessible to 6G requires that both licensed and unlicensed spectrum be utilized to the maximum extent. Spectrum sharing maximizes the spectrum available to the wireless systems.
Example. Preliminary studies indicate that spectrum can be shared between a Terrestrial Network and a Non-Terrestrial Network (e.g., between an indoor 5G TN and an outdoor NTN) [NGA_Spectrum] [Chintalapati].
[NGA_Spectrum] Next G Alliance, “ Spectrum Access Mechanisms,” August 2024.
[Chintalapati] Rahul Varma Chintalapati, Nishith Tripathi, Jeffrey Reed, “Feasibility Analysis of Isolation-Based Spectrum Sharing Between Terrestrial and Non-Terrestrial Networks” 2024 IEEE Texas Symposium on Wireless and Microwave Circuits and Systems (WMCS), Waco, TX, USA, 2024.

## Slide 11: Spectrum Sharing: A Brief Description
An intelligent spectrum coordination system maximizes the utilization of spectrum while minimizing the probability of any interference resulting from sharing of licensed and unlicensed spectrum.
A central automated spectrum coordination system can facilitate near-real-time spectrum coordination between similar services (e.g., terrestrial networks) or dissimilar systems (e.g., (i) a terrestrial system and a non-terrestrial system or (ii) a cellular system and a radar system) [NGA_Spectrum].
Sharing of licensed spectrum may involve financial arrangements between an entity lending spectrum and an entity borrowing spectrum.
In an example implementation, a central spectrum coordination system facilitates sharing of a chunk of licensed spectrum offered by a spectrum owner to spectrum seekers for geography-based and/or time-based usage of licensed spectrum [NGA_Spectrum].
Incumbent Informing Capability (IIC) may be exploited to facilitate spectrum sharing when the victim system consists of passive receivers only [NGA_Radio1].
Consider co-existence with incumbents while facilitating the spectrum sharing framework.
[NGA_Radio1] Next G Alliance, “6G Radio Technology Part I: Basic Radio Technologies.” November 2023.
[NGA_Spectrum] Next G Alliance, “ Spectrum Access Mechanisms,” August 2024.

## Slide 12: Motivation for Integrated Aerial, Terrestrial, and Non-terrestrial Network (IATNN)
Current terrestrial and non-terrestrial networks operate independently.
Aerial networks with UAVs providing coverage are often deployed in an ad hoc manner. A typical 3GPP implementation, the UAV houses a UE. Hence, to provide aerial coverage, the UAV UE can make use of sidelink to provide radio coverage to UEs on the ground.
An integrated aerial, terrestrial, and non-terrestrial network that defines mechanisms for flexible varying degrees of cooperation among these diverse networks can address the problems of coverage and capacity in normal and disaster situations.
Resources (spectrum, power, backhaul) across these domains (aerial, terrestrial, non-terrestrial) can be adapted to the communications and sensing needs of the network applications.

## Slide 13: IATNN: A Brief Description
Example Areas for Coordination
Handover
Load balancing
Spectrum sharing
Expected Benefits
Enhanced user experience
Increased cell and user throughput
Reduced latency
Increased spectrum utility
Improved sensing (ISAC)

## Slide 14: 6G Sidelink Enhancements Proposal Overview
Objective: Enhance sidelink to support device-to-device1 usage trends and capabilities identified in IMT-2030
Proposal | IMT-2030 Capabilities | Benefits
P1. Enhance sidelink to support directional networks | Enhanced coverage, higher peak data rates, higher spectral efficiency, and increased traffic capacities | Increased coverage distances and data rates, and superior spectral efficiencies in applications such as A2X, V2X and XR
P2. Support for device-to-device dynamic mesh networks | Enhanced coverage and ubiquitous connectivity, and increased mobility for dynamic networks | Essential for coverage enhancements for A2X, V2X, first-responder, and mobile IoT networks
P3. Support for self-secure MANET | Enhanced coverage and ubiquitous connectivity, enhanced reliability, enhanced interoperability, and advanced security and resilience | Support first responders, affected citizens, and search and rescue teams from different regions and countries, gather at the scene to conduct disaster relief operation where cellular infrastructure (include core) and power infrastructure are not available.
P1, P2, P3
P1
P1
P1
P1
P2
P2
1 Recommendation ITU-R M.2160, "Framework and overall objectives of the future development of IMT for 2030 and beyond." 11/2023.
P3
P3
P3

## Slide 15: 6G Sidelink Enhancements Proposal Overview
P1: Support for Directional Networks
Application scenario and background
  Commercial uses of Aerial-to-Everything (A2X) applications have increased significantly in the past few years
  To support such uses, the FCC1 recently dedicated the 5030 – 5091 MHz band for control-related communications of Unmanned Aircraft Systems (UAS)
  Release 18 Study Item considered enhancing sidelink to support operations in the FR2 frequency range
    Beam management was the focus of this Study Item
  Specification work is necessary to support these directional networks
Proposed enhancement
  Enhance sidelink to support directional networks
Benefits
  Longer coverage distances, increased data rates, and superior spectral usage in applications such as A2X, V2X and XR
1 FCC, Report and Order. Spectrum Rules and Policies for the Operation of Unmanned Aircraft Systems." WT Docket No. 22-323, August 29, 2024.
P2: Support for Device-to-Device Dynamic Mesh Networks
Application scenario and background
  Mesh connectivity is essential to support usage trends identified in IMT-2030, including A2X, V2X, and IoT networks
  Release 19 RAN Work Item supports multi-hop relaying but not does not support a UE-based mesh network
    Dynamic mesh networks are necessary for high-mobility UE networks, e.g., air-to-air networks
Proposed enhancement
  Support for device-to-device dynamic mesh networks
Benefits
  Essential for coverage enhancements of A2X, V2X, first-responder, and IoT networks
P3: Self-Secure MANET
Application scenario and background
  A system supports instant direct device connection with sidelink relays where a core could not be accessed to support the UEs authentication in disaster response scenarios.
  There are use cases in disaster conditions where UE is not able to get access to a centralized core due to a) gNBs are not available, b) a core is not available, or c) both gNB and a core are not available
Proposed enhancement
  Support for self-secure MANET
Benefits
  Essential for first responders, affected citizens, and search and rescue teams to conduct disaster relief operation.

## Slide 16: 6G NTN Enhancements Proposal Overview
P1,P2
P3
P4
P4
P1,P2
Objective: Enhance NTN to support resiliency, ubiquitous coverage, and seamless connectivity and internetworking with TN
Proposal | IMT-2030 Capabilities | Benefits
P1. Enhance resiliency of NTN | Resiliency against jamming, interference, and cyber threats | Enhanced resiliency, reliability and assured connectivity
P2. GNSS independence | Increased resiliency | Enhanced resiliency and reliability
P3. Enhance network-verified UE location accuracy | Higher position accuracy | Compliance with regulatory requirements, support law enforcement needs, and effective broadcast of emergency warning systems
P4. Spectrum sharing with TN | Enhanced coverage; increased interworking and interoperability with TN | Cost-effective use of spectrum resources for reliable coverage

## Slide 17: 6G NTN Enhancements
Enhance Resiliency of NTN
Application scenario and background
  Satellites, unlike base stations, are susceptible to electromagnetic and cyber attacks from distant locations
  NR NTN waveform is vulnerable to these threats
    Smart jammers could easily target synchronization and control channels
Proposed enhancement
  Enhance resiliency of NTN waveforms, support techniques for satellite, frequency band, and time diversity
Benefits
  Enhanced resiliency, reliability, and assured connectivity
GNSS Independence
Application scenario and background
  The UE position information is necessary for satellite access, which is usually obtained from GNSS
  Jamming and spoofing of GNSS signal will prevent access to the satellite and might result in inefficient use of satellite resources
Proposed enhancement
  Specify signaling, protocols and techniques to support GNSS-independent operations
Benefits
  Enhanced resiliency and reliability
Enhance Accuracy of Network-Verified UE Location
Application scenario and background
  Accurate estimation of UE's position by the network is necessary to comply with regulatory requirements and broadcast emergency messages
  The accuracy specified in Release 18 (5 – 10 km, 3GPP TR 38.882) is not sufficient in many applications
Proposed enhancement
  Enhance the accuracy of network-based UE position estimation techniques
Benefits
  Compliance with regulatory requirements, support law enforcement needs, and effective broadcast of emergency warning systems
Spectrum Sharing with TN Networks
Application scenario and background
  Satellite and terrestrial services have primary status in a large number of frequency bands
  FCC's Supplemental Coverage from Space (SCS) supports the use of satellite services in cellular frequency bands
Proposed enhancement
  Develop signaling, protocols, and architectures to support the spectrum sharing
Benefits
  Cost-effective use of spectrum resources for reliable coverage

## Slide 18: 6G Sensing Enhancements Proposal Overview
Objective: Use the UE network as an effective distributed multi-modal sensor network
Proposal | IMT-2030 Capabilities | Benefits
Support distributed multi-modal sensing | Sensing-related | UE capabilities expanded to realize a cost-effective, crowdsourced IoT network

## Slide 19: Distributed Multi-Modal Sensor Network
Application scenario
  The next-generation UE can be used to sense multi-modal signals, e.g., RF, acoustic, and video
  A large number of such distributed UEs realize a multi-modal crowdsourced sensor network
Proposed enhancement
  Support a multi-modal sensing
Benefits
  UE capabilities expanded to realize a cost-effective, crowdsourced IoT network