## Slide 1: 6G consideration from CT leadership
CT TSG/WG Chairs

## Slide 2: Overview
Introduction
New Scenarios and Services Trends
Lessons from previous generations
Principles of protocol design
Consideration for protocol (re-)evolution
Stage 2 work in CT
Summary

## Slide 3: Introduction
Decision on principal of 6G network structure and protocols have to be taken now for the next 10 years
6G has to consider new scenarios and services trends, and the experience from previous generations
CT takes the lead of technical co-ordination of NAS, control plane signaling and user plane data within the mobile network and to other mobile networks, and signaling within the network capability exposure framework and its interfaces
CT will discuss 6G from Q4 2025 to ensure the protocol study in stage 3 and the co-ordination with other organizations (like IETF) with enough time
2024
#103
Mar.
#111
Mar.
#107
Mar.
#104
Jun.
#108
Jun.
#112
Jun.
#105
Sep.
#109
Sep.
#102
Dec.
#106
Dec.
#110
Dec.
TSGs
Workshop 6G TSGs
Stage 3 6G SID def.
#113
Sep.
#114
Dec.
#115
Mar.
Jun
Workshop IMT-2030 use cases
#116
SA1 6G Study(ies)
SA1 6G SID def.
SA2 6G Study(ies)
Stage 3 6G Study(ies)
2025
2026
2027
SA2 & RAN WGs 6G SID def.
SA3/4/5/6 6G SID def. TBD
or
TBD
SA3/4/5/6 6G Study(ies)TBD

## Slide 4: New Scenarios and Services Trends
Immersive Communication
Supporting mixed traffic of video, audio, and other environment data in a time-synchronized manner
AI and Communication
A set of new capabilities related to the integration of AI (e.g. AI Agent) and compute functionalities
Hyper Reliable and Low-Latency Communication
Applications such as machine interactions, emergency services, tele‑medicine, and monitoring for electrical power transmission and distribution
Ubiquitous Connectivity
Address presently uncovered or scarcely covered areas, particularly rural, remote and sparsely populated areas
Massive Communication
High connection density, and depending on use cases, different data rates, low power consumption, mobility, extended coverage, and high security and reliability
Integrated Sensing and Communication
Support of high-precision positioning and sensing-related capabilities, including range/velocity/angle estimation, object and presence detection, localization, imaging and mapping
Usage scenarios and overarching aspects of IMT-2030

## Slide 5: Lessons from previous generations 1/4
Extensibility and backward compatibility:
  In the very first release, a service is defined with certain essential functionalities, however, the service is extended with more optional functionalities in further releases, and change to those essential functionalities (as defined in early release) should be optional.
    Taking the Nnwdaf_EventSubscription service as an example, in Rel-15, it only support the analytics of network slice load level information as essential analytics Id, however, the analytics is changed to be optional supported in the service from Rel-16, can be optional deployed by the operator network.
    The design of the UE policy delivery protocol in 5GS, which in Rel-15 included only the delivery of URSP & ANDSP, and then in later releases the delivery of additional policies for verticals (V2XP in Rel-16, ProSeP in Rel-17, RSLPP and A2XP in Rel-18) was added, conditional to UE support
  Any feature marked as Mandatory in a release is hard/nearly impossible to be changed to Optional after freeze in later Releases, therefore requires careful consideration during initial release and should not be challenged after freeze, see e.g. SOR-CMCI discussion in Rel-17 after freeze of Rel-18 in CT.
Abbreviations:
NWDAF network data analytics function
URSP UE route selection policy
ANDSP Access network discovery and selection policy
V2XP Vehicle-to-Everything Policy
ProSeP Proximity Service policy
RSLPP Ranging and Sidelink Positioning Policy
A2XP Aircraft-to-Everything policy
SOR-CMCI steering of roaming connected mode control information

## Slide 6: Lessons from previous generations 2/4
Network Reliability:
  Network reliability has been attracting more and more attention and should be considered at the beginning of the architecture design. (A number of 5GC/IMS restoration related topics were brought to CT in R18/19)
    Architectural impact should be considered before it is too late. (The study of FS_IMS_RES was carried out in CT4, but concern was raised that the solutions have much impact on stage2/SA2)
    The features such as generic NF set concept, eSBA was not defined in the initial version of 5G (R15) to support this concept, operators who deployed R15 need to update the overall network planning to introduce those features
    To fulfill the requirements from vertical market, a set of NFs may be deployed on the enterprise side, therefore “legacy” restoration solutions may not apply, this should be considered when defining the architecture
    MINT (CT1), was added in Rel-17 to enable UEs to continue to get service in case of network outage due to e.g. a fire. For 6G, this kind of recovery mechanism ensuring continued service should be available from day 1.
Abbreviations:
IMS IP Multimedia Subsystem
eSBA enhanced Service Based Architecture
MINT Minimization of service Interruption

## Slide 7: Lessons from previous generations 3/4
More careful considerations when defining the services (assuming 6G will still be service-based)
  If a service is intended to be reusable by entities NOT defined by 3GPP, the service should not be very “3GPP specific”, e.g. mandating input of AMF ID
  Coarser or finer granularity of services
    If finer granularity of services are defined, it means different services should be able to be invoked separately, then the dependency of the two services (in term of service context) should be minimized
    Otherwise try to combine services
  More than one services or options/solutions are defined in 5G to support the same functionality or feature. The design of functions or services should avoid redundancy and coupling.
    Taking the NWDAF service as a example, both the Nnwdaf_EventSubscription and the Nnwdaf_AnalyticsInfo services can support to request and obtain different type of analytic event information and context information related to analytics subscriptions.
Abbreviations:
AMF Access and Mobility Function
NWDAF Network Data Analytics Function

## Slide 8: Lessons from previous generations 4/4
Co-ordination between SA and CT:
  Stage 2 should focus on the principle functionalities on high level and leave all impactful studies of protocol and its details to Stage 3
  Stage 2 should leave discussions on protocol limitation to stage 3, stage 3 is asked to report protocol limitation which may have functional impacts to stage 2. Protocol-wise constraint should be taken into account during stage 2 work. E.g. the UPF event exposure service was decided to be used for AI data collection from UPF, however efficiency issue was raised in CT which triggered the study of FS_PAIDC (R19)
  SA WGs when doing their stage 2 and stage 3 work should inform CT as soon as possible on possible CT impacts
  Security and authentication requirements impact protocol design a lot thus should be given in time. E.g. the requirements about “prins” came a bit late for 5G, CT made a systematic update accordingly; one example is the Ambient-IoT work and possible resulting impacts on authentication.
  Grant enough time for TSG cross-coordination between stage 2 freeze and the stage 3 freeze, e.g. ensure a 9 months time frame
Abbreviations:
UPF User Plane Function
PAIDC Protocol for AI Data Collection from UPF
PRINS Protocol for N32 Interconnect application layer Security

## Slide 9: Principles of protocol design
Criteria to consider:
  Reliability: stability, resilience, dependability
  AI-native: future proof for AI related enhancement
  Simplicity: maintenance and configuration
  Migration: Operators shall be able to upgrade their network in steps without interrupting the network service
  Extensibility across releases within 6G: extensible in a backward and forward compatible way
  High efficiency: e.g. lowest possible overhead, compact encoding, etc.
  Security: Protection of the interfaces on the signaling, authentication and user data against attacks
  Scalability: maintain (e.g. improve its performance, efficiency) and support large number of required transactions and not cause hindrance to system performance
  Operable across 3GPP systems and releases.

## Slide 10: Consideration for protocol (re-)evolution
The following aspects (non-exhaustive list) are to be considered for network protocol design in 6G:
  NAS: extend 5G NAS, rework certain aspects of 5G NAS or specify a brand-new NAS protocol for 6G
    Support of requirements on 6G NAS and the interworking with previous NAS generations according to stage 1 requirements
    Support of requirements on pre-6G NAS functionalities and capabilities according to stage 1 requirements
  User plane: Whether new protocol will be chosen or use the current one (GTP-U) as basis, if the new protocol is selected, the coexistence of different protocols will be taken into account
  Control plane, signaling interfaces: Whether new protocol (e.g. HTTP 3) will be chosen or use the current one (HTTP 2), if the new protocol is selected, the coexistence of different protocols will be taken into account; On signaling interfaces in 6G should we continue the use of JSON or replace it with something else
  Network capability exposure e.g.:
    whether the 3rd party will be aware of the exposed API offered by the 6G network;
    reusing HTTP 1.1 (mandatory)/HTTP 2 (recommended) or new protocol like HTTP 3, per interface or API specific
  Data protocol: support efficient data management and transmission protocol, the coexistence of different protocols may be considered
  AI in the network: AI will be everywhere in 6G, the protocol should be studied to support AI, based on the architecture

## Slide 11: Stage 2 work in CT
The topics to be studied in CT for 6G will be determined by CT WGs taking into account their respective ToR e.g. Network selection, Steering of Roaming, Public warning system, SMS, Restoration

## Slide 12: Summary
Stage 2 should focus on the Principle functionalities on high level and should leave all protocol details to Stage 3
Stage 2 should leave discussions on protocol limitation to stage 3, stage 3 is asked to report Protocol limitation which may have functional impacts to stage 2.
Careful check has to be performed on functionalities which are mandatory, Change of Mandatory to optional is only possible until freeze of the release.
MRP’s or other groups, e.g. GSMA, who triggered a feature shall check before freeze of the Release that their requirements are reflected correctly
Features which need to have recovery mechanism shall be identified very early e.g. first Release
Extensibility and backward compatibility remain very important

## Slide 13: Thank You!