## Slide 1: RIS-based Wireless Transmission for Designing Efficient Base-Stations (For 6G)
3GPP 6G Workshop
Vestel Electronics, Turkiye

## Slide 2: Outline
Reconfigurable Intelligent Surface: Features and Applications
RIS-based Wireless Transmission: Concept and Implementation
Requirements for Realizing RIS-based Low-complexity Wireless Base-Stations
  RIS-based beamforming techniques for multi-user scenarios
  RIS-based modulation techniques

## Slide 3: Reconfigurable Intelligent Surface (RIS)
Important Features
RIS is a Programmable device that can configure the wireless channel dynamically.
Low-cost
Energy-efficient operation
Applications:
Beamforming
Channel Conditioning
Modulation (Conventional and Index Modulation)
Types:
Passive/Active RIS
Reflective/STAR RIS
3D Stacked RIS
Flexible RIS
6G: The next horizon, from connected people and thing to connected intelligence, 2021, Huawei Technologies Co., Ltd.

## Slide 4: Why RIS-based Wireless Transmission?
Motivation: RIS can be used to design wireless transmitters which are:
  Low-complexity: because modulation, beamforming, precoding, and RF processing are performed by RIS, without requiring conventional RF front ends and multiple antennas at transmitter.
  Low-cost: as RIS, which is a low-cost device, replaces all of the above components of a conventional wireless transmitter.
  Energy-efficient: RIS is intrinsically highly energy efficient in its operation.
  Spectrally efficient: as RIS can be used to transmit data both using conventional modulation and index modulation by utilizing multiple distinct channels associated with RIS elements.

## Slide 5
  Unmodulated RF signal is generated and transmitted towards RIS by a single antenna source.
  RIS can use beamforming schemes to direct the reflected beams to multiple users in a cell.
  Each reflected beam can be modulated by RIS (using conventional or IM) for corresponding user.
  Realizing the vision of RIS-based Wireless transmission requires efficient works in:
  RIS-based beamforming schemes for multi-user scenarios.
  RIS-based modulation schemes.
  Multi-RIS Coordination
RIS-based Wireless Transmission: Concept and Implementation

## Slide 6
  A number of RIS-based modulation schemes have been proposed in literature. The following summarizes some of the schemes
Space-Time Block Coding (STBC) with RIS
Quadrature Reflection Modulation with RIS
Index Modulation/Spatial Modulation with RIS
RIS based QAM/PSK/APM Modulation
Orthogonal Frequency Division Multiplexing (OFDM) with RIS
Differential RIS Modulation
E. Basar, "Reconfigurable Intelligent Surface-Based Index Modulation: A New Beyond MIMO Paradigm for 6G," in IEEE Transactions on Communications, vol. 68, no. 5, pp. 3187-3196, May 2020, doi: 10.1109/TCOMM.2020.2971486.
S. Lin, M. Di Renzo and F. Chen, "RIS-Based Quadrature Reflection Modulation," ICC 2021 - IEEE International Conference on Communications, Montreal, QC, Canada, 2021, pp. 1-6, doi: 10.1109/ICC42927.2021.9500782.
J. Yuan, M. Wen, E. Basar, G. C. Alexandropoulos and G. Chen, "Receive Quadrature Reflecting Modulation for RIS-Empowered Wireless Communications," in IVT, vol. 70, no. 5, pp. 5121-5125, May 2021, doi: 10.1109/TVT.2021.3073161.
Canbilen, A.E., Basar, E. and Ikki, S.S., 2020. Reconfigurable intelligent surface-assisted space shift keying. IEEE wireless communications letters, 9(9), pp.1495-1499.
Dinan, Mohamad H., Nemanja Stefan Perović, and Mark F. Flanagan. "RIS-assisted receive quadrature space-shift keying: A new paradigm and performance analysis." IEEE Transactions on Communications 70.10 (2022): 6874-6889.
Dinan, M.H., Di Renzo, M. and Flanagan, M.F., 2023. RIS-Assisted Receive Quadrature Spatial Modulation with Low-Complexity Greedy Detection. arXiv preprint arXiv:2301.00707.
K. Ntontin et al., "Reconfigurable Intelligent Surface-Assisted Space-Time Block Coding," IEEE Transactions on Communications, 2021.
H. Zhang et al., "Reconfigurable Intelligent Surfaces Assisted OFDM Wireless Communications," IEEE Transactions on Wireless Communications, 2021.
Y. Liu et al., "Reconfigurable Intelligent Surface-Based Amplitude and Phase Modulation for 6G," IEEE Communications Magazine, 2021
M. Elbir et al., "Reconfigurable Intelligent Surfaces for Phase Shift Keying Modulation," IEEE Wireless Communications Letters, 2020.
E. Basar, "Reconfigurable Intelligent Surface-Based Index Modulation: A New Beyond MIMO Paradigm for 6G," IEEE Transactions on Communications, 2020.
S. Lin et al., "Differential Modulation for Reconfigurable Intelligent Surface-Assisted Wireless Communications," IEEE Communications Letters, 2021.
RIS-Based Modulation Schemes