## Slide 1: Vision & priorities for next generation system architecture, core networks and protocols based on activities of HORIZON JU-SNS ORIGAMI research project
Source: Fibercop
With HORIZON-JU-SNS ORIGAMI project

## Slide 2: Novel components for the SA
Requirements | Flexibility & Scalability
GSBA | To tear down the silo-based design of different network domains, integrating one single bus to link them all
ZTL | Enhances the interactions from the mobile network operator to other entities (either other operators or application service providers) that usually have complex or limited interactions, yielding to inefficient network operation
CCL | will democratize access to extremely heterogeneous computing resources and will boost resource sharing with reliability guarantees, encouraging green transition, sustainability and greater accessibility

## Slide 3: Content
In the current architecture we identified some areas that can be improved towards 6G
Barrier: inadequate networking data representation
  Open interactions among service providers and operators with zero trust capabilities
  Improvement of the Operator Information Model as a common bases of all its Network Management Processes
Barrier: inadequate role of NDT in the OAM processes:
  Modular Architecture and Scalability
  Lifecycle Coordination and Traceability
  Enhanced Interoperability and Multi-Domain/Multi-Role Collaboration
  Adaptive Simulation and Predictive Analysis
  Efficient Resource Utilization and Cost Management
We propose some architectural modules and associated UCs that remove these barriers

## Slide 4: The Zero Trust Layer
The Zero Trust layer brings two major changes to the ecosystem:
Enables MNOs and other Network Stakeholders to have a dynamic cooperation and enable emerging models of operators establish relationships and perform financial clearing in almost real time
  The current process using Data Clearing Houses is slow, and money move slowly across geographies
  Enables new business opportunities at the service side, providing zero (or limited) trust interaction among MNO and application service providers
Enables the end-user to have control over its mobile connection
  Currently, the end–user is locked-in only with one operator and migrating (though technically possible) is cumbersome and risky
Interconnection Provider
RAN Resource Provider
Interconnection Provider
Global Operator
(Core Network)
AA.73
AA.73
AA.74
Service Charge
Service Charge
Inter-Operator tariff

## Slide 5: ZTL Use Case: Anomaly detection
In this context we leverage the monitoring data model and propose AI/ML models for (proactive) anomaly detection
  Leverage the GSBA for data collection
  Focus on data processing, and represent the expert knowledge in features to guide the anomaly detection approaches
  Closed-loop approach: anomaly detection solution to generate Incident Tickets within the incident management system of the GMNO
This use case enables network performance management via the GSBA
  Focus on integration with the incident management system within the GMNO
  Dimension the data collection and knowledge representation to achieve high efficiency in terms of processing overhead

## Slide 6: Compute Continuum Layer
The Compute Continuum Layer (CCL)
  CCL Broker: Abstractions of heterog. computing resources
  CCL ctrl: Compute-aware NF-control & management
Real-time CCL-x interfaces
  Sub-ms latency is expected
Compute awareness is required in NF control
  To avoid saturation of computing resources
  To provide compute latency guarantees
Library|Driver
LPU 1
request
request
response
response
PPU 1 (e.g., FPGA, GPU, ASIC or SIMD CPU)
PPU M (e.g., FPGA, GPU, ASIC or SIMD CPU)
…
Library|Driver
LPU M
request
request
response
response
…
Abstraction
Layer
Resource Broker
DU-U
request
response
…
DU-C
CCL-P
CCL-P
CCL-S
CCL-S
GSBA
CCL-P
CCL-S

## Slide 7: Use Case: Integration of NDT
The task offloading strategies implemented through the CCL require hardware abstraction to efficiently exploit resource pooling at the edge
Different Computiong Platform (x86 CPUs, ARM CPUs, GPUs, Quantum Computing Platform) require a common layer for basic wireless operation, decoupled from the actual execution platforms.
  To train the AI/ML algorithm that empower the Use Case, the usage of Network Digital Twins of the specific Computing Platform
  The management system can deal with this aspects, triggering online training requirements or re-training of the solutions

## Slide 8: Proposal
To evaluate the feasibility for the introduction of a SBA to all domains in the network for 6G Release 20.
To evaluate the extension of specific Network Functions towards these extended functionality enabled by the GSBA
To evaluate the feasibility for introduction of a CCL layer for the abstraction of different computing capabilities over the cloud continuum.
To evaluate the feasibility of the coupling of NDT at the NF and Network Resource level
To evaluate the feasibility of extending the exposure capabilities of the network through the integration of a Zero Trust Layer and the enforcement of a Global Operator Model

## Slide 9: References
ORIGAMI Project. Deliverable D2.1: Initial report on requirements and definition of KVIs and KPIs (Final). Zenodo. https://doi.org/10.5281/zenodo.12580929
L. E. Chatzieleftheriou et al., "Towards 6G: Architectural Innovations and Challenges in the ORIGAMI Framework," 2024 Joint European Conference on Networks and Communications & 6G Summit (EuCNC/6G Summit), Antwerp, Belgium, 2024, pp. 1139-1144, doi: 10.1109/EuCNC/6GSummit60053.2024.10597105.
Viktoria Vomhoff et al. Challenges and Opportunities for Global Cellular Connectivity https://doi.org/10.48550/arXiv.2411.19706
S. Geißler et al., "Untangling IoT Global Connectivity: The Importance of Mobile Signaling Traffic," in IEEE Transactions on Network and Service Management, vol. 21, no. 4, pp. 4435-4449, Aug. 2024, doi: 10.1109/TNSM.2024.3414975.
N. Apostolakis, L. E. Chatzieleftheriou, D. Bega, M. Gramaglia and A. Banchs, "Digital Twins for Next-Generation Mobile Networks: Applications and Solutions," in IEEE Communications Magazine, vol. 61, no. 11, pp. 80-86, November 2023, doi: 10.1109/MCOM.001.2200854.