## Slide 1
3GPP 6G Workshop 6GWS-250203
Incheon, Korea, March 10-11, 2025
EURECOM View on 6G RAN
Agenda Item: 4

## Slide 2: 6G RAN Design Principles
Concise and Efficient Specification
Avoid redundant options with identical functionality
Prioritize commercially valuable features
Unified Design
Seamlessly integrate features (ISAC, Low-Power Signals, NTN, RedCap,…) from the start
Harness synergies for enhanced efficiency and functionality
Compatibility with 5G
Support same sub-carrier spacing, waveform and modulation
Spectrum sharing and 5G channel coding as base-line
6G
5G
Energy-Efficient Communication
Support of Energy Saving techniques from the start
Mandatory support for basic low-power communication capabilities at UE

## Slide 3: Selected Key Features
ISAC
Including low-power communication
RAN Security
Enhance security of low-level signaling especially during initial access
Integrated Low-Power Design
PHY design compatible with Energy Detectors
Enhancements for Small Data Transmission
Enhancements to Small Block Length Coding
For instance DMRS-less control transmission
Extreme MIMO
Serve large number of users (>128) on same resources
Use device memory to super-charge MU-MIMO  Cache-Aided MU-MIMO

## Slide 4: Cache-Aided Multi-User MIMO
Device Memory as New PHY Resource

## Slide 5: Motivation
Plenty of DL Use Cases for Cache-Aided Transmission
Wired or wireless communications
Satellite communications
In-flight communications
Virtual Reality
Video on-demand (VoD): ≥ 70% of mobile data traffic
Very costly for providers to deliver VoD
Most VoD is cachable and most users have a lot of memory in their pockets (cell phones)
 Use Device Memory as New PHY Resource !

## Slide 6: Technology
Cache placed in device memory
e.g. when network load is low
Subpacketization
…
Overlaid MU-MIMO Transmissions
Every UE can request any file in the library
MU-MIMO transmissions are super-imposed
Library
Known symbols from local cache
Mitigated via Precoding
Estimated via DMRS
Example: Received signal of UE 1 in Group 1
Intra-group interference is subtracted
Single MU-MIMO transmission
6G

## Slide 7: Potential Gains are Significant
[1] H. Zhao, A. Bazco-Nogueras and P. Elia, “Vector Coded Caching Multiplicatively Increases the Throughput of Realistic Downlink Systems”, IEEE Trans. Wireless Com., April 2023
With realistic CSIT costs  still gain of 3-4.5 over cache-less system
Library of 90% of Netflix Traffic
About 100 most popular movies
Assume each movie is 90min
Buffering is 2min 1/45 of a movie
Full-HD Movies (2.47GB)
Cache size = 25GB
 Potential Gain Factor = 6 !
HD Movies (1.3GB)
Cache size = 25GB
 Potential Gain Factor = 7 !
SD Movies (1.3GB)
Cache size = 5GB
 Potential Gain Factor = 5 !

## Slide 8: Summary
Multimedia Services (VoD, Virtual Reality,…) are consuming significant DL communication resources
Devices have memory to intelligently cache this content
The device cache can be used to super-charge the DL transmission
The content can be delivered with large gains (300%-500%) in spectral efficiency
Requires less RF-chains (and power/cost) than comparable conventional MU-MIMO transmission