## Slide 1
Rob Davies
Philips International B.V.
Philips view on 6G (RAN)
17 February 2025

## Slide 2: Introduction
5G has brought many new features that are beneficial for healthcare related verticals:
  Enhanced communication reliability
  More robust coverage using different types of relays
  Enhanced location services
  Satellite communication
  Enhanced security
  First generation Ambient IoT to come in 2025.
We have a strong preference that 6G will build on what 5G brings, focusing on new features and feature enhancements, rather than removing features.

## Slide 3: Use cases illustration

## Slide 4: 6G radio expectations
Improved coverage over 5G NR
Improved robustness over 5G NR
Improved energy savings over 5G NR
Improved data rates over 5G NR
Support for Low Power Wide Area (LPWA)
Native support for Sidelink communication
Using RAN + UE side AIML to improve signal transmission and reception.
New wave forms where beneficial

For small battery operated wearables with at least same characteristics as NB-IoT or better (e.g., lower peak power)


With simplified operation for relays and ranging

## Slide 5: 6G support for wireless sensing
Unobtrusive way to perform e.g. activity monitoring or asset tracking etc.
6G should have native support for wireless sensing with the following features
  Wider coverage area and longer range than Wi-Fi sensing
  Support for bi-static/distributed sensing (e.g., CSI-based, similar to Wi-Fi sensing)
  Possibly new waveforms dedicated for wireless sensing for better accuracy
  Service continuity to allow tracking of moving objects over a wide area
  Improved location estimation by combining UE location and sensing

## Slide 6: 6G support for Ambient IoT
Ambient IoT = Ultra low power IoT  NB-IoT and LTE-M energy consumption and peak power requirements still too high
Very useful for applications with limited space for a good battery and (logistical) difficulties for recharging
  Inventory management, asset/patient tracking and possibly body-worn sensors
To achieve expected KPIs it requires 6G to support the current Ambient IoT air interface with extended support for:
  Device Originated Autonomous (DOA) communication
  Additional topologies, e.g. Multistatic operation
  New positioning methods
  Possibly further reducing complexity of protocols.

## Slide 7: 6G NTN communication
5G Advanced will further improve NTN communication in Rel. 20
This will provide a good basis for 6G enabling ubiquitous coverage and seamless handover across all the different types of base stations at different altitudes, including Terrestrial Network base stations.
We would like 6G NTN to incorporate improvements to lower UE energy requirements and provide improved low-energy positioning methods that do not rely on GNSS.

## Slide 8: 6G enhanced security
In 5G many new security and privacy protection features were developed
We would like 6G to support additional security improvements with RAN impact, including:
  Addressing issue of fake base stations
  Creating quantum-resistant security protocols
  Adding physical layer security to protect, e.g., RACH and MAC CE

## Slide 9: Other topics for 6G
Other features/topics that we would like to see supported in 6G with RAN impact include:
Regulatory services, including:
  robust and energy efficient PWS support
  improved location estimation for emergency situations
Interworking with 4G and 5G
Network resiliency
Computing as a service
Further improved immersive communication
Reflective Intelligent Surfaces (RIS)