## Slide 1: Results on Relative Delay under NLOS
Huawei Technologies
Fraunhofer IIS

## Slide 2: Measurement Setup #1
TX
RX LOS
RX NLOS
Production line
Production line
Corridor
Corridor
RX2a
RX2b
RX3a
RX3b
RX4a
RX1c
RX5a
RX7b
 | x [m] | y [m] | z [m]
TX | 0 | 0 | 4.2
RX1a | 20 | 0 | 1.96
RX1b | 20 | -3.7 | 1.96
RX2a | 18.5 | 0 | 1.96
RX2b | 18.5 | -3.7 | 1.96
RX3a | 17 | 0 | 1.96
RX3b | 17 | -3.7 | 1.96
RX4a | 15.5 | 0 | 1.96
RX4b | 15.5 | -3.7 | 1.96
RX5a | 14 | 0 | 1.96
RX5b | 14 | -3.7 | 1.96
RX6a | 12.5 | 0 | 1.96
RX6b | 12.5 | -3.7 | 1.96
RX7a | 11 | 0 | 1.96
RX7b | 11 | -3.7 | 1.96
RX8a | 9.5 | 0 | 1.96
RX1c | 15.7 | -7.4 | 1.96
x
y
z
RX6a
RX7a
RX8a
Corridor
RX1a
RX1b
Elevation scanned at RX only from -30° to 30°
NLOS Positions
Industry 4.0 Plant for automotive related production, Germany
Multi-band measurements: 3-10 GHz, 28-38 GHz, and 56-66 GHz
30°HPBW at TX and RX
  Azimuth&Elevation scan
TX height: approx. 4.2m
RX height: approx. 1.96m
3D TX-RX2 distance ~18m

## Slide 3: Measurement Setup #2
Machine Lab at TU Ilmenau, Germany
Multi-band measurements TX
  Directive antennas with 30° HPBW
  Scanning in azimuth: - 60° to 60° with 30° steps
  Scanning in elevation 0° to -30° with 30° steps
N1
N4
N5
N8
N9
N23
L1
L23
N17
N14
6.5m
2m
2m
TX1/2
TX1
TX2
2x Tx positions
  TX1: clutter level (at approx. 2 m heigth) – subcenario 2
  TX2: above clutter level (at approx. 4 m heigth) – subscenario 4
23x Rx positions incl. LOS and NLOS
2x23x2 = 96 triple band measurement points

## Slide 4
Position RX1b Measurement Setup #1
Extraction of relative delay in NLOS
Use peak detection to identify multpath clusters/components
The delay of the „virtual LOS“ is calculated
The relative delay is the delay difference between the first detected peak and the „virtual LOS“ of the channel
Peak dection: MATLAB® peak detection algorithm is used, which intends to find local maximas in the PDPs. Only those peaks are considered as valid peaks which cross a threshold of maximum- 5dB value.

## Slide 5: Model for relative delay in NLOS (Combined 30 GHz data of meas. setup 1&2)
Chart: Distance [m]
| 18.5 | 17 | 15.5 | 14 | 12.5 | 11 | 15.7 | 41.0072143043148 | 40.181739633818701 | 40.762625344793499 | 39.932094861151498 | 40.615164963348398 | 39.781556027888101 | 38.874948553020602 | 38.0714092200433 | 38.409134655704001 | 37.595640704741299 | 38.042891911630498 | 37.2213943854875 | 37.779116254883498 | 36.951755032745098 | 37.6199631180043 | 36.7890228193139 | 31.5989180985679 | 30.802146029132398 | 31.152714568717801 | 30.344228446279502 | 30.830044193935201 | 30.012867240568699 | 24.325328877530101 | 23.5395879318224 | 23.910701056221701 | 23.110867573503199 | 23.658436655873899 | 22.849774615956299 | 10.3851636963507 | 9.9825948530429702 | 7.7363831988856404 | 6.9174868991563701 | 6.2969992853739498
Measured | 4.11 | 2.89 | 3 | 3.41 | 3.52 | 4.07 | 6.48 | 116.9317 | 117.9687 | 118.8576 | 110.1171 | 100.3396 | 101.0804 | 104.7839 | 95.1546 | 119.0057 | 104.7839 | 117.8206 | 110.4134 | 103.3025 | 103.5988 | 92.6362 | 120.4872 | 70.2665 | 71.5998 | 80.3402 | 79.1551 | 78.8588 | 149.9677 | 44.7858 | 44.7858 | 58.2668 | 56.9336 | 57.6743 | 56.1928 | 29.0825 | 23.3049 | 2.1204 | 1.3797 | 2.4167
Model (slope=3.67, intercept=-33.33, std. Error=17.1) | 34.5648 | 29.0595 | 23.5542 | 18.0489 | 12.5436 | 7.0383 | 24.2882 | 117.1706 | 114.141 | 116.2729 | 113.2247 | 115.7317 | 112.6722 | 109.3448 | 106.3957 | 107.6352 | 104.6495 | 106.291 | 103.2759 | 105.3229 | 102.2863 | 104.7388 | 101.6891 | 82.6404 | 79.716 | 81.0027 | 78.0354 | 79.8184 | 76.8192 | 55.9449 | 53.061 | 54.4231 | 51.4876 | 53.4972 | 50.5293 | 4.7817 | 3.3042 | -4.9398 | -7.9453 | -10.2226
Clear dependence on Tx-Rx distance!

## Slide 6: Standard error analysis –Normal Distribution (Combined 30 GHz data of meas. setup 1&2)
Proposed Model 1
Relative Delay = max(alpha*d + C + n, 0)
where
alpha=3.67
C=-33.33
n~N(0,17.1)
Normal Distribution fit

## Slide 7: Standard error analysis (Combined 30 GHz data of meas. setup 1&2)
Proposed Model 2
Relative Delay = max(alpha*d + C + n,0)
Where
alpha=3.67, C=-33.33
Sign of n is uniformly distributed (+ or -)
Abs(n) follows lognormal or exponential distribution
Lognormal- and Exponential Distribution fit
Model error analysis
Let correspond to the integral square error
For Normal distribution =0.0125
For lognormal distribution =0.0167
For exponential distribution =0.0047
Exponential distribution fits best!

## Slide 8: Conclusion
Strong dependence of the relative delay on the Tx-Rx distance is observed
We have proposed two model the relative delay
  Exponential distribution seems the best fit for the variation around the linear function
  So the best model would be:
    Relative Delay = max(alpha*d + C + n,0)
      Where alpha=3.67, C=-33.33, sign of n is uniformly distributed (+ or -)
      Abs(n) follows exponential distribution