## Slide 1: Delay spread vs hall volume

## Slide 2: Background (1)
In R1-1905202 in Xi’an, Ericsson and CEA-LETI compiled all contributions on RMS delay spread in Industrial halls
  Based on the compilation, Ericsson proposed a model for the delay spread that is dependent on the hall volume

## Slide 3: Background (2)
In the email discussion [97-NR-10] different proposals on LSP parameters including DS have been collected
  Includes the hall volume-dependent function but also proposals based on new measurements and simulations
The purpose of this presentation is to see whether these proposals support or contradict the volume-dependent model proposal

## Slide 4: Parameter proposals converted to 99th percentile
For a Gaussian distribution, the 99th percentile is equal to the mean + 2.33 times sigma: mlgDS+2.33*slgDS
Using the LSP DS proposals in [97-NR-10] and the HHI contribution to the F2F, the 99th percentiles in NLOS have been estimated as follows:
Source | Hall volume, V [m3] | Estimated 99th percentile DS [ns] | Notes
ZTE | 360000 | 260-300 | Ray-tracing
CMCC | ? | 338-382 | Hall volume unknown
DOCOMO |  |  | Data already included(?)
CEA-LETI | ? | 192 | Hall volume unknown
Huawei: Shanghai | 150000 | 316 | Sigma not given, have assumed 0.18
Huawei: Munich | 2875 | 71-107 | Sigma not given, have assumed 0.18
Fraunhofer HHI + IIS | 8126-65541 | 30-270 | Hall sizes taken from arxiv paper DS is increasing with Tx height and frequency

## Slide 5: Adding these proposals to the plot of DS vs hall volume
New proposals in red
These proposals appear to be reasonably aligned with the model
CMCC and CEA-LETI results can be included as well if hall volume can be supplied
ZTE
Huawei: Shanghai
Huawei: Munich
Fraunhofer HHI + IIS