3GPP TSG-RAN WG2 AH Meeting #1807	R2-1809493

Montreal, Canada, 2-6 July 2018

Agenda item:	10.4.3.2

Source: 	Qualcomm Incorporated

Title: 	ASN.1 review Q015/Q016: Handling of FDD/TDD and FR1/FR2 capability differences

Document for:	Discussion and decision

# Discussion / Proposal

The UE can indicate different capability between FDD and TDD or between FR1 and FR2 for some of the features. In the current ASN.1, each UE capability is grouped into the following categories.

- Common:		Capability cannot be different between FDD and TDD or between FR1 and FR2

- XDD-diff:	Capability can be different between FDD and TDD

- FRX-diff:		Capability can be different between FR1 and FR2

This is done in UE-MRDC-Capability and UE-NR-Capability as shown in the figures below.

Figure-1:		the structure of UE-MRDC-Capability

Figure-2:		the structure of UE-NR-Capability

As shown by colouring in the figures, multiple instances of the same UE capability group are defined in different places. Taking generalParametersMRDC-XDD-Diff in UE-MRDC-Capability (orange in figure-1) for instance, the intention was that generalParametersMRDC-XDD-Diff is included in UE-MRDC-CapabilityAddXDD-Mode when at least one of the UE capabilities is different between FDD and TDD, otherwise it is included in generalParametersMRDC. The principle should also apply to other UE capability groups which are repeated multiple times. This principle is however not clearly specified in the current specifications.

Proposal:	To clarify the following in TS368.306.

UE-MRDC-Capability

- generalParametersMRDC-XDD-Diff is included in UE-MRDC-CapabilityAddXDD-Mode when at least one of the UE capabilities defined therein is different between FDD and TDD, otherwise it is included in generalParametersMRDC.

- measParametersMRDC-XDD-Diff is included in UE-MRDC-CapabilityAddXDD-Mode when at least one of the UE capabilities defined therein is different between FDD and TDD, otherwise it is included in measParametersMRDC.

- measParametersMRDC-FRX-Diff is included in UE-MRDC-CapabilityAddFRX-Mode when at least one of the UE capabilities defined therein is different between FR1 and FR2, otherwise it is included in measParametersMRDC.

UE-NR-Capability

- mac-ParametersXDD-Diff is included in UE-NR-CapabilityAddXDD-Mode when at least one of the UE capabilities defined therein is different between FDD and TDD, otherwise it is included in mac-Parameters.

- phy-ParametersXDD-Diff is included in UE-NR-CapabilityAddXDD-Mode when at least one of the UE capabilities defined therein is different between FDD and TDD, otherwise it is included in phy-Parameters.

- phy-ParametersFRX-Diff is included in UE-NR-CapabilityAddFRX-Mode when at least one of the UE capabilities defined therein is different between FR1 and FR2, otherwise it is included in phy-Parameters.

- measParametersXDD-Diff is included in UE-NR-CapabilityAddXDD-Mode when at least one of the UE capabilities defined therein is different between FDD and TDD, otherwise it is included in measParameters.

- measParametersFRX-Diff is included in UE-NR-CapabilityAddFRX-Mode when at least one of the UE capabilities defined therein is different between FR1 and FR2, otherwise it is included in measParameters.