3GPP TSG-RAN WG2 #103bis	R2-1815994

Chengdu, China, October 8–12, 2018

Title:	[DRAFT] LS to SA1 on RRCReject T302 Timer Exemption for MPS and MCS

Response to:

Release:	REL-15

Work Item:	NR_newRAT-Core

Source:	Vencore Labs (to be replaced by RAN2)

To:	SA1

Cc:	CT1

Contact Person:

#### Name:	Achilles Kogiantis

E-mail Address:	akogiantis@vencorelabs.com

1. Overall Description:

In NR, as part of the UAC mechanism the UE’s access attempt can be rejected. The RRCReject message includes the waitTime (T302) that takes a value from 1 to 16 seconds. All access attempts following an RRCReject message reception by the UE are subject to re-attempt delay by the timer T302, except for Emergency calls and MT access. For those attempts not exempted, only after T302 expiration the UE is allowed to make a new access attempt.

RAN2 has discussed the scenario for Multimedia Priority Services (MPS) subscribers, and wondered whether MPS subscribers should be exempt from the ‘waitTime’ timer to receive the same prioritized treatment as mobile originated Emergency Calls and MT access. This exemption from the ‘waitTime’ timer should also be applicable to Mission Critical Services (MCS)?

2. Actions:

To SA WG1, CC: CT WG1

# RAN2 kindly asks SA1 to answer the question if MPS and MCS subscribers should be exempt from the RRC Reject message with ‘waitTime’ timer to receive the same prioritized treatment as mobile originated Emergency Calls and MT access?

3. Date of Next TSG-SA WG1 Meetings:

TSG RAN WG2 Meeting #104	Nov 12–16 2018		Spokane, WA, USA

TSG RAN WG2 Meeting #105	Feb 25– March 1, 2019		Athens, Greece