3GPP TSG-RAN WG2 Meeting #104	R2-181xxxx

# Spokane, USA, 12-16 November 2018

| CR-Form-v11.2 |
| --- |
| CHANGE REQUEST |
|  | 36.331 | CR | 3749 | rev | 1 | Current version: | 15.3.0 |  |
| For HELP on using this form: comprehensive instructions can be found at http://www.3gpp.org/Change-Requests. |

| Proposed change affects: | UICC apps |  | ME | x | Radio Access Network | x | Core Network |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

| Title: | EN-DC configurations upon re-establishement |
| --- | --- |
| Source to WG: | Qualcomm Incorporated |
| Source to TSG: |  |
| Work item code: | NR_newRAT-Core |  | Date: | 2018-11-27 |
| Category: | F |  | Release: | Rel-15 |
|  | Use one of the following categories: F (correction) A (mirror corresponding to a change in an earlier release) B (addition of feature), C (functional modification of feature) D (editorial modification) Detailed explanations of the above categories can be found in 3GPP TR 21.900. | Use one of the following releases: Rel-8 (Release 8) Rel-9 (Release 9) Rel-10 (Release 10) Rel-11 (Release 11) Rel-12 (Release 12) Rel-13 (Release 13) Rel-14 (Release 14) Rel-15 (Release 15) Rel-16 (Release 16) |
| Reason for change: | There are configurations for LTE link for the purpose of multi-radio interworking in EN-DC as follows. p-MaxEUTRA-r15 p-MaxUE-FR1-r15 tdm-PatternConfig-r15 Those configurations are restricting the operation in LTE link and necessary only when the trasmission and reception in NR link are taking place. Handling of those configurations upon RRC connection re-establishment is not entirely clear in the current specification. |
| Summary of change: | Upon the initiation of RRC connection re-establishent procedure, the UE releases the following configurations. p-MaxEUTRA-r15 p-MaxUE-FR1-r15 tdm-PatternConfig-r15 |
| Consequences if not approved: | Handling of the following configurations upon RRC connection re-establishment is not entirely clear in the standard. p-MaxEUTRA-r15 p-MaxUE-FR1-r15 tdm-PatternConfig-r15 Impact Analysis: Impacted functionality: RRC connection re-establishment Inter-operability: If the network is implemented according to the CR and the UE is not, the UE may restrict its transmission power unnecessarily in radio link failure scenarios, which risks the successful completion of the recovery procedure. In addition, the de-synchronization on the TDM configuration between the network and the UE may result in transmission and reception errors. If the UE is implemented according to the CR and the network is not, the de-synchronization on the TDM configuration between the network and the UE may result in transmission and reception errors. |
| Clauses affected: | 5.3.7.2 |
|  | Y | N |  |  |
| Other specs |  | X | Other core specifications | TS/TR ... CR ... |
| affected: |  | X | Test specifications | TS/TR ... CR ... |
| (show related CRs) |  | X | O&M Specifications | TS/TR ... CR ... |
| Other comments: |  |

#### 5.3.7.2	Initiation

The UE shall only initiate the procedure either when AS security has been activated or for a NB-IoT UE supporting RRC connection re-establishment for the Control Plane CIoT EPS optimisation. The UE initiates the procedure when one of the following conditions is met:

1>	upon detecting radio link failure, in accordance with 5.3.11; or

1>	upon handover failure, in accordance with 5.3.5.6; or

1>	upon mobility from E-UTRA failure, in accordance with 5.4.3.5; or

1>	upon integrity check failure indication from lower layers concerning SRB1 or SRB2; or

1>	upon an RRC connection reconfiguration failure, in accordance with 5.3.5.5; or

1>	upon an RRC connection reconfiguration failure, in accordance with TS38.331 [82, 5.3.5.5].

Upon initiation of the procedure, the UE shall:

1>	stop timer T310, if running;

1>	stop timer T312, if running;

1>	stop timer T313, if running;

1>	stop timer T307, if running;

1>	start timer T311;

1>	stop timer T370, if running;

1>	release uplinkDataCompression, if configured;

1>	suspend all RBs, including RBs configured with NR PDCP, except SRB0;

1>	reset MAC;

1>	release the MCG SCell(s), if configured, in accordance with 5.3.10.3a;

1>	apply the default physical channel configuration as specified in 9.2.4;

1>	except for NB-IoT, for the MCG, apply the default semi-persistent scheduling configuration as specified in 9.2.3;

1>	for the MCG, apply the default MAC main configuration as specified in 9.2.2;

1>	release powerPrefIndicationConfig, if configured and stop timer T340, if running;

1>	release reportProximityConfig, if configured and clear any associated proximity status reporting timer;

1>	release obtainLocationConfig, if configured;

1>	release idc-Config, if configured;

1>	release sps-AssistanceInfoReport, if configured;

1>	release measSubframePatternPCell, if configured;

1>	release the entire SCG configuration, if configured, except for the DRB configuration (as configured by drb-ToAddModListSCG);

1>	if EN-DC is configured:

2>	perform EN-DC release, as specified in TS 38.331[82, 5.3.5.10];

2>	release p-MaxEUTRA, if configured;

2>	release p-MaxUE-FR1, if configured;

2>	release tdm-PatternConfig, if configured;

1>	release naics-Info for the PCell, if configured;

1>	if connected as an RN and configured with an RN subframe configuration:

2>	release the RN subframe configuration;

1>	release the LWA configuration, if configured, as described in 5.6.14.3;

1>	release the LWIP configuration, if configured, as described in 5.6.17.3;

1>	release delayBudgetReportingConfig, if configured and stop timer T342, if running;

1>	perform cell selection in accordance with the cell selection process as specified in TS 36.304 [4];

1>	release bw-PreferenceIndicationTimer, if configured and stop timer T341, if running;

1>	release overheatingAssistanceConfig, if configured and stop timer T345, if running;

- release ailc-BitConfig, if configured;