3GPP TSG-RAN WG2 Meeting #113bis-e		R2-210xxxx

Electronic, 12th Apr. – 20th Apr. 2021

Title:	[Draft] Reply LS to RAN4 on signalling scheme of transparent TxD

Response to:	R2-2102646 (R4-2103360)

Release:	Rel-16

Work Item:	TEI16

Source:	vivo [to be RAN2]

To:	RAN4

Cc:	RAN1, RAN5

# Contact Person:

# Name:	                Chenli

E-mail Address:	 Chenli5g@vivo.com

# 1. Overall Description:

RAN2 thanks RAN4 for the LS on signalling scheme of transparent TxD.

Regarding the new per-band capability signaling in Rel-16 for FR1 UEs supporting transparent TxD, RAN2 agreed to capture the corresponding capability in corresponding specification (TS 38.331 and TS 38.306).

RAN2 has discussed whether to enable release-independent support of this new capability from Rel-15, and the following agreements have been achieved:

- RAN2 can support release independent capability of transparent TxD for Rel-15, by allowing early implementation of the Rel-16 CRs.

- It is possible to only apply the change for this new capability for PC2 UEs for Rel-15.

# 2. Actions:

# To RAN WG4

# RAN2 kindly request RAN4 to take the above information into account during the following work, and provide feedback, if any.

# 3. Date of Next RAN2 Meetings:

TSG RAN WG2 Meeting #114-e		19 – 27 May 2021				e-Meeting

TSG RAN WG2 Meeting #115-e		TBD							e-Meeting

# Comments

I made some update on the online conclusions to adapt RAN4 LS.

What is this?

{Seau Sian}

We understand the bracketed part is in the agreement. However, we do not think this is needed to be included in the LS since RAN4 will not care how RAN2 achieve the release independent with only for PC2 in Rel-15.

Thanks for Masato and Seau Sian’s comments. That is true. This sentence comes from agreement.

I assume it means the approach that how to implement the release independence capability in RAN2 spec. My understanding is that this is trying to address comments from Ericsson/Henning that we may need two independent capability signaling with/without PC2 restriction.

But anyway, this is part is FFS, which is only related to RAN2 capability signaling. I agree we don’t need to inform RAN4. So I remove it. Thanks.