3GPP TSG-RAN WG2#113bis-e	R1-210xxxx

e-Meeting, 12th – 20th April 2021

Title:	[draft] LS on PLMN ID and cell ID for L3 relay

Response to:

Release:	Rel-17

Work Item:	NR_SL_Relay-Core

Source:	InterDigital (to be RAN WG2)

To:	SA WG2

Cc:

Contact Person:

#### Name:	Martino Freda

E-mail Address:	martino.freda@interdigital.com

1. Overall Description:

In RAN2#113bis-e, RAN2 discussed criteria for relay (re)selection, and the following agreements were made:

Agreements:

Proposal 2-1 [easy]: For L3 relay, the use of PLMN ID and cell ID is up to SA2

Proposal 2-2 [easy]: For L2 relay, PLMN ID supported as additional AS criteria for relay (re)selection.  Whether cell ID is used can be further discussed by RAN2.

Proposal 3-1 [easy]: Besides serving cell ID, PLMN ID, L2/L3 relay support (if agreed in discovery session) and relay load, other additional AS criteria are not considered in this release.

2. Actions:

To SA WG2:

ACTION: 	RAN2 kindly asks SA2 to take the above information into account.

3. Date of Next TSG-RAN WG2 Meetings:

TSG-RAN2 Meeting #114e		19-27 May 2021			Electronic Meeting

TSG-RAN2 Meeting #115e		16-27 August 2021			Electronic Meeting