3GPP TSG-RAN WG2#113bis-e	R1-210xxxx

e-Meeting, 12th – 20th April 2021

Title:	[draft] LS on PLMN ID and cell ID for L3 relay

Response to:

Release:	Rel-17

Work Item:	NR_SL_Relay-Core

Source:	InterDigital (to be RAN WG2)

To:	SA WG2

Cc:

Contact Person:

#### Name:	Martino Freda

E-mail Address:	martino.freda@interdigital.com

1. Overall Description:

In RAN2#113bis-e, RAN2 discussed criteria for relay (re)selection, and the following agreements were made:

Agreements:

Proposal 2-1: For L3 relay, the use of PLMN ID and cell ID is up to SA2

Proposal 2-2: For L2 relay, PLMN ID supported as additional AS criteria for relay (re)selection.  Whether cell ID is used can be further discussed by RAN2.

Proposal 3-1: Besides serving cell ID, PLMN ID, L2/L3 relay support (if agreed in discovery session) and relay load, other additional AS criteria are not considered in this release.

RAN2 have not decided and will further discuss whether to adopt relay load as an additional criterion for relay UE (re)selection.

2. Actions:

To SA WG2:

ACTION: 	RAN2 kindly asks SA2 to take the above information into account.

3. Date of Next TSG-RAN WG2 Meetings:

TSG-RAN2 Meeting #114e		19-27 May 2021				Electronic Meeting

TSG-RAN2 Meeting #115e		16-27 August 2021			Electronic Meeting

# Comments

To avoid misunderstanding that R2 has already decided on the necessity of relay load.