SA WG2 Meeting #124	S2-178368

Nov 27 – Dec 1, 2017, Reno, NV, USA	(was S2-17----)

Source:	Rapporteurs

Title:	5GS Ph1 Critical Open items for SA2#124

Document for:	Endorsement

Agenda Item:	5G_ph1

Work Item / Release:	5G_ph1 / Rel-15

Abstract of the contribution: This contribution proposes to identify Open items critical for completion of 5G System Phase 1 work item.

# 1. Introduction

This document intends to collect essential open or missing issues where some resolution is still needed for specifying a complete, operational phase 1 system within the scope defined by the WI objectives.2. Critical opens for completion of 5G System Ph-1 WID

The first version of the critical open items can refer to S2-177252 for SA2#123.

| Item # | Agenda Item | Title | Description | Comments | Known contributors |
| --- | --- | --- | --- | --- | --- |
| OI#1 | 6.5.8 | LCS architecture | LCS architecture is incomplete thus still in the annex of 501 at the moment. Need to conclude on LCS architecture thus need resolution of LCS architecture open items to ensure completion in rel-15 Ph1 |  | Nokia (Gyuri Wolfner) Huawei (Runze) CMCC (Aihua Li) |
| OI#2a | 6.5.8 | Emergency services fallback | 23.501 part on the basic approach. When NR/5GC does not support emergency services, may trigger procedures, e.g., RRC release w/ redirection. | This is postponed in SA2#123 | Nokia (Devaki) Lenovo (Genadi) |
| OI#2b | 6.5.8 | Emergency services fallback | 23.502 related procedures. | This is postponed in SA2#123 | Nokia (Devaki) |
| OI#3 | 6.5.11 | UDR further clarification | Follow up of UDR architecture decided in SA2#123 to further clarifies in 23.502 how UDR services are invoked in procedures by e.g., UDM, PCF and what are the related Data Set/Subset Identifiers |  | For PCF data set and subset identifiers in 23.503. (Ericsson Belen) |
| OI#3a | 6.5.11 | UDR discovery | Solution for NF consumer to discover the right UDR instance | This is unresolved by the agreed architecture | Nokia (Devaki) CMCC (Tao) Ericsson (MCruz) |
| OI#4a | 6.5.1 | Network Slicing: alignment between specs | Aligning the 501 text with the approved 502 text on clarifying how the multi-level NRFs support the roaming procedures during the UE registration and session establishment. |  | Telecom Italia (Mario), ZTE (Tricci) CMCC (Chen wei) Huawei(Hui) |
| OI#4b | 6.5.1 | NSI ID | Is NSI ID needed? Would NSI ID be allocated by NSSF or by NRF when multiple NSIs correspond to the same S-NSSAI? |  | Huawei (Patrice), KDDI(takeshi) |
| OI#4c | 6.5.1 | Slice privacy | After LS IN S2-176970 received from SA3 clause 5.15.5.4 Slice Privacy Considerations needs to be removed |  | Telecom Italia (Mario) |
| OI#4d | 6.5.1 | Triggering NSSP on UE service policy update correspond-ing to slice configura-tion change | Addressing ENs in 23.501 for multiple possible scenarios when PLMN changes the configured NSSAI which may cause the NSSP to update UE for the network slicing configuration policy |  | ZTE (Tricci) |
| OI#4e | 6.5.1 | SM Procedure updates on handling network slice availability in a PLMN | Updating the existing SM procedures in both 23.501 and 502 to handle network slice availability based on last SA2#123 agreement on the granularity and dynamicity when detecting the change of the network slice availability |  | E///(Peter)? |
| OI#4f | 6.5.1 | Slice isolation | Isolation support among network slices for a given UE | Contentious? People commented to OI#4a of SA2#123 offline & online | Nokia (Alessio) Huawei(Patrice) |
| OI#4g | 6.5.1 | Configuring NSSF with what S-NSSAI a TA supports (or does not support) at the RAN capability level | The NSSF may have business logic configured per UE/TA. this needs to be intersected with the capabilities of the RAN per TA in order to determine the allowed NSSAI) the AMF obtains these capabilities from the RAN at N2 establishment. |  | Nokia (Alessio) Ericsson (Peter) |
| OI#4h | 6.5.1 | Slice and AMF selection at HO procedure | 1) How to select the set of Network Slice(s) in the target PLMN during HO procedure? 2) How to select the target AMF during the HO procedure. |  | Ericsson (Peter) Huawei(Fenqin) Lenovo (Genadi): aligning the HO procedure in case of changed set of Network Slices |
| OI#4i | 6.5.1 | Slice support for UE | Simplifying UE support requirements where possible |  | Huawei (Patrice) |
| OI#4j | 6.5.1 | Minimising SLA dependencies | Avoiding to require SLA updates for each change of S-NSSAIs by the home operator |  | Huawei (Patrice, Fenqin) |
| OI#4k | 6.5.1 | maximum number of simultaneous slices connection per UE | Align with RAN3 agreements on maximum number of simultaneous slices connection per UE |  | DOCOMO (Malla) |
| OI#6 | 6.5.9 | EBI Management | Clarification on EBI management, such as EBI exhaustion, EBI re-building after intra-RAN or inter-RAT mobility | This is postponed in SA2#123 | Huawei (Runze) |
| OI#7a | 6.5.6 | UE Policy Pre-Configure | How to pre-configure policy in UE, and how to use those Policy | Postponed from SA2#123 | Huawei |
| OI#7b | 6.5.6 | UE Policy transfer | Addressing the EN of policy transfer from PCF to UE, e.g., considering limitation of NAS PDU size Whether to use a new procedure or apply UE configuration procedure to transfer UE policies from AMF to UE? |  | Nokia (Gyuri) Huawei Qualcomm (Cheng Hong) Ericsson (Belen) NEC (Iskren) |
| OI#7c | 6.5.6 | UE policy | Define UE Route selection policy and related UE behavior (Clause 6.6 of TS 23.503) |  | Nokia (Gyuri) Huawei(Ouyang) Qualcomm (Cheng Hong) Ericsson (Belen) NEC (Iskren) |
| OI#8a | 6.5.11 | NSSF Service | Defines NSSF services, compliant with both the options for SMF selection in roaming agreed at SA2 #123 |  | Oracle(Uri), Telecom Italia (Mario) |
| OI#8b | 6.5.11 | NRF Discovery in roaming | NFs Discovery across PLMNs needs to be aligned with the procedure for SMF selection in roaming agreed at SA2 #123 Note: NF service discovery may align to have UE identity information (e.g., SUPI as optional parameter. This may also be solved together with OI#3a) |  | Telecom Italia (Mario) |
| OI#8c | 6.5.11 | NRF authorization | To comply with requirements agreed in S2-177633 at least the Requester ID should be added to the Nnrf_NFDiscovery service |  | Telecom Italia (Mario) |
| OI#9 | 6.5.11 | SBA framework | UDSF Services/Service operations | Contentious-whether we need to wait CT progress first. | Oracle(Uri) . Orange (Thouraya) |
| OI#10 | 6.5.9 | Interworking w/o N26 | How to correlate the sessions between source and target systems | Postponed to SA2#124 | NTT DOCOMO (Jari) Orange (Thouraya) |
| OI#11 | 6.5.1 | Network slicing and Interworking with EPS | Resolve the editor’s notes in 5.15.7 in TS 23.501. Add corresponding details to TS 23.502. Determining S-NSSAIs for PDN connections moved from EPC. |  | NTT DOCOMO (Malla) CMCC (Aihua) Huawei(Fenqin) Qualcomm (Sebastian) |
| OI#12 | 6.5.10 |  | N3IWF/ePDG selection | A voice-centric UE MAY need to select an ePDG when IMS voice is not supported | Nokia (Nicolas) |
| OI#13 | 6.5.10 |  | Mobility between 3GPP and NON 3GPP in EPC IWK scenarios Architecture for mobility between ePDG connected to EPC and 5GC. Handover between ePDG and 5GS and Handover between N3IWF and EPS with AMF relocation |  | Nokia (Nicolas) Qualcomm (Sebastian) |
| OI#15 | 6.5.10 |  | ANDS (Access Network Discovery and Selection) | More description is needed to reflect the intension. This related with OI#7. | Nokia (Gyuri) Huawei (Marco) |
| OI#16 | 6.5.10 |  | Support of emergency services over non-3GPP untrusted access authenticated UEs unauthenticated UEs |  | Nokia (Nicolas) |
| OI#17 | 6.5.10 |  | 3GPP based authentication for access to N3GPP Access Network (acknowledged as a valid issue at SA2#123) |  | Nokia (Nicolas) Huawei (Marco) |
| OI#18 | 6.5.3 |  | NAS SM: split between info that any SMF understands and info that V-SMF not meant to understand (CT1 LS + discussion during e-mail approval) |  | Nokia (LTH) |
| OI#19 | 6.5.3 |  | UPF selection related issue (postponed at last SA2) |  | Nokia (LTH) Huawei (Runze, Patrice) |
| OI#20a | 6.5.3 |  | Add the AF control of whether DNAI (i.e. application instance) change should or should not occur when there is ongoing traffic with an application instance at the change of UPF |  | Nokia (LTH) Huawei(Patrice) |
| OI#20b | 6.5.3 |  | Support of application identification at dedicated PDU session setup for AF influence |  | Huawei(Patrice) |
| OI#21 | 6.5.4 |  | AS security: pass security parameters to AN even at registration (also needed by N3GPP) | Postponed from SA2#123 | Nokia (Devaki) Huawei |
| OI#22 | 6.5.9 | Interworking | EPS IWK IDLE mode mobility procedures – Transfer of ETH PDU Sessions as non-IP from 5GS to EPS | Postponed from SA2#123 | Nokia (Devaki) Huawei(Xiaobo) |
| OI#23 | 6.5.1 |  | 5GC Internal overload control. Scope of work to be done in rel-15 needs to be determined; Scope of work to be deferred to CT4 needs to be agreed along with an LS out | Postponed from SA#123 |  |
| OI#25 | 6.5.9 | Interworking | Mapped and native security context handling and related GUTI aspects for EPC-5GC interworking |  | Qualcomm (Sebastian) Huawei (Ouyang) |
| OI#26 | 6.5.10 |  | Home routed handover between 3GPP and N3GPP when a UE is connected via same or different PLMNs in 3GPP and non-3GPP accesses. | Postponed from SA2#123 | LGE (Myungjune) Nokia (Nicolas) Huawei (marco) |
| OI#27 | 6.5.2 |  | AMF and TNL Management – Handling non-UE associated signalling and fixes to AMF planned removal (specifically handling per UE messages) Clarification on the AMF management related NF service | This was partly postponed from SA2#123 | Nokia (Devaki) Huawei(Fenqin) |
| OI#28 | 6.5.2 |  | Relationship between Load re-balancing procedure and AMF planned removal | Open issue identified during SA2#123 | Nokia (Devaki) |
| OI#29 | 6.5.11 |  | NF Management – Deregistration | Gap in the spec | Nokia (Devaki) |
| OI#30 | 6.5.2 |  | How NF can subscribe for AMF planned maintenance? | Postponed from SA2#124 | Huawei(Fenqin) |
| OI#31 | 6.5.10 |  | Service Request procedure for non-3GPP | Postponed from SA2#123 | Huawei(Marco/Hualin) |
| OI#32 | 6.5.1 |  | Removal of EN on Triggering of NSSP update ENs removal |  | Nokia (Alessio) |
| OI#33 | 6.5.6 | Distribution of the policies to UE | Resolving the EN on whether UE can provide information to assist the PCF to decide the UE Policies delivery |  | Orange (Antoine) |