SA WG2 Meeting #127	S2-184078

Apr 16 - 20, 2018, Sanya, China	(revision of S2-183492)

| CR-Form-v11.2.1 |
| --- |
| CHANGE REQUEST |
|  | 23.503 | CR | 0055 | rev | 1 | Current version: | 15.1.0 |  |
| For HELP on using this form: comprehensive instructions can be found at http://www.3gpp.org/Change-Requests. |

| Proposed change affects: | UICC apps |  | ME |  | Radio Access Network |  | Core Network | x |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

| Title: | Network slicing information for binding the AF request to the relevant PCF |
| --- | --- |
| Source to WG: | Nokia, Nokia Shanghai Bell, China Mobile, ZTE |
| Source to TSG: | SA2 |
| Work item code: | 5GS_Ph1 |  | Date: | 2018-04-10 |
| Category: | F |  | Release: | Rel-15 |
|  | Use one of the following categories: F (correction) A (mirror corresponding to a change in an earlier release) B (addition of feature), C (functional modification of feature) D (editorial modification) Detailed explanations of the above categories can be found in 3GPP TR 21.900. | Use one of the following releases: Rel-8 (Release 8) Rel-9 (Release 9) Rel-10 (Release 10) Rel-11 (Release 11) Rel-12 (Release 12) Rel-13 (Release 13) Rel-14 (Release 14) Rel-15 (Release 15) Rel-16 (Release 16) |
| Reason for change: | There is still an unresolved EN left for binding the AF request to the relevant PCF: “Editor's note: Additional information needed by the network functionality, e.g. for network slicing, is FFS.” Concerning the case that there might be multiple network slice instances deployed in a single DNN, each contains a PCF and the same private IPv4 address may be allocated to the UE in different network slice instances, it is necessary to additionally consider the network slicing information for binding the AF request to the PCF, and the slicing information may correspond to S-NSSAI based on operator configuration. |
| Summary of change: | Update the description for binding the AF request to the PCF by adding network slicing information as the binding information. Remove the EN. |
| Consequences if not approved: | Insufficient information to bind the AF request to the PCF and unresolved EN. |
| Clauses affected: | 6.1.1.2.1 and 6.1.1.2.2 |
|  | Y | N |  |  |
| Other specs |  | X | Other core specifications | TS/TR ... CR … |
| affected: |  | X | Test specifications | TS/TR ... CR ... |
| (show related CRs) |  | X | O&M Specifications | TS/TR ... CR ... |
| Other comments: |  |

First Change

#### 6.1.1.2	Binding an AF request targeting an IP address to the relevant PCF

##### 6.1.1.2.1	General

When multiple and separately addressable PCFs have been deployed, a network functionality is required in order to ensure that an AF needing to send policies about UE traffic identified by an UE address can reach over N5/Rx the PCF holding the corresponding PDU Session information. This network functionality has the following characteristics:

-	It has information about the user identity, the DNN, the UE (e.g. IP) address(es), the S-NSSAI and the selected PCF address for a certain PDU Session.

-	For IP PDU Session type, it shall receive information (i.e. the PCF address, the UE address, the DNN and the network slicing information) when an IP address is allocated or released for a PDU Session.

NOTE 2: A private IPv4 address may be allocated. In case the same private IPv4 address is allocated in different slice instance, the network slicing information (i.e. S-NSSAI) is used to bind the request of an AF owned by the operator to the relevant PCF.

-	For Ethernet PDU Sessions supporting binding of AF request based on MAC address, it shall receive information (i.e. the PCF address, the UE address, the DNN and the network slicing information) when a MAC address is detected as being used by the UE over the PDU Session; this detection takes place at the UPF under control of SMF; This is defined in TS 23.501 [2] clause 5.8.2.

-	The functionality determines the PCF address, selected by the PCF discovery and selection function described in TS 23.501 [2], according to the information carried by the incoming requests from the AF. In addition to the UE address, the AF request may also include:

-  either an AF-Service-Identifier for NEF to derive the DNN and network slicing information (i.e. S-NSSAI) as specified in clause 6.3.7.2 of TS 23.501[2];

- or DNN and network slicing information.

-	This functionality is able to proxy or redirect N5/Rx requests targeting a UE IP address.

##### 6.1.1.2.2	The Binding Support Function (BSF)

The BSF has the following characteristics:

-	The BSF stores information about the user identity, the DNN, the UE (IP or Ethernet) address(es), the S-NSSAI, and the selected PCF address for a certain PDU Session. This information may be stored in the UDR as structured data or internally in the BSF.

-	The PCF registers, updates and removes the binding information from the BSF using the Nbsf management service operations defined in TS 23.502 [3].

-	The PCF ensures that it is updated each time an IP address is allocated or de-allocated to the PDU Session or, for Ethernet PDU Sessions supporting binding of AF request based on MAC address, each time it has been detected that a MAC address is used or no more used by the UE in the PDU Session.

-	For retrieval binding information, any NF, such as NEF or AF, that needs to discover the selected PCF for the tuple (UE address, DNN, S-NSSAI, SUPI, GPSI) (or for a subset of this Tuple) uses the Nbsf management service discovery service operation defined in TS 23.502 [3].

The BSF may be deployed standalone or may be collocated with other network functions, such as PCF, UDR, NRF, SMF.

NOTE 2:	Collocation allows combined implementation.

For any AF using Rx, such as P-CSCF, the BSF determines the selected PCF address according to the information carried by the incoming Rx requests. The BSF is able to proxy or redirect Rx requests targeting an IP address of a UE to the selected PCF.

END OF CHANGES