SA WG2 Meeting #128bis 	S2-18xxxx

20 – 24 August 2018, Sophia Antipolis, France	 (revision of S2-18xxxx)

Source:	Nokia, Nokia Shanghai Bell

Title:	Evaluation of solutions per key issue

Document for:	Approval

Agenda Item:	6.16

Work Item / Release:	FS_PARLOS_SA2

Abstract of the contribution: This paper provides a comparison of the solutions on a per key issue basis, and proposes corresponding conclusions.

# Discussion

# Proposal

It is proposed to update TS 23.715 as follows.

FIRST CHANGE

# 2	References

The following documents contain provisions which, through reference in this text, constitute provisions of the present document.

-	References are either specific (identified by date of publication, edition number, version number, etc.) or non-specific.

-	For a specific reference, subsequent revisions do not apply.

-	For a non-specific reference, the latest version applies. In the case of a reference to a 3GPP document (including a GSM document), a non-specific reference implicitly refers to the latest version of that document in the same Release as the present document.

[1]	3GPP TR 21.905: "Vocabulary for 3GPP Specifications".

[2]	3GPP TS 22.101: "3rd Generation Partnership Project; Technical Specification Group Services and Systems Aspects; Service aspects; Service principles".

[3]	3GPP TS 22.115: "3rd Generation Partnership Project; Technical Specification Group Services and System Aspects; Service aspects; Charging and billing".

[4]	3GPP TS 22.228: "3rd Generation Partnership Project; Service requirements for the IP multimedia core network subsystem".

[5]	3GPP TS 23.401: "General Packet Radio Service (GPRS) enhancements for Evolved Universal Terrestrial Radio Access Network (E-UTRAN) access".

[6]	3GPP TS 23.203: "Policies and Charging control architecture; Stage 2".

[7]	3GPP TS 23.228: "IP Multimedia Subsystem (IMS); Stage 2".

[8]	3GPP TS 23.167: "3rd Generation Partnership Project; Technical Specification Group Services and Systems Aspects; IP Multimedia Subsystem (IMS) emergency sessions".

[9]	3GPP TS 24.229: "IP multimedia call control protocol based on Session Initiation Protocol (SIP) and Session Description Protocol (SDP); Stage 3".

[10]	3GPP TS 22.011: “Technical Specification Group Services and System Aspects; Service accessibility”.

NEXT CHANGE

# 8	Evaluation

Editor's note:	This clause will provide a general evaluation of the solutions.

| Key Issue #EPC-1: Network indicating support for Restricted Local Operator Services and related UE behaviour | Description | Advantages | Drawbacks |
| --- | --- | --- | --- |
| Solution #1 | 1)A new SIB provided by E-UTRAN indicates that the PLMN is configured to supports Restricted Local Operator Services. 2)The PLMNs where RLOS is supported may be stored in UICC (or ME) 3)Whether automatic PLMN selection needs to be supported for RLOS will be confirmed by CT WG1. | 1)It is the only way to prevent UEs to even send a message. 2)In line with SA1 3)Automatic selection is contrary to SA2 requirement in TS 22.011 [10] clause 3.2.2.2: “If registration cannot be achieved on any PLMN and at least one PLMN offering restricted local operator services has been found, the UE shall offer the user to select one of these networks (i.e. user consent for RLOS PLMN selection is necessary).” | None |
| Solution #9 | 1)New SIB: same as solution #1 2)PLMN selection by user or configured in ME | 1)Same | 1)None for new SIB. 2)PLMN selection configured in ME would require more specification work. |

| Key Issue #EPC-2: RLOS request indication | Description | Advantages | Drawbacks |
| --- | --- | --- | --- |
| Solution #2 | RLOS indication in Attach (UE-CN) | For entering RLOS EPC procedures | None |
| Solution #4 | RLOS indication in Attach (UE-CN) | For entering RLOS EPC procedures | None |
| Solution #9 | RLOS RRC establishment cause (UE-RAN) | For admission control in RAN | RAN impacts |

| Key Issue #EPC-3: Support of unauthenticated UEs access to RLOS (congestion issue) | Description | Advantages | Drawbacks |
| --- | --- | --- | --- |
| Solution #1 | An operator may decide to unset the SIB indicator e.g. using OAM to prevent access attempts from UEs for RLOS e.g. in case of network congestion | No impacts to the specs | 1) RLOS for all UEs or no UEs 2)Slow mechanism 3)Cannot be extended to CN congestion situations |
| Solution #9 | The E-UTRAN may reject the RRC connection establishment with extended wait timer for RLOS attempts | 1)Per UE mechanism 2)Fast and proportional to the level of congestion 3)Can also apply before congestion 4)Can be extended to CN overload by adding S1 overload message | RAN impacts |

| Key Issue #EPC-3: Support of unauthenticated UEs access to RLOS (EPC access issue) | Description | Advantages | Drawbacks |
| --- | --- | --- | --- |
| Solution #6 | Partial solution: Enabling VoLTE calls after initial attachment: First option: the RLOS APN can lead to a portal that guides the user to various services. Alternatively, if the UE attached to RLOS APN can be IMS authenticated, the UE can use IMS APN to re-(register) in IMS In the second option, the RLOS APN may lead directly to the IMS network to initiate the requested RLOS VoLTE service SIP signalling may not acquire the QCI 5 that would typically be associated with an APN dedicated for IMS | The text related to QCI=5 might not be used should be captured | Not a full solution Apart from non-roamers UEs in limited service state, UEs cannot be authenticated. So, text is incorrect. |
| Solution #2 | RLOS attach with RLOS indication, no authentication, configured APN for RLOS, P-CSCF address in PCO, PGW shall block any traffic that is not from or to addresses of network entities (e.g. P-CSCF, captive portal), UE and Network shall implicitly detach without NAS signalling transactions. | Basic solution. | Some aspects are missing |
| Solution #4 | Same as solution #2 plus charging, location services, mobility aspects. Difference is that authentication is performed for non-roaming UEs in limited service state in order to use credentials (see key issue EPC#4). | Charging aspects, ARP aspects, PCC deployments considerations. | None |

| Key Issue #EPC-4: Support of authenticated UEs access to RLOS | Description | Advantages | Drawbacks |
| --- | --- | --- | --- |
| Solution #2 | UE requesting RLOS is authenticated but in limited state: MME skips the authentication | Simple; authentication is always skipped when RLOS indication is present | No integrity protection nor ciphering for control and user planes |
| Solution #4 | UE requesting RLOS is authenticated and non-roamer but in limited state: MME performs the authentication to get credentials | It allows to integrity protect and cipher control and user planes. | More complex than solution #2 |

| Key Issue #EPC-6: Collection of charging information | Description | Advantages | Drawbacks |
| --- | --- | --- | --- |
| Solution #4 | Charging of RLOS PDN connections can be performed by OFCS and OCS as for regular PDN connections. The rating group provided by PCRF should just be a RLOS specific rating group | No changes. Only configuration for RLOS. | None |

| Key Issue #EPC-7: Level of security | Description | Advantages | Drawbacks |
| --- | --- | --- | --- |
| Solution #2 | Mimics emergency calls for unauthenticated UEs per 23.617 annex K.3. Treats all RLOS requests as for unauthenticated UEs. | The solution supports the requirement "Level of security should not be less than that which is currently applied to existing equivalent network access methods (e.g., unauthenticated emergency calling)". |  |
| Solution #4 | Mimics emergency calls for unauthenticated UEs per 23.617 annex K.3. In addition, for UEs in limited service state for which subscribers belong to the local PLMN, integrity protection and ciphering is ensured for signalling and user plane. | The solution supports the requirement "Level of security should not be less than that which is currently applied to existing equivalent network access methods (e.g., unauthenticated emergency calling)". It allows to integrity protect and cipher control and user planes. |  |
| Solution #11 | In order to reduce the fraud risks associated with RLOS, the UE shall not offer RLOS services to the user unless the serving cell has a Mobile Country Code from the set {310, …, 316} | Simple additional mechanism only impacting the ME | Not possible for other countries to adopt RLOS in the future. Even if this list evolve, the old UEs will not be able to obtain RLOS services in new adopting countries. Partial solution Should it be GSMA decision? |

| Key Issues #IMS-1: Support for unauthenticated and authenticated user #IMS-2: Identification of Restricted Local Operator Services at IMS layer #IMS-3: Handling IMS session for Restricted Local Operator Services | Description | Advantages | Drawbacks |
| --- | --- | --- | --- |
| Solution #3 | RLOS indication in SIP REGISTER. In line with S8HR emergency calls specified in 23.167 Annex K3. No authentication at IMS layer since 23.167 Annex K3 is for unauthenticated UEs. | Minimal changes if 23.167 Annex K.3 is reused as is. | No integrity protection nor ciphering for non-roaming UEs in limited service state. |
| Solution #5 | Same as solution #3 but where the non-roaming UEs in limited service state are authenticated only to retrieve credentials. | It allows to integrity protect and cipher control and user planes. | More complex than solution #3 |
| Solution #7 | In the first scenario (unauthenticated UEs), RLOS UEs are allowed to make VoLTE calls even if their IMS registration cannot be successful. In the second scenario (authenticated UEs), RLOS UEs are registered in IMS with identities specially assigned for RLOS that allow them to make VoLTE calls | To capture: based on operator policy, be configured with a limited set of destinations | No clear description. Looks like solution #5 but does not state whether 23.167 is reused or if it rely on new procedures (which would have more impacts) |
| Solution #10 | Skipping IMS registration as for emergency calls. |  | Not in line with S8HR emergency calls specified in 23.167 Annex K3 |

| Key issue #IMS-4: Support of emergency services by UEs attached for RLOS | Description | Advantages | Drawbacks |
| --- | --- | --- | --- |
| Solution #3 | Not described |  |  |
| Solution #5 | UE does not detach to initiate an emergency call: the P-CSCF will route the emergency call to E-CSCF | No need to detach from RLOS APN to obtain emergency call. Minimal changes to P-CSCF. | None |
| Solution #8 | The UE may detach from RLOS and then do emergency Attach, or the UE may decide to stay RLOS attached and to establish an emergency PDN connectivity towards the emergency APN. |  | Not clear which procedure is intended. Complexity / more impacts if we have to implement both. |

NEXT CHANGE

# 9	Conclusions

Editor's note:	This clause will capture agreed conclusions from the study.

For Key Issue EPC#1, it is agreed that:

-	A new SIB provided by E-UTRAN indicates that the PLMN is configured to supports Restricted Local Operator Services.

-	The PLMNs where RLOS is supported may be stored in UICC (or ME).

-	In automatic PLMN selection, if registration cannot be achieved on any PLMN and at least one PLMN offering restricted local operator services has been found, the UE shall offer the user to select one of these networks (i.e. user consent for RLOS PLMN selection is necessary), per TS 22.011 [x] clause 3.2.2.2.

For Key Issue EPC#2, it is agreed that:

-	The UE shall indicate in the Attach Request that the attachment is for RLOS.

-	During the RRC connection establishment procedure, the UE indicates in the RRC signalling that the RRC connection is for RLOS access, using RLOS RRC establishment cause, per solution #9.

For Key Issue EPC#3, it is agreed that:

-	For congestion issue, solution #9 is adopted.

-	For EPC access issue, solution #4 is adopted.

For Key Issue EPC#4, it is agreed that:

-	Solution #4 is adopted.

For Key Issue EPC#6, it is agreed that:

-	Solution #4 is adopted.

For Key Issue EPC#7, it is agreed that:

-	Solution #4 is adopted.

For Key Issues IMS#1, IMS#2, IMS#3, it is agreed that:

-	Solution #5 is adopted.

-	Based on operator policy, be configured with a limited set of destinations.

For Key Issue IMS#4, it is agreed that:

-	Solution #5 is adopted.

END OF CHANGES