## Slide 1: Discussion on remain editors for FS_PIN
Zhenhua Xie
vivo

## Slide 2
AF manages and releases the PIN session accordingly
  No 5GC impact
5GC manages
  SMF impact
Both AF and 5GC manages
  AF provides information to PCF (directly or indirectly)
  PCF notifies SMF
  SMF and PCF impact
It is FFS how to support of validity duration and time validity for a PIN.
KI#3

## Slide 3
No new parameters
  No 5GC impact
New parameters for XR applications (S2-2210735)
  May need coordination with FS_XRM
  PEGC impact
  Other NF impact?
It is FFS whether more parameters are needed in non-3GPP QoS assistance information.
KI#4 and KI#5

## Slide 4
One PDU Session per PEGC for one PIN session
  PEMC/AF manages PIN and can combine multiple PINs in one PIN session, which is out-of-scope
One PIN session for one PIN, and one PDU session per PEGC for one PIN session
  PEMC/AF manages PIN
  One PIN is mapping into one PIN session, one PDU Session per PEGC is used for one PIN session
KI#4 and KI#5 (Continue)
It is FFS whether one PDU session can serve more than one PIN.

## Slide 5
No
  The user subscribes PIN from operator and indicates GPSIs (including PEMC and PEGC) to the operator during subscription
  The 5GC determines who is PEGC based on the capability (which may also be PEMC if PEMC is collocated with PEGC)
Yes
  The user subscribes PIN from operator and indicates GPSIs (including PEMC and PEGC) to the operator during subscription
  The user additionally indicates who is PEMC/PEGC during the subscription
  The 5GC determines who is PEGC based on the capability (which may also be PEMC if PEMC is collocated with PEGC)
  The 5GC additionally is able to determine who is PEMC based on the subscription
KI#4 and KI#5 (Continue)
It is FFS whether PEMC UE needs a specific 5G subscription for providing PIN service.

## Slide 6
No
  5GC is not able to identify the PINE, especially when the PINE moves to another PEGC, or the PINE disconnects and reconnects to the PEGC and the PEGC reassign a new IP for the PINE
Yes
  The PINE ID is able to be used for charging record, which helps the operator/user identify the traffic
  Authentication/authorization may need the PINE ID
Depends on other WGs
  SA6 and SA3 have corresponding study
  SA6 and/or SA3 may require 5GC aware of the PINE ID
KI#7
It is FFS whether 5GC knows PINE ID.