## Slide 1: FS_IIoT/IIoT (AI#8.5) Show of hands questions and other items
Source: Nokia (Rapporteur)
Document for: Show of Hands and Agreement
Agenda Item: 8.5
Work Item / Release: FS_IIoT /IIoT/ Rel-17

## Slide 2: Key Issue #3A Exposure of deterministic QoS
  Background:
  Conclusion has the following:
  Editor's note: Whether the Burst Spread should be included is FFS.
  Background: AF provides Burst Spread parameter separately
  Should Burst Spread should be included as part of FS_IIoT conclusion and normative work?
  YES
  NO
  Way Forward:

## Slide 3: Key Issue #3A Exposure of deterministic QoS
  Background:
  Conclusion has the following:
  Editor's note: Need for jitter measurement is FFS.
  Should jitter measurement be included as part of FS_IIoT conclusion and normative work?
  YES
  NO
  Way forward:

## Slide 4: Background for KI#3A Burst spread and jitter
5.3.2 Key Issue #3A: Exposure of deterministic QoS
Any AF that has knowledge of deterministic application requirements should be able to request TSC services from the 5GS and as authorized, be notified of pertinent network events. This key issue is intended to support in the 5GS, requirements from TS 22.104 [4] where a TSN bridged network may not be needed and requirements from TS 22.263 [5] for Video, Imaging and Audio for Professional Applications (VIAPA). Applications provide those requirements to 5GS for any type of PDU Session.
This KI focuses on enhancing NEF framework.
For this Key Issue, the following areas should be studied:
a) Ability for AF to request absolute delay and jitter requirements, and mechanisms to enable the PCF to determine the 5GS QoS parameters based on the requirements received from AF.
b) Ability for AF to indicate periodicity, burst size, burst arrival time (as defined in Rel-16 for TSC Assistance information) and Survival Time, optionally burst spread (variation of burst arrival time for DL traffic resulting from jitter on N6, if applicable) along with Time Domain (reference for these parameters) associated with these parameters to the NEF.
c) How to enable an application and 5GS to agree on a TSC configuration that addresses the applications needs and can be supported by 5GS.

## Slide 5: Key Issue #3B Exposure of TSC services Exposure of Time Synchronization
Background:
  Conclusion has the following:
  Editor's note: whether there is a need to include validity time for AF time sync request is FFS. Also, how to support validity time is FFS.
  Options for resolution:
  Option 1: AF assumed to activate and deactivate requests for all the DS-TT(s) (thus maintain validity period accordingly).
  Support Option 1 for Validity period? (YES/NO)
  Option 2: If AF provides validity period for the request, 5GS maintains the validity period. In this case, the time sync services are deactivated when the validity period expires.
  Support Option 2 for Validity period? (YES/NO)
  Way forward: < >