## Slide 1
TEI17_N3SLICE
Laurent Thiébaut,
Jan 18th 2021 SA2 CC

## Slide 2
Different TAI in different N3IWF
N3SLICE:
  The objective for this work item is to specify the support of the possibility for operators to allocate a TAI per non 3GPP access gateway (e.g. N3IWF / TNGF / W-AGF) : each non 3GPP access gateway is locally configured with its own TAI and the slices it supports. The TAI value is provided (as in case of 3GPP access) to AMF over N2 in NG SET UP message. There is one TAI value per non 3GPP access gateway.
  Different non 3GPP access gateways (e.g. different N3IWF / TNGF / W-AGF) can thus advertise different TAI values, and can support different slices.
  As TAI values are not advertised over Non 3GPP access, UE(s) do not need to be aware of the fact that different non 3GPP access gateways may correspond to a different TAI beyond the fact that they (UE) may receive different TAI values within the TAI list sent by the network over successive registration over non 3GPP access.
  No UE impact. No protocol impact
Q: whether different 5G AN serving the same access type (e.g. different N3IWF) can support a different TAI
The answer may be different for N3IWF and for WAGF
The proposal is to let this up to configuration with a warning about the potential consequences

## Slide 3
N3SLICE and N3IWF: Different TAI in different N3IWF
A UE can access multiple N3IWF
AMF
N3IWF1
A
REGISTER
TAI1
REGISTER + TAI1
REGISTER Accept (RA = TAI1)
N3IWF2
AMF
N3IWF1
Service Request
TAI1
N3IWF2
TAI2
(RA = TAI1)
TAI2
SR + TAI2
(RA = TAI1)
De-register ?? UE misbehavior)
We need to understand what happens in following case
A UE registers via a N3WIF1 and gets a registration area = TAI1
N3IWF1 fails; the UE detects this via DPD (IKE)
The UE issues a Service Request via another N3IWF2
If N3IWF2 is associated with a different TAI2 (so the UE issues a service Request outside of its registration area) then the AMF considers this as an UE error
B

## Slide 4
N3SLICE and W-AGF: Different TAI in different W-AGF
A RG can access a very limited number of W-AGF
AMF
WAGF1
Urban area
REGISTER
TAI1
REGISTER + TAI1
REGISTER Accept (RA = TAI1)
AMF
REGISTER
WAGF2
(RA = TAI1)
TAI2
REGISTER + TAI2
(RA = TAI2)
REGISTER Accept (RA = TAI2)
Different W-AGF may correspond to different slices e.g. based on the distance from RG to DSLAM
5G RG
Rural area
5G RG

## Slide 5
Different TAI in different N3IWF
whether different 5G AN serving the same access type (e.g. different N3IWF) can support a different TAI
The answer may be different for N3IWF and for WAGF
The proposal is to let this up to configuration with a warning about the potential consequences