## Slide 1: Discussion on the EC contentious issue
Hui Ni
Huawei
Jun 26, 2021

## Slide 2: Background
EASDF was introduced in TS 23.548 to handle UE DNS messages.
The issue on “how to handle the DNS messages if UE don’t use DNS configuration provided by 5GC” was discussed since SA2 #143 meeting but no conclusion was achieved. Related EN:
Editor's note: How to guarantee that the UE uses the EASDF's IP address for the subsequent DSN Query in step 8 is FFS.
Companies have different views on whether/how UE/NW can detect/report the DNS messages sent to DNS servers other than the DNS configured by 5GC.

## Slide 3: Candidate proposals for removing the EN on SA2 #145E
S2-2104505r03 (SMF indicates to UE that DNS conf is for edge, the left are up to operators’ policy)
  SMF informs UE that the DNS configuration provided by the 5GC is for edge services
  NOTE 1: After the UE is informed that the DNS configuration provided by the 5GC is for edge services, whether and how the UE/application consider this information for DNS resolution depends on implementation.
  NOTE 2: If the UE doesn't use MNO DNS configuration, how to configure the network to handle UE DNS traffic is up to operator's policy.
S2-2104505r05 (No normative work, all are up to operator’s policy)
  NOTE : If the UE doesn't use DNS server provided by 5GC, how to handle UE’s DNS traffic in 5GS is up to UE implementation, operator's configuration and local regulation.
S2-2104482r05 (UPF detect then report to SMF for e.g. logging)
  UPF detects DNS traffic sent by the UE to a different DNS server than the EASDF
  UPF notify to SMF when such traffic is detected.
S2-2104675r02 (UE indicates capability and detect/report to SMF for e.g. logging)
  UE indicates to the SMF whether it’s capable of detecting the usage of DNS settings different from those indicated by the SMF
  If UE supports and SMF instructed, UE detects DNS setting change and DNS traffic sent by the UE to a different DNS server than the EASDF
  UE reports to SMF when such traffic is detected.

## Slide 4: Questions for SoH on SA2 #146E
Can the EN be removed by specifying the following?
Q1: SMF informs UE that the 5GC DNS configuration is for edge services.
  Support
  Object
Q2: SMF informs UE that the 5GC DNS configuration is for edge services AND UE detects DNS query which is using DNS different from that indicated by the SMF, and notify SMF when such DNS query is detected for e.g. logging. (No more consequent action is specified.)
  Support
  Object
Q3: UPF detects DNS query which is using DNS different from that indicated by the SMF, and notify SMF when such DNS query is detected for e.g. logging. (No more consequent action is specified.)
  Support
  Object
Q4: NOTE : If the UE doesn't use DNS server provided by 5GC, how to handle UE’s DNS traffic in 5GS is up to UE implementation, operator's configuration and local regulation.
  Support
  Object
Q5: Remove the EN without specifying anything.
  Support
  Object
Detection in the UE
Edge-specific DNS indication
Detection in the 5GC
No detection is specified.
NOTE: For Q2/Q3, detection/reporting on UE/UPF are based on agreements, local policies and/or configuration.

## Slide 5: Questions for discussion on June CC
Whether UPF detection and reporting to SMF (for e.g. logging) is needed?
  yes, why
  no, why
Whether UE detection and reporting to SMF (for e.g. logging) is needed?
  yes, why
  no, why
Whether the SMF need to informs UE that the 5GC DNS configuration is for edge services.
    yes, why
    no, why
With the pre-condition that all the following inform/detection are allowed by the operator’s policy and local regulation….

## Slide 6: In case we can agree with a specific solution, 2nd level details of each solution need to be discussed
For Edge-specific DNS indication:
  Shall we specify UE lower layer sending this indication to upper layer, i.e. HLOS/App?
    From S2-2104505r01:
      NOTE 1: After the UE is informed that the DNS configuration provided by the 5GC is for edge services, whether and how the UE/application consider this information for DNS resolution depends on implementation.
    From S2-2104505r02:
      NOTE 1: When the UE is informed that the DNS configuration provided by the 5GC is for edge services, the UE which supporting the edge computing feature may send the indication of EC DNS configuration to up-layer, and how the application consider this depends on implementation.
    From S2-2104675r02:
      If the UE receives an indication that such address is associated to the Edge supporting features, the UE shall forward it to the application/HLOS layer.
For UE detection (S2-2104675r02):
  Shall we support UE capability reporting to SMF during PDU Session est. procedure?
  Shall we specify how UE handling on those DNS messages within UE?
    From S2-2104675r02:
      Based on the instructions provided by the SMF to the UE at step 2, if the UE detects that a DNS query is using DNS settings different from those indicated by the SMF, it then executes the specified action and notifies the SMF via PCO at PDU Session Modification accordingly.
For UPF detection(S2-2104482r05):
  Anything?

## Slide 7: Working assumption
TBD