## Slide 1: Discuss on open issues for eNS_Ph2

## Slide 2: What are the functionalities of the new NF
Collecting information on the number of UE and on the number of PDU session within the network slice
Performing access control for each UE registration and each PDU session establishment in the network slice
Exposing information on the number of UE and on the number of PDU session within the network slice

## Slide 3: Issues on collecting UE information
What is the condition to trigger the collecting information?
  After the new NF is configured with global quota of the network slice it starts to collect information from all AMFs/SMFs in the network slice
  The new NF collects information from the AMF/SMF only when the AMF/SMF sends first request for checking network slice access control
How to collect information
  New NF sends subscription to AMF/SMF and the AMF/SMF notifies the UE or PDU session information to new NF
  The AMF report UE information to new NF during each Registration/Deregistration. The AMF/SMF sends session information to new NF during each PDU session establishment/release.
    The AMF/SMF needs to keep the report status. Too complex.

## Slide 4: Issues on performing network slice access control for each registration procedure
What is the condition to perform network slice access control in AMF
  After receiving information from NSSF
  After receiving subscription for collecting information from new NF
  When it is configured by OAM
For UE Registration, when to sends the request to the new NF for network slice access control?
  Before UDM registration
For PDU session establishment, whether AMF or SMF check with the new NF for network slice access control?
  AMF check with new NF for access control before it sends request to SMF
  SMF checks with new NF for access control

## Slide 5: How can the new NF be deployed?
Single new NF per slice
  More flexible
Single new NF per PLMN

## Slide 6: Roaming support
During UE Registration, how to perform network slice access control in both vPLMN and hPLMN for roaming UE
  Dynamic check with HPLMN or local quota
During PDU session establishment, how to perform network slice access control in vPLMN for PDU session with local breakout
  No need check with HPLMN
  Who does this check? AMF or SMF?
During PDU session establishment, how to perform network slice access control in both vPLMN and hPLMN for PDU session with home routed
  Dynamic check with HPLMN or local quota
  Who does this check? AMF or SMF?

## Slide 7: What is the name of the new NFs
Network Slice Access Control Function(NSACF)
Network Slice Quota Access Control(NSQAC)
Network Slice Quota Control Function(NSQCF)