## Slide 1: Discuss on open issues for eNS_Ph2

## Slide 2: Functionalities of the new NF(KI#1)
Configured with whether the slice is subject to NSSAC and the associated Maximum number value
Collecting the current number of UE within the network slice from AMF and checks the quota status
  Option1 :subscribe and notification from AMF
  Option2: AMF sends Request at each Registration
Notifying the AMF about the quota status, so the AMF can determine to accept the procedure or reject the procedure
  Option1: new NF sends notification to AMF
  Option2: new NF sends Response to AMF
Exposing information on the number of UE within the network slice (KI#4)

## Slide 3: Two options for collecting information(KI#1)
AMF
New NF
AMF
2. Subscription for UE number
3. Notification on UE number
6. UE reg req
5. Notification on quota status
7. UE reg reject
New NF
AMF
3. Check quota status request
2. UE reg req
5. Check quota status response
6. UE reg reject
4. Update the quota status
1. Configured with the maximum number value
1. Configured with the maximum number value
4. Update the quota status

## Slide 4: Issues on Request/Response option
How can the AMF trigger the NSSAC procedure to new NF
  Information from NSSF
  UE subscription
  Based on local configuration

## Slide 5: Issues on PDU session establishment
For PDU session establishment, where to collect the number of PDU session
  From AMF
  From SMF

## Slide 6: How can the new NF be deployed?
Single new NF per PLMN
Single new NF per slice
Multiple new NFs per slice

## Slide 7: Roaming support
During UE Registration, how to perform network slice access control in both vPLMN and hPLMN for roaming UE
  Dynamic check with HPLMN or local quota
During PDU session establishment, how to perform network slice access control in vPLMN for PDU session with local breakout
  No need check with HPLMN
  Who does this check? AMF or SMF?
During PDU session establishment, how to perform network slice access control in both vPLMN and hPLMN for PDU session with home routed
  Dynamic check with HPLMN or local quota
  Who does this check? AMF or SMF?

## Slide 8: What is the name of the new NF
Network Slice-Specific Access Control Function(NSSACF)
Network Slice Quota Access Control(NSQAC)
Network Slice Quota Control Function(NSQCF)