## Slide 1: Discuss on open issues for eNS_Ph2
Jinguo (ZTE)

## Slide 2: Functionalities of the new NF(KI#1)
Configured with whether the slice is subject to NSSAC and the associated Maximum number value by OAM
Collecting the current number of UE within the network slice from AMF and checks the over all quota status
  Option1 : subscribe/notify model, see next page
  Option2 : request / response model, see next page
Notifying the AMF about the quota status of the slice, so the AMF can determine to accept or reject the procedure
  Option1 : subscribe/notify model, see next page
  Option2 : request / response model, see next page
Exposing information on the quota status and up-to-date number of UE within the network slice

## Slide 3: Two options for collecting information and notifying the quota status(KI#1)
AMF
New NF
AMF
2. Subscription for UE number
4. Notification on UE number
7. UE reg req
6. Notification on quota status
8. UE reg reject
New NF
AMF
3. Check quota status request
2. UE reg req
5. Check quota status response
6. UE reg reject
4. Update the quota status
1. Configured with the maximum number value
1. Configured with the maximum number value
5. Update the quota status
Option 1(subscribe/notify): the procedure is invoked per slice basis
Option 2(Request/Response): the procedure is invoked are per UE per slice basis
3. Subscription for quota status

## Slide 4: Issues on Option 1 Subscribe/Notify (KI#1)
What is the trigger in AMF to subscribe the quota status from the new NF (step 3 in previous figure)
  Based on local configuration the AMF subscribes the quota status of the slice from the new NF, or
  The AMF subscribes the quota status of the slice from the new NF after it receives subscription event on the number of UE from the new NF

## Slide 5: Issues on Option 2 Request/Response(KI#1)
What is the trigger in AMF to invoke the NSSAC procedure
  Information from NSSF
  UE subscription
  Based on local configuration
Whether the NSSACF needs to keep the registered UE list
  The NSSACF needs to keep the up-to-date registered UE list: In each Registration procedure and in each De-Registration procedure, the AMF invokes the NSSAC process with UE ID and the NSSACF update the UE list.
  The NSSACF doesn’t need to keep the up-to-date registered UE list: The AMF only invokes the NSSAC process only when the S-NSSAI is added to Allowed NSSAI for the first time or removed from the Allowed NSSAI. The Allowed NSSAI should be transferred between AMFs.

## Slide 6: Question: Which option should be specified in normative phase
Option 1:
Option 2:

## Slide 7: Issues on PDU session establishment(KI#2)
For PDU session establishment, where to collect the number of PDU session
  From AMF
  From SMF
For PDU session establishment, whether AMF or SMF rejects the PDU Session establishment request
  AMF
  SMF

## Slide 8: How can the new NF be deployed?
Single new NF per PLMN
Single new NF per slice
Multiple new NFs per slice

## Slide 9: What is the name of the new NF
Network Slice-Specific Access Control Function(NSSACF)
Network Slice Quota Access Control(NSQAC)
Network Slice Quota Control Function(NSQCF)
Network Slice Control Policy Function(NSCPF)

## Slide 10: Roaming support (Depends on solution for non roaming case)
During UE Registration, how to perform network slice access control in both vPLMN and hPLMN for roaming UE
  Dynamic check with HPLMN or local quota
During PDU session establishment, how to perform network slice access control in vPLMN for PDU session with local breakout
  No need check with HPLMN
  Who does this check? AMF or SMF?
During PDU session establishment, how to perform network slice access control in both vPLMN and hPLMN for PDU session with home routed
  Dynamic check with HPLMN or local quota
  Who does this check? AMF or SMF?