3GPP TSG-SA3 Meeting #115 	S3-24xxxx

Athens, Greece, 26 Feb - 01 March 2024

# Source:	Nokia, Nokia Shanghai Bell

# Title:	pCR on KI on AUN3 device connecting to the new 5G-RG

# Document for:	Approval

Agenda Item:	5.8

# 1	Decision/action requested

It is requested to approve the chapter 4 content.

# 2	References

[x] 3GPP TR 33.702: "Study on Security for mobility over non-3GPP access to avoid full primary authentication."

# 3	Rationale

This pCR introduces the KI for  FS_Non3GPPMob_Sec study.

# 4	Detailed proposal

**** START OF CHANGE ****

## 5.x	Key issue #x: Security aspect of AUN3 device connecting to a new 5G-RG within the same W-AGF.

### 5.x.1	Key issue details

When AUN3 device moves from 5G-RG1 and 5G-RG2, where both 5G-RG are nearby or overlapping, the AUN3 device connectivity will break while connecting to the new 5G-RG2. Additionally, AUN3 also goes through another full primary authentication procedure, even though both 5G-RGs connects to the same W-AGF.

Figure 5.X.1-1: AUN3 device moves from 5G-RG to another 5G-RG

A new full primary authentication may lead to additional signalling and may cause latency in the AUN3 device connection. If we skip the full primary authentication, it provides connection time optimisation, but then the security aspect of the AUN3 device to target 5G-RG should be studied.

### 5.x.2	Threats

As it is only AUN3 device connection time optimisation, the threat is not applicable.

### 5.x.3	Potential security requirements

5GS should support a mechanism for communication between the AUN3 device and 5G-RG to establish security with a 5G-RG without performing full primary authentication when the AUN3 device switches from another 5G-RG within the same W-AGF.

While switching from one 5G-RG to another 5G-RG within the same W-AGF, the interface between AUN3 device and the new 5G-RG shall be confidentiality, integrity, and replay protected.

**** END OF CHANGE ****