3GPP TSG-SA3 Meeting #115 	S3-24xxxx

# Athens, Greece, 26 Feb - 01 March 2024

# Source:	Nokia, Nokia Shanghai Bell, Samsung

# Title:	pCR on KI on UE connecting to the new WLAN AP under the same NSWOF

# Document for:	Approval

Agenda Item:	5.8

# 1	Decision/action requested

It is requested to approve the chapter 4 content.

# 2	References

[x] 3GPP TR 33.702: "Study on Security for mobility over non-3GPP access to avoid full primary authentication."

# 3	Rationale

This pCR introduces the KI for  FS_Non3GPPMob_Sec study.

# 4	Detailed proposal

**** START OF CHANGE ****

## 5.x	Key issue #x: Security aspect of UE connecting to a new WLAN AP connected via the same NSWOF.

### 5.x.1	Key issue details

When UE moves from WLAN AP1 and WLAN AP2, where both WLAN AP are nearby or overlapping, the UE connectivity will break while connecting to the new WLAN AP. Additionally, UE also goes through another full primary authentication procedure at the NSWOF, even though both WLAN AP connects to the same NSWOF.

Figure 5.X.1-1: UE moves from WLAN AP to another WLAN AP

A new full primary authentication may lead to additional signalling and may cause latency in the UE connection. If we skip the full primary authentication, it provides connection time optimisation, but then the security aspect of the UE to target WLAN should be studied.

### 5.x.2	Threats

As it is only UE connection time optimisation, the threat is not applicable.

### 5.x.3	Potential security requirements

5GS should support a mechanism for communication between the UE and WLAN AP to establish security with NSWOF without performing full primary authentication when the UE switches from another WLAN AP connected to the same NSWOF.

**** END OF CHANGE ****