## Slide 1
3GPP TSG-SA3 Meeting #110
20 - 24 February 2023
Source: Nokia, Nokia Shanghai Bell
Title: SA WG 3 Status report for WID 5G eSBA Ph2
Document for: Endorsement
Agenda Item: 4.12

## Slide 2: SA WG3 Status report WID ‘5G_eSBA_Ph2’
Anja Jerichow
Nokia
SA3#111

## Slide 3: ‘5G_eSBA_Ph2’ Status after SA3#111
Normative work based on study conclusion in FS_eSBA_SEC, i.e.
    - clarifying security for subscribe/notify use case,
    - address NRF deployment scenarios,
    - authorization of inter-slice access,
    - NRF validation of NFc.
History:
  WID created to conclude normative work on FS_eSBA_SEC in November 2022 (SA3#109).
  WID approved by SA plenary (SP-221145) – CRs on 4 KIs were expected.
Report from April & May meetings:
  Work on WID started already in November with 2 CRs agreed (NRF deployment, slice topic).
  CRs agreed in last meetings
    SCP trust, subscribe/notify and OAM for NFc registration at NRF
    Updates to 33.310 SBA cert in line with SID conclusions
Overall plan

## Slide 4: ‘5G_eSBA_Ph2’ Status after SA3#111
Key Issues from TR 33.875 | -- what is it about | -- CRs expected in WID phase / work done
#1: Authentication of NRF and NF Service Producer in indirect communication | KI#1 is to allow an NF Service Consumer to authenticate an NRF or an NF Service Producer in the scenario of indirect communication via an SCP. Three solutions (Solution #1, #6 and #13). | CR: Clarification on trust of SCP.
#3: Service access authorization in the "Subscribe-Notify" scenarios | KI on subscribe notify: how to assure that the notification messages could be only forwarded to an NF that has been authorized (by the NRF) to receive notifications. | CR: token-based authorization also applies to subscribe and unsubscribe operations.
#4: Authorization of SCP to act on behalf of an NF or another SCP | KI is about authorization of SCP to request services on behalf of an NF or of another SCP and how this authorization is verified by the NRF or NF Service Producer | CR: Clarification on trust of SCP
#8: Service access authorization requirements in intra-PLMN scenarios for PLMN deploying multiple NRFs (in OAuth2.0 AS role) | KI is about different NRF deployment options and related service access authorization | CR: new clause to clarify NRF deployment scenarios
#9: Authorization for Inter-Slice Access | KI is about how to prevent any malicious entity (for instance a NF Service Consumer) from accessing a slice it is not authorized to access, or from requesting a service from a slice which it is not authorized to access | CR: text in clause 13.4.1.1.2. of TS 33.501 + 2 requirements in line with sol#18.
#11: NRF validation of NFc for access token requests | Validation of NFs in case of access token requests for different scenarios in direct or indirect communication. How to validate NFs by NRF? NF registration at NRF versus information in provided certificate, which takes precedence? Etc. | Concluded. Potentially some clarification CR in August needed.

## Slide 5: ‘5G_eSBA_Ph2’ Status after SA3#111
SA3#109
Toulouse
14.-18.11.22
WID agreed
SP-221145
conclusions in SID were finalized for 11 Kis, only one missing
work on normative text
Plan to finalize WID in March
SA3#109-bis
online
16.-20.1.23
No WID work
SA3#110
Athens
20.2.-24.2.23
Several CRs agreed
CR subscribe and notify
CR SCP trust
NF instance ID in cert
SA3#110-bis
online
17.-21.4.23
DraftCRs discussed
SA3#111
Berlin
22-26.5.23
Clarification CR on NRF requirement

## Slide 6: ‘5G_eSBA_Ph2’ Status after SA3#111
General
  Conclusions implemented eSBA study per CRs
  Minor clarifications needed, but in general WID in good shape.
Dependencies
  None (the WID has no RAN impacts)
UID | Name | Acronym | Rel | WG | Target | Old % | New % | Change or comment
920020 | WID 5G SBA Ph2 | 5G_eSBA_Ph2 | Rel-18 | S3 | 08/23 | 85% | 95% | TS 33.501, TS 33.310

## Slide 7: ‘5G_eSBA_Ph2’ Status after SA3#111
  SA2/RAN impacts and dependencies:
  None for RAN and none determined yet for SA2
Contentious Issue:
  None
Focus for the upcoming Meetings:
  Some clarifications may be needed, but in general good shape.
Overall Plan:
  See dedicated slide 3
Risks:
  None