## Slide 1
3GPP TSG-SA3 Meeting #109
14 -18 November 2022
Source: Nokia, Nokia Shanghai Bell
Title: SA WG 3 Status report for FS eSBA SEC study
Document for: Endorsement
Agenda Item: 5.24

## Slide 2: SA WG3 Status report for ‘FS_eSBA_SEC’
Anja Jerichow
Nokia
Updated after SA3#109

## Slide 3
History:
  Started in Rel-17 for documenting security threats
  Conscious decision based on risk versus complexity and whether the achieved security improvements are worthwhile in continuing with normative work.
  It was decided to extend the study to Rel-18, 2 new KIs were added (N32 roaming related)
Report from November meeting:
  We concentrated on conclusions. 9 of 12 Kis concluded.
  Plus 2 Kis concluded to be outsourced in extra TR on N32 roaming, to be continued in R19.
  26 solutions overall. WID agreed for normative work on 4 KIs.
After November meeting the following is planned:
  Prepare to send TR 33.875 for approval (clean up, update on analysis parts, resolving ENs)
  Prepare normative text additions to 33.501 as per conclusions.
  Remove KI#10 & KI#12 including related solutions into new TR with SID (to be continued in Rel.19).
  Finalize Rel-18 TR 33.875 till March 2023.
Overall plan
‘FS_eSBA_SEC’ Status after SA3#108-e

## Slide 4
Key Issues | Sol. | -- what is it about | -- comments
#1: Authentication of NRF and NF Service Producer in indirect communication | #1 #6 #13 | KI#1 is to allow an NF Service Consumer to authenticate an NRF or an NF Service Producer in the scenario of indirect communication via an SCP. Three solutions (Solution #1, #6 and #13). | No normative solution is pursued for addressing this KI.
#2: SCP security domains | #14 | This key issue takes into account the different deployment models in intra-PLMN authorization requests. | The topic is not followed up normatively.
#3: Service access authorization in the "Subscribe-Notify" scenarios | #12 #15 | KI on subscribe notify: how to assure that the notification messages could be only forwarded to an NF that has been authorized (by the NRF) to receive notifications. | No normative work on the solutions described in this study is pursued, but 33.501 needs to be updated with a clarification that token-based authorization also applies to subscribe and unsubscribe operations.
#4: Authorization of SCP to act on behalf of an NF or another SCP | #2 #3 | KI is about authorization of SCP to request services on behalf of an NF or of another SCP and how this authorization is verified by the NRF or NF Service Producer | No normative solution is pursued for addressing this KI.
#5: End-to-end integrity protection of HTTP messages | #4 #5 #8 #16 | KI is about how end-to-end integrity protection of HTTP messages can be achieved while at the same time continue to allow the SCP to perform necessary mediation of HTTP messages. | No normative solution to be pursued for addressing this KI.
#6: Access token usage by all NFs of an NF set | #7 | KI is about whether to allow an access token for NF Set. Ie. any NF in a NF Set targeting a service of an existing resource can use an access token provided to a NF Set | No normative solution to be pursued for addressing this KI.
#7: Authorization mechanism determination | #9 #17 #24 | KI is about how to handle the case that one operator uses token-based authorization, and its roaming partner uses static authorization | In this study no normative work is pursued.
#8: Service access authorization requirements in intra-PLMN scenarios for PLMN deploying multiple NRFs (in OAuth2.0 AS role) | #10 |  | Normative text to be added: a new clause to TS 33.501 to clarify NRF deployment scenarios
#9: Authorization for Inter-Slice Access | #11 #18 | KI is about how to prevent any malicious entity (for instance a NF Service Consumer) from accessing a slice it is not authorized to access, or from requesting a service from a slice which it is not authorized to access | Normative text in clause 13.4.1.1.2. of TS 33.501 will be added together with 2 requirements in line with spl#18.
#10: N32 security in mediated roaming scenarios | #20 #23 #25 | GSMA provides best practice guidance and related specifications for how operators interact with both IPX and roaming hubs. However, the pre-5G architecture of these methods uses the 4G hop-by-hop security paradigm. In 5G, SEPP communication for roaming relies on end-to-end security by design as specified in TS 33.501. Objective is to study in more detail how the migration away from hop-by-hop security can be achieved without loss of the benefits provided by IPX providers and roaming hubs while the 5G security requirements on N32 are met. | KI will be outsourced into a new study.
#11: NRF validation of NFc for access token requests | #21 #22 #26 | Validation of NFs in case of access token requests for different scenarios in direct or indirect communication. How to validate NFs by NRF? NF registration at NRF versus information in provided certificate, which takes precedence? Etc. | No conclusion yet.
#12: security in Hosted SEPP scenarios | #19 | Outsourcing of the operation of a SEPP to an external entity: The Hosted SEPP scenario introduces security requirements which must be fulfilled by N32 and by the connection between PLMN and Hosted SEPP. This key issue documents how they can be fulfilled. | KI will be outsourced into a new study.
‘FS_eSBA_SEC’ Status after SA3#108-e

## Slide 5
‘FS_eSBA_SEC’ Status after SA3#108-e
SA3#107 Adhoc-3 Jun27-July1st 2022
SID was not part of the agenda
KIs are already well established
SA3#108
Aug 22-26, 2022
Deadline for new KIs & solutions
WID was proposed but not yet agreed due to limited conclusions
SA3#108 Adhoc-e Oct 10-14, 2022
Solution focused
Partially conclusions added
prepare for normative work
SA3#109
Nov 14-18, 2022
WID agreed
2 KIs will be outsourced (dependency on GSMA)
conclusions finalized for 9 Kis, only one missing
work on normative text
Plan to finalize WID in March

## Slide 6: ‘FS_eSBA_SEC’ Status after SA3#108-e
Solutions | Key Issues |  |  |  |  |  |  |  |  |  |  | 
 | #1 | #2 | #3 | #4 | #5 | #6 | #7 | #8 | #9 | #10 | #11 | #12
#1: Service response verification in indirect communication without delegated discovery | X |  |  |  |  |  |  |  |  |  |  | 
#6: Verification of Service Response from a NF Service Producer at the expected NF Set | X |  |  |  |  |  |  |  |  |  |  | 
#13: Authentication of NF Producer in Indirect Communication | X |  |  |  |  |  |  |  |  |  |  | 
#14: SCP trust domain or technical domain grouping |  | X |  |  |  |  |  |  |  |  |  | 
#12: Authorization of notification endpoint in “Subscribe-Notify” scenarios |  |  | X |  |  |  |  |  |  |  |  | 
#15: Authorization mechanism for the involved NFs in the delegated “Subscribe-Notify” scenario |  |  | X |  |  |  |  |  |  |  |  | 
#2: Authorization between NFs and SCP |  |  |  | X |  |  |  |  |  |  |  | 
#3: Using existing procedures for authorization of SCP to act on behalf of an NF Consumer |  |  |  | X |  |  |  |  |  |  |  | 
#4: Service request authenticity verification in indirect communication |  |  |  |  | X |  |  |  |  |  |  | 
#5: End-to-end integrity protection of HTTP body and method |  |  |  |  | X |  |  |  |  |  |  | 
#8: integrity protection of HTTP message in consideration of update by SCP |  |  |  |  | X |  |  |  |  |  |  | 
#16: Selective End of End Protection of HTTP Request and Response in Indirect |  |  |  |  | X |  |  |  |  |  |  | 
#7: Access token request for NF Set |  |  |  |  |  | X |  |  |  |  |  | 
#9: Authorization mechanism negotiation |  |  |  |  |  |  | X |  |  |  |  | 
#17: Static auth in roaming with existing methods |  |  |  |  |  |  | X |  |  |  |  | 
#10: NRF deployment clarifications |  |  |  |  |  |  |  | X |  |  |  | 
#11: Registered NF Profile changes for Inter-Slice Access |  |  |  |  |  |  |  |  | X |  |  | 
#18: title TBD |  |  |  |  |  |  |  |  | X |  |  | 
#20: PRINS for RHUB |  |  |  |  |  |  |  |  |  | X |  | 
#21: Certificate solution for NRF validation of NFc for access token requests |  |  |  |  |  |  |  |  |  |  | X | 
#22: Combined certificate and profile solution for NRF validation of NFc for access token |  |  |  |  |  |  |  |  |  |  | X | 
#19 Hosted SEPP requirements |  |  |  |  |  |  |  |  |  |  |  | X
#23: SCP authorization check by NRF |  |  |  | X |  |  |  |  |  |  |  | 
#24: Authorization negotiation with bootstrapping mechanism |  |  |  |  |  |  | X |  |  |  |  | 
#25: N32 security profiles |  |  |  |  |  |  |  |  |  | X |  | 
#26: Authorization verification at NRF |  |  |  |  |  |  |  |  |  |  | X | 

## Slide 7
General
  studies enhanced security aspects of the 5G Service Based Architecture
  analyses potential threats, study necessary security enhancements
  document decisions of solutions to be adopted or not adopted after evaluating the risks versus the complexity
Dependencies
  None (the SID has no RAN impacts)
‘FS_eSBA_SEC’ Status after SA3#108-e
UID | Name | Acronym | Rel | WG | Target | Old % | New % | Change or comment
920020 | Study on enhanced SBA security | FS_eSBA_SEC | Rel-18 | S3 | 03/23 | 87% | 94% | TR 33.875

## Slide 8: ‘FS_eSBA_SEC’ Status after SA3#108-e
  SA2/RAN impacts and dependencies:
  None for RAN and none determined yet for SA2
Contentious Issue:
  None
Focus for the Next f2f Meeting :
  Prepare for normative work in November
Overall Plan:
  See dedicated slide 5
Risks:
  No normative text for eSBA identified threats