## Slide 1: Discussion on reply to LS from 5G ACIA on identified gaps (S3-223147)
Marks Staufer, Bo Bjerrum
SA3 Delegates, Nokia

## Slide 2: Outline
Identify gaps in the LS, which are relevant for SA3
Discussion, whether we agree that the gap is “real”
Discussion, how to handle “real” gaps, e.g.,
  Do nothing, because closing the gap is outside of SA3 scope
  Plan immediate fix as part of maintenance work or ongoing Rel 18 work
  Postpone resolution to a later release (e.g. within dedicated SID/WID)
Agree on main content of a reply to SA (which will collect responses from all WGs and will prepare final response)
  Detailed wording can be handled as part of LS draft.

## Slide 3: Content – Gaps relevant for SA3
G.1 Provisioning of single subscriptions or a bulk of subscriptions
G.3 Provision of security event/logging information
L.6 Fine-grained authorization on the level of specific services and resources, e.g. restricting API requests from specific AFs for specific

## Slide 4: Content – G.1 Subscription Provisioning
The gap covers provisioning of credentials to the 5GC (e.g. UDM) and to the UE (“onboarding”)
The gap is indeed real:
  3GPP did not standardize a mechanism for provisioning of credentials into the 5G core.
  3GPP did in Rel 17 specify a mechanism for providing initial connectivity to un-provisioned UEs, but it did not specify the protocol used for provisioning or the format of the subscriber profile to be provisioned.
Question to SA3:
  Do we see a need or possibility to close the gap within SA3?

## Slide 5: Content – G.3 Security event/logging
Clarifications from 5G ACIA internal report:
The term logging information refers to logging information about the UE originating from the 5GC, but not to logging information originating from the UE.
Security Logging Information includes at a minimum information relating to successful and unsuccessful (primary, secondary, slice specific) authentications of UE and information relating to applied protection of user plane traffic. Information might be extended to other security relevant incidents, like presence of radio jamming)
Use case: A Security Operations Center operated by an enterprise wants to receive security related events from a connected 5GS
To the best of our knowledge the 5G northbound interfaces (NEF, SEAL) do not include the requested events
Question: Does SA3 see definition of these events in scope?

## Slide 6: Content – L.6 Fine-grained authorization
Example Use Case:
  A campus network is used by several tenants (e.g., different departments). The scope of a tenant’s AF shall be restricted to the resources (UEs, LAN groups, …) of this tenant.
SA3 defines that OAuth 2.0 should be used for API authorization (mandatory according to TS 33.501, optional according to TS 33.122 for CAPIF)
  TS 33.501 does not include any statement about scopes and claims
  TS 33.122 only defines scopes on the level of entire service
  Stage 3 OpenAPI (e.g., TS 29.522 for NEF) definitions do not include scopes
 Gap does exist
Resolution of gap might require above all stage 3 work (e.g., adding scopes to OpenAPI files). Should SA3 trigger the changes and provide guidance to SA3 based on a deeper analysis?

## Slide 7: Summary
Main points of a LS reply to be drafted in the meeting