3GPP TSG-SA3 Meeting #115AdHoc-e	S3-24xxxx

Electronic meeting, online, 15 - 19 April 2024

# Source:	Xiaomi

# Title:	Remove the ENs in KI1 of TR 33.700-29

# Document for:	Approval

Agenda Item:	5.7

# 1	Decision/action requested

It is requested to remove the ENs in KI1 of TR 33.700-29.

# 2	References

[1]	3GPP TR 33.700-29: "Study on Security Aspects of 5G Satellite Access in the 5G architecture; Phase 3"

# 3	Rationale

This pCR is proposed to remove the Editor’s Notes in the Key Issue 1: Security protection in Store and Forward Satellite Operation of TR 33.700-29 [1].

Editor’s Note: whether the availability issue is a security threat is FFS.

The availability issue introduced in the S&F service operation is due to the incomplete AKA procedure. Considering the feeder link’s intermittent unavailability, the AKA procedure may be partially completed or failed. This can lead to the UE being unable to attach to the 3GPP system, thereby compromising the service availability.

However, this service availability issue is already included in the current security threats.

-	When the UE and 3GPP network cannot mutually authenticate, such condition may cause availability issue.

And the related security requirement is proposed to address the above security issue.

The 3GPP system shall support mutual authentication between the UE and the 3GPP network in the Store and Forward Satellite Operation.

Therefore, we propose to remove this Editor’s Note.

Editor’s Note: whether there are more security threats is FFS.

Editor’s Note: whether there are more security requirements is FFS.

No new security threats and security requirements are needed. Thus, we propose to remove these two Editor’s Notes.

# 4	Detailed proposal

*************** Start of the 1st Change ****************

## 5.1	Key issue #1: Security protection in Store and Forward Satellite Operation

### 5.1.1	Key issue details

In clause 4 of TR 23.700-29 [2], there is following description about the Store and Forward Satellite Operation:

"The following architecture assumptions are applied to the study:

…

-	Store and Forward Satellite Operation assumes that UE-satellite-ground network connectivity can be intermittent as defined in clause 3.1.

-	Store and Forward Satellite Operation shall work without ISL.

…"

From a security perspective, whether a UE can use Store and Forward Satellite service should be assured by the 3GPP network.

In S&F satellite operations, architectural assumption is that the UE-satellite-ground network connectivity is intermittent. 3GPP Network Functions and/or Network Elements which are located on a satellite may communicate with the ground infrastructure of 3GPP network over an intermittently available feeder link connection between the satellite and the ground network. S&F satellite operational mode is relevant for delay tolerant and non-real time communications via LEO/MEO space segment.

During the feeder link’s intermittent unavailability, the following risks arise.

1.	The EPS/5G AKA procedure may not get fully completed or is partially completed. It results into incomplete procedure for mutual authentication between the network and the UE.

2.	The Security Mode Command (SMC) procedure for Non-Access Stratum (NAS) may not fully complete because the NAS connection between UE and MME/AMF may have been interrupted. In turn it results into incomplete security capabilities negotiation between the UE and the EPS/5GC network.

This key issue is to study the authentication, authorization and data security in Store and Forward Satellite Operation.

### 5.1.2	Security threats

Editor’s Note: the feasibility of the denial of service (i.e. caused by false user-plane data or control-plane data) is FFS.

Editor’s note: The risk of resource depletion of 3GPP system due to UE's incomplete AKA procedure is dependent on agreed architecture solution direction of S&F KI in SA2.

Due to the nature of the S&F mode during the feeder link’s intermittent unavailability, the following threats can manifest themselves:

-	When the UE and 3GPP network cannot mutually authenticate, such condition may cause availability issue.

-	Without the authentication, confidentiality, integrity, and anti-replay protection there will be no security protection of the communication between UE, on board satellite 3GPP systems and ground-based 3GPP systems.

### 5.1.3	Potential security requirements

The 3GPP system shall support mutual authentication between the UE and the 3GPP network in the Store and Forward Satellite Operation.

The 3GPP system shall support means to provide confidentiality, integrity, and anti-replay protection for user-plane and control-plane messages between UE and the 3GPP network in the Store and Forward Satellite Operation.

*************** End of the Change ****************