## Slide 1: Security aspects on Enablers for Network Automation (eNA) for 5G – phase 3
Nokia

## Slide 2: On eNA for 5G – Phase 3
Based on work done in Rel – 17 for supporting network automation and new use cases leveraging network data analytics, further problems and solutions are investigated for Rel -18 in SA2, including enhancements for NWDAF.
The following topics as defined in SA2 study objective for eNA phase 3 are subject to security study:
  Data and Analytics exchange in Roaming cases between NWDAF and the other 5GC NFs, between NWDAFs.
  Data collection and data storage enhancements, including DCCF and ADRF enhancements
  UPF data report to NWDAF for analytics as specified in R16/R17, and additional data identified in R18 (e.g., traffic volumes, service experience, packet rate loss, RTT, anomaly events, etc.)
  NWDAF enhancements considering finer granularity of location information

## Slide 3: Security aspects – Preliminary study objectives
Protection of the data analytics exchanged and/or exposed in Roaming cases
  The NWDAF analytics report contains lots of sensitive information about the network (example: network topology) and UEs (example: location, communication patterns..). Exposing this information to other operators may cause confidentiality and integrity issues in different roaming scenarios (e.g. direct communication, via IPX providers, Roaming Hub, etc.) – To study whether existing security features in roaming are sufficient to cover new analytics data transfer and subscriptions in terms of sensitivity of the data, privacy concerns, etc.
  Scenarios: NWDAF (HPLMN) – NWDAF (VPLMN), NFs (VPLMN) – NWDAF (HPLMN)
Access control mechanisms for Data Collection (DCCF) and Analytics Data Repository Function (ADRF)
Protection of sensitive data reports (e.g. related to user plane data, location information) sent to Analytics platforms
  Exposure of sensitive information
  Privacy
From Rel-17 two key issues may be re-opened for further evaluation due to new developments in eNA:
  Cyber-attacks detection supported by NWDAF
    Justification: No normative work was agreed in phase 2
  Anomalous NF behaviour detection by NWDAF
    Justification: Since standardizing NF abnormal behaviour and the exact inputs requires more time to study, therefore no normative work is considered for KI #2.2 for this release.