3GPP TSG-SA3 Meeting #103-e 	S3-21xxxx

# e-meeting, 17 - 28 May 2021											Revision of S3-20xxxx

# Source:	Ericsson, ?

# Title:	Conclusions for KI#1 (external entity) on AAA interworking

# Document for:	Approval

Agenda Item:	5.12

# 1	Decision/action requested

Appove the pCR below with conclusions for KI#1 (external entity).

# 2	References

[1]	3GPP TR 33.857 "Study on enhanced security support for Non-Public Networks (NPN)"

# 3	Rationale

tbd

# 4	Detailed proposal

***	BEGINNING OF CHANGES ***

## 7.1	Conclusions on KI #1: Credentials owned by an external entity

In case that the external entity is 5GS aware (i.e., has the AUSF/UDM and is capable of deriving 5G key hierarchy after a successful primary authentication), it is concluded that the existing 5GS roaming architecture is reused.

In case that the external entity is non-5GS aware (legacy AAA server), the following is concluded:

- The SNPN access with a credential owned by an external entity is performed via an AUSF in the SNPN that is enhanced to interface with the external entity and act as a pass-through authenticator instead of authentication server.

- From security point of view, it is possible to use an interworking function between the enhanced AUSF and the external entity, if the interworking function complies to the same requirements on handling of session keys as the AUSF.

Editor’s Note: Further conclusion(s) are FFS.

***	END OF CHANGES ***