3GPP TSG-SA3 Meeting #104-e 	S3-211XYZ

# e-meeting, 16 – 27 August 2021

# Source:	Philips International B.V.

# Title:	Conclusions Solution 9

# Document for:	Approval

Agenda Item:	5.11

# 1	Decision/action requested

Acceptance of conclusions in Solution #9 of TR33.850.

# 2	Detailed proposal

***	BEGIN OF 1st CHANGE	***

## 6.9.3	Evaluation

This solution addresses Key issue #3 to manage, distribute, and update the keys required to protect the MBS traffic in the context of transport layer solution #1.

This solution can be applied to service layer solutions, e.g., Solution #2 uses it.

This solution describes a default and a communication optimized approach.

The communication optimized approach allows updating the group key used to protect the MBS traffic in a group with N devices with around root square of N (SQRT(N)) unicast messages in contrast with the default approach that requires N unicast messages. This means that for the same key update signaling overhead, the communication optimized approach allows supporting MBS groups a quadratic factor larger compared with the default approach without increasing the computational or communication overhead to protect/transmit the MBS traffic.

Using M>1 transport keys and including the hash of the group key makes the communication optimized solution more resilient.

Editor’s Note: Further evaluation is FFS.

***	END OF 1st CHANGE	***