3GPP TSG-SA3 Meeting #104-e 	S3-21cccc

# e-meeting, 16 - 27 August 2021											Revision of S3-20xxxx

# Source:	Samsung

# Title:	[EDGE] Conclusion for KI#2

# Document for:	Approval

Agenda Item:	5.8

# 1	Decision/action requested

It is requested to approve the pCR to add conclusion for KI#2 of TR 33.839.

# 2	References

[1]	3GPP TR 33.839 Study on Security Aspects of Enhancement of Support for Edge Computing in 5GC.

# 3	Rationale

This pCR is proposes to add Conclusion for KI#2.

For quick reference, excerpt from TS 33.535:

Figure 4.1-2 shows the AKMA architecture using the reference point representation. Figure 4.1-2: AKMA Architecture in reference point representation for (a) internal AFs and (b) external AFs

# 4	Detailed proposal

******Start of Change******

# 7	Conclusions

## 7.x	Conclusion for Key Issue #2

Authentication between EEC and ECS:

- Solution #3 is recommended as the baseline for the normative work to conclude that AKMA is used for generating the shared key between EEC and ECS and TLS-PSK protocol is used for mutual authentication.

- In case of roaming, as to have support of EDGE service provided in the serving network, it is recommended to use solution#7 as the baseline for normative work for Rel-17, in addition to Solution #3.

  - Currently, AKMA does not support roaming scenarios in Rel-17. Therefore, it is practically impossible for all external AFs (in the roaming networks) to have secure N33 interface with the NEF (in the HN of the roaming UE).

  - Solution#7 to be considered as an interim solution, until AKMA supports roaming scenarios.

******End of Change******