## Slide 1: WID on 256-bit Algo Support over the Air – Rel19
Comments/Agreements from the Meeting on 29.01.24

## Slide 2: Agenda
256-bit algorithm architecture overview (create common understanding of what is encryption, integrity, and combined specific).
Specification related items (brief introduction to TS 35.240 to TS 35.248).
Standardisation related items, here would like to check with you the formatting (=extending) of the algorithm identifiers in TS 33.501 Clause 5.11.x.
Potential changes to the agreed WID (basis will be S3-234334).
AoB (?)
[29.01.24]: on the further proceeding, the skeleton should be made available, so that companies can contribute, if possible material should be made available by end of this week; storage place 3GPP ftp-server

## Slide 3: Justification and Objectives [1]
As detailed in TR 33.841, Quantum computing poses a long-term threat to information security not only for data collected once the ability to compromise existing security is discovered but also for any historic data that may have legal, financial, commercial, or governmental importance that has been collected for future decoding.
TR33.841 identified that whilst symmetric key algorithms are not as susceptible as public key related algorithms to the enhancements in quantum computing, 256-bit algorithms should be developed now in preparation for a possible adoption. The corresponding algorithms have been developed and evaluated by the ETSI SAGE at 3GPP’s request.
The objectives to the WID are:
Define the new 256-bit Integrity and Encryption Algorithms for 5G NAS and AS layers based on AES, SNOW and ZUC.
For all 3 algorithms, define algorithm specification, implementation test data and conformance test data.

## Slide 4: Specification vs. Standardisation
The term „Specification“ relates more to the generation of the 3GPP TS (35-series) of the 256-bit Algorithms, while the term „standardisation“ relates more to the introduction of the 256-bit Algorithms in 3GPP protocol stack (33-series, 38-series).
Standardisation
  TS 33.501, Security Architecture (*)
  TS 38.323, PDCP Specification (*)
  TS 38.331, RRC Specification (*)
  (*) To be analysed
Specification
  Specification of the Snow 5G based 256-bits algorithm set:
  TS 35.240 Document 1: Algorithm specification
  TS 35.241 Document 2: Implementers’ test data
  TS 35.242 Document 3: Design conformance test data
  Specification of the AES based 256-bits algorithm set:
  TS 35.243 Document 1: Algorithm specification
  TS 35.244 Document 2: Implementers’ test data
  TS 35.245 Document 3: Design conformance test data
  Specification of the ZUC based 256-bits algorithm set:
  TS 35.246 Document 1: Algorithm specification
  TS 35.247 Document 2: Implementers’ test data
  TS 35.248 Document 3: Design conformance test data
Scope of the WID on 256-bit [1]
Scope of the SID on 256-bit [2]

## Slide 5: Naming of Algorithms
3rd Generation Partnership Project;
Technical Specification Group Services and System Aspects;
Specification of the Snow 5G based 256-bits algorithm set:
Specification of the NEA4 encryption, the NIA4 integrity, and the NCA4 authenticated encryption algorithm for 5G;
Document 1: Algorithm specification
(Release 19)
For the Naming of the Algorithms we have to consider the already existing identifier and naming rules of modes (see Clause 5.11 of [3]) and we should reuse the short-naming of existing Algorithms (35-series).
Algorithm Name (Label) Algorithm Mode Name
NEA4, NIA4, NCA4 (Snow 5G 256-based)  256-NIA1, 256-NEA1, 256-NCA1
NEA5, NIA5, NCA5 (AES 256-based)  256-NIA2, 256-NEA2, 256-NCA2
NEA6, NIA6, NCA6 (ZUC 256-based)  256-NIA3, 256-NEA3, 256-NCA3
Exemplary Representation for Snow 5G !
Agreed on this format:
256-NIA4
256-NEA4

## Slide 6: Authenticated Encryption
Example: Principle of Enryption-then-MAC
Ciphertext
Enryption
Hash Function
MAC
The combined algorithm can do the encryption and integrity protection in a single process, further on, it could do encprytion-only or integrity-only. The configuration can be done via the Input Parameter. The presence of the input parameters is mandatory.
Specification
Standardisation
3GPP Release 18
Comb. Algo. Parameter
Combined Algorithm Function
3GPP Release 19
= Service Access Point
Plaintext
Parameters for Enc.
Parameters for Int.
We could also run this algo twice, just to keep the PDCP Rel18 order of first MAC-then-Enc.
What is in today spec the order in AS and NAS? To be checked.
WID
SID
In Release 19 there is no need for additional input parameters; these can be specified in future;
It might be needed to edit some note in 33.501 that some input parameters need to be (pre-)defined.

## Slide 7: Changes to the WID [1]
to be agreed
[29.01.24]: please refer to the separate word-file

## Slide 8: References
[1] S3-234334, New WID on Addition of 256-bit security Algorithms
[2] S3-235091, New SID on study on enabling a cryptographic algorithm transition to 256-bits
[3] TS 33.501, System Architecture Specification

## Slide 9: Abbreviations
TS Technical Specification

## Slide 10
Thank You!