3GPP TSG-SA3 Meeting #115	S3-24xxxx

Athens, February 26 - March 01, 2024

# Source:	Lenovo [Draft]

# Title:	Introduction for TR 33.794

# Document for:	Approval

Agenda Item:	6.X

# 1	Decision/action requested

This pCR proposes to add Introduction to the TR 33.794.

# 2	References

[1]	3GPP SP-231784, ''New Study on enablers for Zero Trust Security''.

[2]	3GPP TR 33.794, ''New Study on enablers for Zero Trust Security'', Release 19.

[3]	3GPP TR 33.894, ''Study on applicability of the zero trust security principles in mobile networks'', Release 18.

# 3	Rationale

TR 33.794 [2] has an Introduction section with the following EN:

Editor’s Note: This clause contains some background information for the study.

Rel.18 TR 33.894 [3] covers the fundamental building blocks (e.g., tenet evaluations, key issue, and solution) specific to the applications of ZT principles in 5G core SBA. Therefore, a minimal summary from TR 33.894 can provide a brief background information for the Release 19 TR 33.794 study inline to the EN scope above.

# 4	Detailed proposal

SA3 is kindly requested to agree the pCR below to TR 33.794.

*****Start of Change 1*****

# 2	References

The following documents contain provisions which, through reference in this text, constitute provisions of the present document.

-	References are either specific (identified by date of publication, edition number, version number, etc.) or non-specific.

-	For a specific reference, subsequent revisions do not apply.

-	For a non-specific reference, the latest version applies. In the case of a reference to a 3GPP document (including a GSM document), a non-specific reference implicitly refers to the latest version of that document in the same Release as the present document.

[1]	3GPP TR 21.905: "Vocabulary for 3GPP Specifications".

[2]	3GPP TR 33.894, 2023 September, V18.0.0: "Study on applicability of the zero trust security principles in mobile networks", Release 18.

*****Start of Change 1*****

*****Start of Change 2*****

# Introduction

The application of Zero Trust Security principles for the 5G Core, in specific to SBA has been studied in TR 33.894 [2]. The study resulted in an initial potential 5G system security requirement (in Key Issue#1) to identify, collect and expose necessary data to enable security evaluation and monitoring by the operator’s function (e.g., such as SIEM/SOAR deployed in operator’s domain external to 3GPP). A related Solution#1 also illustrates how existing services can be used to collect the necessary data for security monitoring purposes inline with Tenet 5. Nevertheless, as the data to be considered for exposure needs to be well defined and explicitly specified to allow for interoperability and secure operation of installed base as described in Tenet 5 [2], the current study aims to closely investigate and consolidate the potential data to be considered for exposure to the operator’s function (e.g., for the threat detection).  Further the tenet evaluations 4,5,6 and 7 also resulted in identification of security aspects (i.e., related to leveraging results from the operator function to apply security policies for improved access control in SBA) that needs additional study as covered in the scope of this document.

Editor’s Note: Additional background information for the study (if any) if FFS.

*****End of Change 2*****