## Slide 1: CHF Distributed Availability (SA5#146)
João Rodrigues Nokia

## Slide 2: Current Scenario
TS 23.501
6.3.11 CHF Discovery and selection
The CHF discovery and selection function is supported by the SMF, the AMF, the SMSF and the PCF. It is used by the SMF to select a CHF that manages the online charging or offline charging for a PDU Session of a subscriber. It is used by the AMF to select a CHF that manages the online charging or offline charging for 5G connection and mobility of a subscriber. It is used by the SMSF to select a CHF that manages the online charging or offline charging for the SMS over NAS transactions of a subscriber. It is used by the PCF to select a CHF that manages the spending limits for a PDU Session of a subscriber.
There is already the possibility to choose between diferent CHFs (but in the details its limited to primary and secondary CHF usage)
Application Based Charging is defined (TS32.255) without details
Converged Charging System (ABMF/CGF) Reconciliation/Alignment not possible
TS 32.240: Converged Charging Architecture

## Slide 3: Evolution
Changes that can be expected
Allow the possibility of deploying CHF across 5GS (Management & Control Plane)
CHF closer to the endpoint/UE leads faster response
Nchf_ConvergedCharging, Nnrf_NFDiscovery service are expected to be changed
RF, and ABMF could be deployed close to the endpoint (??)
KEY ISSUES
Real Time Charging
Distributed Charging
Charging Availability / Redundancy
Common Part:
Allow CHF Discovery and Selection across the 5GS
Impacts can be expected in SMF (N40), AMF, SMSF and PCF (N28)

## Slide 4: Evaluation
Supported Scenarios | Support use cases which require real-time charging (e.g. URLLC) Instant Charging scenarios Distributed worload across ecosystem (e.g. closer to location) Allow customized rules for each CHF
Impact on Implementation | Backward compatibility can be kept. Nevertheless, new policy control requests are created through PCF.
Affected TS | TS 23.501 (?? CHF Discovery and Selection) // CHF Group ID / CHF Selection Instance ---- NRF based 23502 NRF to CHF informs (CHF Instance Profile) Charging Characteristics ??? TS 23.503 (Reference Architecture of Policy and Charging Control Framework) TS 29.510 (Nnrf_NFDiscovery) TS 32.240 (Convercharging Architecture, RF) TS 32.255 (Application Based Charging) TS 32.290 (Nchf_Convercharging) TS 32.291 (Charging Function / ChargingData Request/Response Message) TS 32.296 (ABMF) – nok linked to CCS --- PCC (SA2) / Study UPF Discovery and Selection (Gerald) --- Annex Deployment Operation Deployments

## Slide 5: Thank you!