## Slide 1: Discussion paper for asynchronous provisioning operation Rapporteur call, June 2nd, 2022
Joey Chou, Intel

## Slide 2: Background
  In the Rel-17 ECM SI in in TR 28.814, the group agreed:
    To reuse the provisioning MnS to support the edge computing lifecycle management.
    To extend the provisioning MnS to support the asynchronous mode operations,
  In the Rel-17 ECM WI in TS 28.538, the group agreed:
    The EAS instantiation and EAS termination procedures include responses in createMOI and delete MOI to indicate the LCM is in progress.
    A couple editorial notes indicating both procedures needed to be revisited after the asynchronous operations are completed.
  In the Rel-18 eECM WI, the group agreed to continue working on the asynchronous operations.

## Slide 3: Functional Framework for RAN Intelligence
3GPP TS 28.538

## Slide 4: Functional Framework for RAN Intelligence
3GPP TS 28.538

## Slide 5: Potential solutions
  Extend createMOI with the status attribute in output parameter to include HTTP status code “202 Accepted”.
  Use LcmJob IOC containing ProcessMonitor dataType to monitor the progress of LCM operation. The LcmJob IOC should be deleted, once the ICM job is completed.
201 Created | Indicates that the request has succeeded, and a new resource has been created as a result.
202 Accepted | Indicates that the request has been received but not completed yet. It is typically used in log running requests and batch processing.

## Slide 6: LCMJob IOC
Attribute names | S | isReadable | isWritable | isInvariant | isNotifyable
lcmJobId | M | T | F | T | T
lcmOperation | M | T | T | F | T
nfForInstantiation | CM | T | T | T | T
deploymentRequirements | CM | T | T | F | T
vnfLcmInfo | CM | T | T | F | T
meForLcm | CM | T | T | F | T
lcmJobStatus | M | T | F | T | T
Attribute related to role |  |  |  |  | 
meMOIRef | CM | T | T | F | T
This IOC represents a lifecycle management job that is used to trigger LCM operation.

## Slide 7: LCMJob IOC attributes
Attribute names | Documentation and allowed values | Property
lcmJobId | It provides the identifier of a LcmJob job. | String
lcmOperation | It indicates the type of LCM operation (see clause 7.3 in ETSI NFV IFA-013 [v]). AllowedValues: “INSTANTIATE”, “TERMINATE”, “UPDATE”, | ENUM
nfForInstantiation | It indicates the type of network function (e.g., “EAS”, “EES”, “ECS”, “PCF”, “UPF”, “NEF”, … etc,) to be instantiated. | ENUM
deploymentRequirements | The attribute contains the DN of the MOI that contains the requirements used to instantiate a specific network function. For example, to instantiate EAS VNF, this attribute should reference the EASRequirements MOI. | DN
vnfLcmInfo | The attributes contain the information needed to support VNF lifecycle management (see clause 7 ETSI NFV IFA-011 [y] and clause 6.3.4.2 in ETSI NFV IFA-014 [z]). | VnfLcmInfo
meForLcm | The attribute specifies the Managed Element, which contains the NF instance to which the LCM operation specified in lcmOperation will be performed (termination or update). | DN
lcmJobStatus | The attribute indicates the status of LCM job. | ProcessMinitor
meMOIRef | The attribute specifies the Management Element MOI containing the NF instance(s) that have been instantiated. | DN

## Slide 8: LCM Job NRM fragment

## Slide 9: VnfLcmInfo dataType
This datatype contains the attributes needed to support VNF lifecycle management (see clause 7 ETSI NFV IFA-011 and clause 6.3.4.2 in ETSI NFV IFA-014
Attribute names | S | isReadable | isWritable | isInvariant | isNotifyable
swImageInfo | M | T | T | F | T
virtualCpu | M | T | T | F | T
virtualMemory | M | T | T | F | T
virtualDisk | M | T | T | F | T
maxLatency | CM | T | T | F | T
maxBitRate | CM | T | T | F | T
minBitRate | CM | T | T | F | T

## Slide 10: VnfLcmInfo dataType attributes
Attribute names | Documentation and allowed values | Property
swImageInfo | This refers to the software image information (e.g., software image location, minimum RAM, disk requirements) (see clause 7.1.6.5 in ETSI NFV IFA-011 [y]). It is defined as a datatype (see clause 6.3.y). | SoftwareImageInfo
virtualCpu | This attribute contains the requirements related to virtual CPU(s) of a virtual compute resource (see clause 7.1.9.3.2.2 in in ETSI NFV IFA-011 [y]). | Integer
virtualMemory | It indicates the minimum virtual memory size requirements for EAS in megabytes. (see clause 7.1.9.3.2.2 in in ETSI NFV IFA-011 [7]). | Integer
virtualDisk | It indicates the minimum virtual diskstorage requirement for the EAS (see clause 7.1.9.4.3.2 in ETSI NFV IFA-011 [7]). | Integer
maxLatency | This attribute specifies the maximum latency for the virtual link associated with the NF (see clause 6.5.6.2 in ETSI NFV IFA-014 [z]). The unit is millisecond. | Integer
maxBitRate | This attribute specifies the maximum bit rate requirement for the virtual link associated with the NF (see clause 6.3.4.2 in ETSI NFV IFA-014 [z]).The unit is Megabyte. | Integer
minBitRate | This attribute specifies the maximum bit rate requirement for the virtual link associated with the NF (see clause 6.3.4.2 in ETSI NFV IFA-014 [z]).The unit is Megabyte. | Integer

## Slide 11: Proposal
  The group is asked to select a solution:
    CreateMOI operation extension
    LCMJob IOC

## Slide 12: Thank you!