## Slide 1: Discussion on basic concepts in FS_FSEV
Huawei, CMCC

## Slide 2: Outline
Definitions in exiting 3GPP specs
Discussion on whether modifications are needed for existing definitions
Discussion on whether potential new concepts are needed
Annex: Contributions about concepts in SA5#146

## Slide 3: Definitions in exiting 3GPP specs (1)
event
  Network occurrence which has significance for the management of an NE. Events do not have state.
event notification
  Notification used to inform the recipient about the occurrence of an event.
alarm
  An alarm signifies an undesired condition of a resource (e.g. network element, link) for which an operator action is required. It emphasizes a key requirement that operators (above Itf-N) should not be informed about an undesired condition unless it requires operator action. Use of this emphasis does not exclude this case: In certain context, it is not possible for alarm reporters (below Itf-N) to know whether a particular undesired condition requires operator action or not. In such context, the NM may receive alarms that do not require operator action.
alarm notification
  Notification used to inform the recipient about the occurrence of an alarm.
active alarm
  An alarm that has not been cleared and which is active until the fault that caused the alarm is corrected and a "clear alarm" is generated.
clear alarm
  Alarm where the severity value is set to "cleared"
managed alarm
  The management representation of the alarm in the NM domain.
References:
  [1] TS 32.111-1: "Fault Management; Part 1: 3G fault management requirements“

## Slide 4: Definitions in exiting 3GPP specs (2)
Fault
  A deviation of a system from normal operation, which may result in the loss of operational capabilities of the element or the loss of redundancy in case of a redundant configuration.
ADAC Faults
  Faults that are "Automatically Detected and Automatically Cleared" by the system when they occur and when they are repaired.
ADMC Faults
  Faults that are Automatically Detected by the system when they occur and Manually Cleared by the operator when they are repaired.
The following are not specified as definitions, but descriptions are available:
  Correlation: The correlation describes relations between network events (e.g. current alarms as those captured in AlarmList, historical alarms as those captured in Notification Log, network configuration changes).
  Root cause analysis: Root Cause Analysis is a process that can determine and identify the network condition (e.g. fault, mis‑configuration) causing the alarms.
References:
  [1] TS 32.111-1: "Fault Management; Part 1: 3G fault management requirements“

## Slide 5: Discussion on whether modifications are needed for existing definitions
Event
  There was proposal not to restrict the event to occurrences in the network, e.g. threshold crossing in the management system is also an event.
alarm
  In certain context, it is not possible for alarm reporters (below Itf-N) to know whether a particular undesired condition requires operator action or not. In such context, the NM may receive alarms that do not require operator action.
  The severity of the fault (indeterminate, warning, minor, major, critical), as defined in ITU‑T Recommendation X.733 [9]. In X.733: Early detection of faults before significant effects have been felt by the user is a desirable requirement of communicating systems. Threshold mechanisms on counters and gauges are a method of detecting such trends and providing a warning to managers when the rate becomes high.
  It is expected that two aspects could be enhanced from both the resource layer and the NM layer. (1) Identification of alarms which require operator action; (2) Extend “warning” severity level alarms to “prediction” type of alarms.
managed alarm
  An operator’s view can obviously be very different from the alarm severity defined by the NEs' resource focused views. Within the NM, the received resource alarms are transformed so that the alarm severity is no longer resource focused but service impact focused, to prevent or mitigate network and service outage and degradation. The transformation applies to all severity levels.
  There were no detail descriptions in existing specs. The aspect regarding resource focused alarm and service impact focused alarm may need some enhancement in both resource layer and the NM layer.
Fault
  There was proposal to modify definition of fault to the cause for error and failure, and to differentiate error and failure as “small problem” and “big problem”.
  There are already severity level of the fault (indeterminate, warning, minor, major, critical), as defined in ITU‑T Recommendation X.733 [9]. Discussions are needed on how to use them altogether.
References:
  [1] TS 32.111-1: "Fault Management; Part 1: 3G fault management requirements“.

## Slide 6: Discussion on whether potential new concepts are needed
Existing definitions have not explicitly differentiated alarm/fault which occurred or may occur in the future.
Existing definitions for “managed alarm” is vague. It may need to be redefined in 3GPP context regarding “service focused”, resource layer may also have such capability e.g. alarm/fault for network slice subnet service.
There may be alarm notifications which do not require operator action.
Analytics management capability are available in FM and eMDAS, it is “analytics report” in eMDAS spec, there are no definitions for analytics in FM spec.
  There are texts regarding analytics management capabilities in existing specs for Alarm/fault management, e.g., FM also includes…such as…the provision and analysis of the alarm and state history of the network; “4.1.9 Root Cause Analysis” etc. [TS 32.111-1].
  There are texts regarding analytics management capabilities in existing specs for eMDAS TS/TR, e.g., “7.2.3 MDA assisted fault management” etc. [TS 28.104].
To cover all above cases, a new term “anomaly event/service anomaly” is introduced (better name?):
  anomaly event/Service anomaly: Deviation from what is standard, normal, or expected which have or will have service and network impacts and need actions to resolve.
  The service anomaly is a generic term to represent the deviation from normal state. It may be fault/performance degradation which have occurred or may occur in the future. It is the analytical result by FM management capability and is applicable both in the resource layer and the NM layer.
  To identify service anomaly, existing alarm notifications, performance data, historical data etc would be used, since it is the analytical result, a new term is used to differentiate from existing alarm/fault. It does not modify exiting FM interface.

## Slide 7: Annex: Contributions about concepts in SA5#146
Event: Anything that occurs, for example a configuration change, a threshold crossing, an error or a failure. Events do not have states [1].
Event notification: A kind of notification used to inform the recipient about the occurrence of an event [1].
Error: A deviation of the actual system state from the correct system state. An error may or may not lead to a service failure. An error is a special kind of event [1].
Failure: A state of inability to deliver the correct service. A service failure may be the result of an error, or because the system function deviates from the service specification. A service failure is a special kind of event [1].
Fault: The (hypothesized or adjudged) cause for an error or a failure [1].
Alarm information: Information item that contains information about an incorrect system state or a potentially future incorrect system state. An alarm information item is created only when operator attention or operator action is required [1].
Alarm notification: A notification reporting the creation, update or deletion of an alarm information item [1].
Alarm: Referring to alarm information or an alarm notification depending on the context [1].
Alarm correlation: The act of identifying relations (correlations) between alarm information items [1].
Root cause analysis: The act of identifying the fault, if any, leading to multiple errors or service failures. In case the root cause analysis works only on errors of failures that raised alarms, the act of identifying the alarm related to the fault causing also other alarms [1].
Anomaly event / service anomaly: Anomaly event (or Service anomaly): Deviation from what is standard, normal, or expected which have or will have service and network impacts and therefore need actions to resolve [2].
Service failure prediction: The capability for providing the analytics output including predictions of potential service failures as well as the possible recommendation actions to prevent failures [2].
References:
  [1] S5-226633 -> S5-226947: "Rel-18 pCR 28.830 Add alarm related definitions“
  [2] S5-226214 -> S5-226946: "DP on concepts in FSEV study"

## Slide 8: Thank you!

## Slide 9: Online discussion-brainstorming
Event (existing)
  Network occurrence which has significance for the management of an NE. Events do not have state.
Event (New)
  (Nokia) Anything that occurs at certain point of time, for example a configuration change, a threshold crossing, an error or a failure. Events do not have states [1].
  (Brendan) Instantaneous change in an observed system, for example a configuration change, a threshold crossing, an error or a failure. Events do not have states.
(Nokia) Error(New): A deviation of the actual system state from the correct system state. An error may or may not lead to a service failure. [1].
(Nokia) Failure(New): A state of inability to deliver the correct service. A service failure may be the result of an error, or because the system function deviates from the service specification. [1].
Fault (existing)
  A deviation of a system from normal operation, which may result in the loss of operational capabilities of the element or the loss of redundancy in case of a redundant configuration.
  Fault (New)
  (Nokia) The (hypothesized or adjudged) cause for an error or a failure [1].
  (Brendan) A reason for deviation of a system from normal operation.
Alarm (existing)
  An alarm signifies an undesired condition of a resource (e.g. network element, link) for which an operator action is required. It emphasizes a key requirement that operators (above Itf-N) should not be informed about an undesired condition unless it requires operator action. Use of this emphasis does not exclude this case: In certain context, it is not possible for alarm reporters (below Itf-N) to know whether a particular undesired condition requires operator action or not. In such context, the NM may receive alarms that do not require operator action.
Alarm (New):
  (Nokia) Referring to alarm information or an alarm notification depending on the context [1].
  Alarms have states.

## Slide 10: Online discussion-brainstorming
event1
alarm1
event2
event3
Error
Failure
trigger
marks
marks
action
consequence
Sb opened the door
The door is open
fault2
fault3
Design of the cabinet
Challenge??