## Slide 1: Discussion of concepts for Network Digital Twin SA5 rapporteur call - xx Feb, 2024
Brendan Hassett, Huawei

## Slide 2: Problem description
There are multiple definitions of “Digital Twin”.
Many formal definitions are very vague and open-ended.
Most examples in literature focus on using “Digital Twin” in an industrial process, there are no good examples which map directly to 3GPP Network Management.
SA5 needs to assess:
Which aspects of “Digital Twin” are relevant for 3GPP Network Management
What value/opportunities can be gained from “Digital Twin”

## Slide 3: Issues with “Digital Twin” terminology
Most of the existing literature on “Digital Twin” refers to industrial processes. Typically, the literature focuses on “greenfield” industrial automation and includes many aspects that are essential enablers for Digital Twin, but are not actually part of Digital Twin, such as:
  How to model an asset
  How to synchronize a model instance with a physical asset
It can be very difficult to map this literature to the problem space of 3GPP Network Management, which is a very mature problem space with well-defined concepts and solutions.

## Slide 4: Useful concepts from published research
A research paper [1] could be useful for 3GPP SA5.
[1] The Concept of Digital Twin and Digital Shadow in Manufacturing 9th CIRP Conference on High Performance Cutting (HPC 2020) https://www.sciencedirect.com/science/article/pii/S2212827121006612
Abstract
There still is a lacking comprehensive understanding of the relevant terms Digital Twin (DT) and Digital Shadow (DS) in particular within the application on the field of manufacturing technology. However, a common, transparent understanding of the concept and its requirements interferes with the implementation and application of these powerful tools. In this sense, the following publication gives a new definition of the concept within the field of manufacturing technology and shows specific applications.

## Slide 5: Digital shadow as described in [1]
A digital representation of a physical asset instance.
Contains aspects of an asset (e.g. attributes and relationships) which are synchronized in near real-time.
May be read from the asset (interrogation) and written to the asset (control).
In SA5, this maps directly to a Managed Object Instance.

## Slide 6: Digital twin as described in [1]
An enhancement of a digital shadow to add extra aspects.
Extra aspects are not modelled in the asset, but can be inferred by how the asset reacts to its environment.
Extra aspects may reflect outside influences on the asset, for example:
  How the asset may be changed by external environment
  How the asset may be changed by lifecycle/workflow
In SA5, this does not map to any existing concepts.

## Slide 7: A way forward
3GPP SA5 already has a concept (MOI) which maps directly to a digital shadow as defined in [1].
3GPP SA5 has no concept which maps to a digital twin as defined in [1].
Therefore, there follows a deeper analysis of the difference between Digital Shadow and Digital Twin in [1] to help guide the future work of 3GPP SA5.

## Slide 8: Differences between DS and DT
As described in [1], the digital twin adds the concept of causality. This means that extra attributes of the asset will change in specific ways which relate to the workflow.
A use case in [1] shows an example of a cutting machine and a piece of metal to be cut.
  As the cutting process (workflow) proceeds, mechanical stresses increase in the metal. The stresses cannot be measured (do not exist in the DS), but the DT of the metal can use the laws of physics to infer an approximate stress level.
  As the cutting process (workflow) proceeds, the cutting tool becomes worn. The wear level cannot be measured (does not exist in the DS), but the DT of the cutting tool can use historical statistics to infer an approximate wear level.

## Slide 9: The unique value of Digital Twin
Therefore, it seems that the unique value of Digital Twin (as compared to Digital Shadow) is to create extra knowledge which is not modelled in the Digital Shadow, but can only be calculated by considering the environment and workflow.
The Digital Twin can infer values for attributes which are difficult to measure or model in the Digital Shadow.
For 3GPP SA5, the NRM represents a static view of the modelled network, but Digital Twin can add information related to the dynamic behavior of the network.

## Slide 10: Some practical examples
For 3GPP SA5, this could manifest as abstract Key Quality Indicators which are difficult to calculate based only on the contents of the MOIs, and which need to consider the network environment and operational workflows.
The stability of a Network Function could be estimated by combining the Network Function MOIs with a proposed repair workflow.
The traffic handling capacity of a network could be estimated by combining the actual traffic levels with a proposed energy saving action.

## Slide 11: Opportunities
A Digital Twin could enable a network operator to explore Key Quality Indicators (e.g. resilience, stability, traffic handling capacity, efficiency) in ways that are not currently possible using the 3GPP Network Resource Model.
A Digital Twin could be used to combine the MOIs with proposed workflows in simulated environments, validate the results, and enable the network operator to approve/disapprove the workflows.

## Slide 12: Guidance for SA5
Avoid use cases which can be satisfied by just using information that exists in the 3GPP Network Resource Model.
Focus on use cases that:
Consumes information from the 3GPP Network Resource Model
Combines with network environment information and/or operational workflow information
Produces new knowledge that did not originally exist in the 3GPP Network Resource Model

## Slide 13: Thank you!