## Slide 1
AUTONOMOUS NETWORKS AND INTENT-BASED OPERATION
JÖRG NIEMÖLLER
Expert of Analytics and Customer Experience Ericsson
KEVIN MCDONNELL
Senior Director, Intelligent Automation Huawei

## Slide 2: Content
Intent in Autonomous Networks
What is Intent?
Architecture of intent management
Intent life-cycle
Intent API
Intent Modelling
(briefly) Model Federation and Intent Manager Capabilities
Q&A
Notes: Kevin slides 1- 17
Joerg slides 18 -28
Kevin slides 29-30
Joerg slides 32-37

## Slide 3: Autonomous Networks Blueprint
Testing & Verification
Outside-In – Across Many Vertical Ecosystems
Inside-out – Autonomous Operations
Business Requirements & Framework
Reference Architecture & Technical Mechanisms
Vision
AN
Levels
Business Growth and Operation Efficiency
Zero-X and Self-X
AN Framework
Business Drivers (Guiding Principles)
Autonomy Principles
Technical Architecture
Mechanisms:
Autonomous Domain, Closed Loop and Intent
AN Reference Architecture
Intent Model and Intent Interfaces
Case Studies
Case Studies
Case Studies
Case Studies
Case Studies
Best Practices
Case Studies
Case Studies
TMF Catalysts
(PoCs)
Other
SDO
Projects
(e.g. ETSI,3GPP, ITU, GSMA, etc.)
Other
TM Forum
Collaboration Projects
(e.g. ODA, AI, API, SID, DMM, etc.)
& Collaboration
IG1193
IG1229
IG1218A and B
IG1218
IG1230
IG1230A and B
IG1251
IG1253
IG1253 A,B,C,D
IG1259
IG1252
IG1269
Notes: Let’s talk about how in ANP we are organized. A framework for Autonomous Networks that goes from vision to real projects.
A top to bottom approach … collaboration on these key mechanisms

## Slide 4: Today’s sessions will focus on Intent-driven AN
Testing & Verification
Outside-In – Across Many Vertical Ecosystems
Inside-out – Autonomous Operations
Business Requirements & Framework
Reference Architecture & Technical Mechanisms
Vision
AN
Levels
Business Growth and Operation Efficiency
Zero-X and Self-X
AN Framework
Business Drivers (Guiding Principles)
Autonomy Principles
Technical Architecture
Mechanisms:
Autonomous Domain, Closed Loop and Intent
AN Reference Architecture
Intent Model and Intent Interfaces
Case Studies
Case Studies
Case Studies
Case Studies
Case Studies
Best Practices
Case Studies
Case Studies
TMF Catalysts
(PoCs)
Other
SDO
Projects
(e.g. ETSI,3GPP, ITU, GSMA, etc.)
Other
TM Forum
Collaboration Projects
(e.g. ODA, AI, API, SID, DMM, etc.)
& Collaboration
Notes: Focus on the green parts intent and how we collorborate with other SDOs

## Slide 5: Where Intent fits in Autonomous Network?
0 1 2 3 4 5
P/S
P/S
P/S
P/S
P/S
Control Loop Management
<<Intent Owner>>
Awareness
Analysis
Execution
Intent
Expectations / Requirements
Experience
SLA compliance
Decision-making
Control
Loop
(AADE)
Intent Management <<Intent Handler>>
Sourced from Autonomous Networks Guides
(IG1218, IG1230, IG1251) TM Forum
Notes: Some high levels from AN Project. AN Levels Table describes the 0 to 5 levels of autonomy. Slider of autonomy shifts responsibility from H to M.
Adaptive and Adpatible..

## Slide 6
AN Reference
Architecture
Notes: All of that comes together in a clean Reference architecture…

## Slide 7: Architectural Principles
01: Decoupled operations layers for operational flexibility
02: Intent-driven, open interfaces
03: Closed Loop Automation
04: Endogenous Intelligence
05: Single-Domain Autonomous
06: Cross-Domain Collaboration
07: Supports interactions between Autonomous Domains of different Autonomy Levels
Intent
Control
Loop
Knowledge
& Intelligence
Autonomous
Domain
AN Level
AN Reference
Architecture
Autonomy
Notes: These principles guide the design of the system capabilities required to achieve the desired autonomy levels within autonomous domains and autonomous networks.
Each principle related to particular concepts
Decouple The Layers. the autonomous networks architecture is separated into three layers, business operations layer, service operations layer, and resource operations layer.
Autonomous Networks should expose standardized interfaces
Automation uses closed loop mechanisms to by continuously adapting to ensure goals and objectives are met. The control loop adjusts and adapts itself (through the decision cycle sages of Awareness, Analysis, Decision, Execution
Domain self contains its intelligence
The autonomy and independence of a domain is a core principle of AN
each domain is autonomous, but domains must also collaborate: the can coordinate, they can federate domains .
All together creates a lego block approach – simple yes but intentially so . Any real life scenario can described by this framework by understanding this principles.

## Slide 8: AUTONOMOUS NETWORKS REFERENCE ARCHITECTURE (IG1251)
Autonomous Domain
Autonomous Domain
Intent Management
Domain Control Loop Management
Awareness
Analysis
Decision
Execution
Domain Intelligence
Knowledge Governance
Knowledge Optimization
Knowledge Base
NE
SI
F3
I3
K3
“AADE” Control Loop
MAPE-K inspired
Intent-driven…
Notes: Lets put it together….. The Autonomous Domain …. 3 Address Points show here as I J and K
Logical contruct – Domain has a control loop in 4 main phases …informs by knowledge.
Awareness
Analysis
Decisionn
Execution..

## Slide 9: AUTONOMOUS NETWORKS REFERENCE ARCHITECTURE (IG1251)
Autonomous Domain (AD)
Intelligence is decentralized and localized
Single Domain Autonomy
Cross Domain Collaboration
Decoupled Operational Layers
Intent-driven, Open Interfaces
F3
Autonomous Domain
Intent Management
Domain Intelligence
Domain Control Loop Management
Awareness
Analysis
Decision
Execution
Knowledge Governance
Knowledge Optimization
Knowledge Base
NE
SI
I3
K3
5. Single Domain Autonomy
1. Decoupled Operational Layers
2. Intent-driven, Open Interfaces
4. Intelligence is decentralized and localized
3. Closed Loop Automation
5 of 7
Architectural Principles embodied in AD

## Slide 10: AUTONOMOUS NETWORKS REFERENCE ARCHITECTURE (IG1251)
Autonomous Domain
Intelligence is decentralized and localized
Single Domain Autonomy
Cross Domain Collaboration
Decoupled Operational Layers
Intent-driven, Open Interfaces
F3
Autonomous Domain
Intent Management
Domain Intelligence
Domain Control Loop Management
Awareness
Analysis
Decision
Execution
Knowledge Governance
Knowledge Optimization
Knowledge Base
NE
SI
I3
K3

## Slide 11: AUTONOMOUS NETWORKS REFERENCE ARCHITECTURE (IG1251)
Reference Points
F3
Autonomous Domain
C (Detailed)
Intent Management
Domain Intelligence
Domain Control Loop Management
Awareness
Analysis
Decision
Execution
Knowledge Governance
Knowledge Optimization
Knowledge Base
NE
SI
I3
Intelligence is decentralized and localized
Single Domain Autonomy
Cross Domain Collaboration
Decoupled Operational Layers
Intent-driven, Open Interfaces
K3

## Slide 12: AUTONOMOUS NETWORKS REFERENCE ARCHITECTURE (IG1251)
Cross Domain Autonomy
* SI: Site Intelligence
F3
Service Operations
ICT Infrastructure
Business Operations
Service Operations
Intelligence
Business Operations
Intelligence
Autonomous Domain
B (Simplified)
Autonomous Domain
C (Detailed)
Knowledge and Intelligence
Data Services
Application
Catalog
Model
Training
Knowledge
Base
Local Intelligence
Local Intelligence
Digital Storefront
Portals
Planning
Deploy
Maintain
Optimization
Other
Intent Management
Domain Intelligence
Domain Control Loop Management
Awareness
Analysis
Decision
Execution
Knowledge Governance
Knowledge Optimization
Knowledge Base
AN Consumers
(External Ecosystem - B2B , B2C, etc.)
K2
K1
K3
I3
I3
NE
SI
Resource
Operations
Domain
Intelligence
NE
SI
I1
I2
I3
…
F3
…
1..N Autonomous Domains (AD)
Only ADs at resource layer shown for simplicity
Resource
Operations
Domain
Intelligence
NE
SI
Autonomous Domain
A (Simplified)
F3
…
F2
…
F1
Intelligence is decentralized and localized
Single Domain Autonomy
Cross Domain Collaboration
Decoupled Operational Layers
Intent-driven, Open Interfaces
7. Support Mismatched AN Levels
5. Cross Domain Collaboration

## Slide 13: AN is assembled from Autonomous Domains
Multiple AD deployment modes
In E2E solution scenarios, there are multiple AD deployment modes, and an overall AD solution is required.
Service Platforms
Business Platforms
Resource Platforms
AN Consumer Platforms
Knowledge and Intelligence
K2
K1
K3
I1
I2
I3
Resource
Operations
Service
Operations
Business
Operations
Autonomous Domains
F3
F2
F1

## Slide 14: A SINGLE INTENT INTERFACE SPECIFICATION USED THROUGHOUT
* SI: Site Intelligence
F3
Service Operations
ICT Infrastructure
Business Operations
Service Operations
Intelligence
Business Operations
Intelligence
Autonomous Domain
B (Simplified)
Autonomous Domain
C (Detailed)
Knowledge and Intelligence
Data Services
Application
Catalog
Model
Training
Knowledge
Base
Local Intelligence
Local Intelligence
Digital Storefront
Portals
Planning
Deploy
Maintain
Optimization
Other
Intent Management
Domain Intelligence
Domain Control Loop Management
Awareness
Analysis
Decision
Execution
Knowledge Governance
Knowledge Optimization
Knowledge Base
AN Consumers
(External Ecosystem - B2B , B2C, etc.)
K2
K1
K3
I3
I3
NE
SI
Resource
Operations
Domain
Intelligence
NE
SI
I1
I2
I3
…
F3
…
1..N Autonomous Domains (AD)
Only ADs at resource layer shown for simplicity
Resource
Operations
Domain
Intelligence
NE
SI
Autonomous Domain
A (Simplified)
F3
…
F2
…
F1
AD E
AD F
Intent API TMF921 can be used at all I and F reference points
I3
F3
AD C
AD D
I2
F2
Business
Operations
Resources
Operations
Service
Operations
AD A
AD B
I1
F1
…
…
…
AN Reference Architecture (IG1251)
Intent API can be used
at I and F Reference Points
Notes: The first of many new APIS but no doubt this is critical…

## Slide 15: TM FORUM INTENT API
JSON
Turtle
JSON-LD
http://<stable> URL
1. Express Intent
Expectation
Context
3. Negotiate Intent
“overloaded” CRUD approach
Not using TaskResource approach
For “JUDGE, PROBE, BEST” etc
2.Report on Intent
IntentReport
Operations
Format
Network Endpoint
Intent Management API
TMF921
http://tmforum.org/intent/v4/intent/123
Asynchronous Request-Reply pattern
STANDARDIZED
“Restful”
“Straightforward”
“Terse Grammar”
Notes: Joerg will take us through some dteial view starting from Defintion …but I’ll preview it here a little..
It will be A TMForum Standard API…
3 purple sections …Functional.
Joerg will talk about Ontology and format…s Turtle.
Straighforward implementation for Developer…..Restfulness helps make it straightforward.

## Slide 16: TMF921 INTENT API
TMF921A Intent Management API Profile
TMF92I API Specification in Development (in TMF Github)
  Open_API_And_Data_Model/apis/TMF921_Intent/
  Uses TMF API Toolchain on AWS environment
https://www.tmforum.org/resources/standard/tmf921a-intent-management-api-profile-v1-0-0/
API User Guide
OAS Specification
Conformance Profile
CTKs
Notes: API spectification
Conformance rules
Postman Examples
CTK.

## Slide 17
What is Intent?

## Slide 18: WHAT IS INTENT?
From user perspective it expresses what a system is expected to achieve
It includes all the system needs to know, including goals, requirements, constraints, …
It needs formal modelling and common semantics to be understandable to the system
It is not only used on the human-machine interface, but in internal goal-setting between of sub-systems
Natural language and other domain-specific languages can be used but it requires local interpretation and translation into the common intent model.
Has its life cycle actively managed by the intent owner/creator/sender through the intent API
Intent is the formal specification of all expectations including requirements, goals, and constraints given to a technical system

## Slide 19
How to operate with Intent?
Architectural Considerations

## Slide 20: INTENT STANDARDIZATION IN THE AUTONOMOUS NETWORKS PROJECT
@prefix imm: https://tmforum.org/2020/07/intent/
@prefix tel: http://sdo1.org/TelecomConcepts/
@prefix met: http://sdo1.org/metrics/version2/
@prefix sli: http://sdo2.org/2021/03/SliceIntent/
@prefix slk: http://sdo2.org/2019/SliceKPI/
@prefix slm: http://sdo3.org/v1.1/SliceManagment/
@prefix tim: http://sdo4.org/time/
@prefix geo: http://sdo4.org/geography/
@prefix cat: http://operator.com/Catalog/
@prefix ope: http://operator.com/Inventory/
ope:ExampleIntent2021031100002 a imm:Intent ; imm:hasExpectation [ a imm:DeliveryExpectation ; imm:target _:function ; imm:params [ cat:amf ]
] ,
[ a imm:DeliveryExpectation ; imm:target _:slice ; imm:params [ cat:SliceTypeA ]
] ,
[ a imm:MinMetricExpectation ; imm:target _:function ; imm:params [ tel:subscribers 1000 ;
met:availablility 99.9 ] ] ,
Intent Interface
Intent Owner
Intent Handler
SET, REMOVE
REPORT
Detection
Investigation
Definition
Distribution
Operation
Intent Manager
Registry
Intent Manager Capability Profiles
Intent Interface
Intent Manager (handler)
Intent Manager (owner)
Intent Manager Registration
Intent Manager Discovery
Intent life-cycle management
Role definitions: owner and handler
Phases in the life-cycle
Intent modelling
Formal definition of intent and intent reports
Vocabulary and semantics of intent expression
Model federation allowing domain specific extensions by SDOs and vendors
Intent interface and API
Life cycle management of intent objects
Negotiation and feasibility
Intent handler capability registration and discovery
Interface is domain agnostic and highly reusable
Concepts, definitions and architecture
Definition of intent
Operation principles
Intent management function
Intent manager capability
Capability profiles
Intent Manager Registration
Intent Manager Discovery

## Slide 21: HOW TO OPERATE WITH INTENT?
Based on: Stuart J. Russel, Peter Norvig 2003: “Artificial Intelligence, A Modern Approach“ (2013)
Zero-touch control
Sensor
Actuator
Thinking
Knowing
Operator
Intent
Percepts
Actions
Environment

## Slide 22: OPERATION WITH INTENT: The Intent Management Function
It is the receiver of intent
It is responsible for a clearly defined operational domain
It measures the state of the domain it operates to compare if intent is met
It decides on corrective actions
It acts through conventional interfaces: configure, set-up, deployment, ...
It acts through additional intent sent to other intent managers
It reports the intent fulfillment status back to the origin of the intent
intent
report
action
update
report
intent
Actuation
Decision
Knowledge
Intent Management Function The basic building block of intent-based operation
Intent Interface
Other (not intent based) Interfaces

## Slide 23: OPERATION WITH INTENT
intent
report
action
update
report
intent
Actuation
Decision
Knowledge
Intent Management Function The basic building block of intent-based operation
Intent Interface
Other (not intent based) Interfaces
Business Intent Manager
Service Intent Manager
Business Portal
Operations Portal
Business Operations
Customer Portal
Service Operation
Resource Operations
Contract and Order Management
ADn Intent Manager
AD1 Intent Manager
AD2 Intent Manager
Intent managers specific to operation sub-domains

## Slide 24: INTENT TRANSLATION
From intent into configurations and actions
Translate the intent into target configurations
Act using conventional (not intent based) interfaces
From direct user intent into formal expression
Intent might be given by a user in natural or domain specific language
The autonomous network operates from formal intent
Interpretation of intent given in natural, or domain specific language is needed to create ambiguity free formal intent expression.
From higher level intent into lower-level intent
Act by using intent to change the requirements in other autonomous domains
One intent can lead to multiple subsequent intents
A mix of intent-based and not intent-based actions is possible
Customer Portal
intent
DSL Interpretation
Intent Handling
intent
action
Intent Handling
intent
intent
Quick

## Slide 25
Interface and Life Cycle
Defining a polymorphic API

## Slide 26: INTENT LIFE CYCLE
ROLES OF INTENT MANAGERS:
Intent Owner: has created the intent and is responsible for managing its life-cycle
Intent Handler: has received the intent and operates its domain accordingly
Every intent has exactly one owner and one handler
An intent manager can be owner of some intents and at the same time handler of others
PHASES:
Detection: Identify the need to define new or change/remove existing intent to set requirements, goals, constraints. React to handling success.
Investigation: Find out what intent feasible and can be required from the underlying handlers.
Definition: Decide what to require from the underlying intent handlers and create, modify or remove intent accordingly.
Distribution: Identify the intent handlers according to the targeted management domains and inform them about the new intent configuration.
Operation: Intent handlers operate their domain according to the given intent and report back to the owner about status and success
Detection
Investigation
Definition
Distribution
Operation

## Slide 27: INTENT INTERFACE OPERATIONS OVERVIEW
Mandatory operations for basic intent lifecycle management
SET: Send a new or modified intent to an intent handler
REMOVE: Withdraw and retire an intent
REPORT: Report the intent handling status and success
Optional operations for advanced intent negotiation
JUDGE: Collaborative evaluation of proposed solutions
PROBE: Asking the handler to estimate the potential success of an intent
BEST: Asking the handler for the best intent it can successfully handle
Intent Interface
Intent Manager (Intent Owner)
Intent Manager (Intent Handler)
SET, REMOVE
REPORT
PROBE BEST
REPORT (PROBE), REPORT (BEST), JUDGE

## Slide 28: INTENT INTERFACE OPERATIONS: BASIC SETTING AND REPORTING
The SET operation is used by an intent owner to communicate an intent to the chosen intent handler.
The REPORT operation is used by the intent handler to report on progress according to the reporting conditions the owner has specified within the intent.
Note: These are conceptual operations of the intent interface. They are be implemented using REST and CRUD operations in API design
Intent Handler
Intent Owner
SET: <intent 1>
REPORT: <intent report 1>
REPORT: <intent report 2>
REPORT: <intent report 3>
…
Notes: Kevin

## Slide 29: INTENT INTERFACE OPERATIONS: BASIC SETTING AND REPORTING (REST)
The SET operation is a POST request from intent owner to intent handler
Handler returns the Id and acknowledges IntentReceived in a 201 Created response
Intent Handler
Intent Owner
POST: /intent
(Body: Intent)
2. : 202 Created
{ Id: “531” }
Processing..
POST Subscription
“call me back at intent/531/<eventchange>”
4. : 201 Created
{
"id": “531",
"callback": "http://in.listener.com"
}
A Subscription i.e. register a Listener at /intents/hub/
Handler returns the Id and acknowledges IntentReceived in a 201 Created response
Notes: Call me back for /531/event = get a hub.
202 Accepted Request has been received in the server but yet to be processed.
Intent API relies on callback functionality for Intent Reporting
Callbacks provides the ability for the server to notify the application of particular events subscribed to.
For example, in the case when the Intent Owner resides in a server-like environment a request URL may be passed by the owner on which it can be notified of particular events that the owner subscribed to.
ASSUMPTION: Paths use "/listener/...". For Client or Owner side API calls.
The “server-side” of this part of API has to be implemented by the clients (intent Owner) of the TMF921 API and is meant to be a "sink" for events emitted by the TMF921 service.

## Slide 30: INTENT INTERFACE OPERATIONS: Notification (REST) “callback”
The Callback is a register
Handler returns the Id and acknowledges IntentReceived in a 201 Created response
Intent Handler
Intent Owner
5. POST {callback_ref} (Notification)
Intent Handler
(taking the role of a HTTP server)
Intent Owner
(taking the role of a HTTP server)
6. : 204 Created
{
"id": “531",
"callback": "http://in.listener.com"
}
Previous slide
3. POST {callback_ref} (Notification)
4. : 201 Created
{
"id": “531",
"callback": "http://in.listener.com"
}
Notes: 202 Accepted Request has been received in the server but yet to be processed.
Intent API relies on callback functionality for Intent Reporting
Callbacks provides the ability for the server to notify the application of particular events subscribed to.
For example, in the case when the Intent Owner resides in a server-like environment a request URL may be passed by the owner on which it can be notified of particular events that the owner subscribed to.
ASSUMPTION: Paths use "/listener/...". For Client or Owner side API calls.
The “server-side” of this part of API has to be implemented by the clients (intent Owner) of the TMF921 API and is meant to be a "sink" for events emitted by the TMF921 service.

## Slide 31: Intent Reports use REST Callbacks
Intent API relies on callback functionality for Intent Reporting
Callbacks provides the ability for the server to notify the application of particular events subscribed to.
For example, in the case when the Intent Owner resides in a server-like environment a request URL may be passed by the owner on which it can be notified of particular events that the owner subscribed to.
ASSUMPTION: Paths use "/listener/...". For Client or Owner side API calls.
The “server-side” of this part of API has to be implemented by the clients (intent Owner) of the TMF921 API and is meant to be a "sink" for events emitted by the TMF921 service.

## Slide 32: INTENT INTERFACE OPERATIONS: REMOVAL OF INTENT
The intent owner can at any time order a removal of the intent.
Only the intent owner can order a removal.
The intent hander will create and send a final report to confirm the removal.
Intent Handler
Intent Owner
SET: <intent 1>
REPORT: <intent report 1>
REPORT: <intent report 2>
REPORT: <intent report 3>
…
REMOVE: <intent 1>
REPORT: <intent report 4>

## Slide 33: INTENT INTERFACE OPERATIONS: REJECTION OF INTENT
The intent handler can reject received intent
The rejection is communicated back to the owner with an intent report.
The rection reason is given within the report, for example:
  Unknown format, Unknown model: the handler does not recognize or support the models and formats used to formulate the intent.
  Success not expected: The handler does not expect it can successfully meet the requirements set by the intent.
Once accepted the handler can only report on its progress, but not reject later
The owner can decide to remove or modify based on the reports it receives.
The intent owner can decide to revise the intent accordingly and try again with a new intent.
Intent Handler
Intent Owner
SET: <intent 1>
REPORT: <intent report 1 (rejection reason)>
…
SET: <intent 2>
REPORT: <intent report 2>
REPORT: <intent report 3>
REPORT: <intent report 4>
…

## Slide 34: INTENT INTERFACE OPERATIONS: FEASIBILITY THROUGH PROBING
The intent owner use the PROBE operation to send an intent to the intent handler.
  The hander is not supposed to consider this intent in its operation.
  The intent handler would however start sending reports that contain the hypothetical results it expects to reach when this intent would be send for operation.
  PROBE works like SET with the difference that the intent is not really influencing the operation.
Modification and removal of probed intent works the same way as after SET operation.
Generating the hypothetical intent reports typically requires predictive capabilities implemented in the intent handler. This is can be very challenging or not needed in certain domains. Probing is therefore an optional operation.
Intent Handler
Intent Owner
PROBE: <intent 1>
REPORT: <intent report 1>
REPORT: <intent report 2>
REPORT: <intent report 3>
…
REMOVE: <intent 1>
REPORT: <intent report 4>

## Slide 35: INTENT INTERFACE OPERATIONS: FINDING MAXIMUM REQUIREMENTS
The intent owner uses the BEST operation to send an intent to the intent handler.
  Some requirements within the intent are marked to indicate that a proposal about the maximum requirement shall be made
  This is the most challenging requirement level that can still be successfully handled.
  Intent received through BEST is not considered for actual operation actions.
  The intent handler would start sending reports that contain proposals for the maximum level/values of the marked requirements
  BEST therefore works like PROBE and SET with the difference that the intent is not really influencing the operation and additional reports are sent with proposals about maximum possible requirements
Modification and removal of probed intent works the same way as after SET operation.
BEST operation is optional.
Intent Handler
Intent Owner
BEST: <intent 1 (with best request)>
REPORT: <intent report 1 (proposal)>
REPORT: <intent report 2 (proposal)>
REPORT: <intent report 3 (proposal)>
…
REMOVE: <intent 1>
REPORT: <intent report 4>

## Slide 36: INTENT INTERFACE OPERATIONS: COLLABORATIVE SOLUTION EVALUATION
The Situation:
  The intent handler might have multiple solution strategies available that all fulfill the intent but with different characteristics.
  From the intent alone it cannot decide which outcome is preferable, but the intent owner has the domain knowledge to judge this.
The intent handler can use the JUDGE operation to send multiple intent reports to the intent owner.
Each intent report represent the expected outcome for a possible solution strategy.
  Note, that the solution details are not shared with the intent owner, but rather the expected effects a solution would have on the intent fulfilment.
The Intent owner communicates its choice to the intent handler using a PREFERENCE operation.
  It is a sorted list of intent report IDs of the reports that it received in the JUDGE operation.
  The most preferred outcome corresponds to the report ID in first position in the list.
Intent Handler
Intent Owner
SET: <intent 1 (including best request)>
REPORT: <intent report 1>
REPORT: <intent report 2>
JUDGE: <intent report 3, … n>
…
PREFERENCE: <preferred reports>
REPORT: <intent report n+1>

## Slide 37: TWO LAYER INFORMATION MODEL
Intent API
Concerns of the API:
  Life-cycle manage intent
  Communication of intent and intent reports
  Feasibility check and negotiation
  Collaborative solution evaluation
Intent and intent reports are generic “string” data types from the perspective of the API data model.
  These strings have a complex internal structure
  Their details are modeled separately
  This makes the interface domain independent and at the same time domain adaptive.
Polymorphic interface design Changeable, configurable, adaptable, dynamic payloads, …
Intent Common and Extension models
Define the structure and content of the intent and intent report parameters
Concerns of the intent common model:
  Define domain and use case independent vocabulary and semantics for intent and intent reports
Concerns of intent extension models:
  Extent the intent common model with domain and use case specific vocabulary and semantics
A model federation/combination of the intent common and a particular choice of intent extension models defines what information can be carried on a particular embodiment of the interface.
The interface/API is always the same, but the federation that determines the content of the intent and intent report is adaptive

## Slide 38: LAYERED API INFORMATION MODEL
API Information Model
Layer 1: TMF921 The API defined by the OpenAPI project with intent and intent report being generic strings
INTENT
JSON:
External SDO
(Model
Federation)
Other
SDO
Formats
Layer 3: External SDO Model
OTHER MODEL
Intent Model Expression
JSON-LD:
Layer 2: Model Federation defining the content of intent and intent report objects
INTENT EXPRESSION
API payloads
are valid JSON
Notes: YANG: may even do without a YANG dictionary…..DeliveryExpectation…

## Slide 39: WHY DEFINING A POLYMORPHIC API
Cost saving by a single and re-useable API implementation.
  Avoid multiple domain specific interfaces that all do the same a little bit different
Dynamic online adaptation to changing capabilities: Intent Managers are intelligent functions that can change their capabilities dynamically
  Use of app-based management systems: Apps have their own life-cycle and this can lead to online addition and removal of capabilities
  Advanced AI techniques can learn and gain new capabilities
  Policies and AI models have separated life-cycles allowing extensions independent from the underlying management system.
The proposed model federation and two-level interface proposal allows controlled online adaptation of the interface information model following the intent manager’s capabilities.
No need to cycle through interface design when introducing new intent content.
Business Intent Manager
Service Intent Manager
Customer Portal
Intent managers specific to operation sub-domains
Intent API Level 1 information model: Same model everywhere
Level 2 information model: Model federation determined by intent manager capability

## Slide 40: MAPPING INTO REST/HTTP
Intent Semantics | Task | “CRUD” | HTTP | REST
SET | Create and send Intent | Create | POST | {api.root}/intent
RETRIEVE | Retrieve Intent | Read | GET | {api.root}/intent/{id}
SET | Modify Intent | Update | PUT | {api.root}/intent
REMOVE | Remove Intent | Delete | DELETE | {api.root}/intent/{id}
PROBE | Probe Intent | Create | POST | {api.root}/intent?probe=true
BEST | Ask for best Intent | Create | POST | {api.root}/intent?best=true
{api.root} = https://...../intentManagement/v4
Notes: Kevin? Stage 2 to Stage 3 Terminology….

## Slide 41
Expressing intent
Models for intent and intent reports

## Slide 42: MODELS DEFINED BY TMFORUM
Intent common model:
  Generic vocabulary and semantics that can be used as generic anchor for all intent modelling
  Formally defined in IG 1253 A
Generic intent extension models:
  Defines optional intent extension models
  They provide additional but still domain independent vocabulary
  Formally defined in IG 1253 B
Intent manager capability profile:
  Express the capabilities an intnet manager would publish
  Formally defined in IG 1253 D
Base ontologies:
  Conceptual vocabulary about intent management
  Formally defined in IG 1253 A and C
Intent Validity (iv) from TM FORUM IG 1253 B
Temporal Validity (itv) from TM FORUM
IG 1253 B
Intent Compliance Latency (icl) from TM FORUM
IG 1253 B
Proposal of Best Intent (pbi) from TM FORUM
IG 1253 B
Intent Management Ontology (imo) from TM FORUM IG 1253
Intent Interface Ontology (iio) from TM FORUM
IG 1253 C
Intent Manager Capability Profile (imcp) from TM FORUM
IG 1253 D
Intent Common Model (icm) from TM FORUM IG 1253 A
Intent Family Relation (ifr) from TM FORUM
IG 1253 B
Acceptance and Rejection Control(arc) from TM FORUM
IG 1253 B
...
...
...
...

## Slide 43: INTENT EXAMPLE 1. Prefix defintion
Defines substitute prefixes for used models
  Each model has its own namespace
  Increases readability
Model federation for this intent:
  Intent Management Ontology
  Intent Common Model
  Models defined by “someSDO” about Slice intent and CEM Metrics
  W3C Time Ontology
  The operator’s inventory, catalogue and intent repository
@prefix imo: <http://tio.labs.tmforum.org/tio/v1.0.0/IntentManagementOntology/> .
@prefix icm: <http://tio.labs.tmforum.org/tio/v1.0.0/IntentCommonModel/> .
@prefix sli: <http://www.someSDO.org/v1/SliceIntent/> .
@prefix met: <http://www.someSDO.org/v1/CEM_Meterics/> .
@prefix t: <http://www.w3.org/2006/time#> .
@prefix inv: <http://www.operator.org/Inventory/> .
@prefix cat: <http://www.operator.org/Catalog/> .
@prefix : <http://www.operator.org/IntentNamespace/> .
@prefix imo: <http://tio.labs.tmforum.org/tio/v1.0.0/IntentManagementOntology/> .
@prefix icm: <http://tio.labs.tmforum.org/tio/v1.0.0/IntentCommonModel/> .
@prefix sli: <http://www.someSDO.org/v1/SliceIntent/> .
@prefix met: <http://www.someSDO.org/v1/CEM_Meterics/> .
@prefix t: <http://www.w3.org/2006/time#> .
@prefix inv: <http://www.operator.org/Inventory/> .
@prefix cat: <http://www.operator.org/Catalog/> .
@prefix : <http://www.operator.org/IntentNamespace/> . :ExampleIntentXYZ a icm:Intent ; imo:intentOwner :IntentManagerXYZ ; icm:hasExpectation :Exp1_slice_delivery , :Exp2_slice_property , :Exp3_service_delivery , :Exp4_service_property , :Exp5_reporting .
:Exp1_slice_delivery a icm:DeliveryExpectation ;
icm:target _:sliceX ; icm:params :Par1_slice_description . :Par1_slice_description a icm:DeliveryParam ; icm:targetDescription cat:ExampleSlice . :Exp2_slice_property a icm:PropertyExpectation ; icm:target _:sliceX ; icm:params :Par2_slice_state . :Par2_slice_state a icm:PropertyParam ; sli:sliceState [ icm:oneOf sli:up, sli:available ] . :Exp3_service_delivery a icm:DeliveryExpectation ; icm:target _:serviceY ; icm:params :Par3_service_description . :Par3_service_description a icm:DeliveryParam ; icm:targetDescription cat:ExampleService . :Exp4_service_property a icm:PropertyExpectation ; icm:target _:serviceY ; icm:params :Par4_latency,
:Par5_throughput,
:Par6_availability . :Par4_latency a icm:PropertyParam ; met:latency [ icm:atMost "10 ms" ]. :Par5_throughput a icm:PropertyParam met:throughput [ icm:atLeast [ met:value 5 ; met:unit met:unitMBPS ] ] . :Par6_availability a icm:PropertyParam ; met:availability [ icm:greater [ met:value 99.9 ; met:unit met:percentage ] ] . :Exp5_reporting a icm:ReportingExpectation ; icm:target ex:ExampleIntentXYZ ; icm:params :Par7_interval, :Par8_event . :Par7_interval a icm:ReportingParam ; icm:reportingInterval [ a t:Duration ; t:numericDuration 10 ; t:temporalUnit t:unitMinute ] . :Par8_event a icm:ReportingParam ; icm:reportingEvent icm:ReportingIntervalExpired , icm:IntentRejected , icm:StateComplies , icm:StateDegrades , icm:HandlingEnded , icm:UpdateRejected , icm:UpdateFinished ] .

## Slide 44: INTENT EXAMPLE 2. Intent and its expectations
Creates intent with identifier “:ExampleIntentXYZ” It is an instance of class “icm:Intent” from the intent common model.
Using the prefix the full URI is: http://www.example.org/IntentNamespace/ExampleIntentXYZ
The intent originates from intent manager instance “:IntentManagerXYZ”
The intent has 5 expectations:
  2 Expectations about a slice
  2 Expectations about a service
  1 Expectation about the criteria for reporting
:ExampleIntentXYZ a icm:Intent ; imo:intentOwner :IntentManagerXYZ ; icm:hasExpectation :Exp1_slice_delivery , :Exp2_slice_property , :Exp3_service_delivery , :Exp4_service_property , :Exp5_reporting .
@prefix imo: <http://tio.labs.tmforum.org/tio/v1.0.0/IntentManagementOntology/> .
@prefix icm: <http://tio.labs.tmforum.org/tio/v1.0.0/IntentCommonModel/> .
@prefix sli: <http://www.someSDO.org/v1/SliceIntent/> .
@prefix met: <http://www.someSDO.org/v1/CEM_Meterics/> .
@prefix t: <http://www.w3.org/2006/time#> .
@prefix inv: <http://www.operator.org/Inventory/> .
@prefix cat: <http://www.operator.org/Catalog/> .
@prefix : <http://www.operator.org/IntentNamespace/> . :ExampleIntentXYZ a icm:Intent ; imo:intentOwner :IntentManagerXYZ ; icm:hasExpectation :Exp1_slice_delivery , :Exp2_slice_property , :Exp3_service_delivery , :Exp4_service_property , :Exp5_reporting .
:Exp1_slice_delivery a icm:DeliveryExpectation ;
icm:target _:sliceX ; icm:params :Par1_slice_description . :Par1_slice_description a icm:DeliveryParam ; icm:targetDescription cat:ExampleSlice . :Exp2_slice_property a icm:PropertyExpectation ; icm:target _:sliceX ; icm:params :Par2_slice_state . :Par2_slice_state a icm:PropertyParam ; sli:sliceState [ icm:oneOf sli:up, sli:available ] . :Exp3_service_delivery a icm:DeliveryExpectation ; icm:target _:serviceY ; icm:params :Par3_service_description . :Par3_service_description a icm:DeliveryParam ; icm:targetDescription cat:ExampleService . :Exp4_service_property a icm:PropertyExpectation ; icm:target _:serviceY ; icm:params :Par4_latency,
:Par5_throughput,
:Par6_availability . :Par4_latency a icm:PropertyParam ; met:latency [ icm:atMost "10 ms" ]. :Par5_throughput a icm:PropertyParam met:throughput [ icm:atLeast [ met:value 5 ; met:unit met:unitMBPS ] ] . :Par6_availability a icm:PropertyParam ; met:availability [ icm:greater [ met:value 99.9 ; met:unit met:percentage ] ] . :Exp5_reporting a icm:ReportingExpectation ; icm:target ex:ExampleIntentXYZ ; icm:params :Par7_interval, :Par8_event . :Par7_interval a icm:ReportingParam ; icm:reportingInterval [ a t:Duration ; t:numericDuration 10 ; t:temporalUnit t:unitMinute ] . :Par8_event a icm:ReportingParam ; icm:reportingEvent icm:ReportingIntervalExpired , icm:IntentRejected , icm:StateComplies , icm:StateDegrades , icm:HandlingEnded , icm:UpdateRejected , icm:UpdateFinished ] .

## Slide 45: INTENT EXAMPLE 3. Requiring a slice
A delivery expectation specifies that “something” need to be delivered and what this “something” is.
The “icm:target” property points at this “something”
  This is the instance that shall fulfill the expectation
  Here the variable (blank node) “_sliceX” is used as placeholder, because the intent handler needs to choose the actual instance
This delivery expectation has one parameter
  It specifies that the “something” shall be the “cat:ExampleService” as defined in the operator’s catalog.
:Exp1_slice_delivery a icm:DeliveryExpectation ;
icm:target _:sliceX ; icm:params :Par1_slice_description . :Par1_slice_description a icm:DeliveryParam ; icm:targetDescription cat:ExampleSlice .
@prefix imo: <http://tio.labs.tmforum.org/tio/v1.0.0/IntentManagementOntology/> .
@prefix icm: <http://tio.labs.tmforum.org/tio/v1.0.0/IntentCommonModel/> .
@prefix sli: <http://www.someSDO.org/v1/SliceIntent/> .
@prefix met: <http://www.someSDO.org/v1/CEM_Meterics/> .
@prefix t: <http://www.w3.org/2006/time#> .
@prefix inv: <http://www.operator.org/Inventory/> .
@prefix cat: <http://www.operator.org/Catalog/> .
@prefix : <http://www.operator.org/IntentNamespace/> . :ExampleIntentXYZ a icm:Intent ; imo:intentOwner :IntentManagerXYZ ; icm:hasExpectation :Exp1_slice_delivery , :Exp2_slice_property , :Exp3_service_delivery , :Exp4_service_property , :Exp5_reporting .
:Exp1_slice_delivery a icm:DeliveryExpectation ;
icm:target _:sliceX ; icm:params :Par1_slice_description . :Par1_slice_description a icm:DeliveryParam ; icm:targetDescription cat:ExampleSlice . :Exp2_slice_property a icm:PropertyExpectation ; icm:target _:sliceX ; icm:params :Par2_slice_state . :Par2_slice_state a icm:PropertyParam ; sli:sliceState [ icm:oneOf sli:up, sli:available ] . :Exp3_service_delivery a icm:DeliveryExpectation ; icm:target _:serviceY ; icm:params :Par3_service_description . :Par3_service_description a icm:DeliveryParam ; icm:targetDescription cat:ExampleService . :Exp4_service_property a icm:PropertyExpectation ; icm:target _:serviceY ; icm:params :Par4_latency,
:Par5_throughput,
:Par6_availability . :Par4_latency a icm:PropertyParam ; met:latency [ icm:atMost "10 ms" ]. :Par5_throughput a icm:PropertyParam met:throughput [ icm:atLeast [ met:value 5 ; met:unit met:unitMBPS ] ] . :Par6_availability a icm:PropertyParam ; met:availability [ icm:greater [ met:value 99.9 ; met:unit met:percentage ] ] . :Exp5_reporting a icm:ReportingExpectation ; icm:target ex:ExampleIntentXYZ ; icm:params :Par7_interval, :Par8_event . :Par7_interval a icm:ReportingParam ; icm:reportingInterval [ a t:Duration ; t:numericDuration 10 ; t:temporalUnit t:unitMinute ] . :Par8_event a icm:ReportingParam ; icm:reportingEvent icm:ReportingIntervalExpired , icm:IntentRejected , icm:StateComplies , icm:StateDegrades , icm:HandlingEnded , icm:UpdateRejected , icm:UpdateFinished ] .

## Slide 46: INTENT EXAMPLE 4. Required properties of the slice
A property expectation specifies non-functional requirements
  For example based on: KPI, metrics, system state, ...
The “icm:target” property defines the same target “_sliceX”.
  This means that here additional requirements about the same “something” are defined.
This property expectation has one parameter
  It specifies that the thate of the slice shall be either “sli:up” or “sli:available” for the expectation to be considered fulfilled
The slice intent model defined by someSDO is used here to specify the details
:Exp2_slice_property a icm:PropertyExpectation ; icm:target _:sliceX ; icm:params :Par2_slice_state . :Par2_slice_state a icm:PropertyParam ; sli:sliceState [ icm:oneOf sli:up, sli:available ] .
@prefix imo: <http://tio.labs.tmforum.org/tio/v1.0.0/IntentManagementOntology/> .
@prefix icm: <http://tio.labs.tmforum.org/tio/v1.0.0/IntentCommonModel/> .
@prefix sli: <http://www.someSDO.org/v1/SliceIntent/> .
@prefix met: <http://www.someSDO.org/v1/CEM_Meterics/> .
@prefix t: <http://www.w3.org/2006/time#> .
@prefix inv: <http://www.operator.org/Inventory/> .
@prefix cat: <http://www.operator.org/Catalog/> .
@prefix : <http://www.operator.org/IntentNamespace/> . :ExampleIntentXYZ a icm:Intent ; imo:intentOwner :IntentManagerXYZ ; icm:hasExpectation :Exp1_slice_delivery , :Exp2_slice_property , :Exp3_service_delivery , :Exp4_service_property , :Exp5_reporting .
:Exp1_slice_delivery a icm:DeliveryExpectation ;
icm:target _:sliceX ; icm:params :Par1_slice_description . :Par1_slice_description a icm:DeliveryParam ; icm:targetDescription cat:ExampleSlice . :Exp2_slice_property a icm:PropertyExpectation ; icm:target _:sliceX ; icm:params :Par2_slice_state . :Par2_slice_state a icm:PropertyParam ; sli:sliceState [ icm:oneOf sli:up, sli:available ] . :Exp3_service_delivery a icm:DeliveryExpectation ; icm:target _:serviceY ; icm:params :Par3_service_description . :Par3_service_description a icm:DeliveryParam ; icm:targetDescription cat:ExampleService . :Exp4_service_property a icm:PropertyExpectation ; icm:target _:serviceY ; icm:params :Par4_latency,
:Par5_throughput,
:Par6_availability . :Par4_latency a icm:PropertyParam ; met:latency [ icm:atMost "10 ms" ]. :Par5_throughput a icm:PropertyParam met:throughput [ icm:atLeast [ met:value 5 ; met:unit met:unitMBPS ] ] . :Par6_availability a icm:PropertyParam ; met:availability [ icm:greater [ met:value 99.9 ; met:unit met:percentage ] ] . :Exp5_reporting a icm:ReportingExpectation ; icm:target ex:ExampleIntentXYZ ; icm:params :Par7_interval, :Par8_event . :Par7_interval a icm:ReportingParam ; icm:reportingInterval [ a t:Duration ; t:numericDuration 10 ; t:temporalUnit t:unitMinute ] . :Par8_event a icm:ReportingParam ; icm:reportingEvent icm:ReportingIntervalExpired , icm:IntentRejected , icm:StateComplies , icm:StateDegrades , icm:HandlingEnded , icm:UpdateRejected , icm:UpdateFinished ] .

## Slide 47: INTENT EXAMPLE 5. Requiring a service
This is another delivery expectation
  Asking for a service to be delivered as well
  It has a target that is different from the previous expectations
Its parameter specifies that it shall be the service “cat:ExampleService” from the operator’s catalog
:Exp3_service_delivery a icm:DeliveryExpectation ; icm:target _:serviceY ; icm:params :Par3_service_description . :Par3_service_description a icm:DeliveryParam ; icm:targetDescription cat:ExampleService .
@prefix imo: <http://tio.labs.tmforum.org/tio/v1.0.0/IntentManagementOntology/> .
@prefix icm: <http://tio.labs.tmforum.org/tio/v1.0.0/IntentCommonModel/> .
@prefix sli: <http://www.someSDO.org/v1/SliceIntent/> .
@prefix met: <http://www.someSDO.org/v1/CEM_Meterics/> .
@prefix t: <http://www.w3.org/2006/time#> .
@prefix inv: <http://www.operator.org/Inventory/> .
@prefix cat: <http://www.operator.org/Catalog/> .
@prefix : <http://www.operator.org/IntentNamespace/> . :ExampleIntentXYZ a icm:Intent ; imo:intentOwner :IntentManagerXYZ ; icm:hasExpectation :Exp1_slice_delivery , :Exp2_slice_property , :Exp3_service_delivery , :Exp4_service_property , :Exp5_reporting .
:Exp1_slice_delivery a icm:DeliveryExpectation ;
icm:target _:sliceX ; icm:params :Par1_slice_description . :Par1_slice_description a icm:DeliveryParam ; icm:targetDescription cat:ExampleSlice . :Exp2_slice_property a icm:PropertyExpectation ; icm:target _:sliceX ; icm:params :Par2_slice_state . :Par2_slice_state a icm:PropertyParam ; sli:sliceState [ icm:oneOf sli:up, sli:available ] . :Exp3_service_delivery a icm:DeliveryExpectation ; icm:target _:serviceY ; icm:params :Par3_service_description . :Par3_service_description a icm:DeliveryParam ; icm:targetDescription cat:ExampleService . :Exp4_service_property a icm:PropertyExpectation ; icm:target _:serviceY ; icm:params :Par4_latency,
:Par5_throughput,
:Par6_availability . :Par4_latency a icm:PropertyParam ; met:latency [ icm:atMost "10 ms" ]. :Par5_throughput a icm:PropertyParam met:throughput [ icm:atLeast [ met:value 5 ; met:unit met:unitMBPS ] ] . :Par6_availability a icm:PropertyParam ; met:availability [ icm:greater [ met:value 99.9 ; met:unit met:percentage ] ] . :Exp5_reporting a icm:ReportingExpectation ; icm:target ex:ExampleIntentXYZ ; icm:params :Par7_interval, :Par8_event . :Par7_interval a icm:ReportingParam ; icm:reportingInterval [ a t:Duration ; t:numericDuration 10 ; t:temporalUnit t:unitMinute ] . :Par8_event a icm:ReportingParam ; icm:reportingEvent icm:ReportingIntervalExpired , icm:IntentRejected , icm:StateComplies , icm:StateDegrades , icm:HandlingEnded , icm:UpdateRejected , icm:UpdateFinished ] .

## Slide 48: INTENT EXAMPLE 6. Required properties of the service
A property expectation about the service has three parameters. They define
  that the latency shall be at most 10 ms,
  that the throughput shall be at least 5 Mbps,
  that the availability shall be greater than 99.9%
These parameters use vocabulary about metrics from the CEM metrics models defined by “someSDO”
@prefix imo: <http://tio.labs.tmforum.org/tio/v1.0.0/IntentManagementOntology/> .
@prefix icm: <http://tio.labs.tmforum.org/tio/v1.0.0/IntentCommonModel/> .
@prefix sli: <http://www.someSDO.org/v1/SliceIntent/> .
@prefix met: <http://www.someSDO.org/v1/CEM_Meterics/> .
@prefix t: <http://www.w3.org/2006/time#> .
@prefix inv: <http://www.operator.org/Inventory/> .
@prefix cat: <http://www.operator.org/Catalog/> .
@prefix : <http://www.operator.org/IntentNamespace/> . :ExampleIntentXYZ a icm:Intent ; imo:intentOwner :IntentManagerXYZ ; icm:hasExpectation :Exp1_slice_delivery , :Exp2_slice_property , :Exp3_service_delivery , :Exp4_service_property , :Exp5_reporting .
:Exp1_slice_delivery a icm:DeliveryExpectation ;
icm:target _:sliceX ; icm:params :Par1_slice_description . :Par1_slice_description a icm:DeliveryParam ; icm:targetDescription cat:ExampleSlice . :Exp2_slice_property a icm:PropertyExpectation ; icm:target _:sliceX ; icm:params :Par2_slice_state . :Par2_slice_state a icm:PropertyParam ; sli:sliceState [ icm:oneOf sli:up, sli:available ] . :Exp3_service_delivery a icm:DeliveryExpectation ; icm:target _:serviceY ; icm:params :Par3_service_description . :Par3_service_description a icm:DeliveryParam ; icm:targetDescription cat:ExampleService . :Exp4_service_property a icm:PropertyExpectation ; icm:target _:serviceY ; icm:params :Par4_latency,
:Par5_throughput,
:Par6_availability . :Par4_latency a icm:PropertyParam ; met:latency [ icm:atMost "10 ms" ]. :Par5_throughput a icm:PropertyParam met:throughput [ icm:atLeast [ met:value 5 ; met:unit met:unitMBPS ] ] . :Par6_availability a icm:PropertyParam ; met:availability [ icm:greater [ met:value 99.9 ; met:unit met:percentage ] ] . :Exp5_reporting a icm:ReportingExpectation ; icm:target ex:ExampleIntentXYZ ; icm:params :Par7_interval, :Par8_event . :Par7_interval a icm:ReportingParam ; icm:reportingInterval [ a t:Duration ; t:numericDuration 10 ; t:temporalUnit t:unitMinute ] . :Par8_event a icm:ReportingParam ; icm:reportingEvent icm:ReportingIntervalExpired , icm:IntentRejected , icm:StateComplies , icm:StateDegrades , icm:HandlingEnded , icm:UpdateRejected , icm:UpdateFinished ] .
:Exp4_service_property a icm:PropertyExpectation ; icm:target _:serviceY ; icm:params :Par4_latency,
:Par5_throughput,
:Par6_availability . :Par4_latency a icm:PropertyParam ; met:latency [ icm:atMost "10 ms" ]. :Par5_throughput a icm:PropertyParam met:throughput [ icm:atLeast [ met:value 5 ; met:unit met:unitMBPS ] ] . :Par6_availability a icm:PropertyParam ; met:availability [ icm:greater [ met:value 99.9 ; met:unit met:percentage ] ] .

## Slide 49: INTENT EXAMPLE 7. Reporting conditions
The reporting expectation defines the conditions to send a report
  Time based condition: every 10 minutes
  Event Based condition: when one of the specified events occurrs
The target of the reporting expectation is the intent itself.
:Exp5_reporting a icm:ReportingExpectation ; icm:target ex:ExampleIntentXYZ ; icm:params :Par7_interval, :Par8_event . :Par7_interval a icm:ReportingParam ; icm:reportingInterval [ a t:Duration ; t:numericDuration 10 ; t:temporalUnit t:unitMinute ] . :Par8_event a icm:ReportingParam ; icm:reportingEvent icm:ReportingIntervalExpired , icm:IntentRejected , icm:StateComplies , icm:StateDegrades , icm:HandlingEnded , icm:UpdateRejected , icm:UpdateFinished ] .
@prefix imo: <http://tio.labs.tmforum.org/tio/v1.0.0/IntentManagementOntology/> .
@prefix icm: <http://tio.labs.tmforum.org/tio/v1.0.0/IntentCommonModel/> .
@prefix sli: <http://www.someSDO.org/v1/SliceIntent/> .
@prefix met: <http://www.someSDO.org/v1/CEM_Meterics/> .
@prefix t: <http://www.w3.org/2006/time#> .
@prefix inv: <http://www.operator.org/Inventory/> .
@prefix cat: <http://www.operator.org/Catalog/> .
@prefix : <http://www.operator.org/IntentNamespace/> . :ExampleIntentXYZ a icm:Intent ; imo:intentOwner :IntentManagerXYZ ; icm:hasExpectation :Exp1_slice_delivery , :Exp2_slice_property , :Exp3_service_delivery , :Exp4_service_property , :Exp5_reporting .
:Exp1_slice_delivery a icm:DeliveryExpectation ;
icm:target _:sliceX ; icm:params :Par1_slice_description . :Par1_slice_description a icm:DeliveryParam ; icm:targetDescription cat:ExampleSlice . :Exp2_slice_property a icm:PropertyExpectation ; icm:target _:sliceX ; icm:params :Par2_slice_state . :Par2_slice_state a icm:PropertyParam ; sli:sliceState [ icm:oneOf sli:up, sli:available ] . :Exp3_service_delivery a icm:DeliveryExpectation ; icm:target _:serviceY ; icm:params :Par3_service_description . :Par3_service_description a icm:DeliveryParam ; icm:targetDescription cat:ExampleService . :Exp4_service_property a icm:PropertyExpectation ; icm:target _:serviceY ; icm:params :Par4_latency,
:Par5_throughput,
:Par6_availability . :Par4_latency a icm:PropertyParam ; met:latency [ icm:atMost "10 ms" ]. :Par5_throughput a icm:PropertyParam met:throughput [ icm:atLeast [ met:value 5 ; met:unit met:unitMBPS ] ] . :Par6_availability a icm:PropertyParam ; met:availability [ icm:greater [ met:value 99.9 ; met:unit met:percentage ] ] . :Exp5_reporting a icm:ReportingExpectation ; icm:target ex:ExampleIntentXYZ ; icm:params :Par7_interval, :Par8_event . :Par7_interval a icm:ReportingParam ; icm:reportingInterval [ a t:Duration ; t:numericDuration 10 ; t:temporalUnit t:unitMinute ] . :Par8_event a icm:ReportingParam ; icm:reportingEvent icm:ReportingIntervalExpired , icm:IntentRejected , icm:StateComplies , icm:StateDegrades , icm:HandlingEnded , icm:UpdateRejected , icm:UpdateFinished ] .

## Slide 50: INTENT REPORTING EXAMPLE 1. Prefix defintion
The models and their namespace prefixes used in this intent report:
  This report also uses the models used in the intent
  in addition it also uses RDFS and XML Schema
@prefix imo: <http://tio.labs.tmforum.org/tio/v1.0.0/IntentManagementOntology/> .
@prefix icm: <http://tio.labs.tmforum.org/tio/v1.0.0/IntentCommonModel/> . @prefix rdfs: <http://www.w3.org/2000/01/rdf-schema#> .
@prefix xsd: <http://www.w3.org/2001/XMLSchema#> .
@prefix sli: <http://www.someSDO.org/v1/SliceIntent/> .
@prefix met: <http://www.someSDO.org/v1/CEM_Meterics/> .
@prefix t: <http://www.w3.org/2006/time#> .
@prefix inv: <http://www.operator.org/Inventory/> .
@prefix cat: <http://www.operator.org/Catalog/> .
@prefix : <http://www.operator.org/IntentNamespace/> .
@prefix imo: <http://tio.labs.tmforum.org/tio/v1.0.0/IntentManagementOntology/> .
@prefix icm: <http://tio.labs.tmforum.org/tio/v1.0.0/IntentCommonModel/> . @prefix rdfs: <http://www.w3.org/2000/01/rdf-schema#> .
@prefix xsd: <http://www.w3.org/2001/XMLSchema#> .
@prefix sli: <http://www.someSDO.org/v1/SliceIntent/> .
@prefix met: <http://www.someSDO.org/v1/CEM_Meterics/> .
@prefix t: <http://www.w3.org/2006/time#> .
@prefix inv: <http://www.operator.org/Inventory/> .
@prefix cat: <http://www.operator.org/Catalog/> .
@prefix : <http://www.operator.org/IntentNamespace/> .
:ExampleIntentReportXYZ a icm:IntentReport ; rdfs:comment "example intent report" ; imo:intentOwner :IntentManagerXYZ ; imo:intentHandler :IntentManagerABC ; icm:reportsAbout :ExampleIntentXYZ ; icm:reportTimestamp [ t:inXSDDateTimeStamp "2022-12-01T10:30:10+10:00"^^xsd:dateTime ] ; icm:currentIntentHandlingState icm:StateCompliant ;
icm:currentIntentUpdateState icm:StateNoUpdate ; icm:reportNumber 42 ;
icm:hasExpectationReport
[ a icm:DeliveryExpectationReport ; icm:reportsAbout :Exp1_slice_delivery ;
icm:targetReport inv:slice000001 ; icm:paramsCompliant
[ a icm:DeliveryParam ; icm:reportsAbout :Par1_slice_description ; icm:targetDescription cat:ExampleSlice ] ; ] ,
[ a icm:PropertyExpectationReport ;
icm:reportsAbout :Exp2_slice_property ;
icm:targetReport inv:slice000001 ; icm:paramsCompliant
[ a icm:PropertyParam icm:reportsAbout :Par2_slice_state ; sli:sliceState sli:available ] ; ] ,
[ a icm:DeliveryExpectationReport ;
icm:reportsAbout :Exp3_service_delivery ;
icm:targetReport inv:service00010 ; icm:paramsCompliant
[ a icm:DeliveryParam ; icm:reportsAbout :Par3_service_description ; icm:targetDescription cat:ExampleService ] ; ] ,
[ a icm:PropertyExpectationReport ;
icm:reportsAbout :Exp4_service_property ; icm:targetReport inv:service00010 ; icm:paramsCompliant [ a icm:PropertyParam ; icm:reportsAbout :Par4_latency ; met:latency [ met:value 8 ;
met:unit met:unitS ] ] ,
[ a icm:PropertyParam ; icm:reportsAbout :Par5_throughput ; met:throughput [ met:value 15 ;
met:unit met:unitMBPS ] ] , [ a icm:PropertyParam ; icm:reportsAbout :Par6_availability ;
met:availability [ met:value 99.93 ;
met:unit met:percentage ] ] ,
] ,
[ a icm:ReportingExpectationReport ;
icm:reportsAbout :Exp5_reporting ;
icm:targetReport ex:ExampleIntentXYZ ; icm:paramsCompliant
[ icm:reportsAbout :Par7_interval ; icm:reportingIntervalLeft
[ a t:Duration ;
t:numericDuration 10 ;
t:temporalUnit t:unitMinute ] ; ] , [ icm:reportsAbout :Par8_event ; icm:reportingEvent icm:reportingIntervalExpired ] ;
] ; ] .

## Slide 51: INTENT REPORTING EXAMPLE 2. Report header
The object “:ExampleIntentReportXYZ” of class “icm:IntentReport” is created
Header with general information about this report:
  Owner of the intent and handler that is sending the report,
  Reference to the intent this report is about,
  Timestamp of report creation,
  Handling and update state,
  Sequence number of the intent.
:ExampleIntentReportXYZ a icm:IntentReport ; rdfs:comment "example intent report" ; imo:intentOwner :IntentManagerXYZ ; imo:intentHandler :IntentManagerABC ; icm:reportsAbout :ExampleIntentXYZ ; icm:reportTimestamp [ t:inXSDDateTimeStamp "2022-12-01T10:30:10+10:00"^^xsd:dateTime ] ; icm:currentIntentHandlingState icm:StateCompliant ;
icm:currentIntentUpdateState icm:StateNoUpdate ; icm:reportNumber 42 ;
@prefix imo: <http://tio.labs.tmforum.org/tio/v1.0.0/IntentManagementOntology/> .
@prefix icm: <http://tio.labs.tmforum.org/tio/v1.0.0/IntentCommonModel/> . @prefix rdfs: <http://www.w3.org/2000/01/rdf-schema#> .
@prefix xsd: <http://www.w3.org/2001/XMLSchema#> .
@prefix sli: <http://www.someSDO.org/v1/SliceIntent/> .
@prefix met: <http://www.someSDO.org/v1/CEM_Meterics/> .
@prefix t: <http://www.w3.org/2006/time#> .
@prefix inv: <http://www.operator.org/Inventory/> .
@prefix cat: <http://www.operator.org/Catalog/> .
@prefix : <http://www.operator.org/IntentNamespace/> .
:ExampleIntentReportXYZ a icm:IntentReport ; rdfs:comment "example intent report" ; imo:intentOwner :IntentManagerXYZ ; imo:intentHandler :IntentManagerABC ; icm:reportsAbout :ExampleIntentXYZ ; icm:reportTimestamp [ t:inXSDDateTimeStamp "2022-12-01T10:30:10+10:00"^^xsd:dateTime ] ; icm:currentIntentHandlingState icm:StateCompliant ;
icm:currentIntentUpdateState icm:StateNoUpdate ; icm:reportNumber 42 ;
icm:hasExpectationReport
[ a icm:DeliveryExpectationReport ; icm:reportsAbout :Exp1_slice_delivery ;
icm:targetReport inv:slice000001 ; icm:paramsCompliant
[ a icm:DeliveryParam ; icm:reportsAbout :Par1_slice_description ; icm:targetDescription cat:ExampleSlice ] ; ] ,
[ a icm:PropertyExpectationReport ;
icm:reportsAbout :Exp2_slice_property ;
icm:targetReport inv:slice000001 ; icm:paramsCompliant
[ a icm:PropertyParam icm:reportsAbout :Par2_slice_state ; sli:sliceState sli:available ] ; ] ,
[ a icm:DeliveryExpectationReport ;
icm:reportsAbout :Exp3_service_delivery ;
icm:targetReport inv:service00010 ; icm:paramsCompliant
[ a icm:DeliveryParam ; icm:reportsAbout :Par3_service_description ; icm:targetDescription cat:ExampleService ] ; ] ,
[ a icm:PropertyExpectationReport ;
icm:reportsAbout :Exp4_service_property ; icm:targetReport inv:service00010 ; icm:paramsCompliant [ a icm:PropertyParam ; icm:reportsAbout :Par4_latency ; met:latency [ met:value 8 ;
met:unit met:unitS ] ] ,
[ a icm:PropertyParam ; icm:reportsAbout :Par5_throughput ; met:throughput [ met:value 15 ;
met:unit met:unitMBPS ] ] , [ a icm:PropertyParam ; icm:reportsAbout :Par6_availability ;
met:availability [ met:value 99.93 ;
met:unit met:percentage ] ] ,
] ,
[ a icm:ReportingExpectationReport ;
icm:reportsAbout :Exp5_reporting ;
icm:targetReport ex:ExampleIntentXYZ ; icm:paramsCompliant
[ icm:reportsAbout :Par7_interval ; icm:reportingIntervalLeft
[ a t:Duration ;
t:numericDuration 10 ;
t:temporalUnit t:unitMinute ] ; ] , [ icm:reportsAbout :Par8_event ; icm:reportingEvent icm:reportingIntervalExpired ] ;
] ; ] .

## Slide 52: INTENT REPORTING EXAMPLE 3. Chosen slice instance
Report about the first expectation: Delivery of a slice
It contains a reference to the respective expectation in the intent
The “icm:targetReport” property is the equivalent to the “icm:target” in the intent:
  Instead of the blank node it points at the actual slice instance that was chosen
The report confirms the compliance to the required kind of slice
icm:hasExpectationReport
[ a icm:DeliveryExpectationReport ; icm:reportsAbout :Exp1_slice_delivery ;
icm:targetReport inv:slice000001 ; icm:paramsCompliant
[ a icm:DeliveryParam ; icm:reportsAbout :Par1_slice_description ; icm:targetDescription cat:ExampleSlice ] ; ] ,
@prefix imo: <http://tio.labs.tmforum.org/tio/v1.0.0/IntentManagementOntology/> .
@prefix icm: <http://tio.labs.tmforum.org/tio/v1.0.0/IntentCommonModel/> . @prefix rdfs: <http://www.w3.org/2000/01/rdf-schema#> .
@prefix xsd: <http://www.w3.org/2001/XMLSchema#> .
@prefix sli: <http://www.someSDO.org/v1/SliceIntent/> .
@prefix met: <http://www.someSDO.org/v1/CEM_Meterics/> .
@prefix t: <http://www.w3.org/2006/time#> .
@prefix inv: <http://www.operator.org/Inventory/> .
@prefix cat: <http://www.operator.org/Catalog/> .
@prefix : <http://www.operator.org/IntentNamespace/> .
:ExampleIntentReportXYZ a icm:IntentReport ; rdfs:comment "example intent report" ; imo:intentOwner :IntentManagerXYZ ; imo:intentHandler :IntentManagerABC ; icm:reportsAbout :ExampleIntentXYZ ; icm:reportTimestamp [ t:inXSDDateTimeStamp "2022-12-01T10:30:10+10:00"^^xsd:dateTime ] ; icm:currentIntentHandlingState icm:StateCompliant ;
icm:currentIntentUpdateState icm:StateNoUpdate ; icm:reportNumber 42 ;
icm:hasExpectationReport
[ a icm:DeliveryExpectationReport ; icm:reportsAbout :Exp1_slice_delivery ;
icm:targetReport inv:slice000001 ; icm:paramsCompliant
[ a icm:DeliveryParam ; icm:reportsAbout :Par1_slice_description ; icm:targetDescription cat:ExampleSlice ] ; ] ,
[ a icm:PropertyExpectationReport ;
icm:reportsAbout :Exp2_slice_property ;
icm:targetReport inv:slice000001 ; icm:paramsCompliant
[ a icm:PropertyParam icm:reportsAbout :Par2_slice_state ; sli:sliceState sli:available ] ; ] ,
[ a icm:DeliveryExpectationReport ;
icm:reportsAbout :Exp3_service_delivery ;
icm:targetReport inv:service00010 ; icm:paramsCompliant
[ a icm:DeliveryParam ; icm:reportsAbout :Par3_service_description ; icm:targetDescription cat:ExampleService ] ; ] ,
[ a icm:PropertyExpectationReport ;
icm:reportsAbout :Exp4_service_property ; icm:targetReport inv:service00010 ; icm:paramsCompliant [ a icm:PropertyParam ; icm:reportsAbout :Par4_latency ; met:latency [ met:value 8 ;
met:unit met:unitS ] ] ,
[ a icm:PropertyParam ; icm:reportsAbout :Par5_throughput ; met:throughput [ met:value 15 ;
met:unit met:unitMBPS ] ] , [ a icm:PropertyParam ; icm:reportsAbout :Par6_availability ;
met:availability [ met:value 99.93 ;
met:unit met:percentage ] ] ,
] ,
[ a icm:ReportingExpectationReport ;
icm:reportsAbout :Exp5_reporting ;
icm:targetReport ex:ExampleIntentXYZ ; icm:paramsCompliant
[ icm:reportsAbout :Par7_interval ; icm:reportingIntervalLeft
[ a t:Duration ;
t:numericDuration 10 ;
t:temporalUnit t:unitMinute ] ; ] , [ icm:reportsAbout :Par8_event ; icm:reportingEvent icm:reportingIntervalExpired ] ;
] ; ] .

## Slide 53: INTENT REPORTING EXAMPLE 4. Properties of the slice
The property expectation report confirms compliance of the required slice state
[ a icm:PropertyExpectationReport ;
icm:reportsAbout :Exp2_slice_property ;
icm:targetReport inv:slice000001 ; icm:paramsCompliant
[ a icm:PropertyParam icm:reportsAbout :Par2_slice_state ; sli:sliceState sli:available ] ; ] ,
@prefix imo: <http://tio.labs.tmforum.org/tio/v1.0.0/IntentManagementOntology/> .
@prefix icm: <http://tio.labs.tmforum.org/tio/v1.0.0/IntentCommonModel/> . @prefix rdfs: <http://www.w3.org/2000/01/rdf-schema#> .
@prefix xsd: <http://www.w3.org/2001/XMLSchema#> .
@prefix sli: <http://www.someSDO.org/v1/SliceIntent/> .
@prefix met: <http://www.someSDO.org/v1/CEM_Meterics/> .
@prefix t: <http://www.w3.org/2006/time#> .
@prefix inv: <http://www.operator.org/Inventory/> .
@prefix cat: <http://www.operator.org/Catalog/> .
@prefix : <http://www.operator.org/IntentNamespace/> .
:ExampleIntentReportXYZ a icm:IntentReport ; rdfs:comment "example intent report" ; imo:intentOwner :IntentManagerXYZ ; imo:intentHandler :IntentManagerABC ; icm:reportsAbout :ExampleIntentXYZ ; icm:reportTimestamp [ t:inXSDDateTimeStamp "2022-12-01T10:30:10+10:00"^^xsd:dateTime ] ; icm:currentIntentHandlingState icm:StateCompliant ;
icm:currentIntentUpdateState icm:StateNoUpdate ; icm:reportNumber 42 ;
icm:hasExpectationReport
[ a icm:DeliveryExpectationReport ; icm:reportsAbout :Exp1_slice_delivery ;
icm:targetReport inv:slice000001 ; icm:paramsCompliant
[ a icm:DeliveryParam ; icm:reportsAbout :Par1_slice_description ; icm:targetDescription cat:ExampleSlice ] ; ] ,
[ a icm:PropertyExpectationReport ;
icm:reportsAbout :Exp2_slice_property ;
icm:targetReport inv:slice000001 ; icm:paramsCompliant
[ a icm:PropertyParam icm:reportsAbout :Par2_slice_state ; sli:sliceState sli:available ] ; ] ,
[ a icm:DeliveryExpectationReport ;
icm:reportsAbout :Exp3_service_delivery ;
icm:targetReport inv:service00010 ; icm:paramsCompliant
[ a icm:DeliveryParam ; icm:reportsAbout :Par3_service_description ; icm:targetDescription cat:ExampleService ] ; ] ,
[ a icm:PropertyExpectationReport ;
icm:reportsAbout :Exp4_service_property ; icm:targetReport inv:service00010 ; icm:paramsCompliant [ a icm:PropertyParam ; icm:reportsAbout :Par4_latency ; met:latency [ met:value 8 ;
met:unit met:unitS ] ] ,
[ a icm:PropertyParam ; icm:reportsAbout :Par5_throughput ; met:throughput [ met:value 15 ;
met:unit met:unitMBPS ] ] , [ a icm:PropertyParam ; icm:reportsAbout :Par6_availability ;
met:availability [ met:value 99.93 ;
met:unit met:percentage ] ] ,
] ,
[ a icm:ReportingExpectationReport ;
icm:reportsAbout :Exp5_reporting ;
icm:targetReport ex:ExampleIntentXYZ ; icm:paramsCompliant
[ icm:reportsAbout :Par7_interval ; icm:reportingIntervalLeft
[ a t:Duration ;
t:numericDuration 10 ;
t:temporalUnit t:unitMinute ] ; ] , [ icm:reportsAbout :Par8_event ; icm:reportingEvent icm:reportingIntervalExpired ] ;
] ; ] .

## Slide 54: INTENT REPORTING EXAMPLE 5. Chosen service instance
Reporting about the required service:
  The “icm:targetReport” property points at the selected service instance
  The compliant params confirm the required kind of service.
[ a icm:DeliveryExpectationReport ;
icm:reportsAbout :Exp3_service_delivery ;
icm:targetReport inv:service00010 ; icm:paramsCompliant
[ a icm:DeliveryParam ; icm:reportsAbout :Par3_service_description ; icm:targetDescription cat:ExampleService ] ; ] ,
@prefix imo: <http://tio.labs.tmforum.org/tio/v1.0.0/IntentManagementOntology/> .
@prefix icm: <http://tio.labs.tmforum.org/tio/v1.0.0/IntentCommonModel/> . @prefix rdfs: <http://www.w3.org/2000/01/rdf-schema#> .
@prefix xsd: <http://www.w3.org/2001/XMLSchema#> .
@prefix sli: <http://www.someSDO.org/v1/SliceIntent/> .
@prefix met: <http://www.someSDO.org/v1/CEM_Meterics/> .
@prefix t: <http://www.w3.org/2006/time#> .
@prefix inv: <http://www.operator.org/Inventory/> .
@prefix cat: <http://www.operator.org/Catalog/> .
@prefix : <http://www.operator.org/IntentNamespace/> .
:ExampleIntentReportXYZ a icm:IntentReport ; rdfs:comment "example intent report" ; imo:intentOwner :IntentManagerXYZ ; imo:intentHandler :IntentManagerABC ; icm:reportsAbout :ExampleIntentXYZ ; icm:reportTimestamp [ t:inXSDDateTimeStamp "2022-12-01T10:30:10+10:00"^^xsd:dateTime ] ; icm:currentIntentHandlingState icm:StateCompliant ;
icm:currentIntentUpdateState icm:StateNoUpdate ; icm:reportNumber 42 ;
icm:hasExpectationReport
[ a icm:DeliveryExpectationReport ; icm:reportsAbout :Exp1_slice_delivery ;
icm:targetReport inv:slice000001 ; icm:paramsCompliant
[ a icm:DeliveryParam ; icm:reportsAbout :Par1_slice_description ; icm:targetDescription cat:ExampleSlice ] ; ] ,
[ a icm:PropertyExpectationReport ;
icm:reportsAbout :Exp2_slice_property ;
icm:targetReport inv:slice000001 ; icm:paramsCompliant
[ a icm:PropertyParam icm:reportsAbout :Par2_slice_state ; sli:sliceState sli:available ] ; ] ,
[ a icm:DeliveryExpectationReport ;
icm:reportsAbout :Exp3_service_delivery ;
icm:targetReport inv:service00010 ; icm:paramsCompliant
[ a icm:DeliveryParam ; icm:reportsAbout :Par3_service_description ; icm:targetDescription cat:ExampleService ] ; ] ,
[ a icm:PropertyExpectationReport ;
icm:reportsAbout :Exp4_service_property ; icm:targetReport inv:service00010 ; icm:paramsCompliant [ a icm:PropertyParam ; icm:reportsAbout :Par4_latency ; met:latency [ met:value 8 ;
met:unit met:unitS ] ] ,
[ a icm:PropertyParam ; icm:reportsAbout :Par5_throughput ; met:throughput [ met:value 15 ;
met:unit met:unitMBPS ] ] , [ a icm:PropertyParam ; icm:reportsAbout :Par6_availability ;
met:availability [ met:value 99.93 ;
met:unit met:percentage ] ] ,
] ,
[ a icm:ReportingExpectationReport ;
icm:reportsAbout :Exp5_reporting ;
icm:targetReport ex:ExampleIntentXYZ ; icm:paramsCompliant
[ icm:reportsAbout :Par7_interval ; icm:reportingIntervalLeft
[ a t:Duration ;
t:numericDuration 10 ;
t:temporalUnit t:unitMinute ] ; ] , [ icm:reportsAbout :Par8_event ; icm:reportingEvent icm:reportingIntervalExpired ] ;
] ; ] .

## Slide 55: INTENT REPORTING EXAMPLE 6. Properties of the service
Reporting about the properties of the service:
  All three required parameters are compliant
  For all of them the value at the time of reporting is stated
[ a icm:PropertyExpectationReport ;
icm:reportsAbout :Exp4_service_property ; icm:targetReport inv:service00010 ; icm:paramsCompliant [ a icm:PropertyParam ; icm:reportsAbout :Par4_latency ; met:latency [ met:value 8 ;
met:unit met:unitS ] ] ,
[ a icm:PropertyParam ; icm:reportsAbout :Par5_throughput ; met:throughput [ met:value 15 ;
met:unit met:unitMBPS ] ] , [ a icm:PropertyParam ; icm:reportsAbout :Par6_availability ;
met:availability [ met:value 99.93 ;
met:unit met:percentage ] ] ,
] ,
@prefix imo: <http://tio.labs.tmforum.org/tio/v1.0.0/IntentManagementOntology/> .
@prefix icm: <http://tio.labs.tmforum.org/tio/v1.0.0/IntentCommonModel/> . @prefix rdfs: <http://www.w3.org/2000/01/rdf-schema#> .
@prefix xsd: <http://www.w3.org/2001/XMLSchema#> .
@prefix sli: <http://www.someSDO.org/v1/SliceIntent/> .
@prefix met: <http://www.someSDO.org/v1/CEM_Meterics/> .
@prefix t: <http://www.w3.org/2006/time#> .
@prefix inv: <http://www.operator.org/Inventory/> .
@prefix cat: <http://www.operator.org/Catalog/> .
@prefix : <http://www.operator.org/IntentNamespace/> .
:ExampleIntentReportXYZ a icm:IntentReport ; rdfs:comment "example intent report" ; imo:intentOwner :IntentManagerXYZ ; imo:intentHandler :IntentManagerABC ; icm:reportsAbout :ExampleIntentXYZ ; icm:reportTimestamp [ t:inXSDDateTimeStamp "2022-12-01T10:30:10+10:00"^^xsd:dateTime ] ; icm:currentIntentHandlingState icm:StateCompliant ;
icm:currentIntentUpdateState icm:StateNoUpdate ; icm:reportNumber 42 ;
icm:hasExpectationReport
[ a icm:DeliveryExpectationReport ; icm:reportsAbout :Exp1_slice_delivery ;
icm:targetReport inv:slice000001 ; icm:paramsCompliant
[ a icm:DeliveryParam ; icm:reportsAbout :Par1_slice_description ; icm:targetDescription cat:ExampleSlice ] ; ] ,
[ a icm:PropertyExpectationReport ;
icm:reportsAbout :Exp2_slice_property ;
icm:targetReport inv:slice000001 ; icm:paramsCompliant
[ a icm:PropertyParam icm:reportsAbout :Par2_slice_state ; sli:sliceState sli:available ] ; ] ,
[ a icm:DeliveryExpectationReport ;
icm:reportsAbout :Exp3_service_delivery ;
icm:targetReport inv:service00010 ; icm:paramsCompliant
[ a icm:DeliveryParam ; icm:reportsAbout :Par3_service_description ; icm:targetDescription cat:ExampleService ] ; ] ,
[ a icm:PropertyExpectationReport ;
icm:reportsAbout :Exp4_service_property ; icm:targetReport inv:service00010 ; icm:paramsCompliant [ a icm:PropertyParam ; icm:reportsAbout :Par4_latency ; met:latency [ met:value 8 ;
met:unit met:unitS ] ] ,
[ a icm:PropertyParam ; icm:reportsAbout :Par5_throughput ; met:throughput [ met:value 15 ;
met:unit met:unitMBPS ] ] , [ a icm:PropertyParam ; icm:reportsAbout :Par6_availability ;
met:availability [ met:value 99.93 ;
met:unit met:percentage ] ] ,
] ,
[ a icm:ReportingExpectationReport ;
icm:reportsAbout :Exp5_reporting ;
icm:targetReport ex:ExampleIntentXYZ ; icm:paramsCompliant
[ icm:reportsAbout :Par7_interval ; icm:reportingIntervalLeft
[ a t:Duration ;
t:numericDuration 10 ;
t:temporalUnit t:unitMinute ] ; ] , [ icm:reportsAbout :Par8_event ; icm:reportingEvent icm:reportingIntervalExpired ] ;
] ; ] .

## Slide 56: INTENT REPORTING EXAMPLE 7. Chosen service instance
Reporting about the reporting conditions
  The time based reporting has 10 Minutes left until it is due.
  The reporting event, which has initiated this report.
[ a icm:ReportingExpectationReport ;
icm:reportsAbout :Exp5_reporting ;
icm:targetReport ex:ExampleIntentXYZ ; icm:paramsCompliant
[ icm:reportsAbout :Par7_interval ; icm:reportingIntervalLeft
[ a t:Duration ;
t:numericDuration 10 ;
t:temporalUnit t:unitMinute ] ; ] , [ icm:reportsAbout :Par8_event ; icm:reportingEvent icm:reportingIntervalExpired ] ;
] ; ] .
@prefix imo: <http://tio.labs.tmforum.org/tio/v1.0.0/IntentManagementOntology/> .
@prefix icm: <http://tio.labs.tmforum.org/tio/v1.0.0/IntentCommonModel/> . @prefix rdfs: <http://www.w3.org/2000/01/rdf-schema#> .
@prefix xsd: <http://www.w3.org/2001/XMLSchema#> .
@prefix sli: <http://www.someSDO.org/v1/SliceIntent/> .
@prefix met: <http://www.someSDO.org/v1/CEM_Meterics/> .
@prefix t: <http://www.w3.org/2006/time#> .
@prefix inv: <http://www.operator.org/Inventory/> .
@prefix cat: <http://www.operator.org/Catalog/> .
@prefix : <http://www.operator.org/IntentNamespace/> .
:ExampleIntentReportXYZ a icm:IntentReport ; rdfs:comment "example intent report" ; imo:intentOwner :IntentManagerXYZ ; imo:intentHandler :IntentManagerABC ; icm:reportsAbout :ExampleIntentXYZ ; icm:reportTimestamp [ t:inXSDDateTimeStamp "2022-12-01T10:30:10+10:00"^^xsd:dateTime ] ; icm:currentIntentHandlingState icm:StateCompliant ;
icm:currentIntentUpdateState icm:StateNoUpdate ; icm:reportNumber 42 ;
icm:hasExpectationReport
[ a icm:DeliveryExpectationReport ; icm:reportsAbout :Exp1_slice_delivery ;
icm:targetReport inv:slice000001 ; icm:paramsCompliant
[ a icm:DeliveryParam ; icm:reportsAbout :Par1_slice_description ; icm:targetDescription cat:ExampleSlice ] ; ] ,
[ a icm:PropertyExpectationReport ;
icm:reportsAbout :Exp2_slice_property ;
icm:targetReport inv:slice000001 ; icm:paramsCompliant
[ a icm:PropertyParam icm:reportsAbout :Par2_slice_state ; sli:sliceState sli:available ] ; ] ,
[ a icm:DeliveryExpectationReport ;
icm:reportsAbout :Exp3_service_delivery ;
icm:targetReport inv:service00010 ; icm:paramsCompliant
[ a icm:DeliveryParam ; icm:reportsAbout :Par3_service_description ; icm:targetDescription cat:ExampleService ] ; ] ,
[ a icm:PropertyExpectationReport ;
icm:reportsAbout :Exp4_service_property ; icm:targetReport inv:service00010 ; icm:paramsCompliant [ a icm:PropertyParam ; icm:reportsAbout :Par4_latency ; met:latency [ met:value 8 ;
met:unit met:unitS ] ] ,
[ a icm:PropertyParam ; icm:reportsAbout :Par5_throughput ; met:throughput [ met:value 15 ;
met:unit met:unitMBPS ] ] , [ a icm:PropertyParam ; icm:reportsAbout :Par6_availability ;
met:availability [ met:value 99.93 ;
met:unit met:percentage ] ] ,
] ,
[ a icm:ReportingExpectationReport ;
icm:reportsAbout :Exp5_reporting ;
icm:targetReport ex:ExampleIntentXYZ ; icm:paramsCompliant
[ icm:reportsAbout :Par7_interval ; icm:reportingIntervalLeft
[ a t:Duration ;
t:numericDuration 10 ;
t:temporalUnit t:unitMinute ] ; ] , [ icm:reportsAbout :Par8_event ; icm:reportingEvent icm:reportingIntervalExpired ] ;
] ; ] .

## Slide 57
Intent Manager Capability
Flexible domain specific support of intent content

## Slide 58: INTENT MANAGER CAPABILITY
Expresses the capability profile of this instance of an intent management function
  Allows intent management functions to discover each other and determine what communication is possible
  For example, an intent owner can discover a suitable intent handler
Intent Manager Scope: Name of the scope of responsibilities of this intent manager instance
Supported Interface Operations: Which optional procedures are supported
Supported Serialization Formats: Which formats for encoding intent and intent report on the interface are available
Supported Models: Which intent models are understood and can be used in the intent and intent report models.
Intent Manager Scope:
Slice Management
Supported Interface Operations:
PROBE, BEST, PROPOSAL
Supported notation formats: TURTLE, XML, JSON
Supported Models: https://tmforum.org/2020/07/intent/
https://tmforum.org/2021/03/intent/
http://sdo1.org/TelecomConcepts/
http://sdo1.org/metrics/version2/
http://sdo2.org/2019/SliceKPI/
http://sdo2.org/2021/03/SliceIntent/
http://sdo2.org/2019/SliceKPI/
http://sdo3.org/v1.1/SliceManagment/
http://sdo3.org/v2.0/SliceManagment/
http://sdo4.org/time/
http://sdo4.org/geography/
http://operator.com/Catalog/
http://operator.com/Inventory/
…

## Slide 59: INTENT MANAGER REGISTRATION AND DISCOVERY
Registration and Discovery scheme for online and dynamic discovery of intent managers
Allows a self adapting, self integrating and easily extensible autonomous network
Allows independent upgrade of intent handlers in separated software life-cycles.
  New capabilities can be used by other intent managers as soon as they are announced through registration
Separation of
  intent interface operations (Communication) and
  model support (Domain semantics).
Intent Manager
Registry
Intent Manager Capability Profiles
Intent Interface
Intent Manager
Intent Manager
Intent Manager Discovery
Intent Manager Registration

## Slide 60: SUMMARY
Intent is defined together with a generic architecture for intent-based operation
An intent API is defined as polymorphic API
  Online adaptive and applicable to all domains of intent handling
  No additional domain specific APIs need to be developed.
Intent modelling scheme is defined:
  Intent common model and intent extension models
  Model federation adapts the intent API to any domain-specific need
Intent Manager Capability
  Discovery of intent managers
  Domain scope of the intent manager
  Support of interface operations and models

## Slide 62
Cross Industry Collaboration
Compatible intent models and API across domains

## Slide 63: REQUIREMENTS AND RATIONALE (1)
Intent need to be expressible through a formal model
  Capture domain specific requirements.
Intent provides separation of concerns between autonomous systems
  Setting requirements without imperative instructions.
  Configuration of the system and actions to take are left to the autonomous (sub-)system that is addressed by intent.
  This strict separation of concerns gives intelligent implementations the needed high degree of freedom to optimize solutions.
The intent mechanism creates a control loop through reporting
  When intent is used to set requirements intent reports are needed to close loop and inform about success
Intent is a life-cylce managed information object
  Intent stays valid while the requirement is carries is needed
  A single intent sets the requirements for fulfillment as well as assurance

## Slide 64: REQUIREMENTS AND RATIONALE (2)
The API need to support dynamically changing Capabilities of the autonomous system
  Automation platforms are based on business logic being deployed and changed: Apps, ML models, policies, ...
  Therfore the capability of the autonomous domain changes online.
  The API need to allow the use of the new capabilities:
A polymorphic API is needed
  Changing the information model online to reflect the current capabilities of the autonomous domain
Online model federation is needed
  It creates the inforamtion model reflecting the currently supported capabilities of the autonomous domain
Intent manager capability need to be managed
  Online change and publication of capability profiles
  Discovery of capabilites by other intent managers

## Slide 65: REQUIREMENTS AND RATIONALE (3)
Avoid similar incompatible parallel work across SDOs
  An autonomous network contains multiple domains driven by intent
  Similarities in mechanisms for intent expression, life-cycle, negotiation, interface/API ...
  Differences in detailed requirements
  Usually, different projects and SDOs have responsibilities for a sub-set of domains
  Cost and lead-time saving is possible when sharing the overall work and not start from scratch in every project
A polymorphic API is needed
  It allows to include domain specific expressiveness in a compatible way
  It introduces a single implmentation for domain independednt
A model federation is needed
  It allows SDO projects to focus on domain specific additional vocabulary and semantics
SDO independence need to be preserved
  No or very lightweight central gouvernance structure. But basic agreement on common principles and artifacts.
  Full authoroty of SDOs over their domain and the respective models

## Slide 66: TASKS OF TM FORUM AUTONOMOUS NETWORKS PROJECT
Define and publish Intent Common Model:
  Generic vocabulary and semantics that can be used as generic anchor for all intent modelling
Define API:
  Intent API level 1 information model
  Intent API scheme for model federation of level 2 information model
  APIs for intent manager capability publication and discovery
Define generic intent extension models:
  Define optional intent extension models
  They provide additional but still domain independent vocabulary
Define other common concepts and models:
  Model and interface for intent manager capability
  Conceptual vocabulary about intent management
Intent Validity (iv) from TM FORUM IG 1253 B
Temporal Validity (itv) from TM FORUM
IG 1253 B
Intent Compliance Latency (icl) from TM FORUM
IG 1253 B
Proposal of Best Intent (pbi) from TM FORUM
IG 1253 B
Intent Management Ontology (imo) from TM FORUM IG 1253
Intent Interface Ontology (iio) from TM FORUM
IG 1253 C
Intent Manager Capability Profile (imcp) from TM FORUM
IG 1253 D
Intent Common Model (icm) from TM FORUM IG 1253 A
Intent Family Relation (ifr) from TM FORUM
IG 1253 B
Acceptance and Rejection Control(arc) from TM FORUM
IG 1253 B

## Slide 67: TASKS OF AN SDO OR DEVELOPMENT PROJECT
Every SDO is invited to create and publish their own intent extension models
  Full responsibility and authority about the content
  Build on Intent Common Model
Define an intent manager:
  Scope of responsibility: Name and document the scope
  Define the content of the model federation recommended for this intent manager: Intent common model version, set of intent common models
  Specify additional intent extension models as extension/specialization of existing models
Use the common intent API:
  No need to define the API from scratch for every reference point
  Level 1 information model is generic
  Level 2 information model is the proposed federation of models
No need for central governance, but
  Intent common model can be influenced through cross SDO liaison mechanism or through membership in
Intent Manager
Intent Manager
Customer Portal
Intent API Level 1 information model: Same model everywhere
Level 2 information model: Model federation determined by intent manager capability
Defined by SDO project
Intent Manager
Intent Manager