3GPP TR ab.cde V0.9.0 (2008-06)

Technical Report

3rd Generation Partnership Project;

Technical Specification Group <TSG name>;

Overview of 3GPP Release 7;

Summary of all Release 7 Features

(Release 7)

The present document has been developed within the 3rd Generation Partnership Project (3GPP TM) and may be further elaborated for the purposes of 3GPP.
The present document has not been subject to any approval process by the 3GPP Organizational Partners and shall not be implemented.	
This Specification is provided for future development work within 3GPP only. The Organizational Partners accept no liability for any use of this Specification.
Specifications and reports for implementation of the 3GPP TM system should be obtained via the 3GPP Organizational Partners' Publications Offices.

Keywords

<keyword[, keyword]>

3GPP

Postal address

3GPP support office address

650 Route des Lucioles - Sophia Antipolis

Valbonne - FRANCE

Tel.: +33 4 92 94 42 00 Fax: +33 4 93 65 47 16

Internet

http://www.3gpp.org

Copyright Notification

No part may be reproduced except as authorized by written permission.
The copyright and the foregoing restriction extend to reproduction in all media.

© 2008, 3GPP Organizational Partners (ARIB, ATIS, CCSA, ETSI, TTA, TTC).

All rights reserved.

Contents

Foreword	6

Introduction	6

1	Scope	7

2	References	7

2.1	Specifications	7

2.2	Tdocs	7

2.3	Work Plan, Work Items and Study Items	8

2.4	Change Request database	8

3	Abbreviations	8

4	New Features applicable to UMTS and GSM	9

4.1	IMS-related new Features	9

4.1.1	Identification of Communication Services in IMS	9

4.1.2	Supporting Globally Routable User Agent URIs in IMS	9

4.1.3	IMS Support of Conferencing and Messaging Group Management	10

4.1.4	Multimedia Telephony Service for IMS (MTSI)  UID_7038 (R5 completion 0%)	11

4.1.4.1	Multimedia Telephony Service for IMS (MTSI) - UE Conformance Testing  UID_350147	12

4.1.5	Performance Characterization of VoIMS over HSDPA\EUL channels	12

4.2	Location-related new Features	13

4.2.1	Location Services enhancements (LCS3)  UID_32079	13

4.2.1.2	Inclusion of Uplink TDOA UE positioning method in the UTRAN specifications  UID_20012	15

4.2.1.3	UE positioning - Velocity  UID_20042	16

4.2.2	Advanced Global Navigation Satellite System (A-GNSS) concept (LCS3-AGNSS)  UID_31051	16

4.2.2.1	Towards A-GNSS Concept  UID_50548	17

4.2.2.2	Global Navigation Satellite System (GNSS) in UTRAN  UID_20050	18

4.2.3	A-GPS Minimum Performance (GAGR)  UID_50581	18

4.3	Combinational Services	19

4.4	System enhancements for fixed broadband access to IMS	20

4.5	Access Class Barring and Overload Protection	22

4.6	USSD message delivery and transfer to USIM	22

4.7	Protocol-related new Features	23

4.7.1	IMS Stage 3 IETF Protocol alignment	23

4.7.2	DIAMETER on the GGSN Gi interface	24

4.7.3	DIAMETER on the PDG Wi inteface	25

4.8	Mp (MRFC - MRFP) interface	25

4.9	Support of SMS over generic 3GPP IP access	26

4.10	Dynamic and Interactive Multimedia Scenes (DIMS)	27

4.11	Security-related new Features	28

4.11.1	Liberty Alliance and 3GPP Security Interworking	28

4.11.2	Trust Requirements for Open Platforms in 3GPP	29

4.11.3	Development of UEA2 and UIA2	30

4.11.4	Lawful Interception in the 3GPP Rel-7 architecture	31

4.11.5	Access Security Enhancements	32

4.12	One Tunnel solution for Optimisation of Packet Data Traffic	32

4.13	End-to-End Multimedia Services Performance Metrics (E2EMSPM)  UID_34036	33

4.14	ISIM API for Java Card	35

4.15	Network Composition	35

4.16	Key establishment between a UICC and a terminal	36

4.17	Selective Disabling of UE Capabilities	37

4.18	Personal Network Management  (PNM)	38

4.19	CSI Terminating Session handling	39

4.20	Interoperability between VGCS/VBS and A/Gb flexibility	39

5	UTRAN Features	40

5.1	Multiple Input Multiple Output antennas (MIMO)  UID_2468	40

5.2	Rel-7 Improvements of the Radio Interface (RInImp)  UID_20028	41

5.2.1	Extended UMTS 1.7/2.1 GHz  UID_20060	41

5.2.2	UMTS 2.6 GHz 7.68 Mcps TDD  UID_20067	41

5.2.3	UMTS 2.6 GHz  UID_20021	41

5.2.4	UMTS 2.6 GHz TDD  UID_20025	42

5.2.5	UMTS 900 MHz  UID_20027	42

5.2.6	UMTS 1700 MHz  UID_20043	43

5.2.7	UE Antenna Performance Evaluation Method and Requirements  UID_20024	43

5.2.8	Improved Performance Requirements for HSDPA UE based on Rx Diversity (Type 1) & LMMSE equalizer (Type 2)  UID_20045	43

5.2.9	Additional minimum UE performance requirement for non-HSDPA channels based on Type 1 enhanced receiver (Rx Diversity)  UID_20062	43

5.3	RAN improvements (RANimp)  UID_20029	45

5.3.1	Optimization of channelization code utilization for 1.28 Mcps TDD  UID_20026	45

5.3.2	Delay optimisation for procedures applicable to CS and PS Connections  UID_20031	45

5.3.3	UE Performance Requirements for MBMS (TDD)  UID_20033	46

5.3.4	Continuous connectivity for packet data users  UID_20046	47

5.3.5	Extended WCDMA Cell Range  UID_7030	48

5.3.6	7.68 Mcps TDD Enhanced Uplink  UID_7031	48

5.3.7	Enhanced CELL_FACH State in FDD  UID_330009	49

5.3.8	64QAM for HSDPA (FDD)  UID_340038	50

5.3.9	Improved L2 support for high data rates  UID_340039	51

5.3.10	Introduction of 16QAM in HSUPA (FDD)  UID_340040	52

5.3.11	Interface to control Tower Mounted Amplifiers (TMAs)  UID_20066	52

5.4	7.68 Mcps TDD option  UID_20014	53

5.5	3.84 Mcps TDD Enhanced Uplink  UID_20035	54

5.6	1.28 Mcps TDD Enhanced Uplink  UID_20055	55

5.6.1	1.28Mcps TDD Enhanced Uplink - UE Conformance Testing  UID_350146 (0% completion)	56

7	Improvements of UMTS and GSM	57

7.1	Evolution of Policy Control and Charging	57

7.2	CAMEL Trunk Triggers	58

7.3	IWLAN-related improvements	59

7.3.1	WLAN-UMTS Interworking Phase 2	59

7.3.2	WLAN Interworking – Private Network access from WLAN 3GPP IP Access	60

7.3.3	Enhancements to support QoS provisioning over 3GPP/WLAN Interworking	61

7.4	Voice call continuity between CS and IMS (incl. I-WLAN)	61

7.5	Operations, Administration, Maintenance & Provisioning (OAM7)  UID_35041	63

7.16	Charging Management small Enhancements (CH7)  UID_320007	70

7.6	Open Service Access (OSA7) UID_31071	70

7.7	Rel7 Security enhancements	72

7.8	Video Codec Performance Requirements	73

7.9	3G-324M Video Telephony Call Setup Times Improvements	74

7.10	VoIMS bearer related enhancements  UID_32099	75

7.10.1	Improved support of IMS Realtime Services using HSDPA/HSUPA  UID_32099	75

7.11	MBMS-related enhancements	76

7.11.1	MBMS Enhancements	76

7.11.2	MBMS FDD Physical layer Enhancements  UID_340042	77

7.11.3	MBMS TDD Physical layer Enhancements  UID_340043	78

7.11.4	MBMS LCR TDD Physical layer Enhancements  UID_350022	79

7.11.5	MBMS User Service Extensions	80

7.12	Optimizations for Multimedia Telephony over IMS	81

7.13	Network selection enhancements (NSP-CR)  UID_7041	82

7.13.1	Network selection enhancements (NSP) - UE Conformance Testing  UID_25048	83

7.14	Packet Switched Streaming Enhancements	83

7.15	Enhanced USIM Phonebook	84

9	GERAN improvements	85

9.1	Enhancements of VGCS for public authority officials (EVGCS)  UID_11045	85

9.2	Improvements of VGCS for parallel use of services (IVGCS)  UID_11055	86

6	GERAN Features	86

6.1	MS Antenna Performance Evaluation Method and Requirements (APEMR)  UID_50118	86

6.2	Lower 700 MHz Inclusion in the GERAN specifications (GSM710)  UID_50119	87

6.3	Support of Conversational Services in A/Gb mode via the PS domain (SCSAGB)  UID_50564	87

6.4	Addition of new frequency band to GSM (TGSM810)  UID_50565	88

6.5	Handover of dedicated and shared resources while in dual transfer mode (HODSRDTM)  UID_50567	88

6.13	Mobile Station Receive Diversity (DARP Phase II) (MSRD2)  UID_50569	89

6.6	Downlink Dual Carrier (GDCDL)  UID_50579	89

6.7	Support of SIGTRAN in GERAN (GSIGT)  UID_50580	90

6.11	Latency Reductions (LATRED)  UID_50582	91

6.8	PS Handover between GERAN/UTRAN mode and GAN Mode (GUGAN)  UID_52147	91

6.9	Higher Uplink performance for GERAN Evolution (HUGE)  UID_50584	92

6.10	REduced symbol Duration, Higher Order modulation and Turbo coding for downlink (REDHOT)  UID_50121	93

10	Feasibility Studies	94

10.1	Study on Multimedia Telephony Capabilities for IMS  UID_31082	94

10.2	Study on Behaviour of Multi system UEs  UID_31050	96

10.3	 Study on IMS with real time services deployment  UID_31054	97

10.4	 Study on Videotelephony teleservice  UID_31075	98

10.5	 Study on Network Selection Principles  UID_31073	99

10.6	Study on Multimedia Priority Service  UID_31041	101

10.7	 Study on Transferring of emergency Call data  UID_31083	102

10.8	 Study on Customised Alerting Tone (CAT) Requirements  UID_7026	103

10.9	 Study on Enhancement of E2E QoS  UID_32073	104

10.10	Study on Terminating Session handling  UID_32117	105

10.11	 Study on Bandwidth Saving at Nb Interface with IP transport  UID_7034	105

10.12	 Study on Routeing of MT-SMs via the HPLMN  UID_14019	106

10.13	 Study on the TCAPsec Gateway concept  UID_7025	107

10.14	 Study on using M2PA in 3GPP network  UID_7050	108

10.15	 Study on Support of (G)MSC-S - (G)MSC-S Nc Interface based on the SIP-I protocol  UID_320018	109

10.16	Study on SOAP/HTTP IRP Solution Sets  UID_35066	110

10.17	Study on Itf-N Implementation Conformance Statement (ICS) template  UID_35067	110

10.18	Study on IRP Information Mode  UID_35068	111

10.19	Study on Evolved UTRA and UTRAN  UID_20023	111

10.20	Study on Performance Evaluation of the UE behaviour in high speed trains with speeds up to 350 kmph  UID_20034	113

10.21	Study on UTRA Tower Mounted Amplifier (FDD)  UID_20041	113

10.22	Study on Continuous connectivity for packet data users  UID_20044	115

10.23	Study on Improvement of Multimedia Broadcast Multicast Service (MBMS) in UTRAN  UID_20051	115

10.24	Study on Performance Improvements in Small Cells using HSDPA/EDCH  UID_20052	116

10.25	Study on Further Improved Performance Requirements for UMTS/HSDPA UE (FDD)  UID_20053	116

10.26	Study on Scope of future FDD HSPA Evolution  UID_20065	117

10.27	Study on Dynamically reconfiguring a FDD UE receiver to reduce power consumption when desired Quality of Service is met  UID_330013	118

10.28	Study on GAN Enhancements (EGAN)  UID_50120	119

10.29	Study on Future GERAN Evolution (FGE)  UID_50568	119

11	Deleted items	123

Annex A:	Change history	125

# Foreword

# Introduction

This document has been produced by the ETSI MCC.

# 1	Scope

The present document contains a high-level description of the 3GPP Release 7 Features.

A Feature is defined as new or substantially enhanced functionality which represents added value to the existing system. A Feature normally embodies an improved service to the customer and / or increased revenue generation potential to the supplier.

Features are as independent as possible from each other, and relationships between features (if any) are clarified here.

In some cases, a feature does not correspond to a single functionality but consists in a grouping of different independent items impacting the same parts of the system (e.g. "RAN improvements"). This grouping is performed to limit the total number of Features per Release.

For each Feature (or independent item), references are given to guide the reader on how to deepen the subject: the Work Item Description (WID) as well as the list of impacted specifications is provided at the beginning of each clause describing the feature. The impact of a given feature on a particular specification is described in the Change Request (CR) list, which can be found at the end of the respective specification, or alternatively in the CR database, which contains the full list of CRs for all 3GPP specifications.

Chapter 2 of the present document contains global references, and provides links towards the 3GPP Specifications, the meeting contributions, the Work Plan, the Work Item Descriptions (WIDs) and the CR database.

The main body of the present document is starting with clause 4 and is structured according to the Features in the 3GPP Release 7 Work Plan.

# 2	References

[1]	3GPP TR 21.905: "Vocabulary for 3GPP Specifications".

## 2.1	Specifications

Global information on the Specifications (also called “specs”) can be found at:

http://www.3gpp.org/specs/specs.htm

The latest versions of all 3GPP specifications, containing the most recent corrections and additions, are available at:

http://www.3gpp.org/ftp/Specs/latest/

For specific purposes, older versions might be needed. These versions are available at:

http://www.3gpp.org/ftp/Specs/Archive/

where the specifications are sorted by series and then by folders containing all the available versions of a given spec (one folder per spec), for all Releases.

## 2.2	Tdocs

The Temporary Documents (tdocs) are mainly the original papers written by the 3GPP Members, and are the inputs for elaborating the specs. They are available (sorted by 3GPP technical groups (Technical Specification Groups (TSGs) and Working Groups (WGs)) at:

http://www.3gpp.org/ftp/

starting with 'tsg....'.

## 2.3	Work Plan, Work Items and Study Items

Work Item Description (“WID”) (also called WI Description) and Study Item (also called "Feasibility Studies") are forms which initial version provides the target to be reached before starting the technical work. Potential subsequent versions narrow the target and foreseen completion date according the actual progress. They are stored in:

http://www.3gpp.org/ftp/Information/WI_sheets/

The 3GPP Work Plan is a living document, updated roughly each month, which contains the full list of Work Items and Study Items, as well as summary information for each WI, as: the WG in charge of it, its starting date and (foreseen or actual) completion date, the actual progress, etc. The Work Plan is available at:

http://www.3gpp.org/ftp/Information/WORK_PLAN/

## 2.4	Change Request database

A specification is originally drafted and maintained by a rapporteur, who compiles the contents from discussions in the WGs and TSGs. When it is considered to be 80% complete, it is brought under a so-called "change control" process. After this, changes to the specification can only be made using Change Requests that are usually agreed by consensus in the Working Group responsible for the specification, and then formally approved by the relevant Technical Specification Group.

The Change Request database contains all available information on Change Requests, including a Work Item code, a Change Request number that is unique within the specification (different versions are possible, but only one can ever be approved), the status of each Change Request and references to relevant temporary document numbers and meetings. This database is available in:

http://www.3gpp.org/ftp/Information/Databases/Change_Request/

Further information on CR is available at:

http://www.3gpp.org/specs/CR.htm

# 3	Abbreviations

For the purposes of the present document, the abbreviations given in TR 21.905 [x] and the following apply. An abbreviation defined in the present document takes precedence over the definition of the same abbreviation, if any, in TR 21.905 [1].

CS	Circuit Switched

IMS	IP Multimedia Subsystem

ISDN	Integrated Services Digital Network

PLMN	Public Land Mobile Network

RAB	Radio Access Bearer

RLC	Radio Link Control

RTP	Real Time Protocol

SIP	Session Initiated Protocol (IETF)

# 4	New Features applicable to UMTS and GSM

## 4.1	IMS-related new Features

### 4.1.1	Identification of Communication Services in IMS

To be written by Maurice

Acronym:		ServID

UID_732097

Main Responsibility:	S2

References for "Identification of Communication Services in IMS "

| Document | Title/Contents |
| --- | --- |
| WID(s) |
| GP-022566 | WID on XXX |
| Impacted Specifications |
| TS 24.008 | Example |
| New Dedicated Specifications/Reports |
| TS 22.146 | Example |

SA5 Charging aspects of ServID (ServID-CH) are implemented as CRs in TSs 32.260, 32.298, 32.299.

| 235 | 732097 | Identification of Communication Services in IMS | 1 | S2 | ServID | 22.228, 23.228, 23.203, 32.260, 32.298, 32.299 | SP-050392 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 236 | 32106 | TR for ICS | 2 | S2 |  | 23.816 |  |
| 237 | 32107 | Stage 2 of ICS | 2 | S2 |  |  |  |
| 238 | 320010 | Stage 3 of ICS | 2 | C1 |  |  | CP-060259 |

### 4.1.2	Supporting Globally Routable User Agent URIs in IMS

To be written by Maurice

Acronym:		GRUU

UID_32116

Main Responsibility:	S2

References for "Supporting Globally Routable User Agent URIs in IMS "

| Document | Title/Contents |
| --- | --- |
| WID(s) |
| GP-022566 | WID on XXX |
| Impacted Specifications |
| TS 24.008 | Example |
| New Dedicated Specifications/Reports |
| TS 22.146 | Example |

Your text: what does it offer? (Stage 1 summary) How does it impact the network? (Stages 2 and 3 summary). PLEASE DON’T JUST COPY-PASTE THE TEXT FROM THE WID BUT CHECK WHAT WAS ACTUALLY DONE!

Extract from the Work Plan (info for the writer only, to be deleted when providing actual text):

| 247 | 32116 | Supporting Globally Routable User Agent URIs in IMS | 1 | S2 | GRUU | 23.8XX, 22.228, 23.228, 23.218, 24.229 | Sp-050633 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 248 | 7009 | TR on GRUU | 2 | S2 |  |  |  |
| 249 | 7010 | Stage 2 of GRUU | 2 | S2 |  |  |  |
| 250 | 320011 | Stage 3 of GRUU | 2 | C1 |  |  | CP-060358 |

### 4.1.3	IMS Support of Conferencing and Messaging Group Management

Written by A. Brekalo

Acronym:		IMSconf

UID_11065

Main Responsibility:	C1

References for “IMS Support of Conferencing and Messaging Group Management”

| Document | Title/Contents |
| --- | --- |
| WID(s) |
| CP-070120 | IMS Support of Conferencing |
| Impacted Specifications |
| TS 24.147 | Conferencing using the IM CN subsystem; Stage 3 |
| TS 24.229 | SIP and SDP stage 3 |
| New Dedicated Specifications/Reports |

In Release 5, the IMS was defined to support IP Multimedia services. The feature set in Release 5 provides a basis for IP Multimedia support. During release 6, additional applications were developed, but due to IETF dependencies, such applications could not be completed in release 6.

The objectives of this work item were to progress Stage 3 work on postponed Release 6 features for IP multimedia applications in accordance with existing release 6 stage 1 requirements and for which the related IETF dependencies have been completed within the release 7 timeframe i.e:

- Floor control for IM CN subsystem conferencing

  - This item is to provide any additional specification that may be necessary in support of floor control, and the appropriate SDP and conference policy control to support provision of a floor control server. 
Note: IETF has finished a floor control specification (named "BFCP"), which can be adopted in Release 7 for IMS conferencing.

- Extensions to conferencing related SIP procedures.

  - This item provides any additional specification that may be necessary to enhance and extend SIP procedures that are related to IM CN subsystem conferencing to fulfil existing release 6 stage 1 requirements.

### 4.1.4	Multimedia Telephony Service for IMS (MTSI)  UID_7038 (R5 completion 0%)

Responsibility:	S1,C1,S4

References

| Document | Title/Contents |
| --- | --- |
| WID(s) |
| SP-060224 | S1 WID on Multimedia Telephony Service for IMS |
| CP-060257 | C1 WID on IMS Multimedia Telephony Service, Stage 3 |
| SP-060225 | S4 WID on IMS Multimedia Telephony; media handling and interaction |
| Impacted Specifications |
| TS 24.229 | Generic enhancements and extensions due to Multimedia Telephony |
| TS 29.163 | Generic enhancements and extensions due to Multimedia Telephony |
| New Dedicated Specifications/Reports |
| TS 22.173 | IP Multimedia Core Network Subsystem (IMS) Multimedia Telephony Service and supplementary services; Stage 1 |
| TS 24.173 | IMS Multimedia telephony communication service and supplementary services |
| TS 26.114 | IMS Multimedia Telephony; Media handling and interaction |
| TS 26.235 | Packet switched conversational multimedia applications; Default codecs |
| TS 26.236 | Packet switched conversational multimedia applications; Transport protocols |
| TS 26.914 | Multimedia telephony over IP Multimedia Subsystem (IMS); Optimization opportunities |

3GPP and TISPAN defined an IMS based Multimedia Telephony service, which is an evolution of the CS based Telephony service provided by traditional ISDNs and PSTNs. The service defined by 3GPP is needed for wireless access to IMS, in order to be able to define services to the end-users, and to support interoperability in multi-vendor and multi-operator environment and to provide the user with the same experience across the different IP based accesses and domains.

One interesting aspect of IMS Multimedia Telephony is that it is possible to have a user experience that has a larger gamut (e.g. for voice; delay and jitter) than for a comparable CS conversational service. It is desirable to specify media behaviour in a predictable manner, so that operators are able to differentiate their service offerings.

This means, among other things, that the services from day one must be well specified and interoperable. In addition, a standardized consistent terminal behaviour is important for the operator to enable tuning of the network with full control over the end users’ experience.  This also means a well specified transmitter and receiver behaviour.

SA1 decided to reuse where applicable Supplementary Service (SS) definitions as specified by ETSI TISPAN. SA1 has, apart from endorsing the relevant TISPAN SSs, also defined any potential additional 3GPP-only SSs and capture those in the same 3GPP specification.

SA4 has specified a basic PS service supporting conversational speech, video and text, with the goal of making these basic services consistent, interoperable and of predictable performance. It was necessary to specify the media handling and behaviour (delay jitter handling, packet loss handling and concealment, interoperability with CS/UTRAN/GERAN, inter-media synchronization, echo and noise cancelling, rate adaptation, media related end-2-end signalling etc). The work focussed on person-to-person calls using RTP-transported media. Add/drop of media during a call were specified.

Written in a forward-compatible way TS 26.114 allows additions of media components and functionality in later Releases.  Interworking with 3GPP-specified telephony services are covered (CS speech, 3G-324M and video telephony) as well as with traditional POTS, and emerging TISPAN network (se also TR 22.973).

TS 26.114 addresses the areas of optimization opportunities identified in TR 26.914.

The optimizations regarded mainly media transport and signalling. Issues on SIP signalling, registration to the network and/or to IMS at power-on or at other occurrences were not included.

TS 26.114 specifies a client for MTSI supporting conversational speech (including DTMF), video and text transported over RTP with the scope to deliver a user experience equivalent to or better than that of CS conversational services using the same amount of network resources. TS 26.235 and TS 26.236 do not include the specification of an MTSI client, although they include conversational multimedia applications. Only those parts of TS 26.235 and TS 26.236 that are specifically referenced by TS 26.114 apply to MTSI.

#### 4.1.4.1	Multimedia Telephony Service for IMS (MTSI) - UE Conformance Testing  UID_350147

Responsibility:	R5

References

| Document | Title/Contents |
| --- | --- |
| WID(s) |
| RP-070664 | R5 WID on Conformance Test Aspects – Multimedia Telephony Services for IMS (MTSI) |
| Impacted Specifications |
| 34.229-1/2/3 | Internet Protocol (IP) multimedia call control protocol based on Session Initiation Protocol (SIP) and Session Description Protocol (SDP) |
| New Dedicated Specifications/Reports |
| None | - |

RAN5 provides conformance testing for MTSI (linked to MTSI Feature UID_7038.

IMS Call Control based on SIP forms the basis of IMS applications. Conformance test specifications must be developed for IMS Call Control protocol to verify correct functionality of the UE when operating in an IMS network. This enables the conformance testing of core Rel-7 enhancements of MTSI.

Status Report in RP-080284; Completion 0%; Target Sep 2008

### 4.1.5	Performance Characterization of VoIMS over HSDPA\EUL channels

Acronym:		VoIMS-PCVoIMS

UID_34033

Main Responsibility:	S2

Reference for "Performance Characterization of VoIMS over HSDPA\EUL channels"

| Document | Title/Contents |
| --- | --- |
| WID(s) |
| SP-050089 | WID on Performance Characterization of VoIMS over HSDPA\EUL channels |
| Impacted Specifications |
| TR 26.935 | Packet Switched (PS) conversational multimedia applications; Performance characterization of default codecs |
| New Dedicated Specifications/Reports |
| - | None |

The idea of carrying voice over shared resources such as HSDPA is becoming quite attractive due to the performance benefits and enhanced code utilization.

TR 26.935 provides information on the performance of default speech codecs in packet switched conversational multimedia applications. The transmission of IP/UDP/RTP/AMR packets over the UMTS air interface (over DCH channels) was simulated using the Conversational Packet Switched Radio Bearers coming from TS 34.108.  This is not an optimal RAB to do PS conversational test but it was the only one available at the time the test bed and the air interface simulator were designed.

RAN2 has recently defined RABs for the support of Voice over IMS on High Speed Downlink Packet Access HSDPA) bearers. In order to allow testing for support of Voice over IP over HSDPA\EUL (EUL = Enhanced UpLink) optimized RABs were simulated, that carry RTP, RTCP and SIP protocols.

This Work Item is about performing a similar set of tests as currently described in TR 26.935 in collaboration with relevant RAN WGs 1 and 2 by using HS-DSCH and E-DPDCH channels instead of DCH for carrying voice on downlink and uplink, respectively. The impact of jitter delay on the speech quality was evaluated by using proprietary Jitter Buffer Management algorithms. The tests performed by France Telecom, Dynastat and Beijing Institute of Technology were based on a generic scheduler and an approved test plan. Funding to compensate the work done by Dynastat and Beijing Institute of Technology was provided by Lucent Technologies (before the merge with Alcatel), while France Telecom kindly offered to perform the conversational subjective tests at their own expenses. The performance of proprietary Jitter Buffer Management algorithm(s) was tested by means of Listening only tests by Ericsson and Nokia, who kindly offered to perform the subjective tests at their own expenses. The tests performed were based on an approved test plan (same experimental conditions used for the conversational tests).

Therefore, the characterization consisted of:

  - Conversation tests to evaluate the performance under real-time conversations.

  - Listening-only tests to bring complementing information of the performance. (These focussed on the effect of jitter and channel errors instead of end-to-end delay, but also delay analysis was included.)

Outline of conversation and listening-only testing conditions (48 test conditions):

  - 3 codecs/modes: AMR 5.9 kbps, AMR 12.2 kbps, and AMR-WB 12.65 kbps (each tested in separate experiment consisting of 16 test conditions).

  - 3 background noise types: car, street and cafeteria.

  - 8 channel conditions consisting of 2 traffic and 2 mobility conditions: 2 traffic conditions (low: 40, 45 or 60 mobile users per cell; high: 80 or 100 mobile users per cell) and 2 terminal mobility scenarios (low: 3 km/h pedestrian; high: 30 or 120 km/h vehicle). Radio access bearer simulations conform to error-delay profiles and the definition of relevant RABs from RAN1 and RAN2.

  - Conversation testing with conversations lasting ca. 3 minutes (conforming to ITU-T SG12 Recommendation P.805 defined scenarios and testing procedures).

The test results were put in the informative Annex 8 of 3GPP TR 26.935.

## 4.2	Location-related new Features

### 4.2.1	Location Services enhancements (LCS3)  UID_32079

Responsibility:	S2

Reference for "Performance Characterization of VoIMS over HSDPA\EUL channels"

| Document | Title/Contents |
| --- | --- |
| WID(s) |
| SP-060291 | SA2 WID on |
| SP-060291 | SA2 WID on |
| SP-060291 | CT4 WID on |
| SP-060291 | SA1 WID on |
| SP-060291 | WID on |
| Impacted Specifications |
| TR 26.935 | Packet Switched (PS) conversational multimedia applications; Performance characterization of default codecs |
| New Dedicated Specifications/Reports |
| - | None |

| 32093 | Global Stage 2 for LCS3 (including IMS emergency location aspects) | S2 | 15/09/2006 | LCS3 | 23.271 | SP-050119 | Ben Rodilitz, SiRF | Approved SA#27. Appropriate place forEmergency work to be found |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

| 14025 | CT4 aspects for LCS | C4 | 01/12/2006 | LCS3-UEPos-LBS |  | CP-050240 |  | CRs approved in CT4#30... |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

| 31052 | LCS for 3GPP Interworking WLAN | S1 | 02/03/2007 | LCS3-IWLAN | 22.935 | SP-040309 | Mike Loushine, (Telcordia) |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

The 3GPP has developed and continues to develop Location Services (LCS) requirements and standards for GSM and UMTS.  To further the advancement of LCS within the 3GPP, LCS requirements and standards may be extended for 3GPP WLAN interworking to support the same location-based services that have been deployed today for GSM and UMTS. LCS with 3GPP WLAN Interworking system is considered to enlarge the area of location service.

This work item proposes that a feasibility study be performed to outline the technical requirements and architecture, scope of work required, and perform a gap analysis to determine whether existing 3GPP specifications can support LCS requirements for 3GPP WLAN interworking.  If it is determined that providing for this service is feasible, then this work item will continue forward to encompass future work. This work will also enable emergency services support in light of  U.S. regulatory requirements for delivering the position of VoIP subscribers. (The FCC released the 1st Report and Order on 3 June)

4		Objective

The purpose of the feasibility study is to study a generic interworking functionality for LCS between 3GPP system and WLAN systems (e.g. IEEE 802.11 family, HIPERLAN/2, …). In specific it aims at:

- Study the LCS requirements for 3GPP WLAN Interworking scenarios.

- Study the different possible LCS architectures  to fulfil the LCS requirements for 3GPP WLAN Interworking scenarios.

- Investigate whether there are WLAN Interworking architecture enhancements necessary to support LCS

- Investigate the LCS aspects for I-WLAN as IP-CAN in the IMS Emergency call, i.e., the emergency location information handling for I-WLAN

10	Expected Output and Time scale (to be updated at each plenary)

| New specifications |
| --- |
| Spec No. | Title | Prime rsp. WG | 2ndary rsp. WG(s) | Presented for information at plenary# | Approved at plenary# | Comments |
| TR 22.935 | Feasibility study on 3GPP system to Wireless Local Area Network (WLAN) Interworking with LCS | SA1 | SA2 | SA#27 | SA#29 |  |
| TR 23.837 | LCS Architecture for 3GPP Interworking WLAN | SA2 |  | SA#33 | SA#34 |  |
| Affected existing specifications |
| Spec No. | CR | Subject | Approved at plenary# | Comments |
| TS 23.234 |  | 3GPP system to WLAN interworking; System description |  |  |
| TS 23.271 |  | Functional stage 2 description of Location Services |  |  |

| 50558 | LCS Enhancements Related to Location-Based Services | GP | 31/08/2007 | LCS3-LBS | 43.059, 44.031, 48.008, 49.031 | GP-050265 | Kevin Judge, SiRF Technologies | Linked to SP-040682 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

| TS 43.059 | Functional stage 2 description of Location Services (LCS) in GERAN |
| --- | --- |
| TS 44.031 | Location Services (LCS); Mobile Station (MS) - Serving Mobile Location Centre (SMLC) Radio Resource LCS Protocol (RRLP) |
| TS 49.031 | Location Services (LCS); Base Station System Application Part LCS Extension (BSSAP-LE) |
| TS 48.008 | MSC - BSS Interface; Layer 3 Specification |

#### 4.2.1.2	Inclusion of Uplink TDOA UE positioning method in the UTRAN specifications  UID_20012

Responsibility:	R2

References

| Document | Title/Contents |
| --- | --- |
| WID(s) |
| RP-040387 | WID on Inclusion of Uplink TDOA UE positioning method in the UTRAN specifications |
| Impacted Specifications |
| TS 25.305 | User Equipment (UE) positioning in Universal Terrestrial Radio Access Network (UTRAN); Stage 2 |
| TS 25.453 | UTRAN Iupc interface Positioning Calculation Application Part (PCAP) signalling |
| New Dedicated Specifications/Reports |
| None | - |

The Uplink TDOA (U-TDOA) location method has been standardized in the GSM Circuit Switched environment and standardization in the GSM Packet Switched environment (GPRS) is proceeding.  
There is an interest in using the U-TDOA location technology for UMTS.

It provides a stand-alone SMLC (SAS) based overlay network interfacing UTRAN on the Iupc interface. 
This is complementary to already standardized location methods.

Completed Nov 2007; Status Report in RP-070797

#### 4.2.1.3	UE positioning - Velocity  UID_20042

Responsibility:	R2

References

| Document | Title/Contents |
| --- | --- |
| WID(s) |
| RP-050300 | WID on LCS Enhancements Related to Location-Based Services |
| Impacted Specifications |
| TS 25.305 | User Equipment (UE) positioning in Universal Terrestrial Radio Access Network (UTRAN); Stage 2 |
| TS 25.331 | Radio Resource Control (RRC); Protocol specification |
| TS 25.410 | UTRAN Iu interface: General aspects and principles |
| TS 25.413 | UTRAN Iu interface Radio Access Network Application Part (RANAP) signalling |
| TS 25.453 | UTRAN Iupc interface Positioning Calculation Application Part (PCAP) signalling |
| New Dedicated Specifications/Reports |
| None | - |

Proposed LCS offerings are migrating beyond the initially targeted Emergency Services toward offerings that provide Location-Based Services (LBS).  These LBS require information to be communicated that is not accounted for in current specifications.  Additionally, Emergency Services are characterized by a single request for position resulting in a single position report.  In contrast, many LBS require multiple reports of an UE’s position with varying update rates. Some of these requests may be call-independent location requests i.e. requests for a mobile’s position when the mobile is not on an active call.  Changes to the current specifications could alleviate the consequences of increased messaging traffic and provide the capabilities required for a feature rich LBS offering.

Specifically, LBS such as mobile tracking, turn-by-turn directions and point-of-interest finding require knowledge of the speed and direction of travel of the UE.  As an example, this requirement could be achieved by providing the ability to report the velocity (speed and bearing) of a UE.  As potential solutions to mitigate the increased messaging and the resultant increased bandwidth required for frequent location updates, modifications such as implementation of periodic position reporting could be considered.

It provides LBS by:

- Providing information required by LBS through enabling the reporting of velocity.

- Mitigating the network impacts encountered by the increased usage of LBS through the enabling of periodic position reporting.

Completed Sept 2006; Status Report in RP-060459

### 4.2.2	Advanced Global Navigation Satellite System (A-GNSS) concept (LCS3-AGNSS)  UID_31051

Responsibility:	S1

References

| Document | Title/Contents |
| --- | --- |
| WID(s) |
| SP-040681 | WID on Advanced Global Navigation Satellite System (A-GNSS) concept |
| Impacted Specifications |
| TS 22.071 | Location Services (LCS); Service description; Stage 1 (22.071-0071r1; SP-050584). |
| New Dedicated Specifications/Reports |
| None | - |

The existing mechanisms of Cell-ID or E-OTD provide high service availability but limited service accuracy. Also, the A-GPS method provides high service accuracy but service availability could be improved, especially when considering the obstacles masking the signals of part of the GPS satellites in urban environments.

With the onset of other satellite positioning systems these conflicting requirements may be harmonized. There are advantages of enlarging the Assisted-GPS concept to Assisted-GNSS, and particularly to the GALILEO system, since it allows improving the above lacks. This has been done in the stage 1 of 22.071.

#### 4.2.2.1	Towards A-GNSS Concept  UID_50548

Responsibility:	GP

References

| Document | Title/Contents |
| --- | --- |
| WID(s) |
| GP-042677 | WID on Towards A-GNSS Concept |
| Impacted Specifications |
| TS 43.030 | Radio network planning aspects |
| TS 43.059 | Functional stage 2 description of Location Services (LCS) in GERAN |
| TS 44.031 | Location Services (LCS); Mobile Station (MS) - Serving Mobile Location Centre (SMLC) Radio Resource LCS Protocol (RRLP) |
| TS 44.035 | LCS - Broadcast Network Assistance for E-OTD and GPS Positioning Methods |
| TS 44.071 | LCS - Mobile radio interface layer 3 - Location Services (LCS) Specification |
| TS 48.008 | MSC - BSS Interface; Layer 3 Specification |
| TS 48.018 | GPRS / BSS / SGSN - BSS GPRS Protocol (BSSGP) |
| TS 48.031 | LCS - SMLC/SMLC - SMLCPP Specification |
| TS 49.031 | Location Services (LCS); Base Station System Application Part LCS Extension (BSSAP-LE) |
| TS 51.010 | Mobile Station (MS) conformance specification |
| New Dedicated Specifications/Reports |
| None | - |

The use of GALILEO either alone or especially in association with GPS improves the availability and the accuracy of the LCS Services provided by the PLMN in difficult situations such as urban or indoor environments where a limited number of satellites are visible and where satellite signals can be highly attenuated. There is therefore an interest to introduce support of Assisted-GALILEO in the 3GPP specifications.

Since other satellite positioning systems are currently being developed or are likely to be developed in the near future, it has been highlighted that it was preferable to introduce Assisted-GALILEO in the 3GPP standards in a generic manner: GALILEO is considered as a particular case of a Global Navigation Satellite System (GNSS) (GPS is the first available GNSS, and other GNSSs can come to existence in the future). The work item was therefore meant to introduce support of Assisted-GALILEO in the 3GPP TSG GERAN specifications as a particular case of an Assisted-GNSS; this approach would minimise additional impacts to the 3GPP specifications in case an interest arises in the future to add further GNSSs to 3GPP.

The introduction of GALILEO would not result in duplication of A-GPS. Changes to TS 44.031 were felt of relevant importance. The following items were developed in Rel-7:

Items

Carrier phase measurements reported by the MS to the Network

Carrier measurements assistance

Non native orbit models

Orbit extension

Non broadcast ephemeris flag

Validity period information for orbit models

Cell timing measurements for neighbouring cells

Cell timing assistance for neighbouring cells

Earth orientation parameters

Stationary indication in MS-Assisted mode

Code phase measurement description

In particular, it was recommended that the full implementation of GALILEO and GNSS in general should include the option to extend the satellite orbits beyond that provided by the native format.

Accurate satellite location information is among the important information content required by an MS in order to navigate well.  This information can be computed from Ephemeris data that can be provided in current assistance messages.  Additional delta packets to the original full shipment can be provided at a greatly reduced data overhead while preserving the ability to accurately compute the satellite location using the satellite location techniques already provided for in today’s implementations.  This technique extends the life of an ephemeris by providing compact updates to the existing ephemeris information.

#### 4.2.2.2	Global Navigation Satellite System (GNSS) in UTRAN  UID_20050

Responsibility:	R2

References

| Document | Title/Contents |
| --- | --- |
| WID(s) |
| RP-060211 | WID on Global Navigation Satellite System (GNSS) in UTRAN |
| Impacted Specifications |
| TS 25.305 | User Equipment (UE) positioning in Universal Terrestrial Radio Access Network (UTRAN); Stage 2 |
| TS 25.331 | Radio Resource Control (RRC); Protocol specification |
| TS 25.306 | UE Radio Access capabilities |
| TS 25.413 | UTRAN Iu interface Radio Access Network Application Part (RANAP) signalling |
| TS 25.423 | UTRAN Iu interface Radio Access Network Application Part (RANAP) signalling |
| TS 25.433 | UTRAN Iub interface Node B Application Part (NBAP) signalling |
| TS 25.453 | UTRAN Iupc interface Positioning Calculation Application Part (PCAP) signalling |
| TS 25.302 | Services provided by the physical layer |
| TS 25.215 | Physical layer; Measurements (FDD) |
| TS 25.401 | UTRAN overall description |
| TS 25.402 | Synchronization in UTRAN Stage 2 |
| TS 25.450 | UTRAN Iupc interface general aspects and principles |
| TS 25.452 | UTRAN Iupc interface: signalling transport |

The Cell-ID or E-OTD methods provide high service availability but limited service accuracy.

The A-GPS method provides high service accuracy but service availability could be improved, especially when considering the obstacles masking the signals of part of the GPS satellites in urban difficult environments.

With the onset of other satellite positioning systems these conflicting requirements may be harmonized. There are advantages of enlarging the Assisted-GPS concept to Assisted-GNSS, and particularly to include the GALILEO system, since it allows improving the above lacks.

It introduces support of Assisted-GALILEO in the 3GPP TSG RAN specifications as a particular case of an Assisted-GNSS (where Assisted-GPS was the first available Assisted-GNSS, and other Assisted-GNSS might existin the future). This approach minimises additional impacts to the 3GPP specifications in case of adding further Assisted-GNSS.

It covers both UE side (UE-assisted and UE-based) and network-assisted techniques.

Completed Sept 2006; Status Report in RP-070482

### 4.2.3	A-GPS Minimum Performance (GAGR)  UID_50581

Responsibility:	G1,G3

References

| Document | Title/Contents |
| --- | --- |
| WID(s) |
| GP-060834 | WID on A-GPS Minimum Performance |
| Impacted Specifications |
| TS 45.005 | Radio transmission and reception |
| TS 51.010 | Mobile Station (MS) conformance specification |
| New Dedicated Specifications/Reports |
| - | None |

A minimum performance specification is desirable to give the operators implementing services based on A-GPS a baseline performance that can be relied on in all equipped MSs.

This work added an A-GPS Minimum Performance core specification and associated Conformance test cases for Mobile Stations supporting A-GPS in the GERAN, by aligning as closely as possible with the two UTRAN specifications for Minimum Performance and associated conformance test cases which are available in 25.171 and 34.171 respectively.

## 4.3	Combinational Services

To be written by Paolo, Maurice

Acronym:		CSICS

UID_31063

Main Responsibility:	S1

References for "Combinational Services "

| Document | Title/Contents |
| --- | --- |
| WID(s) |
| SP-050228 | Specification of Combining CS and IMS services & Capability Detection and Exchange mechanism |
| SP-040479 | Feasibility Study on IMS services using CS bearers |
| NP-050063 | Combining CS and IMS services & Capability Detection mechanism, CT |
| CP-060105 | Stage 3 Specification of Combining CS and IMS services & Capability Detection and Exchange mechanism. |
| SP-050091 | WID for Stage 3 Specification of Combining CS and IMS services (Release 7) |
| Impacted Specifications |
| TS 24.008 | Mobile radio interface Layer 3 specification; Core network protocols; Stage 3 (CR 24.008-1062r1 CP-060121) |
| TS 24.229 | Internet Protocol (IP) multimedia call control protocol based on Session Initiation Protocol (SIP) and Session Description Protocol (SDP); Stage 3 (CR 24.229-1183 CP-060121) |
| TS 26.141 | IP Multimedia System (IMS) Messaging and Presence; Media formats and codecs (CR 26.141-0002r5 SP-050790) |
| TS 26.235 | Packet switched conversational multimedia applications; Default codecs (CR 26.235-0014r3 SP-050790) |
| TS 26.236 | Packet switched conversational multimedia applications; Transport protocols (no CRs with CSICS Paolo but it is in Workplan) |
| New Dedicated Specifications/Reports |
| TS 22.279 | Combining CS and IMS services; Stage 1 |
| TR 22.979 | Feasibility study on combined CS calls and IMS sessions |
| TS 23.279 | Combining CS and IMS services; Stage 2 |
| TS 24.279 | Combining Circuit Switched (CS) and IP Multimedia Subsystem (IMS) services; Stage 3 |
| TR 24.879 | Combining CS calls and IMS sessions |
| TR 24.979 | Combining CS calls and IMS sessions |

Combinational services, which are applicable to both UTRAN and GERAN, are enable the unidirectional or bi-directional (simultaneous send receive) exchange of PS data within the context of an IMS session.

A specific subscription for combinational services is not necessary. However, both users A and B must have valid subscriptions for voice calls as well as for accessing the IMS. The existing address context is reused when the combined service is established, which makes the combined service simple to invoke for the user.

The IMS session may consist of one or more IMS services. Requirements for the following capabilities are included:

-	Radio capability exchange.

-	Terminal capability exchange.

-	E.164 number exchange.

-	Adding IMS session to an ongoing CS call.

-	Adding a CS call to an ongoing IMS session.

-	Supplementary services as they relate to CSICS.

The capabilities defined for CSICS support interoperability between different operator networks, and roaming.

This WI was first started as a feasibility report in TR 22.979 in Rel-6. For Rel-7, the work was concluded to define a stage 1 in 22.279, a stage 2 in 23.279 and stage 3 TS in 24.279.

The combinational service can be establish between two users:

-	within the same PLMN or within different PLMNs.

-	 camped on identical or different RATs.

-	 when roaming, assuming the visited operator supports GPRS roaming.

The user (A or B party) only needs to know one address in order to establish the combinational service. In addition either user can add an IMS session to a CS speech call or a CS Multimedia call, thereby creating a combinational call or vice versa.

Depending on the differing UE implementations, the IMS registration can be performed at switch-on or on demand. Also, interoperability between UEs that implement different approaches is possible.

A user may be invited even though he is not IMS registered. If not, then the invited user is able to accept or reject the IMS registration request.

A combinational service is possible for both unidirectional and bi-directional exchange of PS data within the context of the IMS session.

| 89 | 31063 | Combinational Services | 1 | S1 | CSICS |  | SP-050228 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 90 | 31064 | Stage 1 for CSICS | 2 | S1 |  | 22.279 | SP-050228 |
| 91 | 32084 | Stage 2 for CSICS | 2 | S2 |  | 23.279 |  |
| 92 | 11054 | Stage 3 for CSICS CN aspects | 2 | C1 |  | New TS 24.279, 24.229, 24.008 | CP-060105 |
| 93 | 34031 | Stage 3 for codec aspects | 2 | S4 | CSICS-Codec | TS 26.141, 26.235, 26.236 | SP-050091 |

## 4.4	System enhancements for fixed broadband access to IMS

To be written by Maurice

Acronym:		FBI

UID_32074

Main Responsibility:	S2

SA5 Charging aspects of FBI for PacketCable (FBI-PCBL-CH) are implemented as CRs in TSs 32.240, 32.260, 32.298, 32.299.

References for "System enhancements for fixed broadband access to IMS "

| Document | Title/Contents |
| --- | --- |
| WID(s) |
| GP-022566 | WID on XXX |
| Impacted Specifications |
| TS 24.008 | Example |
| New Dedicated Specifications/Reports |
| TS 22.146 | Example |

Your text: what does it offer? (Stage 1 summary) How does it impact the network? (Stages 2 and 3 summary). PLEASE DON’T JUST COPY-PASTE THE TEXT FROM THE WID BUT CHECK WHAT WAS ACTUALLY DONE!

Extract from the Work Plan (info for the writer only, to be deleted when providing actual text):

SA5 Charging aspects of FBI for PacketCable (FBI-PCBL-CH) are implemented as CRs in TSs 32.240, 32.260, 32.298, 32.299.

| 94 | 32074 | System enhancements for fixed broadband access to IMS | 1 | S2 | FBI |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 95 | 7001 | TISPAN Rel 1 related aspects | 2 | S2 |  |  |  |
| 96 | 32075 | Stage 2 of FBI for TISPAN R1 | 3 | S2 |  |  |  |
| 97 | 11050 | Protocol impact of FBI for TISPAN R1 | 3 | C1 |  | new TR 24.819, 24.229, 29.229, 29.163, 29.209 | NP-040618 |
| 98 | 11060 | CT1 aspects of FBI for TISPAN R1 | 4 | C1 |  | new TR 24.819, 24.229, 29.229, 29.163, 29.209 | NP-040618 |
| 99 | 13025 | CT3 aspects of FBI for TISPAN R1 | 4 | C3 |  | new TR, 29.229, 29.163 | NP-040618 |
| 100 | 14020 | CT4 aspects of FBI for TISPAN R1 | 4 | C4 |  | 29.209 | NP-040618 |
| 101 | 33027 | Security Enhancements for FBI | 3 | S3 | FBI-ISE | 33.102, 43.020 | SP-050395 |
| 102 | 7002 | PacketCable Related aspects | 2 | S2 | FBI-PCBL |  |  |
| 103 | 7003 | Stage 2 of FBI for PacketCable | 3 | S2 |  |  |  |
| 104 | 7004 | Protocol impact of FBI for PacketCable | 3 | C1 |  |  |  |
| 106 | 7005 | TISPAN Rel 2 related aspects | 2 | S2 | FBI-TISP2 |  |  |
| 107 | 7006 | Stage 2 of FBI for TISPAN R2 | 3 | S2 |  |  |  |
| 108 | 7007 | Protocol impact of FBI for TISPAN R2 | 3 | C1 |  |  |  |

## 4.5	Access Class Barring and Overload Protection

To be written by Maurice

Acronym:		ACBOP

UID_32064

Main Responsibility:	S2

References for "Access Class Barring and Overload Protection "

| Document | Title/Contents |
| --- | --- |
| WID(s) |
| GP-022566 | WID on XXX |
| Impacted Specifications |
| TS 24.008 | Example |
| New Dedicated Specifications/Reports |
| TS 22.146 | Example |

Your text: what does it offer? (Stage 1 summary) How does it impact the network? (Stages 2 and 3 summary). PLEASE DON’T JUST COPY-PASTE THE TEXT FROM THE WID BUT CHECK WHAT WAS ACTUALLY DONE!

Extract from the Work Plan (info for the writer only, to be deleted when providing actual text):

Note that no work has been done in GERAN on this work item !!!

| 64 | 32064 | Access Class Barring and Overload Protection | 1 | S2 | ACBOP | 23.898 | SP-040338 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 65 | 32065 | TR on Stage 2 | 2 | S2 |  |  |  |
| 66 | 50117 | Extra ACBOP information in GERAN | 2 | GP |  | 44.018 |  |
| 67 | 11048 | Stage 3 CN aspects of ACBOP | 2 | C1 |  | 24.008 |  |
| 68 | 20010 | Deleted - Potential impact on Iu interface Overload functionality | 2 | RP |  | 25.413 |  |
| 69 | 20009 | Deleted - Extra ACBOP information in RAN | 2 | RP |  | 25.331 |  |

## 4.6	USSD message delivery and transfer to USIM

Written by M. Clayton

Acronym:		USSD-USIM

UID_31048

Main Responsibility:	S1

References for "USSD message delivery and transfer to USIM "

| Document | Title/Contents |
| --- | --- |
| WID(s) |
| SP-040104 | USSD message transfer to USIM |
| TP-040069 | Alignment with requirements regarding USSD usage |
| Impacted Specifications |
| TS 22.090 | Unstructured Supplementary Service Data (USSD); Stage 1 (CR 22.090-0003r3 SP-060445) |
| TS 31.111 | Universal Subscriber Identity Module (USIM) Application Toolkit (USAT) (CR 31.111-144 CP-050141) |
| TS 31.115 | Secured packet structure for (Universal) Subscriber Identity Module (U)SIM Toolkit applications (CR 31.115-005 CP050141) |
| TS 31.130 | (U)SIM Application Programming Interface (API); (U)SIM API for Java Card (CR 33.130-014 CP050141) |
| New Dedicated Specifications/Reports |

Since R99 there has been a mechanism to deliver USSD strings from the USIM to the network and receive the reply. However, there was no specified delivery and transfer mechanism for the USIM to receive Network initiated USSD. This feature is considered to be very desirable by many operators.

Originally this feature was first devised in TSG T3 (now CT6) which identified the need for:

-	the addition of addressing in the USSD message;

-	the addition of a USSD data download command to USAT;

-	the addition of USSD as part of Bearer Independent protocol in USAT;

-	the addition of a USSD clause to TS 23.048 to clarify the use of this specification over USSD;

-	the addition of the Java API routines for the above commands;

-	the provision for backwards compatibility.

The work was started in SA1 where CRs were proposed to 22.090, however, after discussion in SA1 on which was the best specification in which to define a technical solution. Finally, a WI was proposed in T3/CT6 and it was linked with the SA1 WI. CRs were proposed and agreed in CT6, then in CT, fullfiling questions raised in both SA1 and CT6 WIs.

## 4.7	Protocol-related new Features

### 4.7.1	IMS Stage 3 IETF Protocol alignment

Written by A. Brekalo

Acronym:		IMSProtoc

UID_711052

Main Responsibility:	CT1

References

| Document | Title/Contents |
| --- | --- |
| WID(s) |
| CP-060101 | IMS Stage-3 IETF Protocol Alignment |
| Impacted Specifications |
| TS 24.229 | Review of additional capabilities provided in SIP by IETF, and provide documentation as whether these capabilities are supported in the IM CN subsystem or not |
| TS 23.218 | Review of additional capabilities provided in SIP by IETF, and provide documentation as whether these capabilities are supported in the IM CN subsystem or not |
| New Dedicated Specifications/Reports |
| TR 24.930 | Signalling flows for the session setup in the IM CN subsystem based on Session Initiation Protocol (SIP) and Session Description Protocol (SDP); Stage 3 |

In Release 5, the IMS was defined to support IP Multimedia services.  The feature set in Release 5 provides a basis for IP Multimedia support.  At Release 6 further work was identified. At Release 7 the need for other new capabilities is being identified, and there was still significant ongoing work in IETF that should be documented in relation to its impact on IMS.

The areas which were considered by WID:

- Ensure protocol alignment between 3GPP Stage 3 postponed Release 5 and 6 IMS work and IETF. Review existing and future capabilities provided in SIP by IETF, and provide documentation as whether these capabilities are supported in the IM CN subsystem or not.

- Creation of a TR that shows signalling flows reflecting the different options for session setup in the IM CN subsystem.

In addition to the above listed items, it was seen that there may be minor technical improvements and enhancements to IMS Rel-7, not of sufficient significance to be normally covered by a work item, that can be dealt with by this work item.

The scope of this WID was protocol alignment, and those capabilities that may lead to new or enhanced IMS applications were not dealt with as part of this WID.

### 4.7.2	DIAMETER on the GGSN Gi interface

Written by S.D. Han

Acronym:		DIAMGi

UID_13023

Main Responsibility:	C3

References for "DIAMETER on the GGSN Gi interface "

| Document | Title/Contents |
| --- | --- |
| WID(s) |
| CP-060227 | Revised WID for Diameter on the GGSN interface |
| Impacted Specifications |
| TS 29.061 | Interworking between the Public Land Mobile Network (PLMN) supporting packet based services and Packet Data Network (PDN) |
| New Dedicated Specifications/Reports |
| - | None |

Currently, the Gi interface in GPRS (TS29.061, Rel-6) only supports the RADIUS protocol. Other platforms that could have used either RADIUS or Diameter have been allowed to use Diameter in the specifications. Diameter is used on a multitude of interfaces including Cx,  Sh, Gq, Ro, Rf,   in IMS, policy control and IP flow charging. The objective of this work item is to have Diameter specified also for use on the Gi interface.

The usage of Diameter over the GGSN Gi interface was introduced and the Diameter message flows between GGSN and Diameter server was described in TS 29.061 to provide Authentication, Authorization and Accounting services.

### 4.7.3	DIAMETER on the PDG Wi inteface

Written by S.D. Han

Acronym:		DIAMWi

UID_13022

Main Responsibility:	C3

References for "DIAMETER on the PDG Wi inteface "

| Document | Title/Contents |
| --- | --- |
| WID(s) |
| CP-060228 | Revised WID for Diameter on the PDG Wi interface |
| Impacted Specifications |
| TS 29.161 | Interworking between the Public Land Mobile Network (PLMN) supporting packet based services and Packet Data Network (PDN) |
| New Dedicated Specifications/Reports |

The protocol for  Wi interface is currently RADIUS. Other platforms that could have used either RADIUS or Diameter have been allowed to use Diameter in the specifications. Several reference points in Wireless LAN will be using Diameter. The objective of this work item is to have Diameter specified also for use on the Wi interface

The usage of Diameter over the PDG Wi interface was introduced in TS 29.161 to provide Authentication, Authorization and Accounting services. The Diameter messages and AVPs for the Wi interface were defined through reference to TS 29.061.

## 4.8	Mp (MRFC - MRFP) interface

Written by K. Kymalainen

Acronym:		Mp

UID_14012

Main Responsibility:	C4

References for "Mp (MRFC - MRFP) interface"

| Document | Title/Contents |
| --- | --- |
| WID(s) |
| CP-070246 | WID on Mp (MRFC - MRFP) interface |
| Impacted Specifications |
| TS 24.229 | IP Multimedia Call Control Protocol based on SIP and SDP; Stage 3 |
| New Dedicated Specifications/Reports |
| TS 23.333 | Multimedia Resource Function Controller (MRFC) – Multimedia Resource Function Processor (MRFP) Mp interface; Procedures description |
| TS 29.333 | Multimedia Resource Function Controller (MRFC) – Multimedia Resource Function Processor (MRFP) Mp Interface; Stage 3 |

Within the IP Multimedia Subsystem, the Multimedia Resource Function (MRF), through interactions with the User Equipment (UE), Application Server (AS) and Serving Call Session Control Function (S-CSCF), provides, for example, ad-hoc video and audio conference capabilities, and the support of announcements, tones and media streams processing.

The MRF was to decompose into two functions, i.e. the MRFC and MRFP. The Mp Interface, which is located between these two functions, supports the H.248 protocol with the additional support of Multimedia specific H.248 Packages.

The intention of this WI was to define the use of H.248 including the additional H.248 Multimedia Packages between the MRFC and MRFP and to define the relationship between the S-CSCF – MRFC –interface (Mr-interface) SIP and SDP procedures/instructions and the associated H.248, including the additional Packages and procedures.

The MRFC:

- Controls the media stream resources in the MRFP.

- Interprets information coming from an AS and S-CSCF (e.g. session identifier) and control MRFP accordingly.

- Generates CDRs

The MRFP:

- Controls bearers on the Mb reference point.

- Provides resources to be controlled by the MRFC.

- Mixes incoming media streams (e.g. for multiple parties).

- Processes media streams (e.g. media analysis).

- Sources media streams (for multimedia announcements).

## 4.9	Support of SMS over generic 3GPP IP access

To be written by Maurice

Acronym:		SMSIP

UID_32081

Main Responsibility:	S2

References for "Support of SMS and MMS over generic 3GPP IP access "

| Document | Title/Contents |
| --- | --- |
| WID(s) |
| GP-022566 | WID on XXX |
| Impacted Specifications |
| TS 24.008 | Example |
| New Dedicated Specifications/Reports |
| TS 22.146 | Example |

Your text: what does it offer? (Stage 1 summary) How does it impact the network? (Stages 2 and 3 summary). PLEASE DON’T JUST COPY-PASTE THE TEXT FROM THE WID BUT CHECK WHAT WAS ACTUALLY DONE!

Extract from the Work Plan (info for the writer only, to be deleted when providing actual text):

| 116 | 32081 | Support of SMS and MMS over generic 3GPP IP access | 1 | S2 | SMSIP | TR 23.abc, TS 23.abc | SP-050626 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 117 | 32094 | FS on SMSIP | 2 | S2 |  | 23.804 |  |
| 118 | 32095 | Stage 2 for SMSIP | 2 | S2 |  | 23.204 |  |
| 119 | 310001 | Stage 3 for SMSIP | 2 | C4 |  |  | CP-060172 |
| 120 | 310002 | CT1 aspects for SMSIP | 3 | C1 |  |  |  |
| 121 | 310003 | CT4 aspects for SMSIP | 3 | C4 |  |  |  |

## 4.10	Dynamic and Interactive Multimedia Scenes (DIMS)

Written by P. Usai

Acronym:		DIMS

UID_34032

Main Responsibility:	S4

References for "Dynamic and interactive multimedia scenes"

| Document | Title/Contents |
| --- | --- |
| WID(s) |
| SP-050195 | WID on Dynamic and interactive multimedia scenes |
| Impacted Specifications |
| TS 26.140 | Multimedia Messaging Service (MMS); Media formats and codes |
| TS 26.234 | Transparent end-to-end Packet-switched Streaming Service (PSS); Protocols and codecs |
| TS 26.244 | Transparent end-to-end packet switched streaming service (PSS); 3GPP file format (3GP) |
| TS 26.346 | Multimedia Broadcast/Multicast Service (MBMS); Protocols and codecs |
| New Dedicated Specifications/Reports |
| - | None |

This WI aims to specify the dynamic and interactive multimedia scenes of PSS, MMS, MBMS services relative to SA4 specifications (bearer dependant aspects of service enablers).

There are existing non-standard solutions in this area which are enjoying some adoption into 3G terminals, but the market and 3G community will greatly benefit from a standard, open, stable, multi-vendor and interoperable specification.

Scene is understood as a presentation of multimedia content including a service logic (animation, menu, links, etc. …).

Existing capability in 3GPP specifications is limited to download and progressive download; full incremental update is not possible, and interactivity is limited.  In addition, existing support for compression and binarization is limited. An update of a piece of content within a multimedia presentation is not possible without reloading a complete page, e.g. : changing frequently a quote within a stock-exchange service or adding a voting button in an iTV service.

This solution will enable content owners to build enhanced user experiences, and existing capabilities in user input and display can be leveraged (but there might be impact on MMI). In fact, the user experience of multimedia on 3G terminals can be enhanced if the selection, control and display of the multimedia scenes are integrated into a single user interface; also, it would be possible to update animated applications and displays incrementally in order to use bandwidth appropriately.

The specification for multimedia scene management will include:

- scene format and scene definition

- container and delivery formats including both file and stream forms

- the compatibility with, integration of, and building upon existing media types and formats in 3GPP specifications, including but not limited to video, audio (including both sampled audio and synthetic audio), images and graphics (SVG Tiny),  storage format such as 3GPP file format and stream formats such as RTP.

- management of user interactivity

- incrementally updated scenes and animations

- integration with capabilities for secure/encrypted delivery.

- efficient use of the bandwidth of the radio network.

In summary, this work item will provide a media type, which can be delivered using existing services, and integrated with existing media types. The adoption of this media type into MBMS, PSS (including progressive download), and MMS services is envisaged. This work would leverage capabilities in both delivery (messaging, download, streaming etc.) and security (encryption etc.); there is no impact on security specifications.

Completion : 40 %.

## 4.11	Security-related new Features

### 4.11.1	Liberty Alliance and 3GPP Security Interworking

Written by M. Clayton

Acronym:		LibSec

UID_33022

Main Responsibility:	S3

References for "Liberty Alliance and 3GPP Security Interworking "

| Document | Title/Contents |
| --- | --- |
| WID(s) |
| SP-050145 | WID on [Alain] |
| Impacted Specifications |
| - | - |
| New Dedicated Specifications/Reports |
| TS 33.980 | Liberty Alliance and 3GPP security interworking; Interworking of Liberty Alliance Identity Federation Framework (ID-FF), Identity Web Services Framework (ID-WSF) and Generic Authentication Architecture (GAA) |

The GAA system provides mobile subscriber and an application with a shared secret or provides a certificate to the subscriber. The Liberty Alliance Project (LAP) defines in the ID-FF and ID-WSF specifications a family of protocols. Those protocols enable reuse of an authentication done at an Identity Provider (IdP) for user authentication towards a Service Provider, that trusts this authentication confirmation of the IdP. LAP does not specify the actual means of authentication, but leaves that for agreement between the business partners. The Liberty Alliance specifications use the provided authentication to the IdP means without restricting the type of authentication mechanism, to enable easy integration with the existing infrastructure and legacy authentication mechanism (e.g. username / password). GAA, which is specific to mobile subscribers, is one of the methods that can be used to provide the authentication towards the Liberty IdP. There may also be other 3GPP security methods that could be used to authentication towards the Liberty IdP. 3GPP services might utilize the authentication model defined by LAP, but details of this interworking are not fully studied and specified. In order to enable the use of 3GPP authentication methods within the Liberty framework, and hence leverage the access of 3G subscribers to Liberty-enabled services, it is therefore required to study the 3GPP security - Liberty interworking.

The 3GPP security specifications (e.g. GAA, IMS) and the Liberty Alliance specifications (i.e. ID-FF and ID-WSF) have been drafted with different goals, hence their deployment should be kept independent of each other, but the interworking between them should be made possible and optimised.

The interworking of 3GPP authentication technologies and Liberty has been discussed in SA3 and some areas for optimisation and enhancement for interworking were outlined. New developments in related organisations that affect the interworking need to be studied in further detail. The enabling of optimal interworking of technologies might require work that lies outside the current GAA area and therefore interworking should be studied in a separate work item outlined by this WID. Another area of interworking is the use of an authentication done at a Liberty IdP to a 3GPP service or applications.

This work item

-	Investigated relevant standards and technologies, both existing as well as the ones that are work-in-progress

-	Identified clearly areas of interworking

-	Investigated possible architectural scenarios for 3GPP security – Liberty interworking

-	Studied possible optimisation of the 3GPP security and LAP interworking and propose enhancements to the relevant specifications

-	Investigated the need and define, if applicable, guidelines on the usage of 3GPP security and Liberty Alliance protocols for 3GPP services and applications.

-	Identified suitable format, standards and forums to incorporate the interworking optimisation suggestions.

The result was a report on how an interworking between 3G security methods and the Liberty Alliance framework could be realised, and suggestions to optimise the interworking between LAP and GAA.

### 4.11.2	Trust Requirements for Open Platforms in 3GPP

Written by M. Clayton

Acronym:		TrustOP

UID_33023

Main Responsibility:	S3

References for "Trust Requirements for Open Platforms in 3GPP "

| Document | Title/Contents |
| --- | --- |
| WID(s) |
| SP-040863 | WID on Trust Requirements for Open Platforms in 3GPP |
| Impacted Specifications |
| - | - |
| New Dedicated Specifications/Reports |
| TR 33.905 | Trust recommendations for open platforms |

Securing the storage, processing, and input and output of sensitive data on an Open Platform is of critical importance. Also, isolation of some applications (e.g., applications that are managing (U)SIMs and (U)SIM readers), and protocols from Trojans that can attack such applications and spoof sensitive identities is imperative.  Protecting the interface between the Open Platform and the UICC is also of critcal importance.

Therefore, it is very much desirable that the Open Platform must have secure authentication and authorization mechanisms to protect against eavesdropping, and malicious modification of user data and operator applications residing on the Open Platform.

Consequently, for the diverse 3GPP usage models of the Open Platform, such as the ones described in 3GPP TS 33.234, appropriate trust requirements need to be specified to counteract the threats. This work item suggests to study and evaluate the trust requirements, study the issues and further develop the additional trust requirements for the usage models described in 3GPP.

The work item sought to:

-	Investigate relevant trust standards and technologies, both existing as well as the ones that are work-in-progress.

-	Develop the open platform trust requirements for delivery of new applications and services to open platforms. Such new applications and services include the 3GPP-WLAN Interworking usage models described in 3GPP TS 33.234.

-	Achieve the following characteristics for the Open Platform in 3GPP environment:

- Trusted – the Open Platform acts in a recognized manner and in able to communicate what that manner is supposed to be.

- Reliable – the Open Platform is readily available for transactions and communications, as well as prepared to act against viruses and other intrusions (intrusion prevention and detection).

- Protected – the Open Platform is shares information with only those that need to know within commonly accepted parameters for computer privacy.

The results of the study were provided in the form of TR that contained requirements for trusted open platforms.

### 4.11.3	Development of UEA2 and UIA2

Written by M. Clayton

Acronym:		AlgUEA2

UID_33024

Main Responsibility:	S3

References for "Development of UEA2 and UIA2"

| Document | Title/Contents |
| --- | --- |
| WID(s) |
| SP-040864 | WID on Development of UEA2 and UIA2 |
| Impacted Specifications |
| - | - |
| New Dedicated Specifications/Reports |
| TS 35.215 | Specification of the 3GPP Confidentiality and Integrity Algorithms UEA2 & UIA2; Document 1: UEA2 and UIA2 specifications |
| TS 35.216 | Specification of the 3GPP Confidentiality and Integrity Algorithms UEA2 & UIA2; Document 2: SNOW 3G specification |
| TS 35.217 | Specification of the 3GPP Confidentiality and Integrity Algorithms UEA2 & UIA2; Document 3: Implementors’ test data |
| TS 35.218 | Specification of the 3GPP Confidentiality and Integrity Algorithms UEA2 & UIA2; Document 4: Design conformance test data |
| TS 35.919 | Specification of the 3GPP Confidentiality and Integrity Algorithms UEA2 & UIA2; Document 5: Design and evaluation report |

SA3 agreed on the need to develop backup algorithms for UTRAN access confidentiality and integrity protection, the UEA2 and UIA2 to be. There are no current indications that the existing UMTS cipher and integrity protection algorithms (based on KASUMI) are in danger of being broken but cryptanalysis advances all the time. It seems sensible to have a second pair of algorithms developed and deployed in handsets, so that if KASUMI is ever broken, the alternative is ready to use. Of course the new algorithms needed to be fundamentally different from KASUMI, so that an attack on one algorithm is very unlikely to translate into an attack on the other.

The overall objectives were:

-	To develop new algorithms for confidentiality and integrity protection for UTRAN to be in place in mobile terminals should the existing KASUMI-based algorithms be broken in the future.

-	To enable operators to quickly and easily re-establish a high level of security by switching their networks to use the new algorithms

The following issues needed at least be handled in the WI:

-	Confirm GSMA policy and budget allocation to develop new algorithm

-	Agree requirement specification with ETSI SAGE for development of new algorithms

-	Liaise with GSMA for the commission from ETSI SAGE to develop the new algorithms

-	Delivery of algorithm specification, test data and design and evaluation reports

Public evaluation of the algorithm by independent experts is currently not included in the scope. It is SA3's responsibility, based on advice from SAGE, to determine whether public evaluation of the new algorithms is needed.

The algorithms were provided by SAGE and allocated TS numbers 35.215, 35.216, 35.217, 35.218, and TR number 35.919 for the Design and evaluation report. A public evaluation is in the process of being run.

### 4.11.4	Lawful Interception in the 3GPP Rel-7 architecture

Written by M. Clayton

Acronym:		LI-7A

UID_33026

Main Responsibility:	S3

References for "Lawful Interception in the 3GPP Rel-7 architecture "

| Document | Title/Contents |
| --- | --- |
| WID(s) |
| SP-050237 | Lawful Interception in the 3GPP Rel-7 architecture |
| Impacted Specifications |
| TS 33.106 | Lawful interception requirements |
| TS 33.107 | 3G security; Lawful interception architecture and functions |
| TS 33.108 | 3G security; Handover interface for Lawful Interception (LI) |
| New Dedicated Specifications/Reports |
| - | - |

The 3GPP Rel-7 architecture continues to develop IP-based Services, which need to be addressed by lawful interception.  SA WG3-LI will study advanced IMS services, Multimedia Broadcast and Multicast Services, Subscriber Certificates, and I-WLAN for possible lawful interception systems. This work item was provided to create a lawful interception specification for the latest Rel-7 architecture these.

The enhancements to specifications TS 33.106, TS 33.107 and  TS 33.108 addressed the additional work to specify the HI2 (Intercepted Related Information) and the HI3 (Content) interfaces for Packet Data and advanced IMS delivery to the Law Enforcement Monitoring Facilities for 3G networks for Release 7.

The 3G Packet Domain and phase 2 Multi Media Domain have been addressed in these specifications for Rel 6. In specification TS 33.107  I-WLAN first step has been addressed for Rel. 6.

HI1 (Administration) is not covered in this specification and is considered to be a matter of national regulation.

### 4.11.5	Access Security Enhancements

Written by M. Clayton

Acronym:		ACCSEC2

UID_33025

Main Responsibility:	S3

References for "Access Security  Enhancements "

| Document | Title/Contents |
| --- | --- |
| WID(s) |
| SP-040865 | WID for Access Security Enhancements |
| Impacted Specifications |
| TS 33.102 | 3G security; Security architecture |
| TS 43.020 | Security-related network functions |
| New Dedicated Specifications/Reports |
| - | - |

SA3 agreed that long-term security enhancements are needed to protect GERAN Access Network in the future. A deeper review of GERAN security weaknesses, in particular security dependencies between various uses of the GSM security context, and consideration of potential future attack scenarios is needed, to decide on suitable long-term enhancements of security for GERAN Access Network and other access types relying on GSM security context. Re-use of UMTS security context also needed to be taken into account.

The overall objectives were:

-	to complete a threat analysis and security requirements capture for GERAN Access Network.

-	to develop suitable, feasible and cost effective long-term security enhancements for GERAN (and possibly UTRAN) Access Network

-	to develop a cost-effective migration strategy for improving access security in 3GPP systems

## 4.12	One Tunnel solution for Optimisation of Packet Data Traffic

To be written by Maurice

Acronym:		OPTUNEL

UID_7046

Main Responsibility:	S2

References for "One Tunnel solution for Optimisation of Packet Data Traffic"

| Document | Title/Contents |
| --- | --- |
| WID(s) |
| GP-022566 | WID on XXX |
| Impacted Specifications |
| TS 24.008 | Example |
| New Dedicated Specifications/Reports |
| TS 22.146 | Example |

Your text: what does it offer? (Stage 1 summary) How does it impact the network? (Stages 2 and 3 summary). PLEASE DON’T JUST COPY-PASTE THE TEXT FROM THE WID BUT CHECK WHAT WAS ACTUALLY DONE!

Extract from the Work Plan (info for the writer only, to be deleted when providing actual text):

| 289 | 7046 | One Tunnel solution | 1 | S2 | OPTUNEL |  | SP-060142 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 290 | 320002 | Stage 2 Study for One Tunnel solution | 2 | S2 | OPTUNEL-Study | 23.8de |  |
| 291 | 320003 | Stage 2 specification for One Tunnel solution | 2 | S2 | OPTUNEL-Stage2 | 23.060 |  |

## 4.13	End-to-End Multimedia Services Performance Metrics (E2EMSPM)  UID_34036

Responsibility:	S4

References

| Document | Title/Contents |
| --- | --- |
| WID(s) |
| SP-050433 | WID on End-to-End Multimedia Services Performance Metrics |
| Impacted Specifications |
| - |  |
| New Dedicated Specifications/Reports |
| TR 26.944 | End-2-End Multimedia Services Performance Metrics |

The objective of this Work Item is to provide operators, service providers and device providers with a universal method and some systematic metrics to characterize the end-to-end performance of multimedia services, like PSS, MBMS, PSC, IMS, MMS.

This work item covers "Multimedia service performance evaluation methods", by using Subjective and

Objective methods.

Multimedia services are very important services in 3G networks. However, there isn’t any standard about how to characterize the performance of such services. This has the following consequences:

- To operators. When deploying 3G network to provide multimedia services, they don’t know how to evaluate the equipments of the various providers without standardized metrics and methods. Besides, they lack the necessary metrics to determine whether the multimedia services running on these equipments can meet the requirements of consumers.

- To device providers. They have to provide a set of performance data to operators in order to prove that their products can support multimedia services very well. Without standardized metrics, it is difficult to convince the operators.

- To consumers. They can’t be provided with clear quality requirements when subscribing multimedia services from operators.

With a standard about end-to-end multimedia services performance evaluation metrics, both operators and providers would know how to do when deploying multimedia service. At the same time, customers could enjoy the satisfying multimedia services as they required. All of these will promote the multimedia services deployment.

This work item focused on the end-to-end performance characterization and metrics for multimedia services. It avoids deploying multimedia services without satisfying effects or waste of network resources.

An example of systematic service performance metrics framework is given in the following figure :

| End-to-End Multimedia Service Metrics |
| --- |
| Methods | User Service Performance Indicators |
| Subjective & Objective | Setup delay, End-to-end delay, Re-buffering duration, Corruption duration, Mean time between corruption, Content quality (e.g. digital TV-like quality, analog TV-like quality, DSL-like video conferencing quality, ISDN-like video conferencing quality, etc.), Lip sync, Service availability (Initial availability and Dropped stream ratio) …… |
|  | QoE |
|  | Initial connection duration, Initial buffering duration, Video quality, Audio quality, Audio/video sync …… |
|  | QoS |
|  | Codec, system an transport aspects |
|  | Codec | Terminal Capabilities |
|  | Inter-frame (Temporal) | Intra-frame (Spatial) | CPU, Memory, Decoder…… |
|  | Freeze Frames, Dropped Frames, pDVD, average frame rate, quality variation over time…… | PSNR, Blurriness, Edge noise, Blocky level, Colourfulness…… |  |
|  | Transport Layer |
|  | Underlying networks aspects |
|  | Access | Transfer | …… |
|  | Access ratio…… | Delay, Jitter, BLER…… | …… |

The Technical Report 26.944 describes and defines performance metrics for use in multimedia services in 3G networks, including packed-switched streaming service (PSS), multimedia broadcast multicast service (MBMS), video telephony (VT), and IP multimedia subsystem service (IMS). The TR has a top-down approach, which starts with the quality of experience (QoE) parameters, and then provides the End-to-end Service QoS (ESQoS) and  System QoS (SQoS) parameters and mapping between these performance metrics for different layers. The TR defines the QoE, ESQoS and SQoS parameters for each of the relevant services.

The QoE parameters reflect  the end-to-end quality as experienced by the end user. These metrics can be reported by the end users.

The ESQoS parameters describe the QoS of the end-to-end service. They are obtained directly from the QoE parameters by mapping them into parameters more relevant to operators and service providers.

The SQoS parameters reflect the point-to-point QoS in system parts within networks. They are defined separately for each system part (client, radio access network, wireless transport network, wireline transport network, transaction node) and are identified for the different layers (e.g. application, transport). The SQoS parameters are the inherent attributes of the networks and are important in guaranteeing that the QoE requirements of the users are met.

The TR contains an annex (Annex A) on PSS performance analysis with theoretical models. Theoretical models are introduced to study the ESQoS and SQoS parameters. The inherent relationship between the ESQoS and SQoS parameters of PSS is described, and operational methods are provided for the operators/service providers to guarantee  service performance.

Comparison with TS 102 250 of ETSI STQ is contained in Annex C of the TR, that was developed taking into account also ITU-T work in the area of QoE and QoS.

## 4.14	ISIM API for Java Card

To be written by Xavier

Acronym:		APIJAVA

UID_743009

Main Responsibility:	C6

References for "ISIM API for Java Card "

| Document | Title/Contents |
| --- | --- |
| WID(s) |
| GP-022566 | WID on XXX |
| Impacted Specifications |
| TS 24.008 | Example |
| New Dedicated Specifications/Reports |
| TS 22.146 | Example |

Your text: what does it offer? (Stage 1 summary) How does it impact the network? (Stages 2 and 3 summary). PLEASE DON’T JUST COPY-PASTE THE TEXT FROM THE WID BUT CHECK WHAT WAS ACTUALLY DONE!

Extract from the Work Plan (info for the writer only, to be deleted when providing actual text):

| 251 | 743009 | ISIM API for Java Card | 1 | C6 | APIJAVA | 31.103, TS 102 241 | CP-050145 |
| --- | --- | --- | --- | --- | --- | --- | --- |

## 4.15	Network Composition

Written by M. Clayton

Acronym:		NetComp

UID_31089

Main Responsibility:	S1

References for "Network Composition "

| Document | Title/Contents |
| --- | --- |
| WID(s) |
| SP-060331 | WID on Network Composition |
| Impacted Specifications |
| - | - |
| New Dedicated Specifications/Reports |
| TR 22.980 | Feasibility Study for Network Composition |

This new study item builds on the work on AIPN and to adresses the concept of heterogeneous network/system integration and interworking in more detail. This “Network Composition"includes integration of networks with different administrative domains, and the dynamic and flexible integration of ad-hoc networks, PANs, sensor networks etc. The goal is to explore a uniform composition procedure independent of what kind of network is "composed"with the 3GPP system. Complementing the AIPN work a concrete dynamic “plug&play"and flexible composition procedure shall be studied.

The WI explores the feasibility of a uniform procedure for the integration of, and the interworking with, a large variety of heterogeneous network types. It focuses on ad-hoc networks, PANs, moving networks etc., but also includes access systems. The goal being to avoid the need for defining a new procedure for integration / interworking with each newly emerging network type and to explore the feasibility of making the composition procedure dynamic and to minimize human intervention ("plug and play"). 
This uniform procedure is called network composition.

**This WI is still in the early stages of development** [Alain]

## 4.16	Key establishment between a UICC and a terminal

To be written by Dionsio

Acronym:		KeyEstUTerm

UID_33028

Main Responsibility:	S3

References for "Key establishment between a UICC and a terminal"

| Document | Title/Contents |
| --- | --- |
| WID(s) |
| GP-022566 | WID on XXX |
| Impacted Specifications |
| TS 24.008 | Example |
| New Dedicated Specifications/Reports |
| TS 22.146 | Example |

Your text: what does it offer? (Stage 1 summary) How does it impact the network? (Stages 2 and 3 summary). PLEASE DON’T JUST COPY-PASTE THE TEXT FROM THE WID BUT CHECK WHAT WAS ACTUALLY DONE!

Extract from the Work Plan (info for the writer only, to be deleted when providing actual text):

| 260 | 33028 | Key establishment between a UICC and a terminal | 1 | S3 | KeyEstUTerm | 33.110 | SP-050780 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 261 | 50569 | Mobile Station Receive Diversity (DARP Phase II) | 1 | GP | MSRD2 | 24.008, 45.005, 51.010 | GP-061491 |
| 262 | 50570 | MS conformance test of DARP Phase II (MSRD) | 2 | GP | MSRD2-Msconf | 51.010 | GP-060114 |
| 263 | 50571 | Performance Requirements for Mobile Station Receive Diversity, DARP Phase II | 2 | GP | MSRD2-PerfReq | 45.005 | GP-060115 |
| 264 | 50572 | Capability signalling of Mobile Station Receive Diversity, DARP Phase II | 2 | GP | MSRD2-CapSig | 24.008 | GP-060116 |
| 265 | 50573 | Test Scenarios for Mobile Station Receive Diversity, DARP Phase II | 2 | GP | MSRD2-TestSc | 45.005 | GP-060117 |

## 4.17	Selective Disabling of UE Capabilities

Written by M. Clayton

Acronym:		SDoUE

UID_31053

Main Responsibility:	S1

References for "Selective Disabling of UE Capabilities "

| Document | Title/Contents |
| --- | --- |
| WID(s) |
| SP-050182 | Selective Disabling of UE Capabilities |
| CP-060181 | Support of Selective Disabling of UE Capabilities (SDoUE) |
| Impacted Specifications |
| TS 22.011 | Service accessibility |
| New Dedicated Specifications/Reports |
| TS 23.805 | Selective disabling of User Equipment (UE) capabilities; Report on technical options and conclusions |
| TS 24.305 | Selective Disabling of UE Capabilities (SDoUE) Management Object (MO) |

With increasing data usage and the drive towards increasing the ARPU per subscriber from increased data usage, the need for effective methods of dealing with the consequences of downloading and activating a virus in a mobile telephone needed to be addressed.

Similar problems may also arise with downloaded applications that are not functioning correctly and which could repeatedly make a connection request requiring both allocation of radio resources and network signalling processing. This can also be a substantial threat. The misbehaving application may be downloaded by the user through various means: e-mail, SMS and Push services, and (exceptionally) fail to be detected and disabled by application layer preventative measures. While operators may be able to maintain some degree of control this poses a significant threat to the industry at large. Similar problems may also arise with viruses.

This work item provides a means of disabling an infected device from registering again on the network, both in the current network and any other network, i.e. effectively quarantining the device. The WI also provides a means of maintaining the disabled status of the device, even if the mobile has been successively switched off and on.

The criteria for determining when an application is misbehaving are not included in the scope of this work item.

**** no changes yet have been made for this ******** [Alain]

## 4.18	Personal Network Management  (PNM)

Written by M. Clayton

Acronym:		PNPAN

UID_31081

Main Responsibility:	S1

References for "Personal Network Management  (PNM)"

| Document | Title/Contents |
| --- | --- |
| WID(s) |
| SP-050386 | WID on Personal Network Management (PNM) |
| Impacted Specifications |
| TS 24.008 | Example |
| New Dedicated Specifications/Reports |
| TS 22.259 | Service requirements for Personal Network Management (PNM); Stage 1 |

The purpose of this WI is to define a Personal Network and a Personal Area Network within the scope of AIPN.

A Personal Network (PN), in the context of Personal Network Management, consists of more than one Personal Network Element under the control of one user providing access to the serving PLMNs. There shall be at least one Personal Network Element with a USIM subscription in a PN. Authentication of the user for each PLMN access is based on the USIM(s) of the PN. The Personal Network Elements are managed in a way that the user perceives a continuous secure connection regardless of their relative locations. The Personal Network Elements belonging to the User’s PN maybe registered to different PLMNs at a time. The user controls the PN using facilities provided by the Personal Network Management (PNM).

A Personal Area Network (PAN) is a local network of the user.  In the context of Personal Network Management, the PAN consists of at least one UE and may additionally comprise a number of MEs/MTs, with own radio access means that allow them to directly access the PLMN of the UE. The UE and locally connected additional MEs/MTs are the PNEs of the PAN. Alternatively the UE components, i.e TEs and MT, may be handled as separate PNEs. The UE contains the single active USIM of the PAN.

The stage 1 for this feature is defined in 22.259.

**** as yet, nothing more can be said **** [Alain]

## 4.19	CSI Terminating Session handling

To be written by Maurice

Acronym:		CSItermS

UID_320029

Main Responsibility:	S2

References for "CSI Terminating Session handling "

| Document | Title/Contents |
| --- | --- |
| WID(s) |
| GP-022566 | WID on XXX |
| Impacted Specifications |
| TS 24.008 | Example |
| New Dedicated Specifications/Reports |
| TS 22.146 | Example |

Your text: what does it offer? (Stage 1 summary) How does it impact the network? (Stages 2 and 3 summary). PLEASE DON’T JUST COPY-PASTE THE TEXT FROM THE WID BUT CHECK WHAT WAS ACTUALLY DONE!

Extract from the Work Plan (info for the writer only, to be deleted when providing actual text):

| 307 | 320029 | CSI Terminating Session handling | 1 | S2 | CSItermS | 23.228, 23.279 | SP-060437 |
| --- | --- | --- | --- | --- | --- | --- | --- |

## 4.20	Interoperability between VGCS/VBS and A/Gb flexibility

Written by A. Brekalo

Acronym:		VGCSFlex

UID_7043

Main Responsibility:	C1

References for "Interoperability between VGCS/VBS and A/Gb flexibility "

| Document | Title/Contents |
| --- | --- |
| WID(s) |
| CP-060102 | Interoperability between VGCS/VBS and A/Gb flexibility |
| Impacted Specifications |
| TS 43.068 | Stage 2 description for VGCS-RANflex interoperability |
| TS 43.069 | Stage 2 description for VBS-RANflex interoperability |
| TS 29.002 | New MAP message between group call channel controlling MSC/VLR and serving MSC/VLR |
| New Dedicated Specifications/Reports |

3GPP SA WG2 identified that A/Gb flexibility (IuFlex) and VGCS/VBS do not interoperate and therefore should not be operated together in the same service area of a network. It was intended to get rid of this limitation and to achieve full interoperability between VGCS/VBS and A/Gb flexibility from Rel-7 onwards.

The objective was to specify stage 2 architecture and stage 3 protocol enhancements that are necessary for VGCS/VBS and A/Gb flexibility to be operated together in the same service area of a network.

A new MAP messages was also introdused between group call channel controlling MSC/VLR and serving MSC/VLR.

# 5	UTRAN Features

## 5.1	Multiple Input Multiple Output antennas (MIMO)  UID_2468

Responsibility:	RP

References

| Document | Title/Contents |
| --- | --- |
| WID(s) |
| RP-0300192 | WID on Multiple Input Multiple Output Antennas |
| Impacted Specifications |
| TS 25.211 | Physical channels and mapping of transport channels onto physical channels (FDD) |
| TS 25.212 | Multiplexing and channel coding (FDD) |
| TS 25.213 | Spreading and modulation (FDD) |
| TS 25.214 | Physical layer procedures (FDD) |
| TS 25.215 | Physical layer; Measurements (FDD) |
| TS 25.221 | Physical channels and mapping of transport channels onto physical channels (TDD) |
| New Dedicated Specifications/Reports |
| TR 25.876 | Multiple Input Multiple Output (MIMO) antennae in UTRA |
| TR 25.996 | Spatial channel model for Multiple Input Multiple Output (MIMO) simulations |

MIMO improves system capacity and spectral efficiency by increasing the data throughput in the downlink within the existing 5 MHz carrier. This is achieved by using multiple antennas at both UE and Node-B sides. The MIMO functionality was integrated in UTRA (FDD and TDD) to improve capacity and spectral efficiency.

RAN1 TR 25.876 contains the working assumptions and evaluation criteria of the different techniques considered for MIMO in UTRA.

The PARC scheme was selected for TDD and Dual-codeword MIMO based on D-TxAA was selected for FDD, with the weights being signalled on the HS-SCCH in the downlink.

Stage 3 focussed on UTRA FDD. TS 25.212 covers coding for HS-SCCH (Downlink) and HS-PDCCH (Uplink). TS 25.214 covers the definition of MIMO operation on HS-PDSCH.

Completed Sep 2007; Status Report in RP-070037and RP-070531.

## 5.2	Rel-7 Improvements of the Radio Interface (RInImp)  UID_20028

### 5.2.1	Extended UMTS 1.7/2.1 GHz  UID_20060

Responsibility:	R4

WRC 2000 identified additional spectrum for IMT-2000, including the band 1710-1885 MHz. 3GPP has specified three bands that include parts of this frequency range: Band III (UMTS 1800), Band IV (UMTS 1.7/2.1) and Band IX (UMTS 1700). It specifies the extended 1.7/2.1 GHz FDD system for potential deployment in ITU Region 2 only.

TR 25.806 (radio requirements for UTRA FDD in the Extended 1.7/2.1 GHz Band) defines as a new operating band:

- 1710 – 1770 MHz: Up-link (UE transmit, Node B receive);

- 2110 – 2170 MHz: Down-link (Node B transmit, UE receive).

This extended operating band contains the whole Band IV (1710-1755/2110-2155 MHz) as a sub-band. TR 25.806 investigates possible commonality between the new Extended 1.7/2.1 GHz band and Band IV radio requirements.

WID in RP-060180; affected specifications 25.806, 25.101, 25.104, 25.133, 24.141, 25.331, 25.306, 25.307, 25.423, 25.461, 25.463, 34.121

Completed Dec 2006; Status Report in RP-060681

### 5.2.2	UMTS 2.6 GHz 7.68 Mcps TDD  UID_20067

Responsibility:	R4

Harmonised spectrum scheme for IMT-2000/UMTS in the band 2500 - 2690 MHz as considered by CEPT/PT1:

- the frequency band 2500 – 2570 MHz is paired with 2620 – 2690 MHz for FDD operation with the mobile transmit within the lower band and base transmit within the upper band;

- Administrations may assign the frequency band 2570 – 2620 MHz either for TDD or for FDD downlink (external). Any guard bands required to ensure adjacent band compatibility at 2570 MHz and 2620 MHz boundaries to be decided on a national basis and taken within the band 2570 – 2620 MHz.

- Assigned blocks shall be in multiple of 5.0 MHz.

Within a previous work item (UMTS 2.6 GHz TDD), operation of the 3GPP TDD mode was specified for operation in the band 2570 – 2620 MHz.  This work covers the 3.84Mcps and 1.28Mcps TDD options.

During the UMTS 2.6 GHz TDD work item, work was also ongoing on a further work item to include the 7.68 Mcps TDD option.  This initially did not include operation in the 2.6 GHz band due to lack of completion of the UMTS 2.6 GHz TDD work item.

This work provides the necessary information for 2.6 GHz 7.68 Mcps TDD system operation, in particular for RAN4 to consider co-existence with IMT2000 technology within 2500 – 2690 MHz under the same constraints used for the UMTS 2.6 GHz TDD work item.

WID in RP-060349; affected specifications 25.102, 25.105, 25.123, 25.113, 25.142, 34.124

Completed Sep 2006; Status Report in RP-060451

### 5.2.3	UMTS 2.6 GHz  UID_20021

Responsibility:	R4

Work within CEPT/PT1 regarding the ECC Decision on harmonised utilization of spectrum for IMT-2000/UMTS systems operating within the band 2500 - 2690 MHz has progressed to the extent that 3GPP TSG RAN had sufficient information to commence work on specification for UMTS operating within the band 2500 - 2690 MHz.

The harmonised spectrum scheme for IMT-2000/UMTS in the band 2500 - 2690 MHz as considered by CEPT/PT1 is:

- The frequency band 2500 – 2570 MHz is paired with 2620 – 2690 MHz for FDD operation with the mobile transmit within the lower band and base transmit within the upper band.

- Administrations may assign the frequency band 2570 – 2620 MHz either for TDD or for FDD downlink (external). Any guard bands required to ensure adjacent band compatibility at 2570 MHz and 2620 MHz boundaries will be decided on a national basis and taken within the band 2570 – 2620 MHz.

- Assigned blocks shall be in multiple of 5.0 MHz.

This work provides the necessary information of 2.6 GHz FDD system:

- Generate a report summarizing a study of radio requirements UTRA FDD in the 2.6 GHz Band:

    - 2500 – 2570 MHz: Up-link (UE transmit, Node B receive)

    - 2620 – 2690 MHz: Down-link (Node B transmit, UE receive)

- The co-existence with IMT2000 technology within 2500 – 2690 MHz shall be considered.

WID in RP-040397; affected specifications 25.101, 25.104, 25.133, 25.141, 25.331, 25.942, 25.306, 25.307, 34.121

Completed Jun 2005, Status Report in RP-050184

### 5.2.4	UMTS 2.6 GHz TDD  UID_20025

Responsibility:	R4

Work within CEPT/PT1 regarding the ECC Decision on harmonised utilization of spectrum for IMT-2000/UMTS systems operating within the band 2500 - 2690 MHz has progressed to the extent that 3GPP TSG RAN had sufficient information to commence work on specification for UMTS operating within the band 2500 - 2690 MHz.

The harmonised spectrum scheme for IMT-2000/UMTS in the band 2500 - 2690 MHz as considered by CEPT/PT1 is:

- The frequency band 2500 – 2570 MHz is paired with 2620 – 2690 MHz for FDD operation with the mobile transmit within the lower band and base transmit within the upper band.

- Administrations may assign the frequency band 2570 – 2620 MHz either for TDD or for FDD downlink (external). Any guard bands required to ensure adjacent band compatibility at 2570 MHz and 2620 MHz boundaries to be decided on a national basis and taken within the band 2570 – 2620 MHz.

- Assigned blocks shall be in multiple of 5.0 MHz.

This work provides the necessary information for 2.6 GHz TDD, i.e. a report summarizing a study of radio requirements for UTRA TDD in the 2.6 GHz Band (2570 - 2620 MHz TDD ). The co-existence with IMT2000 technology within 2500 – 2690 MHz shall be considered.

WID in RP-040553; affected specifications 25.102, 25.105, 25.113, 25.123, 25.142, 25.331, 25.942, 25.306, 25.307, 34.122, 34.124

Completed Dec 2005, Status Report in RP-050661

### 5.2.5	UMTS 900 MHz  UID_20027

Responsibility:	R4

RAN4 performed the necessary work to allow the introduction of UMTS in the 900 MHz, produce the necessary UMTS900 specifications and check the current RF Scenarios against the requirements in the band:

- 880 – 915 MHz: Up-link (UE transmit, Node B receive)

- 925 – 960 MHz: Down-link (Node B transmit, UE receive)

RAN 4 evaluated the BS and UE minimum RF performance requirements necessary to ensure the good co-existence of GSM and UMTS in the 900 MHz band in practical deployment scenarios.

WID in RP-040541; affected specifications 25.101, 25.104, 25.113, 25.133, 25.141, 25.331, 25.942, 25.306, 25.307, 34.121

Completed Dec 2005, Status Report in RP-050662

### 5.2.6	UMTS 1700 MHz  UID_20043

Responsibility:	R4

This work evaluates UMTS 1700 for potential deployment in Japan in:

- 1749.9 – 1784.9 MHz: Up-link (UE transmit, Node B receive)

- 1844.9 – 1879.9 MHz: Down-link (Node B transmit, UE receive)

It studied co-existence with ARIB STD-28 (PHS), taking the frequency reframing plan in Japan into account.

WID in RP-050385; affected specifications 25.101, 25.104, 25.113, 25.133, 25.141, 25.306, 25.307, 25.331, 34.121

Completed Dec 2005; Status Report in RP-050824

### 5.2.7	UE Antenna Performance Evaluation Method and Requirements  UID_20024

Responsibility:	R4

UE antenna performance has critical impact on both system performance (throughput) and coverage. In order to ensure a certain level of coverage and QoS for the user, minimal requirements for UE antenna performance are needed. 
For the speech mode (UE close to head) it:

- introduces a method for UE antenna performance evaluation;

- defines UE antenna minimal performance requirements.

WID in RP-050122; affected specifications 25.101, 25.963

Completed May 2007; Status Report in RP-070281.

### 5.2.8	Improved Performance Requirements for HSDPA UE based on Rx Diversity (Type 1) & LMMSE equalizer (Type 2)  UID_20045

Responsibility:	R4

To further increase attractiveness and performance of the higher code capability UE classes, further improvements for HSDPA performance requirements for 10 code UEs (i.e. for categories 7 and 8) were introduced above the Rel-6 improvements based on reference receiver LMMSE chip-level equalizer and a reference receiver with receive diversity.

It provides the benefits of Rx diversity for all (Ior/Ioc) geometries while the LMMSE augments the benefits of Rx diversity when effectively operating at the higher (Ior/Ioc) geometries. The combined reference receiver can be based on the receiver structures that were used for defining HSDPA performance improvements in Rel-6 (Type 1 and Type 2 performance improvements). No specific implementation solution is mandated by the performance requirements.

WID in RP-050362; affected specifications 25.101

Completed Mar 2006, Status Report in RP-060015

### 5.2.9	Additional minimum UE performance requirement for non-HSDPA channels based on Type 1 enhanced receiver (Rx Diversity)  UID_20062

Responsibility:	R4

Improved performance requirements have been included in TS 25.101 for HSDPA on the basis of enhanced receivers of Type 1 and 2 (Rx diversity and LMMSE). The performance benefits of Rx diversity are potentially large for non-HSDPA transport channels as well, and it is expected that diversity receivers for HSDPA can also readily operate with diversity for non-HSDPA channels.  This would enable potential gains from diversity to be utilized for services such as circuit-switched voice and MBMS.

The proposed performance requirements would enable verification that such receivers do achieve expected improved performance with non-HSDPA channels. A subset of the current non-HSDPA receiver performance requirements would need to be improved to ensure the main expected benefits.

It defines optional performance requirements for enhanced receivers Type 1, for selected key non-HSDPA transport channels using receiver diversity as the baseline receiver. However, no specific implementation solution is mandated by the performance requirements. No specific UE implementation is mandated by these enhanced HSDPA requirements.

Additional minimum UE performance requirement for DL physical channels in support of DCH/HS-DSCH operation based on Type 1 enhanced receiver (RX-Diversity)

Improved performance requirements have been included in TS 25.101 for HSDPA on the basis of enhanced receivers of Type 1 and 2 (RX diversity and LMMSE). The performance benefits of RX diversity are potentially large for non-HSDPA transport channels as well, and it is expected that diversity receivers for HSDPA can also readily operate with diversity for non-HSDPA channels.  This would enable potential gains from diversity to be utilized for services such as circuit-switched voice and MBMS.

The proposed performance requirements would enable verification that such receivers do achieve expected improved performance with non-HSDPA channels. A subset of the current non-HSDPA receiver performance requirements would need to be improved to ensure the main expected benefits.

It defines optional performance requirements for enhanced receivers Type 1, for selected key non-HSDPA transport channels using receiver diversity as the baseline receiver. However, no specific implementation solution is mandated by the performance requirements.

WID in RP-060185; affected specifications 25.101

Completed Jun 2006, Status Report in RP-060235

Additional minimum UE performance requirement for downlink physical channels in support of MTCH and MCCH operation based on Type 1 enhanced receiver (Rx-Diversity)

Minimum UE performance requirements based on Type 1 receiver have been defined for downlink physical channels related to Release-5 HS-DSCH operation (HS-PDSCH, HS-SCCH); minimum UE performance requirements based on Type 1 receiver have not been defined for other physical channels. Yet, UE supporting Type 1 receiver for HS-DSCH operation could also use the Type 1 receiver capability to improve the demodulation performance for other downlink physical channel. It defines new optional minimum UE performance requirements based on Type 1 receiver for the MICH and S-CCPCH considering MTCH and MCCH operation. No specific implementation solution is mandated by the performance requirements.

WID in RP-060183; affected specifications 25.101

Completed Dec 2006, Status Report in RP-060678

Additional minimum UE performance requirement for downlink physical channels in support of E-DCH operation based on Type 1 enhanced receiver (Rx-Diversity)

Minimum UE performance requirements based on Type 1 receiver have been defined for downlink physical channels related to Release-5 HS-DSCH operation (HS-PDSCH, HS-SCCH). Minimum UE performance requirements based on Type 1 receiver have not been defined for other physical channels. Yet, UE supporting Type 1 receiver for HS-DSCH operation could also use the Type 1 receiver capability to improve the demodulation performance for other downlink physical channels. It defines new optional minimum UE performance requirements based on Type 1 receiver for the 
E-RGCH, E-AGCH and E-HICH. No specific implementation solution is mandated by the performance requirements.

WID in RP-060184; affected specifications 25.101

Completed Dec 2006, Status Report in RP-060679

## 5.3	RAN improvements (RANimp)  UID_20029

### 5.3.1	Optimization of channelization code utilization for 1.28 Mcps TDD  UID_20026

Responsibility:	R1

References

| Document | Title/Contents |
| --- | --- |
| WID(s) |
| RP-040552 | WID on Optimization of channelization code utilization 1.28 Mcps TDD |
| Impacted Specifications |
| TS 25.221 | Physical channels and mapping of transport channels onto physical channels (TDD) |
| TS 25.222 | Multiplexing and channel coding (TDD) |
| TS 25.224 | Physical layer procedures (TDD) |
| TS 25.331 | Radio Resource Control (RRC); Protocol specification |
| TS 25.423 | UTRAN Iur interface Radio Network Subsystem Application Part (RNSAP) signalling |
| TS 25.430 | UTRAN Iub Interface: general aspects and principles |
| TS 25.433 | UTRAN Iub interface Node B Application Part (NBAP) signalling |
| TS 25.1xx |  |
| New Dedicated Specifications/Reports |
| No | No |

Code utilization is an important element for the uplink and downlink efficiency of UTRA-TDD cells. Several features require a UE specific code for a dedicated channel, such as HSDPA which requires an associated DPCH, IMS with infrequent RTCP packets and full headers which have to be sent with low delay.

HSDPA transmissions also require channelization codes and so efficient code utilization of dedicated channels also improves HSDPA performance. For TDD code resources are limited on both uplink and downlink.  Efficient utilization and careful management of both downlink and uplink code resources is desirable.

It allows a better utilization of codes for dedicated channels. This applies to the downlink and uplink for TDD.

A new physical channel PLCCH (Physical Layer Common Control Channel) was introduced to efficiently carry SS/TPC signalling to multiple users, thus removing the need for the associated DL DPCH in the case that no higher layer data is mapped to it.  This enables code resources to be released which may be re-used by other DL channels. 
The new channel was intoroduced in TS 25.221, 25.222 and 25.224. Also, the corresponding changes to layer 2 and 3 apects, and Iub/Iur protocol aspects were intorduced.

Completed Dec 2006; Status Report in RP-060682

### 5.3.2	Delay optimisation for procedures applicable to CS and PS Connections  UID_20031

Responsibility:	R2

References

| Document | Title/Contents |
| --- | --- |
| WID(s) |
| RP-050386 | WID on Delay optimisation for procedures applicable to CS and PS Connections |
| Impacted Specifications |
| TS 25.321 | Medium Access Control (MAC) protocol specification |
| TS 25.322 | Radio Link Control (RLC) protocol specification |
| TS 25.331 | Packet Data Convergence Protocol (PDCP) specification |
| New Dedicated Specifications/Reports |
| TR 25.815 | Signalling enhancements for Circuit-Switched (CS) and Packet-Switched (PS) connections; Analyses and recommendations |

In a modern telecommunication network such as UMTS, the aim of the operator is to offer high Quality of Service (QoS) to users.  The QoS is the collective effect of service performances, which determine the degree of satisfaction of a user of a service.

Under the general heading of quality of experience (QoE) one of the more noticeable points faced by the user is the apparent delay in set up or channel allocation times for different connections. The set up and channel allocation delay can be defined as the time interval from the instant the user initiate a connection request until the complete message indicating call disposition is received by the calling terminal or the by application server. When establishing a connection the user, due to this delay, may think that the connection has not gone through or the network is not responding which may prompt the user to re-dial, reconnect or even in some cases to abandon the connection attempt. From the service provider’s perspective improving the quality of service is very important giving their users a good perception of the network performance and efficiency.

This work investigates mechanisms to improve the connection establishment times. The delay in set up or channel allocation times can be attributed to:

- Processing time in the UTRAN

- Processing time in the Core network

- Processing time in UE

- Call setup and alerting phase in the core network

- UTRAN and CN Protocols and associated overhead including protocol conversion

- Signalling delay on the air interface

- Signalling delay on UTRAN interfaces and towards CN

- NAS procedures

The objectives are:

- To review the CS and PS Call and session Setup and channel allocation procedures in UMTS

- To highlight the improvements where call and session setup process can be improved and consider impacts the relevant specifications

- To highlight the improvements to the existing RRC state transitions

- To identify possible ways to enhance call and session setup performance whilst keeping in mind R99 backwards compatibility

- To put forward change request relevant to specifications

- To focus on the reduction of delay caused by RAN related aspects

- To review performance requirements for e.g. RRC procedures

- To review network RRM strategies

TR 25.815 proposes enhancements and changes to existing specifications (TS 25.321, 25.322, 25.331). 
Priorities were given to decrease the latency caused by the various factors. 
Solutions with limited impact on the UE development were preferred in order to ensure a fast delivery.

Completed Sep 2006; Status Report in RP-060453

### 5.3.3	UE Performance Requirements for MBMS (TDD)  UID_20033

Responsibility:	R4

References

| Document | Title/Contents |
| --- | --- |
| WID(s) |
| RP-050156 | WID on UE Performance Requirements for MBMS (TDD) |
| Impacted Specifications |
| TS 25.102 | User Equipment (UE) radio transmission and reception (TDD) |
| TS 25.123 | Requirements for support of radio resource management (TDD) |
| New Dedicated Specifications/Reports |
| None | - |

In order to facilitate the deployment MBMS, it is essential to ensure that MBMS capable UES are supporting a minimum level of performance in terms of P2M radio link reception.

It defines performance requirements for the support of the MBMS feature in the UE. It defines performance requirements for the support of MBMS P2M radio links and MICH by the UE.  Performance requirements take into account the potential impacts of interruptions (e.g. measurements) (inter-RAT and/or inter-frequency). 
Results of SA4 on MBMS were considered.

Completed Sep 2006; Status Report in RP-060477

### 5.3.4	Continuous connectivity for packet data users  UID_20046

Responsibility:	R1

References

| Document | Title/Contents |
| --- | --- |
| WID(s) |
| RP-050870 | WID on Continuous connectivity for packet data users |
| Impacted Specifications |
| TS 25.201 | Physical layer - general description |
| TS 25.211 | Physical channels and mapping of transport channels onto physical channels (FDD) |
| TS 25.212 | Multiplexing and channel coding (FDD) |
| TS 25.214 | Physical layer procedures (FDD) |
| TS 25.308 | High Speed Downlink Packet Access (HSDPA); Overall description; Stage 2 |
| TS 25.321 | Medium Access Control (MAC) protocol specification |
| TS 25.331 | Radio Resource Control (RRC); Protocol specification |
| TS 25.423 | UTRAN Iur interface Radio Network Subsystem Application Part (RNSAP) signalling |
| TS 25.433 | UTRAN Iub interface Node B Application Part (NBAP) signalling |
| TS 25.101 | User Equipment (UE) radio transmission and reception (FDD) |
| TS 25.133 | Requirements for support of radio resource management (FDD) |
| New Dedicated Specifications/Reports |
| TR 25.903 | Continuous connectivity for packet data users |

Packet-oriented features like HSDPA and E-DCH in WCDMA/UMTS systems will promote the subscribers’ desire for continuous connectivity, where the user stays connected over a long time span with only occasional active periods of data transmission, and avoiding frequent connection termination and re-establishment with its inherent overhead and delay.

To support a high number of HSDPA users in the code limited downlink the feature F-DPCH was introduced in Rel-6. In the uplink, the limiting factor for supporting a similarly high number of E-DCH users is the noise rise. For such a high number of users in the cell it can be assumed that many users are not transmitting any user data for some time (e.g. for reading during web browsing or in between packets for periodic packet transmission such as VoIP). 
The corresponding overhead in the noise rise caused by maintained control channels will significantly limit the number of users that can be efficiently supported. As completely releasing dedicated channels during periods of temporary traffic inactivity would cause considerable delays for re-establishing data transmission and a corresponding bad user perception, it is intended to reduce the impact of control channels while maintaining the DCH state and allowing a much faster reactivation for temporarily inactive users.

The objective is to reduce the overhead of physical control channels or related signalling messages of packet data users for both real-time (e.g. VoIP) and non real-time services, e.g.  for users which have temporarily no data transmission in either uplink or downlink. Packet data users as considered here are using only HS-DSCH/E-DCH channels without UL DPDCH and DL DPCH. Focus is on the uplink, but reduction of overhead in downlink is considered as well.

As for physical layer aspects for Continuous Packet Connectivity (CPC) feature, two features were introduced, one is HS-SCCH less operation and the other is DTX/DRX at the UE. To support these features, new slot format of HS-SCCH (type 2) were introduced to be used for:

- HS-SCCH less operation: CRC type 2 for HS-PDSCH and HS-SCCH format for retransmissions added.

- HS-SCCH orders: L1 command to activate/deactivate DTX and/or DRX at the UE.

Completed at Mar 2007; Status Report in RP-070033

### 5.3.5	Extended WCDMA Cell Range  UID_7030

Responsibility:	R3

References

| Document | Title/Contents |
| --- | --- |
| WID(s) |
| RP-060212 | WID on Extended WCDMA Cell Range |
| Impacted Specifications |
| TS 25.133 | Requirements for support of radio resource management (FDD) |
| TS 25.331 | Radio Resource Control (RRC) protocol specification |
| TS 25.423 | UTRAN Iur interface Radio Network Subsystem Application Part (RNSAP) signalling |
| TS 25.425 | UTRAN Iur interface user plane protocols for Common Transport Channel data streams |
| TS 25.433 | UTRAN Iub interface Node B Application Part (NBAP) signalling |
| TS 25.435 | UTRAN Iub interface user plane protocols for Common Transport Channel data streams |
| TS 25.453 | UTRAN Iupc interface Positioning Calculation Application Part (PCAP) signalling |
| New Dedicated Specifications/Reports |
| None | - |

Before Re-7, signalling in the UTRAN protocols did not allow cell ranges higher than around 60 km. The range that could be reported for PRACH propagation delay was around 60 km and the range for Round Trip Time (RTT) measurements in the Node B was around 68 km. As scenarios were identified which require larger WCDMA cell sizes, it was decided to remove these restrictions in Rel-7 and to allow extended WCDMA cell ranges as exist today in GSM (120 km for extended range GSM cells).

Extended WCDMA Cell Range works with legacy terminals, no new requirements for the UE were added. However, UTRAN performance requirements for PRACH propagation delay and RTT measurements in the extended reporting ranges were specified.

The accuracy requirements for extended RTT and PRACH propagation delay were kept the same as before, i.e. ( 0.5 chip and 2 chips respectively. These two values are specified for cell ranges up to 180 km while the signalling allows cell sizes up to 240 km.

On the Iub interface a new Extended Propagation Delay IE was introduced which optionally complements the previously existing Propagation Delay IE, in the RADIO LINK SETUP REQUEST, RADIO LINK ACTIVATION and UPLINK SIGNALLING TRANSFER messages. For Protocol Compatibility, whenever Extended Propagation Delay IE is present, the Propagation Delay IE shall be set to its maximum value to provide best approximate value for legacy systems. The range of the new Extended Propagation Delay IE is selected to allow for cell radius of at least 180 km and this requires 10bits in the CCH RACH frame protocol. The introduced range 0.3069 chips corresponds to 240 km.

The new Extended Round Trip Time IE is a new choice when reporting measurements, by messages DEDICATED MEASUREMENT INITIATION RESPONSE and DEDICATED MEASUREMENT REPORT.

Completed Dec 2006; Status Report in RP-060685

### 5.3.6	7.68 Mcps TDD Enhanced Uplink  UID_7031

Responsibility:	R1

References

| Document | Title/Contents |
| --- | --- |
| WID(s) |
| RP-060119 | WID on 7.68 Mcps TDD Enhanced Uplink |
| Impacted Specifications |
| TS 25.201 | Physical layer - general description |
| TS 25.202 | 7.68Mcps Time Division Duplex (TDD) option ; Overall description: Stage 2 |
| TS 25.221 | Physical channels and mapping of transport channels onto physical channels (TDD) |
| TS 25.222 | Multiplexing and channel coding (TDD) |
| TS 25.223 | Spreading and modulation (TDD) |
| TS 25.224 | Physical layer procedures (TDD) |
| TS 25.225 | Physical layer; Measurements (TDD) |
| TS 25.302 | Services provided by the physical layer |
| TS 25.306 | UE Radio Access capabilities |
| TS 25.319 | Enhanced uplink; Overall description; Stage 2 |
| TS 25.321 | Medium Access Control (MAC) protocol specification |
| TS 25.331 | Radio Resource Control (RRC); Protocol specification |
| TS 25.401 | UTRAN overall description |
| TS 25.420 | UTRAN Iur interface general aspects and principles |
| TS 25.423 | UTRAN Iur interface Radio Network Subsystem Application Part (RNSAP) signalling |
| TS 25.427 | UTRAN Iur/Iub interface user plane protocol for DCH data streams |
| TS 25.430 | UTRAN Iub Interface: general aspects and principles |
| TS 25.433 | UTRAN Iub interface Node B Application Part (NBAP) signalling |
| TR 25.902 | Iub/Iur congestion control |
| TR 25.931 | UTRAN functions, examples on signalling procedures |
| TS 25.102 | User Equipment (UE) radio transmission and reception (TDD)" |
| TS 25.105 | Base Station (BS) radio transmission and reception (TDD) |
| TS 25.142 | Base Station (BS) conformance testing (TDD) |
| New Dedicated Specifications/Reports |
| None | - |

As features available with the 7.68 Mcps TDD option are limited to those provided by Rel-6, the Enhanced Uplink feature or HSUPA is also required for the 7.68 Mcps TDD option. This is expected to provide the natural uplink complement to 7.68Mcps HSDPA and also to provide double the peak uplink user data rate with respect to 3.84 Mcps TDD.

Procedures for 3.84Mcps E-DCH can be almost entirely reused at 7.68Mcps.  The only substantive changes identified are that the channelization code hopping sequences would need to be extended to accommodate SF32 and that the SF-dependent power gain factors would need to be amended to accommodate SF32.

Completed Dec 2006; Status Report in RP-060684

### 5.3.7	Enhanced CELL_FACH State in FDD  UID_330009

Responsibility: R2

References

| Document | Title/Contents |
| --- | --- |
| WID(s) |
| RP-070245 | WID on Enhanced CELL_FACH State in FDD |
| Impacted Specifications |
| TR 25.815 | Signalling enhancements for Circuit-Switched (CS) and Packet-Switched (PS) Connections; Analyses and recommendations |
| TS 25.211 | Physical channels and mapping of transport channels onto physical channels (FDD) |
| TS 25.304 | User Equipment (UE) procedures in idle mode and procedures for cell reselection in connected mode |
| TS 25.306 | UE Radio Access capabilities |
| TS 25.308 | High Speed Downlink Packet Access (HSDPA); Overall description; Stage 2 |
| TS 25.321 | Medium Access Control (MAC) protocol specification |
| TS 25.331 | Radio Resource Control (RRC); Protocol specification |
| TS 25.423 | UTRAN Iur interface Radio Network Subsystem Application Part (RNSAP) signalling |
| TS 25.423 | UTRAN Iur interface Radio Network Subsystem Application(RNSAP) signalling |
| TS 25.425 | UTRAN Iur interface user plane protocols for Common Transport Channel data streams |
| TS 25.433 | UTRAN Iub interface Node B Application Part (NBAP) signalling |
| TS 25.435 | UTRAN Iub interface user plane protocols for Common Transport Channel data streams |
| New Dedicated Specifications/Reports |
| None | - |

This builds upon the enhancements done by the Work Item UID_340039 (Improved L2 support for high data rates) due to common Layer 2 architecture.

It improves (i.e. reduces) the delay in setup and channel allocation, for CS and PS. This is achieved by applying HSDPA (HS-DSCH channels) to Signalling Radio Bearers (SRBs) (without re-use of uplink feedback and specific physical channel DP-CCH, e.g. without closed loop power control).

Other gains provided:

- Possibility to increase available downlink peak rates in all states other than Cell_DCH (i.e. idle, Cell_FACH, Cell-PCH, URA_PCH States);

- Reduce state transitions delays, from all States towards the Cell_DCH State.

As a consequence, this also allows mobiles to remain in the Cell_FACH state longer (i.e. without transiting to "more dedicated" states), and hence allows power consumption saving.

In a modern telecommunication network such as UMTS, the aim of the operator is to offer high Quality of Service (QoS) to users. The QoS is the collective effect of service performances, which determine the degree of satisfaction of a user of a service.

Under the general heading of quality of experience (QoE) one of the more noticeable points faced by the user is the apparent delay in set up or channel allocation times for different connections including response times of different PS data connections.

TR 25.815 shows that setup delays on PS and also CS domain can significantly be reduced by using HSPA for SRBs. The target is to reduce UTRAN latencies and concentrate on how the HSPA resources can be activated for the UE in the most efficient manner.

In addition, the work considered how the data rates available in CELL_FACH can be increased to reduce signalling latencies as well as address the cases where the usage of CELL_DCH state is not preferred by the network. This could be due to high interest on "always on" type services like PoC, Push email and VPN connections, which introduce frequent but small packets to be transmitted between UE and server.

In light of continuous progress to packet optimised radio together with Node B based scheduling, the use of HSDPA in CELL_FACH state was investigated to obtain smaller signalling delays and higher bit rate in CELL_FACH state.

This work provides the necessary modifications to Rel-7 improving the CELL_FACH state by:

- Increasing the available peak rate for UEs in CELL_FACH state, e.g. by utilising HSDPA in CELL_FACH state.

- Reducing the latency of user and control plane in the CELL_FACH, CELL_PCH and URA_PCH state by higher data peak rate

- Reducing state transition delay from CELL_FACH, CELL_PCH and URA_PCH state to CELL_DCH state

- Allowing lower UE power consumption in CELL_FACH state by discontinuous reception

In addition, this work considered the enhancements provided by Continuous Packet Connectivity (CPC), to achieve best suited solutions in the areas they may overlap.

Completed May 2007; Status Report in RP-070286

### 5.3.8	64QAM for HSDPA (FDD)  UID_340038

Responsibility: R1

References

| Document | Title/Contents |
| --- | --- |
| WID(s) |
| RP-070223 | WID on 64QAM for HSDPA (FDD) |
| Impacted Specifications |
| TS 25.308 | UE Radio Access capabilities |
| TS 25.211 | Physical channels and mapping of transport channels onto physical channels (FDD) |
| TS 25.212 | Multiplexing and channel coding (FDD) |
| TS 25.213 | Spreading and modulation (FDD) |
| TS 25.306 | UE Radio Access capabilities |
| TS 25.331 | Radio Resource Control (RRC); Protocol specification |
| TS 25.433 | UTRAN Iub interface Node B Application Part (NBAP) signalling |
| TS 25.435 | UTRAN Iub interface user plane protocols for Common Transport Channel data streams |
| TS 25.423 | UTRAN Iur interface Radio Network Subsystem Application Part (RNSAP) signalling |
| TS 25.425 | UTRAN Iur interface user plane protocols for Common Transport Channel data streams |
| TS 25.101 | User Equipment (UE) radio transmission and reception (FDD |
| TS 25.104 | Base Station (BS) radio transmission and reception (FDD) |
| TS 25.141 | Base Station (BS) conformance testing (FDD) |
| New Dedicated Specifications/Reports |
| None | - |

The use of 64QAM in the downlink is an attractive complement to multi-antenna techniques (MIMO) in the downlink, e.g. in scenarios where deployment of MIMO is not possible.

Significant gains were observed by the provision of 64QAM in scenarios (cells with isolation) where users can benefit in terms of increased throughput from favourable radio conditions such as in well tuned outdoor systems or indoor system solutions.

It adds 64QAM support as a downlink modulation scheme for HSDPA in FDD for Type II/III UEs.

Completed May 2007; Status Report in RP-070287

### 5.3.9	Improved L2 support for high data rates  UID_340039

Responsibility: R2

References

| Document | Title/Contents |
| --- | --- |
| WID(s) |
| RP-070242 | WID on Improved L2 support for high data rates |
| Impacted Specifications |
| TS 25.301 | Radio interface protocol architecture |
| TS 25.308 | High Speed Downlink Packet Access (HSDPA); Overall description |
| TS 25.306 | UE Radio Access capabilities |
| TS 25.321 | Medium Access Control (MAC) protocol specification |
| TS 25.322 | Radio Link Control (RLC) protocol specification |
| TS 25.331 | Radio Resource Control (RRC); Protocol specification |
| TS 25.433 | UTRAN Iub interface Node B Application Part (NBAP) signalling |
| TS 25.435 | UTRAN Iub interface user plane protocols for Common Transport Channel data streams |
| TS 25.423 | UTRAN Iur interface Radio Network Subsystem Application Part (RNSAP) signalling |
| TS 25.425 | UTRAN Iur interface user plane protocols for Common Transport Channel data streams |
| TR 25.999 | High Speed Packet Access (HSPA) evolution; Frequency Division Duplex (FDD) |
| New Dedicated Specifications/Reports |
| None | - |

This Work Item is in fact a baseline feature for other Work Items such as MIMO, 64QAM for HSDPA (FDD) and Enhanced CELL_FACH state in FDD. It is itself built upon HSDPA (use of the HS-DSCH channels).

It optimizes the Radio Link Control (RLC) layer, in order to support higher data rates. This is achieved through flexible RLC sizes, Medium Access Control (MAC) segmentation, and the multiplexing of different priority schemes (direct multiplexing of logical channels in the MAC header) in the downlink.

The reason was that the RLC peak data rate was limited by the RLC Packet Data Unit (PDU) size, the round trip time (RTT) and the RLC window size (creating a situation where under some scenarios the RLC protocol was the bottleneck of the system).

The introduction of MIMO significantly increases the data rates of the HSDPA and other improvements, such as higher order modulation targeted for HSPA evolution to further increase the DL data rates.

It is known from the work on HSDPA that the RLC peak data rate is limited by the RLC PDU size, the RTT and the RLC window size. For reasonable RLC PDU sizes, such as 320 or 640 bit, the RLC protocol can not sustain the current peak data rate of the physical layer in HS-DSCH. For increased data rates achieved by MIMO and other improvements, it is likely that the limitations of the RLC are even more pronounced, leading to a situation, in which the RLC protocol is the bottleneck of the system. Therefore, in TR 25.999 it is proposed to introduce support for flexible RLC PDU sizes and MAC segmentation in downlink in order to reach high data rates and reduce protocol overhead and padding.

As changes to the link layer protocols are already needed for the introduction of the MIMO, it would be beneficial to incorporate future-proof solutions already in Rel-7 to support high data rates in the link layer protocols.

In order to facilitate easy deployment of the enhanced protocols, as well as backward compatibility, the methods to enhance transition between old and new PDU formats had been evaluated.

It provides the necessary modifications in order to:

- Allow link layer support for high data rates in downlink by introducing support for flexible RLC PDU sizes, MAC-hs multiplexing and segmentation;

- Provide a single L2 protocol evolution for all performance enhancements;

- Evaluate the necessity to support MAC-d multiplexing and RLC concatenation;

- Allow smooth transition between old and new protocol formats.

The link layer support for high data rates in the uplink may be provided in the future.

Completed May 2007; Status Report in RP-070289

### 5.3.10	Introduction of 16QAM in HSUPA (FDD)  UID_340040

Responsibility: R2

References

| Document | Title/Contents |
| --- | --- |
| WID(s) |
| RP-060844 | WID on Introduction of 16QAM in HSUPA (FDD) |
| Impacted Specifications |
| TS 25.319 | Enhanced uplink; Overall description; Stage 2 |
| TS 25.101 | User Equipment (UE) radio transmission and reception (FDD) |
| TS 25.104 | Base Station (BS) radio transmission and reception (FDD) |
| TS 25.133 | Requirements for support of radio resource management (FDD) |
| TS 25.141 | Base Station (BS) conformance testing (FDD) |
| TS 25.211 | Physical channels and mapping of transport channels onto physical channels (FDD) |
| TS 25.212 | Multiplexing and channel coding (FDD) |
| TS 25.213 | Spreading and modulation (FDD) |
| TS 25.214 | Physical layer procedures (FDD) |
| TS 25.306 | UE Radio Access capabilities |
| TS 25.321 | Medium Access Control (MAC) protocol specification |
| TS 25.331 | Radio Resource Control (RRC); Protocol specification |
| TS 25.423 | UTRAN Iur interface Radio Network Subsystem Application Part (RNSAP) signalling |
| TS 25.433 | UTRAN Iub interface Node B Application Part (NBAP) signalling |
| New Dedicated Specifications/Reports |
| None | - |

With the introduction of MIMO or 64QAM in the downlink, higher data rates can be provided for users in favourable conditions. To match the increased downlink throughput, the introduction of 16QAM in the uplink is an attractive addition to the enhanced uplink concept, providing the users also with increased uplink data rates.

Significant gains in terms of throughput were observed by the provision of 16QAM in scenarios (cells with isolation) where users can benefit from favourable radio conditions such as in well tuned outdoor systems or indoor system solutions.

It specifies the support of 16QAM as a uplink modulation scheme for HSUPA in FDD

Completed May 2007; Status Report in RP-070288

### 5.3.11	Interface to control Tower Mounted Amplifiers (TMAs)  UID_20066

Responsibility:	R3,S5

References

| Document | Title/Contents |
| --- | --- |
| WID(s) |
| RP-060418 | WID on Interface to control Tower mounted amplifiers |
| Impacted Specifications |
| 25.401 | UTRAN Overall Description |
| 25.460 | UTRAN Iuant interface: General aspects and principles |
| 25.461 | UTRAN Iuant Interface: Layer 1 |
| 25.462 | UTRAN Iuant interface: Signalling transport |
| 25.463 | UTRAN Iuant Interface: Remote Electrical Tilting (RET) antennas Application Part (RETAP) signalling |
| 32.642 | Configuration Management (CM); UTRAN network resources Integration Reference Point (IRP): Network Resource Model (NRM) |
| 32.643 | Telecommunication management; Configuration Management (CM); UTRAN network resources Integration Reference Point (IRP): Common Object Request Broker Architecture (CORBA) Solution Set (SS) |
| 32.645 | Telecommunication management; Telecommunication management; Configuration Management (CM); UTRAN network resources Integration Reference Point (IRP): Bulk CM eXtensible Markup Language (XML) file format definition |
| New Dedicated Specifications/Reports |
| 25.466 | UTRAN Iuant interface: Application part |

Before the introduction of this feature the control of TMAs was only possible by means of proprietary interfaces between Node B and Operator's O&M System.

As a result Operators could not mix equipment from different Node B and TMA Vendors.

As a consequence, a standardized interface was required to save Operator's costs for site visits and to enable Operators to independently choose Vendors of Node B and TMA equipment.

Furthermore, a common set of parameters and commands in a multi-vendor network allows the Operator to perform network optimization from the Network Element Manager over the Ift-N interface.

To control TMAs the existing Iuant interface introduced in Rel-6 for "Remote Electrical Tilting Antennas" was re-used (25.460, 25.461, 25.462, 25.463). These specifications were updated with the TMA functionality according to the table above, except for the Application Part signalling.

25.463 was closed (i.e. no further Rel-7 maintenance) and replaced by the new 25.466 describing both Applications, RET and TMA.

Completed Mar 2007; Status Report in RP-070140

## 5.4	7.68 Mcps TDD option  UID_20014

Responsibility: RP

References

| Document | Title/Contents |
| --- | --- |
| WID(s) |
| RP-060119 | WID on 7.68 Mcps TDD Enhanced Uplink |
| Impacted Specifications |
| TS 25.201 | Physical layer - general description |
| TS 25.221 | Physical channels and mapping of transport channels onto physical channels (TDD) |
| TS 25.222 | Multiplexing and channel coding (TDD) |
| TS 25.223 | Spreading and modulation (TDD) |
| TS 25.224 | Physical layer procedures (TDD) |
| TS25.225 | Physical layer; Measurements (TDD) |
| TS 25.301 | Radio interface protocol architecture |
| TS 25.302 | Services provided by the physical layer |
| TS 25.304 | User Equipment (UE) procedures in idle mode and procedures for cell reselection in connected mode |
| TS 25.305 | User Equipment (UE) positioning in Universal Terrestrial Radio Access Network (UTRAN); Stage 2 |
| TS 25.306 | UE Radio Access capabilities |
| TS 25.321 | Medium Access Control (MAC) protocol specification |
| TS 25.331 | Radio Resource Control (RRC); Protocol specification |
| TS 25.401 | UTRAN overall description |
| TS 25.402 | Synchronization in UTRAN Stage 2 |
| TS 25.423 | UTRAN Iur interface Radio Network Subsystem Application Part (RNSAP) signalling |
| TS 25.425 | UTRAN Iur interface user plane protocols for Common Transport Channel data streams |
| TS 25.427 | UTRAN Iur/Iub interface user plane protocol for DCH data streams |
| TS 25.433 | UTRAN Iub interface Node B Application Part (NBAP) signalling |
| TR 25.435 | UTRAN Iub interface user plane protocols for Common Transport Channel data streams |
| TR 25.453 | UTRAN Iupc interface Positioning Calculation Application Part (PCAP) signalling |
| TS 25.102 | User Equipment (UE) radio transmission and reception (TDD) |
| TS 25.105 | Base Station (BS) radio transmission and reception (TDD) |
| TS 25.123 | Requirements for support of radio resource management (TDD) |
| TS 25.142 | Base Station (BS) conformance testing (TDD) |
| TS 34.124 | Electromagnetic compatibility (EMC) requirements for mobile terminals and ancillary equipment |
| New Dedicated Specifications/Reports |
| TS 25.202 | 7.68Mcps Time Division Duplex (TDD) option ; Overall description: Stage 2 |

The 7.68Mcps TDD option is an evolution of the 3.84Mcps TDD option to a higher chip rate. There exists a great degree of commonality between the 3.84Mcps TDD option and the 7.68Mcps TDD option. Nevertheless, there are many aspects of the 7.68Mcps TDD option that require separate specification.

As for physical layer structure, the 7.68Mcps TDD option frame is of length 10ms and consists of 15 timeslots of duration 5120 * Tc, where Tc is the chip duration (Tc = 1 / 7.68 * 106 = 130.2ns). Any timeslot in the frame can be either uplink or downlink. At least one timeslot in the frame is assigned to the uplink and at least one timeslot in the frame is assigned to the downlink. The frame structure is shown in Figure 5.4-1.

Physical layer procedures such as power control, timing advance, HSDPA procedures, synchronisation procedures, RACH procedures, and so on are aligned with that of 3.84Mcps TDD. UE capabilities for the 7.68 Mcps TDD mode are based on the 3.84 Mcps TDD. The capabilities for 7.68Mcps TDD account for the higher number of physical channels supported and additionally support higher peak bit rates. The minimum MBMS capability at 7.68Mcps is twice the minimum capability at 3.84Mcps.

Next, as for layer 2/3 protocol aspects, the protocol architecture for 7.68 Mcps TDD is the same as the protocol architecture for 3.84 Mcps TDD, there are some impact on signalling. The differences between 7.68 Mcps TDD and 3.84 Mcps TDD concern L2/MAC and L3/RRC only. L2/RLC, L2/BMC, L2/PDCP and L3 U-plane information are not impacted.

The L2/MAC differences between 7.68Mcps TDD and 3.84Mcps TDD are due to the support of a higher capability HSDPA UE at 7.68Mcps (20.4Mbps). The L2/MAC differences concern:

-	the maximum number of PDUs transmitted in a single TTI (636 at 7.68Mcps compared to 318 for3.84 Mcps TDD).

-	HSPDA transport block size signalling. The maximum transport block size that can be signalled at 7.68Mcps is twice that at 3.84Mcps.

Regarding Radio aspects, Tx and Rx characteristics for both of UE and BS are updated, such as Spectrum Emission Mask, Adjacent Channel Leakage power (ACLR), Adjacent Channel Selectivity (ACS), Spurious response and so on.

Completed Dec 2006, Status Report in RP-060684

## 5.5	3.84 Mcps TDD Enhanced Uplink  UID_20035

Responsibility:	RP

References

| Document | Title/Contents |
| --- | --- |
| WID(s) |
| RP-050100 | WID on 3.84 Mcps TDD Enhanced Uplink |
| Impacted Specifications |
| TS 25.201 | Physical layer - general description |
| TS 25.221 | Physical channels and mapping of transport channels onto physical channels (TDD) |
| TS 25.222 | Multiplexing and channel coding (TDD) |
| TS 25.223 | Spreading and modulation (TDD) |
| TS 25.224 | Physical layer procedures (TDD) |
| TS 25.225 | Physical layer; Measurements (TDD) |
| TS 25.301 | Radio interface protocol architecture |
| TS 25.302 | Services provided by the physical layer |
| TS 25.306 | UE Radio Access capabilities |
| TS 25.321 | Medium Access Control (MAC) protocol specification |
| TS 25.331 | Radio Resource Control (RRC); Protocol specification |
| TS 25.401 | UTRAN overall description |
| TS 25.420 | UTRAN Iur interface general aspects and principles |
| TS 25.423 | UTRAN Iur interface Radio Network Subsystem Application Part (RNSAP) signalling |
| TS 25.427 | UTRAN Iur/Iub interface user plane protocol for DCH data streams |
| TS 25.430 | UTRAN Iub Interface: general aspects and principles |
| TS 25.433 | UTRAN Iub interface Node B Application Part (NBAP) signalling |
| TS 25.435 | UTRAN Iub interface user plane protocols for Common Transport Channel data streams |
| TS 25.102 | User Equipment (UE) radio transmission and reception (TDD) |
| TS 25.105 | Base Station (BS) radio transmission and reception (TDD) |
| TS 25.123 | Requirements for support of radio resource management (TDD) |
| TS 25.142 | Base Station (BS) conformance testing (TDD) |
| New Dedicated Specifications/Reports |
| None | - |

The target was uplink enhancement techniques to increase the coverage and throughput and reduce the delay of the uplink for packet-based services. Incorporation of Node-B controlled rate- and physical resource scheduling, hybrid ARQ, and support for higher-order modulation deliver significant performance improvement with manageable complexity whilst maintaining backwards compatibility.

- For radio interface physical layer:

- Physical and Transport Channels mapping

- Multiplexing and Channel Coding

- Physical Layer procedures

- Physical layer measurements

- UE physical layer capabilities

- For radio interface higher RAN layers:

- Architecture aspects

- MAC entity (Scheduling and hybrid ARQ protocol)

- Interlayer interactions in connected mode

- Control plane protocols

- User plane protocols

- UE capabilities

- For Iur/Iub interface:

- Control plane protocols

- User plane protocols

- For radio transmission and reception:

- UE radio transmission and reception

- Base Station radio transmission and reception

- Base Station conformance testing

- Requirements for support of Radio Resource Management

Completed Sep 2006, Status Report in RP-060462

## 5.6	1.28 Mcps TDD Enhanced Uplink  UID_20055

Responsibility:	RP

References

| Document | Title/Contents |
| --- | --- |
| WID(s) |
| RP-060202 | WID on 1.28 Mcps TDD Enhanced Uplink |
| Impacted Specifications |
| TS 25.201 | Physical layer - general description |
| TS 25.221 | Physical channels and mapping of transport channels onto physical channels (TDD) |
| TS 25.222 | Multiplexing and channel coding (TDD) |
| TS 25.223 | Spreading and modulation (TDD) |
| TS 25.224 | Physical layer procedures (TDD) |
| TS 25.225 | Physical layer; Measurements (TDD) |
| TS 25.301 | Radio interface protocol architecture |
| TS 25.302 | Services provided by the physical layer |
| TS 25.306 | UE Radio Access capabilities |
| TS 25.321 | Medium Access Control (MAC) protocol specification |
| TS 25.331 | Radio Resource Control (RRC); Protocol specification |
| TS 25.401 | UTRAN overall description |
| TS 25.420 | UTRAN Iur interface general aspects and principles |
| TS 25.423 | UTRAN Iur interface Radio Network Subsystem Application Part (RNSAP) signalling |
| TS 25.425 | UTRAN Iur interface user plane protocols for Common Transport Channel data streams |
| TS 25.427 | UTRAN Iur/Iub interface user plane protocol for DCH data streams |
| TS 25.430 | UTRAN Iub Interface: general aspects and principles |
| TS 25.433 | UTRAN Iub interface Node B Application Part (NBAP) signalling |
| TS 25.435 | UTRAN Iub interface user plane protocols for Common Transport Channel data streams |
| TS 25.102 | User Equipment (UE) radio transmission and reception (TDD) |
| TS 25.105 | Base Station (BS) radio transmission and reception (TDD) |
| TS 25.123 | Requirements for support of radio resource management (TDD) |
| TS 25.142 | Base Station (BS) conformance testing (TDD) |
| New Dedicated Specifications/Reports |
| None | - |

The target was uplink enhancement techniques to increase the coverage and throughput and reduce the delay of the uplink for packet-based services. Incorporation of Node-B controlled rate- and physical resource scheduling, hybrid ARQ, and support for higher-order modulation deliver significant performance improvement with manageable complexity whilst maintaining backwards compatibility.

- For radio interface physical layer:

- Physical and Transport Channels mapping

- Multiplexing and Channel Coding

- Spreading and modulation

- Physical Layer procedures

- Physical layer measurements

- UE physical layer capabilities

- For radio interface higher RAN layers:

- Architecture aspects

- MAC entity (Scheduling and hybrid ARQ protocol)

- Interlayer interactions in connected mode

- Control plane protocols

- User plane protocols

- UE capabilities

- For Iur/Iub interface:

- Control plane protocols

- User plane protocols

- For radio transmission and reception:

- UE radio transmission and reception

- Base Station radio transmission and reception

- Base Station conformance testing

- Requirements for support of Radio Resource Management

Completed May 2007; Status Report in RP-070038 and RP-070296

### 5.6.1	1.28Mcps TDD Enhanced Uplink - UE Conformance Testing  UID_350146 (0% completion)

Responsibility:	R5

References

| Document | Title/Contents |
| --- | --- |
| WID(s) |
| RP-060202 | WID on UE conformance test aspects - 1.28Mcps TDD Enhanced Uplink |
| Impacted Specifications |
| TS 34.108 | Common test environments for User Equipment (UE) conformance testing |
| TS 34.122 | Terminal Conformance Specification, Radio Transmission and Reception (FDD) |
| TS 34.123-1/2/3 | User Equipment (UE) conformance specification |
| New Dedicated Specifications/Reports |
| None | - |

Status Report in RP-080285

Completion target 	11/09/2008

# 7	Improvements of UMTS and GSM

## 7.1	Evolution of Policy Control and Charging

Written by Seung Don Han

[SA2 part To be written by Maurice]

Acronym:		PCC

UID_32082

Main Responsibility:	S2

References for "Evolution of Policy Control and Charging "

| Document | Title/Contents |
| --- | --- |
| WID(s) |
| GP-022566 | WID on XXX |
| Impacted Specifications |
| TS 24.008 | Example |
| New Dedicated Specifications/Reports |
| TS 22.146 | Example |

The single reference point between the PCRF and the PCEF combining Go and Rel-6 Gx with a single protocol was introduced based on TR 23.803. The protocol for the Gx reference point on a stage-3 level was defined in TS 29.212.

The Rx reference point combining Rel-6 Rx and Gq within a single protocol was introduced in TS 29.214 based on the requirements defined in the Rel-7 TS 23.203 for PCC architecture. TS 29.213 incorporates the necessary call flows for the different procedures involved in a PCC architecture, as well as the necessary methodology (e.g. algorithms) to map QoS and policies between the application and transport domains.

[Maurice: above text from CT3/Seung Don, SA2 part missing]

Extract from the Work Plan (info for the writer only, to be deleted when providing actual text):

SA5 Charging aspects of PCC (PCC-CH) are implemented as CRs in TSs 32.250, 32.251, 32.298, 32.299.

| 122 | 32082 | Evolution of Policy Control and Charging | 1 | S2 | PCC |  | SP-040533 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 123 | 32102 | TR for PCC | 2 | S2 |  |  |  |
| 124 | 32103 | Stage 2 for PCC | 2 | S2 |  | 23.203 |  |
| 125 | 32109 | Evolution of policy control and flow based bearer level charging | 2 | S2 |  | 23.207, 23.125, 23.002, 23.228 | SP-050486 |
| 127 | 13029 | Gx reference point for Policy and Charging Control | 2 | C3 |  | 29.210, 29.207, 29.208 | CP-060054 |
| 128 | 13030 | Rx reference point for PCC CT3 aspects | 2 | C3 | PCC-Rx | 29.209, 29.211, 24.229 | CP-060055 |
| 129 | 310006 | PCC-Rx CT3 aspects | 3 | C3 |  | 29.209, 29.211, 24.229 | CP-060055 |
| 130 | 7008 | PCC-Rx CT1 aspects | 3 | C1 |  |  |  |

## 7.2	CAMEL Trunk Triggers

Written by M. Clayton

Acronym:		TTCAMEL

UID_31065

Main Responsibility:	S1

References for "CAMEL Trunk Triggers "

| Document | Title/Contents |
| --- | --- |
| WID(s) |
| SP-040743 | WID on CAMEL Trunk Originated Trigger Detection Points |
| NP-040550 | CAMEL Trunk Originated Trigger Detection Points |
| Impacted Specifications |
| TS 22.078 | Customized Applications for Mobile network Enhanced Logic (CAMEL); Service description; Stage 1 (CR 22.078-0182r1 SP-050064) (CR 22.078-0192 SP-050744) |
| TS 23.018 | Basic Call Handling; Technical realization (CR 23.018-0145r1 CP-050103) |
| TS 23.078 | Customized Applications for Mobile network Enhanced Logic (CAMEL) Phase X; Stage 2 (CR 23.078-0764r1; CR 23.078-0770r1 CP-050103) (CR 23.078-0792r2: CR 23.078-0793r1 CP-050626) |
| TS 29.002 | Mobile Application Part (MAP) specification (CR 29.002-0765r1 CP-050103) |
| TS 29.078 | Customized Applications for Mobile network Enhanced Logic (CAMEL) Phase X; CAMEL Application Part (CAP) specification (CR 29.078-0392r1 CP-050103) (CR 29.078-0396r1 CP-050626) |
| New Dedicated Specifications/Reports |
| - | - |

CAMEL was defined for mobile originated & mobile forwarded calls in the VMSC, mobile terminated calls in the GMSC and VMSC and gsmSCF initiated new call or new party in an existing call. There are however some existing and new service scenarios that would benefit from CAMEL being defined for trunk originated calls at the MSC.

Some GSM-R operators wanted to use CAMEL to provide number translation functions in multi-vendor GSM-R networks. In addition to mobile originated calls, this required CSE interaction for calls from fixed terminals (received over a trunk interface at the MSC) and calls from foreign GSM-R networks (received over a trunk interface at the MSC).

Operators who incorporated wireline access to existing CSE-based services may also want to use the CAMEL standard to provide this capability for multi-vendor networks. This requires CSE interaction for calls from fixed terminals received at the MSC from a public (e.g. ISDN/ PSTN) trunk interface.

In addition, operators could use CAMEL trunk originated TDPs to allow access to existing CSE-based services for calls from fixed terminals received at the MSC from a private (i.e. PRI) trunk interface.

The CAMEL standard already provided Network CAMEL Service Information (N-CSI), to identify services offered by the serving PLMN operator equally for all subscribers. This work item requires CAMEL Service Information to identify services offered by the serving PLMN operator for all calls received over a specific trunk at the MSC.

This Work Item Description describes the work to be done for CAMEL Phase 4 to include the feature ‘CAMEL Trunk Originated TDPs.

## 7.3	IWLAN-related improvements

### 7.3.1	WLAN-UMTS Interworking Phase 2

Written by M. Clayton

Acronym:		WLAN2

UID_31062

Main Responsibility:	S1

References for "WLAN-UMTS Interworking Phase 2"

| Document | Title/Contents |
| --- | --- |
| WID(s) |
| SP-030712 | WID on 3GPP system - WLAN- Interworking |
| Impacted Specifications |
|  | [Alain, you didn’t swap Impacted Spec with New Specs?] |
| New Dedicated Specifications/Reports |
| TS 22.234 | Requirements on 3GPP system to WLAN interworking (CR 22.234-0010 SP-040737) (CR 22.234-0011; CR 22.234-0012 SP-050066) (CR 22.234-0021 SP-060305) |

This work item is an extension of the WLAN-UMTS Interworking Rel-6. The I-WLAN work item defines the interworking between 3GPP systems and Wireless Local Area Networks (WLANs). For this purpose, “3GPP - WLAN interworking"refers to the utilization of resources and access to services within the 3GPP system by respectively the WLAN UE and user. The intent of 3GPP - WLAN Interworking is to extend 3GPP services and functionality to the WLAN access environment. Thus the WLAN effectively becomes a complementary radio access technology to the 3GPP system.

The WLAN provides access to services located in WLANs and/or networks behind the WLAN. In 3GPP - WLAN interworking, 3GPP system functionalities can reside behind the WLAN or in parallel to the WLAN.

The feasibility document TR 22.934 includes a number of different scenarios of 3GPP-WLAN interworking ranging from common billing to the provision of services seamlessly between the WLAN and the 3GPP system, referred as Scenarios 1 to 6. In addition, the study includes the analysis of a number of environments where both the 3GPP system and WLAN may be deployed, and outlines some of the different WLAN technologies that may be interworked with 3GPP systems.

The stage 1 in 22.234 took the conclusions of the feasibility study and defines the highly level requirements for I_WLAN.

### 7.3.2	WLAN Interworking – Private Network access from WLAN 3GPP IP Access

To be written by Maurice

Acronym:		WLANPNA

UID_32110

Main Responsibility:	S2

References for "WLAN Interworking – Private Network access from WLAN 3GPP IP Access"

| Document | Title/Contents |
| --- | --- |
| WID(s) |
| GP-022566 | WID on XXX |
| Impacted Specifications |
| TS 24.008 | Example |
| New Dedicated Specifications/Reports |
| TS 22.146 | Example |

Your text: what does it offer? (Stage 1 summary) How does it impact the network? (Stages 2 and 3 summary). PLEASE DON’T JUST COPY-PASTE THE TEXT FROM THE WID BUT CHECK WHAT WAS ACTUALLY DONE!

Extract from the Work Plan (info for the writer only, to be deleted when providing actual text):

| 167 | 32110 | WLAN Interworking – Private Network access from WLAN 3GPP IP Access | 1 | S2 | WLANPNA |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 168 | 32111 | WLAN-PNA - Stage 2 | 2 | S2 | WLANPNA-st2 | 23.234, 33.234 | SP-050489 |
| 169 | 11059 | WLAN-PNA - Stage 3 | 2 | C1 | WLANPNA-st3 |  | CP-060256 |
| 170 | 11064 | CT1 aspets for WLAN-PNA | 3 | C1 | WLANPNA-st3 | 24.234 | CP-050350 |
| 171 | 13027 | CT3 aspets for WLAN-PNA | 3 | C3 | WLANPNA-st3 | 29.161 | CP-060256 |
| 172 | 14024 | CT4 aspets for WLAN-PNA | 3 | C4 | WLANPNA-st3 | 29.234 | CP-050350 |

### 7.3.3	Enhancements to support QoS provisioning over 3GPP/WLAN Interworking

To be written by Maurice

Acronym:		WLAN-QOS

UID_32092

Main Responsibility:	S2

References for "Enhancements to support QoS provisioning over 3GPP/WLAN Interworking"

| Document | Title/Contents |
| --- | --- |
| WID(s) |
| GP-022566 | WID on XXX |
| Impacted Specifications |
| TS 24.008 | Example |
| New Dedicated Specifications/Reports |
| TS 22.146 | Example |

Your text: what does it offer? (Stage 1 summary) How does it impact the network? (Stages 2 and 3 summary). PLEASE DON’T JUST COPY-PASTE THE TEXT FROM THE WID BUT CHECK WHAT WAS ACTUALLY DONE!

Extract from the Work Plan (info for the writer only, to be deleted when providing actual text):

| 173 | 32092 | Enhancements to support QoS provisioning over 3GPP/WLAN Interworking | 1 | S2 | WLAN-QOS | 23.836 | SP-050682 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 174 | 7015 | TR on support of QoS on WLAN | 2 | S2 |  |  |  |
| 175 | 7016 | Stage 2 on support of QoS over 3GPP/WLAN interworking | 2 | S2 |  |  |  |

## 7.4	Voice call continuity between CS and IMS (incl. I-WLAN)

To be written by Maurice

Acronym:		VCC

UID_32091

Main Responsibility:	S2

References for "Voice call continuity between CS and IMS (incl. I-WLAN)"

| Document | Title/Contents |
| --- | --- |
| WID(s) |
| GP-022566 | WID on XXX |
| Impacted Specifications |
| TS 24.008 | Example |
| New Dedicated Specifications/Reports |
| TS 22.146 | Example |

Your text: what does it offer? (Stage 1 summary) How does it impact the network? (Stages 2 and 3 summary). PLEASE DON’T JUST COPY-PASTE THE TEXT FROM THE WID BUT CHECK WHAT WAS ACTUALLY DONE!

Extract from the Work Plan (info for the writer only, to be deleted when providing actual text):

SA5 Charging aspects of VCC (VCC-CH) are implemented as CRs in TSs 32.250, 32.260, 32.298, 32.299.

| 176 | 32091 | Voice call continuity between CS and IMS (incl. I-WLAN) | 1 | S2 | VCC | 22.101, 23.228, 32.250, 32.260, 32.299, 32.298 | SP-060922 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 177 | 32104 | TR for VCC | 2 | S2 |  | 23.806 |  |
| 178 | 31085 | Stage 1 for VCC | 2 | S1 |  |  | SP-050177 |
| 179 | 32105 | Stage 2 for VCC | 2 | S2 |  | 23.206 |  |
| 180 | 11058 | Stage 3 for VCC | 2 | C1 |  | new TS, 24.229, 23.008, 23.009, 23.078, 29.078, 29.163, 29.228, 29.229, 29.230, 29.278, 29.328, 29.329 | CP-050458 |
| 181 | 11066 | CT1 aspects of VCC | 3 | C1 |  | new TS, 24.229 | CP-050458 |
| 182 | 13032 | CT3 aspects of VCC | 3 | C3 |  | 29.163 | CP-050458 |
| 183 | 14027 | CT4 aspects of VCC | 3 | C4 |  | 23.008, 23.009, 23.078, 29.078, 29.228, 29.229, 29.230, 29.278, 29.328, 29.329 | CP-050458 |

## 7.5	Operations, Administration, Maintenance & Provisioning (OAM7)  UID_35041

Acronym:		OAM7

Responsibility:	S5, C1/3/4, RAN3 (only for End-to-end tracing for IMS UID_35039)

TR 30.817 "Telecommunication management; Project scheduling and open issues for SA5, Release 7"contains the updated Work Item Descriptions (WIDs) for OAM and Charging management.

The Feature OAM7 contains three (3) Building Blocks as follows:

Network Infrastructure Management	OAM7-NIM

Performance Management	OAM7-PM

Trace Management	OAM7-Trace

References

| Document | Title/Contents |
| --- | --- |
| WID(s) |
| TR 30.817 | Telecommunication management; Project scheduling and open issues for SA5, Release 7 |
| Impacted Specifications |
| TS 32.101 | Telecommunication management; Principles and high level requirements |
| TS 32.102 | Telecommunication management; Architecture |
| TS 32.111-2 | Fault Management; Part 2: Alarm IRP: Information Service |
| TS 32.111-3 | Fault Management; Part 3: Alarm IRP: CORBA Solution Set |
| TS 32.150 | IRP Concept and definitions |
| TS 32.151 | IRP Information Service (IS) template |
| TS 32.152 | IRP Information Service UML repertoire |
| TS 32.321 | Test management IRP: Requirements |
| TS 32.335 | Notification Log (NL) IRP: XML solution definitions |
| TS 32.371 | Security Management concept and requirements |
| TS 32.401 | Performance Management (PM); Concept and requirements |
| TS 32.421 | Subscriber and equipment trace; Trace concepts and requirements |
| TS 32.422 | Subscriber and equipment trace; Trace control and configuration management |
| TS 32.423 | Subscriber and equipment trace; Trace data definition and management |
| TS 32.432 | Performance measurement: File format definition |
| TS 32.435 | Performance measurement: XML file format definition |
| TS 32.436 | Performance measurement: ASN.1 file format definition |
| TS 32.601 | Configuration Management (CM); Basic CM IRP; Requirements |
| TS 32.612 | Configuration Management (CM); Bulk CM IRP: Information Service |
| TS 32.615 | Configuration Management (CM); Bulk CM IRP: XML file format definition |
| TS 32.631 | Configuration Management (CM); Core network resources IRP: Requirements |
| TS 32.632 | Configuration Management (CM); Core Network Resources IRP: NRM |
| TS 32.633 | Configuration Management (CM); Core network resources IRP: CORBA Solution Set |
| TS 32.635 | Configuration Management (CM); Core network resources IRP: Bulk CM XML file format definition |
| TS 32.642 | Configuration Management (CM); UTRAN network resources IRP: NRM |
| TS 32.643 | Configuration Management (CM); UTRAN network resources IRP: CORBA Solution Set |
| TS 32.645 | Configuration Management (CM); UTRAN network resources IRP: Bulk CM XML file format definition |
| TS 32.675 | Configuration Management (CM); State Management IRP: Bulk CM XML file format definition |
| TS 32.741 | Configuration Management (CM); Signalling Transport Network (STN) interface NRM IRP: Requirements |
| TS 32.742 | Configuration Management (CM); Signalling Transport Network (STN) interface NRM IRP: Information Service |
| TS 32.743 | Configuration Management (CM); Signalling Transport Network (STN) interface NRM IRP: CORBA Solution Set |
| TS 32.745 | Configuration Management (CM); Signalling Transport Network (STN) interface NRM IRP: Bulk CM XML file format definition |
| New Dedicated Specifications/Reports |
| TS 32.154 | Backward and Forward Compatibility (BFC); Concept and definitions |
| TS 32.307 | Configuration Management (CM); Notification IRP SOAP Solution Set |
| TS 32.317 | Generic IRP management; SOAP Solution Set |
| TS 32.607 | Configuration Management (CM); Basic CM IRP SOAP Solution Set |
| TS 32.667 | Configuration Management (CM); Kernel CM IRP SOAP Solution Set |
| TS 32.325 | Test management IRP XML definitions |
| TS 32.345 | File Transfer IRP XML definitions |
| TS 32.365 | Entry Point IRP XML definitions |
| TS 32.415 | Performance Management (PM) IRP XML definitions |
| TS 32.665 | Configuration Management; Kernel CM IRP XML definitions |
| TS 32.372 | Security services for IRP Information Service |
| TS 32.373 | Security services for IRP CORBA Solution |
| TS 32.375 | Security services for IRP File integrity solution |
| TS 32.381 | Partial Suspension of Itf-N IRP Requirements |
| TS 32.382 | Partial Suspension of Itf-N IRP Information Service (IS) |
| TS 32.383 | Partial Suspension of Itf-N IRP CORBA Solution Set |
| TS 32.385 | Partial Suspension of Itf-N IRP XML file format definition |
| TS 32.391 | Delta synchronization IRP Requirements |
| TS 32.392 | Delta synchronization IRP Information Service (IS) |
| TS 32.393 | Delta synchronization IRP CORBA Solution Set |
| TS 32.395 | Delta synchronization IRP XML file format definition |
| TS 32.404 | Performance Management (PM); Performance measurements - Definitions and template |
| TS 32.405 | Performance Management (PM); Performance measurements UTRAN |
| TS 32.406 | Performance Management (PM); Performance measurements Core Network PS domain |
| TS 32.407 | Performance Management (PM); Performance measurements Core Network CS domain |
| TS 32.408 | Performance Management (PM); Performance measurements Teleservice |
| TS 32.409 | Performance Management (PM); Performance measurements IMS |
| TS 32.441 | Trace Management IRP Requirements |
| TS 32.442 | Trace Management IRP Information Service (IS) |
| TS 32.443 | Trace Management IRP CORBA Solution Set |
| TS 32.445 | Trace Management (Trace) IRP XML file format definition |
| TS 32.721 | Configuration Management (CM); Repeater network resources IRP Requirements |
| TS 32.722 | Configuration Management (CM); Repeater network resources IRP information Service |
| TS 32.723 | Configuration Management (CM); Repeater network resources IRP CORBA Solution Set |
| TS 32.725 | Configuration Management (CM); Repeater network resources IRP Bulk CM XML file format definition |
| TS 32.731 | IP Multimedia Subsystem (IMS) Network Resource Model (NRM) IRP Requirements |
| TS 32.732 | IP Multimedia Subsystem (IMS) Network Resource Model (NRM) IRP Information Service |
| TS 32.733 | IP Multimedia Subsystem (IMS) Network Resource Model (NRM) IRP CORBA Solution Set |
| TS 32.735 | IP Multimedia Subsystem (IMS) Network Resource Model (NRM) IRP XML file format definition |
| TR 32.806 | Application guide for use of Integration Reference Points (IRPs) on peer-to-peer (p2p) interface |
| TR 32.811 | Itf-N performance criteria: Requirements |
| TR 32.814 | UTRAN and GERAN Key Performance Indicators (KPI) |

Network Infrastructure Management (OAM7-NIM) - UID_35042

- Enhance NRM to accommodate NGN (IMS as basis of the Next Generation Network) - UID_35044

The IMS has been adopted as the basis of the NGN.

The 3GPP Core Network Resource Model (NRM) in TS 32.63x Configuration Management (CM); Core Network Resources Integration Reference Point (IRP) was enhanced to accommodate additional requirements of NGN Release 1 and VoIP coming from other groups (e.g. ETSI TISPAN, ITU-T SG4, TMF, Multiservice Switching Forum (MSF) resulting in a new TS family TS 32.73x "IMS NRM IRP".

- Co-operative Element Management interface (CO-OP) - UID_35046

Networks are often multi-vendor, whereas Operations Support Systems (OSSs) are single vendor.

Traditional architectures allow multi-vendor capabilities to be provided through integration to a vendor-independent Network Management System (NMS), by means of northbound interfaces (i.e. the existing 3GPP IRPs). This enables the NMS (and the human operator) to monitor and configure border aspects between Element Management Systems (EMSs)/IRP Agents (within a vendor’s domain and across vendors' domains). This is achieved through sharing of information, responsibility and management knowledge between EMSs over a horizontal Peer-to-Peer (P2P) interface. It is possible to share information, responsibility and management knowledge between EMSs over a horizontal P2P interface (by reusing and/or enhancing existing 3GPP IRPs).

Shared responsibility and management knowledge between EMSs addressed are as follows:

  - Read domain topology data

  - Subscribe to state changes

  - Receive events/alarms

  - Requests functions

  - Common Key Performance Indicators (KPIs)

TR 32.806 shows how P2P horizontal interfaces can be added to the existing Telecommunication Management (TM) architecture and how existing IRPs can be applied to this architecture.

TR 32.814 details two methods of defining KPIs. The first method is characterized by using performance measurements defined in TS 32.4xy. The second method takes a higher level approach that does not require the use of standardised performance measurements. The TR concludes that where standardised measurements are available, the first definition approach should be used, however when standardised measurements are not available or not appropriate to use, e.g. when differing implementation alternatives have led to non uniform counter updates or even different counter definitions between vendors, then a higher level KPI definition approach may be used.

This study has not used a uniform template between the two different KPI methods; this is something that should be addressed in any future KPI standardisation work.

- Network Management (NM) Itf-N performance criteria - UID_35047

Performance is a key point to ensure the quality of a product. This is also valid for the UMTS network management Itf-N. The current SA5 specifications define the function requirements and solution for the UMTS network management Itf-N. However, to ensure the all-around quality of the Itf-N, reasonable performance criteria are needed. Performance criteria reveal the potential risk for UMTS network management Itf-N. It is necessary to accurately reflect the performance bottle-necks of the Itf-N.

The performance criteria are considered by vendors when developing their products, especially when designing the internal architecture of the IRP Agent which may influence the performance of Itf-N. These performance criteria are also useful for operators as a guide to evaluate Itf-N products. The value definition of itf-N performance criteria was out of the scope of this WID.

TR 32.811 provides for all IRP specifications produced by 3GPP the overall performance criteria (interface IRP data consistency, capacity and reliability). It gives examples of Test Environment and Measurement Point.

- Delta synchronization between IRP Manager and IRP Agent - UID_35048

If the connection between IRPManager and IRPAgent is lost, the only way for the IRPManager to synchronize again after re-establishment of the connection was to synchronize the complete data.

This can be a huge amount of data, both and individually for Configuration Management (CM) and Fault Management (FM) data, even if only very little data actually has changed in the meantime. This puts an unnecessary load on both IRPManager and IRPAgent and can take a long time – even if there was only a short interruption of the connection.

Other cases where synchronization is needed are e.g.:

- IRPAgent does not send notifications

- IRPManager does not evaluate notifications

- loss of notifications on IRPManager side because of system problems

- inability to generate notifications on IRPAgent side because of system problems

TS 32.39x Delta Synchronization IRP define an interface through which an IRPManager can request only the data which has changed (i.e. new/modified/deleted data) from a synchronization point onwards.

- Subscription Management (SuM) IRP Solution Sets - UID_35049

Standardization of SuM operations significantly enhances the ability of 3GPP based networks to provision and administer complex services in the area of multimedia, data services, value added services, end-to-end applications. To enable service providers to administer the subscription data defined in the Network Resource Model (NRM) an adequate Interface IRP fulfilling the SuM operations requirements has been specified. SOAP has been agreed to be the suitable technology for SuM.

As a result:

- Added new SOAP SS in TS 32.101 Telecom management; Principles & high level requirements

- Aligned TS 32.175 SuM NRM IRP XML definition with the SOAP SS used for Interface IRP

- For existing IRPs new TSs on SuM Interface IRP SOAP SSs were created as follows:

32.307	Notification IRP SOAP SS

32.317	Generic IRP Management SOAP SS

32.607	Basic CM IRP SOAP SS

32.665	Kernel CM IRP XML definitions

32.667	Kernel CM IRP SOAP SS

- Integration Reference Point (IRP) Security Management - UID_35050

The 3G Mobile Network is sensitive to fraud and contains very sensitive data which is essential for the correct operation. A 3G Mobile Network exchanges sensitive data between the management system and the mobile network. This work builds upon and enhances the Release 6 work on security management to further ensure secure access and data protection throughout the OAM network.

TS 32.372/3/5 specify the necessary security features, services and functions to protect the network management data, including Requests, Responses, Notifications and Files, exchanged across the Itf-N.

- Partial suspension of Itf-N during maintenance/testing - UID_35052

In certain scenarios floods of unwanted notifications including alarms is sent to the IRP Manager by network object instances. Thereby the interface and the management systems bear unnecessary load. Even worse: the operator’s awareness is drawn away from really urgent events.

In these scenarios it can also be important that no commands via the Itf-N interfere with actions from the local craft interface (e.g. people working close to antennas would like to have complete control when the radiation is switched on).

Consequently suspending for a period of time Itf-N is beneficial (i.e. not to send notifications of the involved network elements and/or to disallow Itf-N management operations). 
TS 32.38x specify an interface through which an IRP Manager can suspend the forwarding of notifications via Itf-N which were generated in parts of the managed systems.

- Backward and Forward Compatibility of IRP systems - UID_35064

This sets the rules that IRP authors can use to evolve existing IRP specifications such that implementations of the new IRP specifications can result in systems that are backward compatible to systems that have implemented the existing specification.

Given that

- 3GPP is publishing the Interface, NRM and Data Definition IRP specifications rapidly, i.e. multiple versions per release period; and will continue to do so in the future, and

- Vendors are making products that support Vendor Specific Extension (VSE) that are based on 3GPP IRP specifications; and

- Operators are planning to use 3GPP IRP to manage large multi-vendor networks; and

- Operators may want to use a managing system that is compliant to vendor-A VSE (that is based on 3GPP IRP specifications) to manage multi-vendor managed systems that may not be supporting vendor-A VSE but are supporting vendor-B VSE (that is based on 3GPP IRP specifications); and

- It requires less coordination and less service disruption if managing systems and managed systems upgrades in a large network, be done in a gradual basis; and

- It is inconceivable that, in a large multi-vendor network, all IRPManagers (may be from various vendors) and IRPAgents (may be from various vendors as well) must use the same 3GPP specification release at all time;

there is a need for 3GPP to specify rules such that, if and when used by IRP standard authors to develop a new release, the implementations supporting the resultant new release can interoperate with implementations supporting the “older" release. Such rules are called Backward Compatibility (BC) rules.

There is also a need for 3GPP to specify rules such that when used by IRP standard authors to specify a standard of a release, the implementation supporting the resultant release can have a better chance of interoperating with implementations supporting future release.  Such rules are called Forward Compatibility (FC) rules.  FC is harder to achieve than BC, since in the BC case the ‘old’ system behaviour is known whereas a FC system needs to cope gracefully with unknown future features.  The standardization of these FC rules is the secondary focus of this work item.

SA5 considered industry best practices for defining systems that are BC and/or FC.

BC rules had been studied in Release 6 TR 32.805 under the SA5 Work Task “Backward Compatibility”.

Release 7 sets the rules for BC (primary focus) and the requirements and rules for FC (secondary focus).

TS 32.154 recommends developing future IRP specifications in a Backward Compatible (BC) way so that the group of IRPManager(s) and IRPAgent(s) are not forced to be upgraded in lock step.

- Repeater Network Resource Model (NRM) definition - UID_35071

Repeater is the equipment which can be used in the UTRAN network to improve the network coverage. 
Often vendors implement repeater OMC to manage the repeaters and carry the necessary OAM&P functions defined in TMN.  
From the TMN view point, the repeater OMC is a kind of Element Management System (EMS) which should be managed by the Network Management System (NMS) through itf-N. 
Existing 3GPP TS 32.xyz were lacking repeater related NRM specifications needed by the NMS. 
This work covers the need and solutions for Repeater NRM definition in UMTS.

Tower Mounted Amplifier/Booster (TMA/B) is not within the scope.

TS 32.72x define the Configuration Management (CM); Repeater network resources IRP.

- UTRAN radio channel power monitoring - UID_35072

Power is a very important and limited resource in the WCDMA UTRAN network. High or low power value of each kind of channel has different impact on the network. So effective monitoring of the radio channel power is very helpful for operators’ daily OAM&P work and network estimation.

In UTRAN, there are three different levels of radio channels: logical, transport and physical channels. 
The power can be assigned on transport channel or physical channel.  Operators require grasping the configured and dynamic value of those channels’ power. For those which are not related to power control, the operator only needs to grasp the configured value of channel power. While for the others, it is necessary to measure the dynamic value of channel power.

The result of this work resulted in CRs against:

- 32.64x	UTRAN network resources IRP

- 32.405	Performance Measurements - UMTS and combined UMTS/GSM

- Notification XML Schema - UID_340009

Notification Log IRP is defined to be a general Notification Logging mechanism which can hold notifications related to different functional areas in the network.

TS 32.331 (Notification Log IRP requirement) states that: "Any Notification Log must, at any one point in time, be capable of holding fault management alarms, configuration management events, performance management events, and event log management events. A log is capable of capturing all semantics carried in a notification." Based on TS 32.331 it is necessary to define XML Schema for the remaining Itf-N Notifications: i.e. BulkCMIRP (32.61x), EPIRP (32.36x), FTIRP (32.34x), KernelCMIRP (32.66x), NotificationLogIRP (32.33x), PMIRP (32.41x), TestIRP (32.32x).

This resulted in new TSs 32.325/ 345/ 365/ 415 and CRs against TSs 32.335/ 615/ 665.

Performance Management (OAM7-PM) - UID_35043

- Performance measurements definition for CN CS - UID_35057

Performance measurement data is important for an operator to analyze the network performance. So far the necessary performance measurements related to RNC, SGSN, GGSN and MMS were defined. The performance measurement data related to the CN, especially CN CS (IP-based) is added. This leads to comparable measurement data produced in a multi-vendor network, for those measurement types that can be standardised across all vendors' implementations.

TS 32.407 contains the Performance measurements for the Core Network (CN) Circuit Switched (CS) domain for both UMTS and combined UMTS/GSM.

TS 32.408 contains the Performance measurements Teleservice for both UMTS and combined UMTS/GSM. Measurements related to 3GPP-"external"technologies (such as ATM or IP) as defined by other standards bodies (e.g. ITU-T or IETF) are only referenced in this specification.

- Enhancement UTRAN performance measurements definition - UID_35058

Performance measurement data is important for an operator to analyze the network performance. So far the necessary performance measurements related to RNC RAB management, signalling connection, RRC connection, RLC connection, soft handover, radio link addition, hard handover, relocation, circuit switched inter-RAT handover, and Iu connection release.

For a good monitoring of the UTRAN new performance measurements were added to TS 32.405 e.g.:

- Inter-frequency and intra-frequency hard handovers for use in network optimization

- Inter-system HO measurements to show CS and PS domain hard handover stability and reliability

- RAB drop rate per service type to analyze quality of service

- IuCS, IuPS, Iur and Iub interface throughput measurements needed to reflect the interface load

- RNC resource usage measurements to reflect the equipment load

- Cell soft handover scale radio link measurements for network planning and optimization

- Cell paging measurements to reflect the paging channel resource usage

- RAB establishment measurements per cell to analyze service quality

- Cell frequency usage measurements to analyze service quality

- Cell code resource usage for use in network planning and optimization

- Add TDD specific counters in Performance measurement - UID_35059

In Release 6 all the counters were either FDD specific or FDD/TDD specific. Some TDD specific counters are missing in TS 32.405. It is therefore necessary to specify a comprehensive set of measurement types for the TDD network elements to deliver TDD network information across the UMTS system.

- ATM bearer network Performance measurements - UID_35060

Performance measurements are very important in analyzing, optimizing and forecasting the UMTS system performance. In R6 TS 32.403 there are performance measurements families related to the RNC but there are missing performance measurement definitions of the bearer network which help evaluating the transport network layer (TNL) performance and give more detail to analyse RNC performance.

In R99 and R4 the TNL in UTRAN was based on ATM. In R5, the TNL based on IP was introduced in TS 25.401, however the TNL based on ATM is still an allowed option. Therefore, it is necessary to study the ATM bearer network performance measurement definitions to analyse network performance more efficiently. The work focussed on ATM bearer network performance measurement definitions related to the RNC, including the protocols of TNL (SCCP, ALCAP, SSCOP, MTP3B). The work was not restricted to UTRAN.

From two options the 2nd one was preferred:

- Include in TSs 32.404 / 405 / 406 / 407 support for ATM bearer network Performance Measurement Counters by reference to existing measurements from other standards bodies (ITU-T, ATM Forum).

- Interested companies should approach the other standards bodies to include the identified counters.

- Performance measurements definition for IMS - UID_35069

Performance measurement data is important for operator to analyze network performance. 
The performance measurement data related to IMS is missing. If an operator deploys IMS, no 3GPP defined performance measurements can be used.

TS 32.404, 32.409 contain the Performance measurements applicable to IMS.

- HSDPA performance measurements - UID_35073

In WCDMA 3GPP Release 5, a new transport channel was introduced: the High-Speed Downlink Shared Channel (HS-DSCH), which provides enhanced support for interactive, background, and to some extent, streaming Radio Access Bearer (RAB) services in the downlink. HS-DSCH transmission facilitates several new features. But to support them with minimum impact on the existing radio interface protocol architecture, a new MAC sub-layer, MAC-hs, has been introduced for HS-DSCH transmission.

HSDPA O&M requirements are need to satisfy the requirement of HSDPA

TS 32.405 contains performance measurements for HSDPA with both FDD and TDD modes.

Trace Management (OAM7-Trace) - UID_35039

Subscriber and Equipment Trace provide very detailed information at call level on one or more specific mobile(s). This data is an additional source of information to Performance Measurements and allows going further in monitoring and optimisation operations.

Contrary to Performance Measurements, which are a permanent source of information, Trace is activated on user demand for a limited period of time for specific analysis purposes.

Trace plays a major role in activities such as determination of the root cause of a malfunctioning mobile, advanced troubleshooting, optimisation of resource usage and quality, RF coverage control and capacity improvement, dropped call analysis, Core Network and UTRAN end-to-end 3G procedure validation.

Hence, specifications for Subscriber and Equipment Trace pertaining to high-level concepts and requirements of trace, to Subscriber and UE activity trace data definition and management, to trace data collection control and configuration management, and to bulk interfaces for trace data transfer from the network to the Network Manager were produced by:

- SA5 (having primary responsibility)

- CT1, CT4, RAN3 (having secondary responsibility) on trace activation/deactivation

- CT1, CT3, CT4 (having secondary responsibility) on End-to-end tracing for IMS

In particular it was added:

- End-to-end tracing for IMS: Stage 1 by OMA, Stage 2/3 SA5, CT1/3/4 - UID_35040

The Open Mobile Alliance™ (URL:http://www.openmobilealliance.org/) has developed a set of technology agnostic service level tracing requirements (OMA-RD-OSPE-V1_0-20050614-C.pdf).

Service Level Tracing (SLT) improves and simplifies end-to-end service diagnostics and enhances the Mobile Operators' ability to manage complex services. SLT is aimed at end-to-end service-level diagnostics, rather than per node tracing. By definition, SLT is the ability to capture and log all relevant information at each component within a service chain, associated with a specific service that is initiated either by an end user or a component (OMA-RD-OSPE-V1_0-20050614-C.pdf).

3GPP SA5 (by CRs 32.101, 32.421/2/3), in coordination with 3GPP CT1, CT3, CT4 has developed the appropriate specifications for end-to-end service tracing for IMS to fulfil the OMA OSPE service level tracing requirements. OMA OSPE service level tracing requirements specific to OMA enablers utilising IMS (OMA-IMSinOMA-V1_0-20050204-C.zip) were addressed within OMA.

- IRP for Subscriber and Equipment Trace Management - UID_35063

Trace management IRP (TS 32.441/2/3/5, CRs 32.632/3/5) applies to both Signalling Based Activation and Management Based Activation and allows:

- Activation/Deactivation/Interrogation of a Trace Session from the NM with one unique Trace Reference

- Trace report to be notified to NM with the known Trace Reference

Without the Trace management IRP there is no standardized centralized way for managing the trace.

## 7.16	Charging Management small Enhancements (CH7)  UID_320007

Acronym:		CH7

Responsibility:	S5

References

| Document | Title/Contents |
| --- | --- |
| WID(s) |
| SP-060442 | WID on Alternate Charged Party (ACP) for IMS |
| SP-060546 | WID on Align 3GPP Charging with OMA PoC Enabler Release 2.0 |
| Impacted Specifications |
| 32.240 | Charging architecture and principles |
| 32.250 | Circuit Switched (CS) domain charging |
| 32.251 | Packet Switched (PS) domain charging |
| 32.252 | Wireless Local Area Network (WLAN) charging |
| 32.260 | IP Multimedia Subsystem (IMS) charging |
| 32.270 | Multimedia Messaging Service (MMS) charging |
| 32.272 | Push-to-talk over Cellular (PoC) charging |
| 32.273 | Multimedia Broadcast and Multicast Service (MBMS) charging |
| 32.296 | Online Charging System (OCS): Applications and interfaces |
| 32.297 | Charging Data Record (CDR) file format and transfer |
| 32.298 | Charging Data Record (CDR) parameter description |
| 32.299 | Diameter charging applications |
| New Dedicated Specifications/Reports |
| none | none |

- Alternate Charged Party (ACP) for IMS (CH7-IMS-ACP) - UID_320008

The charging specifications were not supporting any other billing model than "Calling party pays". 
A mechanism to guarantee the delivery of the charged party indication in a trusted manner was needed in a standardized optional way for IMS sessions to be charged to an alternate subscriber, or service within a serving network. It was provided an alternate charged party in the Charging Data Function (CDF).

The function is based on the service aspects that define the service as charging a subscriber who is not the originating party, but has been identified as being responsible for the charges. This was implemented via CRs to offline charging functions in 32.240, 32.260, 32.298, 32.299. Online charging was out of scope of this release.

- Align 3GPP Charging with OMA PoC Enabler Release 2.0 (CH7-PoC) - UID_330004

OMA has asked 3GPP SA5 to provide a PoC Charging solution for the enhancements of OMA PoC Release 2.
The OMA Push-to-Talk over Cellular Version 2.0 includes several new chargeable features which impact the 3GPP SA5 TS 32.272 defining charging for OMA PoC version 1.0, when used with 3GPP IMS core network. 
This alignment has been realized via CRs against 32.240, 32.272, 32.299 and 32.298.

## 7.6	Open Service Access (OSA7) UID_31071

Acronym:		OSA7

Responsibility:	S1,C5

The Open Service Access (OSA) enables service application developers to make use of network functionality through open, standardised, secure, extensible and scalable interfaces. Applications see the network functionality offered to them as a set of Service Capability Features (SCFs) in the OSA API. 
These SCFs provide access to the network capabilities on which the application developers can rely when designing their applications. The OSA API is independent of where or which network capabilities are implemented in the network, and of vendor specific solutions and programming languages.

A secure OSA API is a key enabler for the Virtual Home Environment (VHE) system concept, which requires users to be consistently presented with the same personalised services in whatever network and terminal, subject to the capabilities of both. OSA needs to evolve in form of small technical enhancements based on market/ implementations feedback and also addition of new functionality. The OSA specifications were developed by the Joint-Working-Group (JWG) of Parlay, the ETSI TISPAN Project OSA and 3GPP CT5. The 3GPP2 is using the 3GPP Stage 3 specifications, where an annex defines the extension of the capabilities to enable operation in cdma2000 systems environment.

OSA APIs (29.198-family)

- The OSA specifications define a set of APIs that enables operator and 3rd party applications to make use of network functionality through a set of open, standardized interfaces.

- The specifications are derived from a UML model of the OSA API.  Using the latest document and code generation techniques, the detailed technical description documents, the IDL code, WSDL code and Java API are all produced from a single source UML model.  This ensures alignment between all versions, all formats of the API.

OSA Web Services (29.199-family)

- Access to Service Capability Features is realised by using modern state of the art access technologies, like distributed object oriented technique and Web Services technologies. WSDL description of the interfaces are attached to the technical specifications.

References

| Document | Title/Contents |
| --- | --- |
| WID(s) |
| SP-050183 | S1 WID on OSA Stage 1 |
| CP-070200 | C5 WID on OSA Stage 2/3 enhancements |
| Impacted Specifications |
| 22.127 | OSA; Stage 1 (SA1) |
| 23.198 | OSA; Stage 2 (CT5) |
| - | Stage 3 Specifications |
| 29.198-01 | OSA API; Part 1: Overview |
| 29.198-02 | OSA API; Part 2: Common data definitions |
| 29.198-03 | OSA API; Part 3: Framework |
| 29.198-04-1 | OSA API; Part 4: Call control; Subpart 1: Call control common definitions |
| 29.198-04-2 | OSA API; Part 4: Call control; Subpart 2: Generic call control SCF |
| 29.198-04-3 | OSA API; Part 4: Call control; Subpart 3: Multi-party call control SCF |
| 29.198-04-4 | OSA API; Part 4: Call control; Subpart 4: Multimedia call control SCF |
| 29.198-05 | OSA API; Part 5: User interaction SCF |
| 29.198-06 | OSA API; Part 6: Mobility SCF |
| 29.198-07 | OSA API; Part 7: Terminal capabilities SCF |
| 29.198-08 | OSA API; Part 8: Data session control SCF |
| 29.198-11 | OSA API; Part 11: Account management SCF |
| 29.198-12 | OSA API; Part 12: Charging SCF |
| 29.198-13 | OSA API; Part 13: Policy management SCF |
| 29.198-14 | OSA API; Part 14: Presence and Availability Management (PAM) SCF |
| 29.198-15 | OSA API; Part 15: Multi-media Messaging (MM) SCF |
| 29.199-01 | OSA; Parlay X web services; Part 1: Common |
| 29.199-02 | OSA; Parlay X web services; Part 2: Third party call |
| 29.199-03 | OSA; Parlay X web services; Part 3: Call notification |
| 29.199-04 | OSA; Parlay X web services; Part 4: Short messaging |
| 29.199-05 | OSA; Parlay X web services; Part 5: Multimedia messaging |
| 29.199-06 | OSA; Parlay X web services; Part 6: Payment |
| 29.199-07 | OSA; Parlay X web services; Part 7: Account management |
| 29.199-08 | OSA; Parlay X web services; Part 8: Terminal status |
| 29.199-09 | OSA; Parlay X web services; Part 9: Terminal location |
| 29.199-10 | OSA; Parlay X web services; Part 10: Call handling |
| 29.199-11 | OSA; Parlay X web services; Part 11: Audio call |
| 29.199-12 | OSA; Parlay X web services; Part 12: Multimedia conference |
| 29.199-13 | OSA; Parlay X web services; Part 13: Address list management |
| 29.199-14 | OSA; Parlay X web services; Part 14: Presence |
| New Dedicated Specifications/Reports |
| - | Stage 3 Specifications |
| 29.198-04-5 | OSA API; Part 5: Call control; Subpart 4: Conference call control SCF |
| 29.198-16 | OSA API; Part 16: Service broker SCF |
| 29.199-15 | OSA; Parlay X web services; Part 15: Message broadcast |
| 29.199-16 | OSA; Parlay X web services; Part 16: Geocoding |
| 29.199-17 | OSA; Parlay X web services; Part 17: Application-driven Quality of Service (QoS) |
| 29.199-18 | OSA; Parlay X web services; Part 18: Device capabilities and configuration |
| 29.199-19 | OSA; Parlay X web services; Part 19: Multimedia streaming control |
| 29.199-20 | OSA; Parlay X web services; Part 20: Multimedia multicast session management |
| 29.998-06-1 | OSA API Mapping; Part 6: User location - user status service mapping; Subpart 1: Mapping to MAP |
| 29.998-06-2 | OSA API Mapping; Part 6: User location - user status service mapping; Subpart 2: Mapping to SIP |

New and enhanced functionality was added in Release 7 as follows:

- OSA Service Brokering 	(new TS 29.198-16)
The Service Broker function enables the delivery of multiple services in the network of an operator in a managed and controlled fashion, providing an API that supports functionality including Service Selection, Service Provisioning, Feature Interaction and Service Chaining.

- Message Broadcast Web Service 	(new TS 29.199-15)

- Geocoding Web Service 	(new TS 29.199-16)

- Application Driven QoS Web Service 	(new TS 29.199-17)

- Device Capabilities and Configuration Web Service 	(new TS 29.199-18)

- Multimedia Streaming Control Web Service 	(new TS 29.199-19)

- Multimedia Multicast Control Web Service 	(new TS 29.199-20)

- OSA API Conference Call Control SCF 	(new TS 29.198-04-5)

- Update OSA Stage 2/3 to take account of Web Service industry developments

- Update Web Services to align with completion of IETF work (impact also on previous Releases)

## 7.7	Rel7 Security enhancements

To be written by Xavier [as stated by Michael]

Acronym:		APIJAVA

UID_743009

Main Responsibility:	C6

References for "Rel7 Security enhancements"

| Document | Title/Contents |
| --- | --- |
| WID(s) |
| GP-022566 | WID on XXX |
| Impacted Specifications |
| TS 24.008 | Example |
| New Dedicated Specifications/Reports |
| TS 22.146 | Example |

Your text: what does it offer? (Stage 1 summary) How does it impact the network? (Stages 2 and 3 summary). PLEASE DON’T JUST COPY-PASTE THE TEXT FROM THE WID BUT CHECK WHAT WAS ACTUALLY DONE!

Extract from the Work Plan (info for the writer only, to be deleted when providing actual text):

| 252 | 732030 | Rel7 Security enhancements | 1 | S3 | SEC7 |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 253 | 732031 | HTTPS connection between a UICC and a NAF | 2 | S3 | SEC7-HSUN | 33.222, 24.109, 33.918 | SP-050573 |
| 254 | 732032 | 2G GBA: 2G SIM usage in 3GPP GAA framework | 2 | S3 | SEC7-2GGBA | 33.220, 33.290 | SP-050576 |
| 255 | 732033 | Generic Authentication Architecture usage extensions and optimisations | 2 | S3 | SEC7-GAA2 | 33.220, 29.109 | SP-050578 |
| 256 | 32034 | SS7 TCAP security Gateway | 2 | S3 | SEC7-NDS-TCAPsec | 33.200, 33.204 | SP-050579 |
| 257 | 310004 | SA3 aspects of SEC7-NDS-TCAPsec | 3 | S3 | SEC7-NDS-TCAPsec-SA3 | 33.200, 33.204 | SP-050579 |
| 258 | 310005 | TCAPsec Gateway | 3 | C4 | SEC7-NDS-TCAPsec-CT4 | new TS 29.204 | CP-060170 |

## 7.8	Video Codec Performance Requirements

Written by P. Usai

Acronym:		VICPer

UID_34030

Main Responsibility:	S4

References for "Video Codec Performance Requirements "

| Document | Title/Contents |
| --- | --- |
| WID(s) |
| SP-040836 | WID on Video Codec Performance Requirements |
| Impacted Specifications |
| TS 26.140 | Multimedia Messaging Service (MMS); Media formats and codes |
| TS 26.234 | Transparent end-to-end Packet-switched Streaming Service (PSS); Protocols and codecs |
| TS 26.235 | Packet switched conversational multimedia applications; Default codecs |
| TS 26.346 | Multimedia Broadcast/Multicast Service (MBMS); Protocols and codecs |
| New Dedicated Specifications/Reports |
| - | None |

Traditionally, MPEG and ITU have specified only encoded bitstream syntax and decoders normatively for audio and video codecs. The decoders specified are only for error-free bitstreams, i.e., packet losses are not considered. In contrast, 3GPP speech/audio specifications include encoders and decoders pair. They also address the codec operation over typical channel conditions.

The scope of this work item is to specify Video encoder quality metrics, quality requirements, and to  provide a specification that meets those requirements; besides, to specify decoder quality requirements under channel errors for 3GPP packet switched services. The specifications will include minimum performance requirements and reference implementations.

The encoder specifications are informative. The error concealment techniques at the decoder are also informative. The reference implementations shall meet the minimum performance requirements specified. The vendors are encouraged to surpass the specified minimum performance requirements.

Objectives :

- Create a specification that describes decoder operation under typical GERAN/UTRAN channel conditions including

  - A reference decoder implementation

  - Capability to detect packet losses

  - Ability to perform minimal concealment for video regions in error (e.g., copy from co-located regions in previous frame(s))

- Create a specification that describes encoder operation including

  - A reference encoder implementation

  - Generate valid bitstreams that under the constraint of average and peak bitrates achieve specified video quality when decoded by above specified decoder

Completion: 55%

## 7.9	3G-324M Video Telephony Call Setup Times Improvements

Written by P. Usai

Acronym:		VTCSTI

UID_34034

Main Responsibility:	S4

References for "3G-324M Video Telephony Call Setup Times Improvements "

| Document | Title/Contents |
| --- | --- |
| WID(s) |
| SP-050404 | WID on 3G-324M Video Telephony Call Setup Times Improvements |
| Impacted Specifications |
|  | [Paolo, Table incomplete] |
| New Dedicated Specifications/Reports |
|  | [Paolo, Table incomplete] |

Video telephony is very important for the successful adoption of UMTS. 3G-324M, the basis for 3GPP circuit-switched multimedia calls, was based on H.324 and has been evolving ever since its first introduction into 3GPP specifications in Rel-99. As part of this evolution, new codecs have been proposed and adopted in 3GPP to improve the quality of service. These evolutions have been focusing so far on the media quality and not on other aspects such as call set-up time, which also greatly affects user experience.

Using Rel-99, the time taken to set up a 3G-324M call is currently significantly longer than that taken to set up a voice call. This quality of experience is broadly acceptable to early UMTS adopters. However, as adoption becomes broader, this tolerance will decrease.

In the interest of facilitating broader adoption of UMTS and mobile video telephony, further solutions should be identified to accelerate 3G-324M. This may be accomplished by several methods including optimizing the in-band call control (H.245).

The objective of this work item is to reduce 3G-324M call set-up time to the equivalent of a voice call. Since methods to achieve this goal have already been proposed and adopted in other standards bodies, SA4 decided to reuse as much as is relevant of the existing solutions. Therefore SA4 suggested a phased approach to this work. First SA4 liaised to SA1 to get requirements for this work and liased also with GERAN (depending on the output on the Feasibility Study on Enhanced Support of Video Telephony).  Then SA4 decided to consider the work of ITU-T SG16 WP2 Q.1 that developed a H.324M call setup acceleration solution at the April, 2006 meetings in Geneva.  The solution is a combination of three different proposals, previously known as FastMedia, Fast Session Setup, and Accelerated Call negotiation.

[Paolo, please update this statement]

The SA4 plan is to accept the Annex K/H.324 approved at a special WP2/16 Plenary meeting held on June 13, 2006.

## 7.10	VoIMS bearer related enhancements  UID_32099

Responsibility:	S2

References

| Document | Title/Contents |
| --- | --- |
| WID(s) |
| GP-022566 | WID on XXX |
| Impacted Specifications |
| TS 24.008 | Example |
| New Dedicated Specifications/Reports |
| TS 22.146 | Example |

Your text: what does it offer? (Stage 1 summary) How does it impact the network? (Stages 2 and 3 summary). PLEASE DON’T JUST COPY-PASTE THE TEXT FROM THE WID BUT CHECK WHAT WAS ACTUALLY DONE!

Extract from the Work Plan (info for the writer only, to be deleted when providing actual text):

| 240 | 32099 | VoIMS bearer related enhancements | 1 | S2 | VoIMS |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 241 | 20032 | Improved support of IMS Realtime Services using HSDPA/HSUPA | 2 | R2 | RANimp-IMSRealTime |  | RAN_Work_Items_History |

### 7.10.1	Improved support of IMS Realtime Services using HSDPA/HSUPA  UID_32099

Responsibility:	R2

References

| Document | Title/Contents |
| --- | --- |
| WID(s) |
| RP-050160 | WID on Improved support of IMS Realtime Services using HSDPA/HSUPA |
| Impacted Specifications |
| None | - |
| New Dedicated Specifications/Reports |
| None | - |

HSDPA and HSUPA are very important features for operators to carry efficient multimedia services in conjunction with IMS. However, there is a need to investigate further the possibilities to enhance the support for IMS real time services, e.g. minimizing the service interruption time in case of handover and ensuring efficient radio resource utilization.

The objective is to improve the support for IMS real time services using HSDPA/HSUPA.

Conclusion: there is enough functionality in Rel-6 to support VoIP over HSDPA/HSUPA; however, the VoIP capacity and RT Gaming issues have not been optimized. Remaining open items moved to the following WIs:

- Improved support of gaming over HSDPA/EDCH

- Continuous connectivity for packet data users

Closed Dec 2005; Status Report in RP-050667

## 7.11	MBMS-related enhancements

### 7.11.1	MBMS Enhancements

Written by M. Clayton

Acronym:		MBMSE

UID_31084

Main Responsibility:	S1

References

| Document | Title/Contents |
| --- | --- |
| WID(s) |
| SP-050389 | WID on MBMS Enhancements |
| Impacted Specifications |
| TS 22.146 | Multimedia Broadcast/Multicast Service (MBMS); Stage 1 (CR 22.146-0046 SP-050742) |
| TS 22.246 | Multimedia Broadcast/Multicast Service (MBMS) user services; Stage 1 (CR 22.246-0006; CR 22.246-0007 SP-050530) (CR 22.246-0009 SP-060308) |
| TS 22.228 | Service requirements for the Internet Protocol (IP) multimedia core network subsystem (IMS); Stage 1 (CR 22.228-0034 SP-050510) |
| New Dedicated Specifications/Reports |
| - | - |

With the increasing deployment of MBMS services in networks, users will expect more stable services and more access alternatives for accessing them, e.g. via IP accesses such as WLAN. From operators’ point of view it would also be desirable to profit from the radio-resource efficient broadcast / multicast mechanisms provided by MBMS transport services for IMS based services. Examples could be value-added services like e-learning or PoC-enhancements. Additionally, MBMS should provide higher bit-rates for applications like digital TV etc.

For these purposes, although the basic functionality already exists in Rel-6 MBMS, additional requirements are necessary to enhance the current MBMS in Rel-7 and enable IMS to use MBMS transport.

The additional requirements identified are:

-	Enabling IMS to use the MBMS bearer service;

-	MBMS reception over IP accesses, e.g. I-WLAN;

-	Higher MBMS bit-rate services (The impact on the throughputs in the RAN should be investigated).

-	Support for adaptation of MBMS to the QoS resources provided by the access network(s).

These new requirements have been carefully considered regarding their effects on Rel-6 terminals and MBMS Rel 6 bearer service to ensure backwards compatibility.

### 7.11.2	MBMS FDD Physical layer Enhancements  UID_340042

Responsibility:	R1

References

| Document | Title/Contents |
| --- | --- |
| WID(s) |
| RP-070226 | WID on MBMS FDD Physical layer Enhancements |
| Impacted Specifications |
| TR 25.905 | Feasibility study on improvement of the Multimedia Broadcast / Multicast Service (MBMS) in UTRAN |
| TS 25.101 | User Equipment (UE) radio transmission and reception (FDD) |
| TS 25.104 | Base Station (BS) radio transmission and reception (FDD) |
| TS 25.211 | Physical Channels and mapping of Transport channels (FDD) |
| TS 25.212 | Multiplexing and Channel coding (FDD) |
| TS 25.213 | Spreading and modulation (FDD) |
| TS 25.214 | Physical Layer procedures (FDD) |
| TS 25.306 | UE Radio Access capabilities definition |
| TS 25.331 | Radio Resource Control (RRC) protocol specification |
| TS 25.346 | Introduction of the Multimedia Broadcast Multicast Service (MBMS) in the Radio Access network (RAN); Stage 2 |
| TS 25.402 | Synchronisation in UTRAN Stage 2 |
| TS 25.433 | UTRAN Iub interface NBAP signalling |
| New Dedicated Specifications/Reports |
| None | - |

TR 25.905 studied the possibility of transmitting the MBMS service on a DL only carrier using a SFN network with an FDD channel structure. The study shows that the attainable data rates using a SFN operation for MBMS can be greatly increased with a minimum impact on the physical channel structure, and thus minimum impact on UE receivers. 
In order to take full advantage of the attainable data rates however higher order modulation and receiver performance supporting SFN operation is necessary.

It adds support for DL only SFN operation for FDD including:

- Configuration of a common primary scrambling code,

- Receiver support for suitable equaliser technology, i.e. similar to Type-2 and Type-3,

- Handling of delay spread in the UE receiver to support reception of SFN MBMS that supports the assumed deployment scenario (to be discussed by RAN4)

- Ensuring backwards compatibility with the existing UTRA physical layer architectures in existing spectral assignments (legacy UEs should not camp on a dedicated SFN MBMS carrier),

- Support for 16QAM on S-CCPCH,

- Necessary radio protocol enhancements to support FDD SFN operation on a DL only MBMS carrier

- SFN area selection and reselection for the dedicated SFN MBMS carrier

- Minimum UE capabilities related to the support of SFN MBMS reception and the support of simultaneous services on the unicast carrier

- Iub user and control plane protocols to support FDD SFN operation

- UE reception performance requirements for applicable bands for the SFN transmission

- BTS requirements for 16QAM transmission on S-CCPCH for applicable bands for the SFN transmission

Conditions applied:

- The UE mobility requirements and procedures related to the unicast carrier must be met.

- No optimisations are done within this work item for single receiver (one local oscillator) UEs, i.e. MBMS data loss may occur during periods where a single receiver UE is receiving on the unicast carrier.

- The SFN area will be limited to the RNC area.

- The unicast serving RNC does not need to be aware of a UE receiving transmissions from a SFN MBMS carrier.

Completed May 2007; Status Report in RP-070290

### 7.11.3	MBMS TDD Physical layer Enhancements  UID_340043

Responsibility:	R1

References

| Document | Title/Contents |
| --- | --- |
| WID(s) |
| RP-070241 | WID on MBMS TDD Physical layer Enhancements |
| Impacted Specifications |
| TR 25.905 | Feasibility study on improvement of the Multimedia Broadcast / Multicast Service (MBMS) in UTRAN |
| TS 25.102 | User Equipment (UE) radio transmission and reception (TDD) |
| TS 25.105 | BS radio transmission and reception (TDD) requirements |
| TS 25.123 | Requirements for support of radio resource management (TDD) |
| TS 25.221 | Physical channels and mapping of transport channels onto physical channels (TDD) |
| TS 25.222 | Multiplexing and channel coding (TDD) |
| TS 25.223 | Spreading and modulation (TDD) |
| TS 25.224 | Physical layer procedures (TDD) |
| TS 25.306 | UE Radio Access capabilities definition |
| TS 25.331 | Radio Resource Control (RRC) protocol specification |
| TS 25.346 | Introduction of the Multimedia Broadcast Multicast Service (MBMS) in the Radio Access network (RAN); Stage 2 |
| TS 25.402 | Synchronisation in UTRAN Stage 2 |
| TS 25.433 | UTRAN Iub interface NBAP signalling |
| New Dedicated Specifications/Reports |
| None | - |

TR 25.905 studied the possibility of transmitting the MBMS service on DL using an SFN network with a TDD channel structure. The study shows that the attainable data rates using a SFN operation for MBMS can be greatly increased with a minimum impact on the physical channel structure, and thus minimum impact on UE receivers. 
In order to take full advantage of the attainable data rates however higher order modulation and receiver performance supporting more delay spread is necessary.

It adds support for SFN operation for TDD 3.84Mcps / 7.68Mcps including:

- Configuration of a common scrambling code for a subset or a all timeslots,

- Receiver support for suitable equaliser technology, including diversity reception

- Handling of delay spread in the UE receiver to support reception of SFN MBMS that supports the assumed deployment scenario (to be discussed by RAN4)

- Ensuring backwards compatibility with the existing UTRA physical layer architectures in existing spectral assignments (legacy UEs should not camp on a dedicated SFN MBMS carrier),

- Support for 16QAM on S-CCPCH,

- Necessary radio protocol enhancements to support TDD SFN operation

- SFN area selection and reselection for the dedicated SFN MBMS carrier

- Minimum UE capabilities related to the support of SFN MBMS reception and the support of simultaneous services on the unicast carrier

- Iub user and control plane protocols to support TDD SFN operation

- UE reception performance requirements for applicable bands/slots for the SFN transmission

- BTS requirements for 16QAM transmission on S-CCPCH for applicable bands/slots for the SFN transmission

- RF Coexistence

Conditions applied:

- The UE mobility requirements and procedures related to the unicast carrier must be met.

- No optimisations are done within this work item for single receiver (one local oscillator) UEs, i.e. MBMS data loss may occur during periods where a single receiver UE is receiving on the unicast carrier.

- The SFN area will be limited to the RNC area.

- The unicast serving RNC does not need to be aware of a UE receiving transmissions from a SFN MBMS carrier.

Completed May 2007; Status Report in RP-070291

### 7.11.4	MBMS LCR TDD Physical layer Enhancements  UID_350022

Responsibility:	R1

References

| Document | Title/Contents |
| --- | --- |
| WID(s) |
| RP-070253 | WID on MBMS LCR TDD Physical layer Enhancements |
| Impacted Specifications |
| TR 25.905 | Feasibility study on improvement of the Multimedia Broadcast / Multicast Service (MBMS) in UTRAN |
| TS 25.102 | User Equipment (UE) radio transmission and reception (TDD) |
| TS 25.105 | BS radio transmission and reception (TDD) requirements |
| TS 25.123 | Requirements for support of radio resource management (TDD) |
| TS 25.221 | Physical channels and mapping of transport channels onto physical channels (TDD) |
| TS 25.222 | Multiplexing and channel coding (TDD) |
| TS 25.223 | Spreading and modulation (TDD) |
| TS 25.224 | Physical layer procedures (TDD) |
| TS 25.306 | UE Radio Access capabilities definition |
| TS 25.331 | Radio Resource Control (RRC) protocol specification |
| TS 25.346 | Introduction of the Multimedia Broadcast Multicast Service (MBMS) in the Radio Access network (RAN); Stage 2 |
| TS 25.402 | Synchronisation in UTRAN Stage 2 |
| TS 25.433 | UTRAN Iub interface NBAP signalling |
| New Dedicated Specifications/Reports |
| None | - |

TR 25.905 studied the possibility of transmitting the MBMS service on DL using an SFN network with a 3.84 Mcps TDD channel structure. The study shows that the attainable data rates using a SFN operation for MBMS can be greatly increased (with a minimum impact on the physical channel structure, and thus minimum impact on UE receivers.). In order to take full advantage of the attainable data rates however higher order modulation and receiver performance supporting more delay spread is necessary. It is assumed that similar performance gains can be achieved with respect to 1.28 Mcps TDD.

It adds support for SFN operation for TDD 1.28Mcps including:

- Demonstrate gains with respect to Rel-6 MBMS

- Configuration of a common scrambling code for a subset or a all timeslots

- Receiver support for suitable equaliser technology including joint detection.

- Handling of delay spread in the UE receiver to support reception of SFN MBMS that supports the assumed deployment scenario

- Phase shifting for SFN transmission

- Ensuring maximum backwards compatibility with the existing UTRA physical layer architectures in existing spectral assignments(legacy UEs should not camp on a dedicated SFN MBMS carrier)

- No precluding Rel6 MBMS transmission modes in the same deployment

- Support for 16QAM on S-CCPCH

- Support for TDD SFN operation coexisting with R6 MBMS on a unicast carrier

- Necessary protocol enhancements to support TDD SFN operation

- SFN area selection and reselection for the dedicated SFN MBMS carrier

- Minimum UE capabilities related to the support of SFN MBMS reception and the support of simultaneous services on a unicast carrier

- Iub user and control plane protocols to support TDD SFN operation

- UE reception performance requirements for applicable slots for the SFN transmission

- BTS requirements for 16QAM transmission on S-CCPCH for applicable slots for the SFN transmission

- RF Coexistence

Conditions applied:

- The UE mobility requirements and procedures related to the unicast carrier must be met.

- No optimisations are done within this work item for single receiver (one local oscillator) UEs, i.e. MBMS data loss may occur during periods where a single receiver UE is receiving on the unicast carrier.

- The SFN area will be limited to the RNC area.

- The unicast serving RNC does not need to be aware of a UE receiving transmissions from a SFN MBMS carrier.

Completed May 2007; Status Report in RP-070292

### 7.11.5	MBMS User Service Extensions

Written by P. Usai

Acronym:		MBMSUSE

UID_34038

Main Responsibility:	S4

References for "MBMS User Service Extensions "

| Document | Title/Contents |
| --- | --- |
| WID(s) |
| SP-050838 | WID on "MBMS User Service Extensions" |
| Impacted Specifications |
| TS 26.346 | Multimedia Broadcast/Multicast Service (MBMS); Protocols and codecs |
| TS 26.946 | Multimedia Broadcast/Multicast Service (MBMS) user service guidelines |
| New Dedicated Specifications/Reports |
| - | None |

It is expected, that the user equipment capabilities will evolve and that the minimal UE capability requirements increases and allow more flexible services for the release 7 time frame.  For instance, one limiting UE capability for MBMS release 6 was that the UE should avoid using interactive bearer resources or any other uplink bearer resources while receiving an MBMS transmission. A number of useful service functions become possible and need to be specified, if MBMS UEs may start using an uplink communication channel in parallel with an MBMS reception channel. Since MBMS is intended to serve large audience, the usage of the uplink resources must be controlled to avoid overload situations in the uplink and in infrastructure nodes.

Also OMA BAC-BCAST is currently preparing a Mobile Broadcast Service specification. MBMS is considered as one of their broadcast distribution systems. The MBMS User Services should be aligned with the OMA BAC-BCAST service enabler.

The objective of the work is to extend MBMS release 6 procedures and provide the required changes in the release7 specifications.  The intention is that MBMS Release 7 extensions provide backward compatibility to MBMS Release 6 terminals. Main objectives are :

- MBMS User Service optimizations, whenever the gain justifies the changes.

- Enhanced services such as interactive services while consuming an MBMS stream and protecting the network against possible overload situations due to these enhanced services.

- Usage of interactive and streaming bearers for MBMS user service delivery, including bearer independent procedure.

- Alignment with OMA BCAST where appropriate.

Completion : 20%

## 7.12	Optimizations for Multimedia Telephony over IMS

Written by P. Usai

Acronym:		OMTIMS

UID_34035

Main Responsibility:	S4

References for "Optimizations for Multimedia Telephony over IMS "

| Document | Title/Contents |
| --- | --- |
| WID(s) |
| SP-060226 | WID on Optimizations for Multimedia Telephony over IMS |
| Impacted Specifications |
| TS 26.235 | Packet switched conversational multimedia applications; Default codecs |
| TS 26.236 | Packet switched conversational multimedia applications; Transport protocols |
| New Dedicated Specifications/Reports |
| - | None |

A number of existing SA4 specifications related to Multimedia telephony over IMS were originally created for CS conversational services for which they are concise. For multimedia telephony over IMS however there is a much larger degree of freedom in how to implement the service, implying that the direct adoption of the existing specifications is neither necessarily optimal nor unambiguous. Moreover, the referenced IETF transport protocols are defined service agnostic, which consequently also leaves room for optimisations considering the architectural constraints of IMS.

The ongoing work in SA1, SA2 and RAN2 (see linked work items above) have further implications on SA4 owned specifications related to Multimedia telephony over IMS and it is regarded appropriate to make the required specification updates in a co-ordinated effort.

A couple of optimisation opportunities such as transport protocol optimisations, advanced techniques for jitter buffering, packet loss concealment, media handling in video-conferencing or echo-cancellation have already been pointed out. However, in order to allow a co-ordinated effort and even possibly to include further promising opportunities this work item aims in a phased approach to

- identify,

- explore, and

- evaluate

the optimisation opportunities under consideration of the above-mentioned ongoing work in the other groups in parallel with their development. This leads to improved service quality and efficiency, and facilitates the optimisation of existing work items, e.g.

“Multimedia Telephony capabilities for IMS (MITE)”,

“Improved Support of IMS Realtime Services using HSDPA/HSUPA”,

“Study Item on IMS enhancements and optimisations for real time communication. (IMS-RT)”, and

“Characterisation of Adaptive Jitter Management Performance for VoIP Services, (OMTIMS-CAJMP)”.

About the last work item (BB) listed above, the aim is to quantify the effects of jitter on voice quality at the terminal and core network. Current work aims to define and optimize end-to-end VoIMS for HSDPA/EUL, where voice is required to meet or exceed the performance of CS in terms of voice distortion, delay and capacity.  A major factor limiting HSDPA/EUL performance is the amount of packet jitter passed to the decoder or transcoder.  As users are added to the system, jitter increases until the delay or packet loss exceeds the acceptable target levels.  Currently it is assumed, if adaptive jitter management is not used, that jitter will be converted directly to delay; therefore, jitter, and capacity, can only increase.  However, examples of a class of Jitter Management algorithms that use well-known signal processing techniques may mitigate jitter without increasing the end-to-end delay.  Such algorithms will be limited by their effect on voice quality, but can remove the subjective effect of the delay .  These algorithms provide also a tool for adaptive jitter management for both SA1 and SA2 when evaluating end-to-end VoIMS performance.  Therefore, it is felt appropriate for SA4 to quantify the amount of jitter the decoder can accommodate while maintaining voice quality at target levels.

By analogy, this is similar to the ability of decoders to perform packet loss concealment (PLC).  While PLC produces speech that has less quality than a perfect channel would produce, the effects on the user are such that a modest level of loss will have minimal impact on quality, and allows for relatively large increases in capacity.  If network capacity were planned with the assumption that there can be no packet loss, then capacity would be quite low.  Similarly, the current assumption that jitter is converted to an equivalent amount of delay is also unnecessarily limiting capacity.

In addition, it will be possible for different manufacturers to create their own version of the jitter buffer algorithm, as is currently done for PLC.  However, PLC tests are well-known and a reference implementation is given for every codec. The same is planned for adaptive jitter management, providing an example methodology for assessing the subjective quality of any given algorithm, as well as an example adaptive jitter management algorithm (one "static and one "dynamic"example).  The example algorithms will provide information on acceptable jitter range in the network. Again by analogy, packet loss targets are taken from subjective tests of the reference PLC algorithm.

It should be noted that PLC algorithms can directly reduce packet loss effects by using packets that arrive beyond their jitter protection; in other words, packets that have already been replaced by concealment algorithms can be resynchronized into the decoder if they arrive late, and this can greatly mitigate the effects of packet loss, further increasing capacity, and quality beyond CS performance.

Completion : 50 %

## 7.13	Network selection enhancements (NSP-CR)  UID_7041

Responsibility:	S1

References

| Document | Title/Contents |
| --- | --- |
| WID(s) |
| SP-050227 | SA1 SID on Review of Network Selection Principles |
| SP-060220 | SA1 WID on Network selection enhancements |
| CP-060357 | CT1 WID on Network Selection Enhancements – Procedural aspects |
| Impacted Specifications |
| TS 21.905 | Vocabulary for 3GPP Specifications |
| TS 22.011 | Service accessibility |
| TS 22.101 | Service aspects; Service principles |
| TS 23.122 | Non-Access-Stratum (NAS) functions related to Mobile Station (MS) in idle mode |
| TS 24.008 | Mobile radio interface Layer 3 specification; Core network protocols; Stage 3 |
| TS 25.304 | User Equipment (UE) procedures in idle mode and procedures for cell reselection in connected mode |
| TS 31.102 | Characteristics of the Universal Subscriber Identity Module (USIM) application |
| TS 45.008 | Radio subsystem link control |
| New Dedicated Specifications/Reports |
| None | - |

Following TR 22.811 (Study on Network Selection Principles (NetSel)  UID_31073) and the network selection workshop, this work translates the findings into specifications. Changes included:

- The definitions in 21.905 are corrected to align the definitions with those already used in the existing stage 2 and stage 3 specifications of the protocol. One definition corrected (VPLMN), three definitions and one abbreviation added, style changed (HPLMN) in one definition to match the others (CR 21.905-0068 SP-060033).

- An optional requirement is added to allow alternate UE behaviour which would allow the UE to go to the HPLMN if available and not return to the last RPLMN. This behaviour is under the control of the operator (CR 22.011-0069r2 SP-060221).

- A new feature is introduced that prompts the end user to confirm that roaming is required when near a border (CR 22.011-0070 SP-060033).

- A clarification is added to clause 3.2.2.1 to clarify that the ME shall utilise all the information stored in the USIM related to network selection (CR 22.011-0071 SP-060033).

- An option was added to display either all the available EHPLMNS or just the highest available based on a USIM flag when in Manual Network Selection mode (CR 22.011-0072 SP-060033).

- A new requirement was added in clause B of 3.2.2.2 indicating that additional information on the available PLMN may be presented when the user is in manual mode (CR 22.011-0073 SP-060033).

- A new requirement added as an optional feature of the ME, for the user to be able to set a preference in the ME for the mode that shall be used at switch on. If set then the ME would select this preference rather than the default mode (CR 22.011-0074 SP-060033).

- Steering of Roaming requirements were introduced that allow the HPLMN to direct the UE to select a specific VPLMN and to direct the UE to steer away from a specific VPLMN (CR 22.011-0075 SP-060033).

- A statement was added to indicate that the safe roaming functionality is only applicable if the UE is in automatic mode of operation (CR 22.011-0076 SP-060311).

- The list of PLMN types listed to include Forbidden PLMNs was extended as this is considered useful information to a user (CR 22.011-0077 SP-060311).

- An implementation option is added to indicate that at power-on only, if RPLMN is not available in the SIM/USIM, or if RPLMN and EPLMN are not available, but the HPLMN is, then the UE should register on the HPLMN/EHPLMN immediately. This is an exception and the UE remains in manual mode (CR 22.011-0078r1 SP-060426).

- A small addition was made to clause 3.2.2.8 on Steering of Roaming to clarify the effect on the User Controlled PLMN List and the Forbidden List. The restriction that a successful registration on a forbidden PLMN only happens in manual mode was removed (CR 22.011-0079r3 SP-060451).

- A change was made to 23.011 clause 4.4.3 that the ME shall read all the information of data files stored in the SIM related to network selection (CR 23.122-0098r2 CP-060359).

### 7.13.1	Network selection enhancements (NSP) - UE Conformance Testing  UID_25048

Responsibility:	R5

References

| Document | Title/Contents |
| --- | --- |
| WID(s) |
| RP-080135 | WID on Network Selection Enhancements – Procedural aspects |
| Impacted Specifications |
| TS 34.108 | Common test environments for User Equipment (UE) conformance testing |
| TS 34.123-1/2/3 | User Equipment (UE) conformance specification |
| New Dedicated Specifications/Reports |
| None | - |

Status Report in RP-080286; Completion 30%; Target Dec 2008

## 7.14	Packet Switched Streaming Enhancements

Written by P. Usai

Acronym:		PSSe

UID_34039

Main Responsibility:	S4

References for "Packet Switched Streaming Enhancements "

| Document | Title/Contents |
| --- | --- |
| WID(s) |
| SP-060361 | WID on Packet Switched Streaming Enhancements (PSSe) |
| Impacted Specifications |
| TS 26.234 | Transparent end-to-end Packet-switched Streaming Service (PSS); Protocols and codecs |
| TS 26.244 | Transparent end-to-end packet switched streaming service (PSS); 3GPP file format (3GP) |
| New Dedicated Specifications/Reports |
| - | None |

3GPP RAN groups have developed high capacity HSDPA bearers which allow for higher video frame rates and sizes, and media quality than currently defined. The H.264 Baseline Profile Level 1b for instance allows only for bitrates up to 128kbps.

Further, the Packet-switched Streaming Service (PSS) feature must be enhanced to allow provision of MBMS User Service using PSS where MBMS Bearer Service is not available or desirable.

It is well known that user experience is strongly influenced by the switching time between channels (“channel surfing”) and the ability to provide feedback (interactivity such as voting, etc).  Improvements in this area will make PSS even more valuable.

The 3GPP file format (3GP) is defined in PSS, although it is used by many services, including MMS, IMS and MBMS. In order for 3GP files to support new features of these services as well as other improvements, e.g. carriage of the new DIMS (Dynamic and Interactive Multimedia Scenes) media type, server file extensions (FLUTE), some improvements will be necessary.

The objective of the work is to enhance the existing Packet Switched Streaming (PSS) specifications with new functionality and state of the art configurations of media codec configurations.

- Adjustments to allow MBMS transmission using PSS

- Align media codec configurations to available bearer rates

- Improve the interactivity between the client and the server.

- File format enhancements (carriage of DIMS etc)

- Improve switching time between channels

Completion : 0 %

## 7.15	Enhanced USIM Phonebook

To be written by Xavier

Acronym:

UID_

Main Responsibility:	C6

References for "Enhanced USIM Phonebook"

| Document | Title/Contents |
| --- | --- |
| WID(s) |
| GP-022566 | WID on XXX |
| Impacted Specifications |
| TS 24.008 | Example |
| New Dedicated Specifications/Reports |
| TS 22.146 | Example |

Your text: what does it offer? (Stage 1 summary) How does it impact the network? (Stages 2 and 3 summary). PLEASE DON’T JUST COPY-PASTE THE TEXT FROM THE WID BUT CHECK WHAT WAS ACTUALLY DONE!

Extract from the Work Plan (info for the writer only, to be deleted when providing actual text):

| 298 | 320014 | Enhanced USIM Phonebook | 1 | C6 | eUPHBOOK |  | CP-060355 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 299 | 320015 | Requirements for eUPHBOOK | 2 | C6 |  | 21.111 | CP-060355 |
| 300 | 320016 | Implementation of eUPHBOOK | 2 | C6 |  | 31.102 | CP-060355 |

# 9	GERAN improvements

## 9.1	Enhancements of VGCS for public authority officials (EVGCS)  UID_11045

Responsibility:	S1,C1

References

| Document | Title/Contents |
| --- | --- |
| WID(s) |
| CP-050528 | Enhancements of VGCS in public networks for communication of public authority officials |
| Impacted Specifications |
| TS 43.068 | Stage 2 modifications for talker priorisation and display of additional information about the current talker |
| TS 44.068 | Stage 3 modifications for talker priorisation |
| TS 29.002 | Stage 3 enhancements of MAP messages for talker priorisation and display of additional information about the current talker |
| TS 43.068 | Stage 2 modifications for E2E encryption and SMS delivery |
| TS 23.040 | Stage 2 modifications of SMS delivery |
| TS 24.011 | Stage 3 modifications of SMS protocol |
| TS 44.068 | Stage 3 modifications for E2E encryption |
| TS 29.002 | Stage 3 enhancements of MAP messages for E2E encryption and SMS delivery |
| New Dedicated Specifications/Reports |
| - | None |

Voice Group Call Services (VGCS) can be used in public networks for communication of public authority officials (police, firebrigade, etc.). To meet the particular requirements for this purpose additional functionality needs to be supported by VGCS (e.g. encryption, emergency handling, SMS support).

## 9.2	Improvements of VGCS for parallel use of services (IVGCS)  UID_11055

Responsibility:	S1,C1,G2

References

| Document | Title/Contents |
| --- | --- |
| WID(s) |
| SP-050075 | WID on Improvements of VGCS in public networks for parallel use of services |
| SP-040304 | WID on Enhancements of VGCS in public networks for communication of public authority officials |
| NP-050141 | WID on Improvements of VGCS in public networks for parallel use of services |
| GP-071855 | WID on Enhancements for VGCS Applications |
| Impacted Specifications |
| TS 42.068 | Voice Group Call Service (VGCS); Stage 1 (CR 42.068-0013; CR 42.068-0014 SP-050224) |
| TS 43.068 | Voice Group Call Service (VGCS); Stage 2 (CR 43.068-0069r1 CP-060123) |
| TS 44.068 | Group Call Control (GCC) Protocol |
| TS 24.008 | Mobile radio interface Layer 3 specification; Core network protocols; Stage 3 |
| TS 29.002 | Mobile Application Part (MAP) specification |
| TS 48.008 | Mobile Switching Centre - Base Station system (MSC-BSS) interface; Layer 3 specification |
| TS 44.018 | Mobile radio interface layer 3 specification; Radio Resource Control (RRC) protocol |
| New Dedicated Specifications/Reports |
| - | None |

Requirements for use of VGCS in public networks for communication of public authority officials have been defined (SP-040304). These enhancements affect the group call itself. However, further improvements, not directly concerning the group call but the use of other services in parallel, were needed (e.g. SMS to single users during an active group call, use of GPRS in parallel to a VGCS).

# 6	GERAN Features

## 6.1	MS Antenna Performance Evaluation Method and Requirements (APEMR)  UID_50118

Responsibility:	G1,R4

References

| Document | Title/Contents |
| --- | --- |
| WID(s) |
| GP 050284 | WID on MS Antenna Performance Evaluation Method and Requirements |
| Impacted Specifications |
| TS 45.005 | Radio transmission and reception |
| New Dedicated Specifications/Reports |
| TR 25.914 | Measurements of radio performances for UMTS terminals in speech mode |
| TS 25.144 | User Equipment (UE) and Mobile Station (MS) over the air performance requirements |

COST273 has finalized the specification of a method for measurement of radiated output power and radiated sensitivity. This method is applicable both to 3G UE, 2G MS, as well as dual-mode 2G/3G MS/UE antennas for the "speech mode" (MS/UE close to the head). Future envisaged steps will cover the "data mode" and diversity antenna MS/UE. MS/UE antenna performance has a critical impact on coverage and capacity. 
To enable for operators to plan their networks in a systematic manner, ensuring a certain coverage and QoS for their customers, a method for MS/UE antenna performance evaluation and MS/UE antenna minimal performance requirements are needed.

## 6.2	Lower 700 MHz Inclusion in the GERAN specifications (GSM710)  UID_50119

Responsibility:	GP

References

| Document | Title/Contents |
| --- | --- |
| WID(s) |
| GP-050543 | WID on Lower 700 MHz Inclusion in the GERAN Specifications |
| Impacted Specifications |
| TS 24.008 | Mobile radio interface Layer 3 specification; Core network protocols; Stage 3 |
| TS 43.022 | Functions related to Mobile Station (MS) in idle mode and group receive mode |
| TS 44.018 | Mobile radio interface layer 3 specification; Radio Resource Control (RRC) protocol |
| TS 44.118 | Mobile radio interface layer 3 specification, Radio Resource Control (RRC) protocol; Iu mode |
| TS 45.001 | Physical layer on the radio path; General description |
| TS 45.005 | Radio transmission and reception |
| TS 51.010 | Mobile Station (MS) conformance specification |
| TS 51.021 | Base Station System (BSS) equipment specification; Radio aspects |
| New Dedicated Specifications/Reports |
| - | None |

This work included the 698-746 MHz band in the GERAN test specifications.

## 6.3	Support of Conversational Services in A/Gb mode via the PS domain (SCSAGB)  UID_50564

Responsibility:	GP

References

| Document | Title/Contents |
| --- | --- |
| WID(s) |
| GP-061501 | WID on Support of Conversational Services in A/Gb mode via the PS domain |
| Impacted Specifications |
| TS 43.055 | Dual Transfer Mode (DTM); Stage 2 |
| TS 43.064 | Overall description of the GPRS radio interface; Stage 2 |
| TS 44.060 | General Packet Radio Service (GPRS); Mobile Station (MS) - Base Station System (BSS) interface; Radio Link Control/ Medium Access Control (RLC/MAC) protocol |
| TS 45.001 | Physical layer on the radio path; General description |
| TS 45.002 | Multiplexing and multiple access on the radio path |
| TS 45.003 | Channel coding |
| TS 45.005 | Radio transmission and reception |
| TS 45.010 | Radio subsystem synchronization |
| TS 51.010 | Mobile Station (MS) conformance specification |
| TS 51.021 | GSM radio aspects base station system equipment specification |
| New Dedicated Specifications/Reports |
| - | None |

Packet-switched Handover for GERAN A/Gb mode is a prerequisite for supporting conversational services.

It introduces support for conversational services with minimum impact to existing systems. The current functional split of the protocol architecture between core and radio access network is maintained.

To support conversational services in the PS domain in A/Gb mode there is a need to optimise various aspects of the GERAN packet service. For instance, the conversational services would need a reduced transfer delay and a fast acknowledgement procedure over the radio interface, which today are not possible in GERAN A/Gb mode through the PS domain. This work makes possible to:

- Minimise the transfer delay between the SGSN and the MS;

- Improve the feedback reporting mechanism;

- Define a suitable RLC mode allowing retransmissions for delay-sensitive applications;

- Define radio resource management functionalities in order to efficiently support Conversational Services like VoIP in the PS domain in A/Gb mode;

- Optimise radio channel support for conversational QoS (e.g. support of dedicated channels);

- Minimise the protocol overhead on the user plane (e.g. optimisation of IP header adaptation, modifications to LLC/SNDCP protocol headers).

Stage 3 defines the modification of radio resource management functionalities in order to efficiently support Conversational Services in A/Gb mode via the PS domain. Issues like radio resource sharing, impact of DTX, radio performance in case of different AMR modes and impact of RoHC re-initialization are taken into account.
Stage 3 extended the Non-Persistent RLC mode to non-MBMS services.

## 6.4	Addition of new frequency band to GSM (TGSM810)  UID_50565

Responsibility:	GP

References

| Document | Title/Contents |
| --- | --- |
| WID(s) |
| GP-050945 | WID on Addition of new frequency band to GSM (T-GSM810) |
| Impacted Specifications |
| TS 24.008 | Mobile radio interface Layer 3 specification; Core network protocols; Stage 3 |
| TS 43.022 | Functions related to Mobile Station (MS) in idle mode and group receive mode |
| TS 43.030 | Radio network planning aspects |
| TS 44.018 | Mobile radio interface layer 3 specification; Radio Resource Control (RRC) protocol |
| TS 44.060 | General Packet Radio Service (GPRS); Mobile Station (MS) - Base Station System (BSS) interface; Radio Link Control/ Medium Access Control (RLC/MAC) protocol |
| TS 45.001 | Physical layer on the radio path; General description |
| TS 45.005 | Radio transmission and reception |
| TS 45.008 | Radio subsystem link control |
| TS 45.010 | Radio subsystem synchronization |
| TS 45.050 | Background for RF Requirements |
| TS 51.010 | Mobile Station (MS) conformance specification |
| TS 51.021 | GSM radio aspects base station system equipment specification |
| New Dedicated Specifications/Reports |
| - | None |

This work adds a new frequency band to GSM (T-GSM810):

- 806 MHz to 821 MHz:  mobile transmit, base receive;

- 851 MHz to 866 MHz:  base transmit, mobile receive.

## 6.5	Handover of dedicated and shared resources while in dual transfer mode (HODSRDTM)  UID_50567

Responsibility:	GP

References

| Document | Title/Contents |
| --- | --- |
| WID(s) |
| GP-050979 | WID on Handover of dedicated and shared resources while in dual transfer mode |
| Impacted Specifications |
| TS 43.055 | Dual Transfer Mode (DTM); Stage 2 |
| TS 44.018 | Mobile radio interface layer 3 specification; Radio Resource Control (RRC) protocol |
| TS 44.060 | General Packet Radio Service (GPRS); Mobile Station (MS) - Base Station System (BSS) interface; Radio Link Control/ Medium Access Control (RLC/MAC) protocol |
| New Dedicated Specifications/Reports |
| - | None |

Dual Transfer Mode (DTM) enhancements for reduction of the PS service interruption in DTM were completed in Release 6 and focused on improving both the release of the RR connection while in dual transfer mode and the initiation of the RR connection while in packet transfer mode.

However, the PS service interruption caused by a (CS) handover in DTM prevents real-time PS services with strict delay requirements from being used in DTM (e.g. voice call while gaming, voice call while sharing real-time video). While such scenarios are possible in UTRAN, service continuity must also be ensured between UTRAN and GERAN.

It is thus necessary to minimize the PS service interruption at handover in DTM to enable the deployment of any real-time PS service also in DTM and ensure service continuity with UTRAN.

This work evaluates possible solutions for handover of dedicated and shared resources while in DTM, in order to meet QoS requirements for conversational PS services and potentially standardize a solution.

No Mobile Station (MS) and no GSM base station system equipment conformance testing were developed.

## 6.13	Mobile Station Receive Diversity (DARP Phase II) (MSRD2)  UID_50569

Main Responsibility:	GP

References

| Document | Title/Contents |
| --- | --- |
| WID(s) |
| GP-061491 | WID on Mobile Station Receive Diversity (DARP Phase II) |
| Impacted Specifications |
| TS 24.008 | Mobile radio interface Layer 3 specification; Core network protocols; Stage 3 |
| TS 45.005 | Radio transmission and reception |
| TS 51.010-1 | Mobile Station (MS) conformance specification; Part 1: Conformance specification |
| New Dedicated Specifications/Reports |
| - | None |

The feasibility of MS Receive Diversity (MSRD) has been determined in TR 45.912 on evolved GSM/EDGE Radio Access Network (FGE) UID_50568.

MSRD is a downlink feature, which improves the receiver performance of the MS by means of an additional antenna. The introduction of Single Antenna Interference Cancellation (SAIC) characterised by the Downlink Advanced Receiver Performance (DARP) requirements has shown that receiver enhancements in the MS provide significant gains in terms of spectral efficiency. MSRD enhances channel diversity, improves interference cancellation performance for GMSK modulated signals and provides significant gains for 8PSK-modulated signals. Therefore gains in both user throughput and system capacity can be achieved.

Since MSRD is a downlink receiver improvement, it may be specified as a DARP phase II in:

- TS 24.008 as far as concerns the DARP Phase II capability indication;

- TS 45.005 for the Performance requirements and Test Scenarios for MSRD;

- TS 51.010 included the MS conformance Tests.

No hardware upgrades are required in the network to support this feature.

## 6.6	Downlink Dual Carrier (GDCDL)  UID_50579

Responsibility:	GP

References

| Document | Title/Contents |
| --- | --- |
| WID(s) |
| GP-061331 | WID on Downlink Dual Carrier |
| Impacted Specifications |
| TS 24.008 | Mobile radio interface Layer 3 specification; Core network protocols; Stage 3 |
| TS 43.055 | Dual Transfer Mode (DTM); Stage 2 |
| TS 43.064 | General Packet Radio Service (GPRS); Overall description of the GPRS radio interface; Stage 2 |
| TS 44.018 | Mobile radio interface layer 3 specification; Radio Resource Control (RRC) protocol |
| TS 44.060 | General Packet Radio Service (GPRS); Mobile Station (MS) - Base Station System (BSS) interface; Radio Link Control / Medium Access Control (RLC/MAC) protocol |
| TS 45.001 | Physical layer on the radio path; General description |
| TS 45.002 | Multiplexing and multiple access on the radio path |
| TS 45.005 | Radio transmission and reception |
| TS 45.008 | Radio subsystem link control |
| TS 51.010 | Mobile Station (MS) conformance specification |
| New Dedicated Specifications/Reports |
| - | None |

The feasibility of dual-carrier in downlink has been determined during the feasibility study for evolved GSM/EDGE Radio Access Network (see 3GPP TR 45.912, clause 7).

Dual-carrier transmission allows for doubling downlink peak and average user throughputs in a flexible and backwards compatible manner; the peak data rate would be close to 1Mb/s (473.6kbps ( 2). It overcomes one limitation of the GSM radio interface – the 200 kHz carrier bandwidth. This limitation puts a restriction on the rate of data transfer to one and the same user. Dual-carrier GERAN gives increased flexibility in how the system throughput is divided among users.

It is expected that no hardware upgrades are required in the network to support this feature.

The objective of this work item was to specify the support for simultaneous transmissions over two independent carriers in downlink in GERAN.

The possibility for a dual antenna terminal to switch between dual carrier reception and MS receive diversity is envisaged.

Status:	The Stage 2 and Stage 3 are completed. MS conformance tests supporting simultaneous transmissions over two independent carriers in downlink in GERAN is ongoing.

## 6.7	Support of SIGTRAN in GERAN (GSIGT)  UID_50580

Responsibility:	GP

References

| Document | Title/Contents |
| --- | --- |
| WID(s) |
| GP-060450 | WID on Support of SIGTRAN in GERAN |
| Impacted Specifications |
| TS 43.059 | Functional stage 2 description of Location Services (LCS) in GERAN |
| TS 48.001 | Base Station System - Mobile-services Switching Centre (BSS - MSC) interface; General aspects |
| TS 48.006 | Signalling Transport Mechanism Specification for the Base Station System - Mobile Services Switching Centre (BSS-MSC) Interface |
| TS 49.031 | Location Services (LCS); Base Station System Application Part LCS Extension (BSSAP-LE) |
| New Dedicated Specifications/Reports |
| - | None |

Some functions in GERAN (e.g. MSC in Pool, Layered Architecture and Location Services) require an intermediate signalling network for best performance. The Signalling Transport (SIGTRAN) based protocols M3UA and SCTP provide these features to low cost at the same time as it is preparing the interfaces for packet transport rather than dedicated circuits as is the case today. The M3UA and SCTP are used in UTRAN while adopting these protocols in GERAN will also give synergy effects in the core network. Furthermore, signalling over IP removes the link bandwidth constraints of the E1/T1 links in existing SS7 networks.

This work provides a concept for supporting M3UA and SCTP on A-, Lb- and Lp-interfaces and defines the stage 3; making possible SS7 signalling over IP transport between the nodes on each side of the concerned interfaces. 
It introduces support for M3UA and SCTP on A-, Lb- and Lp-interfaces with a minimum of impacts to existing systems. The functional split of the protocol architecture between core and radio access network is maintained.

## 6.11	Latency Reductions (LATRED)  UID_50582

Responsibility:	GP

References

| Document | Title/Contents |
| --- | --- |
| WID(s) |
| GP-061519 | WID on Latency Reductions |
| Impacted Specifications |
| TS 45.001 | Physical layer on the radio path; General description |
| TS 45.002 | Multiplexing and multiple access on the radio path |
| TS 45.003 | Channel coding |
| TS 45.005 | Radio transmission and reception |
| TS 45.010 | Radio subsystem synchronization |
| TS 43.055 | Dual Transfer Mode (DTM); Stage 2 |
| TS 43.064 | General Packet Radio Service (GPRS); Overall description of the GPRS radio interface; Stage 2 |
| TS 44.060 | General Packet Radio Service (GPRS); Mobile Station (MS) - Base Station System (BSS) interface; Radio Link Control / Medium Access Control (RLC/MAC) protocol |
| TS 51.010-1 | Mobile Station (MS) conformance specification; Part 1: Conformance specification |
| TS 51.021 | Base Station System (BSS) equipment specification; Radio aspects |
| New Dedicated Specifications/Reports |
| - | None |

The feasibility to reduce latency has been determined in TR 45.912 on evolved GSM/EDGE Radio Access Network (FGE) UID_50568.

By reducing latency in the radio access network decreases Round Trip Times (RTT) in both, ideal and non-ideal radio conditions. The reduced latency makes it possible to provide low-delay services otherwise not feasible in GERAN (e.g. conversational services such as VoIP and gaming applications) by utilising efficient RLC re-transmission schemes.  
In addition, it would also make applications having many client/server interactions faster. A shorter RTT would also increase the throughput for Transmission Control Protocol (TCP) based services.

Latency reduction techniques were specified, including improved Ack/Nack reporting and reduced Transmission Time Interval (TTI) that characterizes low-latency Temporary Block Flow (TBF). This includes a solution maintaining legacy Uplink State Flag (USF) scheduling and decoding (to allow multiplexing on the same radio resources of low-latency TBFs with legacy ones), and an optimized solution allowing fast USF scheduling and decoding (to be used when multiplexing on the same radio resources of low-latency TBFs with legacy ones is not required). 
Support of DTM was insured as well.

## 6.8	PS Handover between GERAN/UTRAN mode and GAN Mode (GUGAN)  UID_52147

Responsibility:	G2

References

| Document | Title/Contents |
| --- | --- |
| WID(s) |
| GP-061349 | WID on PS Handover between GERAN/UTRAN mode and GAN Mode |
| Impacted Specifications |
| TS 43.318 | Generic access to the A/Gb interface; Stage 2 |
| TS 44.318 | Generic Access (GA) to the A/Gb interface; Mobile GA interface layer 3 specification |
| TS 43.129 | Packed-switched handover for GERAN A/Gb mode; Stage 2 |
| TS 25.306 | UE Radio Access capabilities |
| TS 24.008 | Mobile radio interface Layer 3 specification; Core network protocols; Stage 3 |
| TS 44.060 | General Packet Radio Service (GPRS); Mobile Station (MS) - Base Station System (BSS) interface; Radio Link Control / Medium Access Control (RLC/MAC) protocol |
| TS 25.331 | Radio Resource Control (RRC); Protocol specification |
| TS 51.010 | Mobile Station (MS) conformance specification |
| New Dedicated Specifications/Reports |
| - | None |

The existing GERAN specifications support the Um interface signalling mechanisms required to perform PS handover to/from an MS operating in A/Gb mode. The working assumption for Generic Access (as specified in 3GPP TS 43.318 and 44.318) has so far been that requirements on GERAN should also apply for Generic Access. However, various specifications currently lack procedures applicable for PS handover between GERAN/UTRAN mode and GAN mode as follows:

- a mechanism by which an MS can indicate it supports PS Handover between GERAN/UTRAN and GAN mode;

- PS handover preparation and execution phase activities performed by a target or source GANC;

- a mechanism by which a source GANC can determine the System Information applicable to a target BSS;

- new Up interface control plane messages required to support PS handover between GERAN/UTRAN mode and GAN mode.

The work provides the support for PS handover between GERAN/UTRAN mode and GAN mode.

## 6.9	Higher Uplink performance for GERAN Evolution (HUGE)  UID_50584

Responsibility:	GP

References

| Document | Title/Contents |
| --- | --- |
| WID(s) |
| GP-071083 | WID on Higher Uplink performance for GERAN Evolution |
| Impacted Specifications |
| TS 24.008 | Mobile radio interface Layer 3 specification; Core network protocols; Stage 3 |
| TS 45.001 | Physical layer on the radio path; General description |
| TS 45.002 | Multiplexing and multiple access on the radio path |
| TS 45.003 | Channel coding |
| TS 45.004 | Modulation |
| TS 45.005 | Radio transmission and reception |
| TS 45.008 | Radio subsystem link control |
| TS 45.010 | Radio subsystem synchronization |
| TS 43.055 | Dual Transfer Mode (DTM); Stage 2 |
| TS 43.064 | General Packet Radio Service (GPRS); Overall description of the GPRS radio interface; Stage 2 |
| TS 44.018 | Mobile radio interface layer 3 specification; Radio Resource Control (RRC) protocol |
| TS 44.060 | General Packet Radio Service (GPRS); Mobile Station (MS) - Base Station System (BSS) interface; Radio Link Control / Medium Access Control (RLC/MAC) protocol |
| TS 51.010-1 | Mobile Station (MS) conformance specification; Part 1: Conformance specification |
| TS 51.021 | Base Station System (BSS) equipment specification; Radio aspects |
| New Dedicated Specifications/Reports |
| - | None |

The following have been studied in TR 45.912 on evolved GSM/EDGE Radio Access Network (FGE) UID_50568.

- higher symbol rates in uplink;

- higher order modulations and turbo codes;

- a combination of higher symbol rate and higher order modulations.

Significant improvements in spectral efficiency, peak / average bit rates and bit rates at cell border have been shown.

The compatibility objectives of GERAN evolution can be met. Two compatibility objectives of special concern are the impact to legacy BSS hardware and to legacy frequency planning (which could not be met with a 2 TRX implementation option). Those could be met if a symbol rate of 1.2 times the legacy symbol rate is chosen (i.e. 325ksymbols/s), the transmitted signal bandwidth is small enough to be received by a single legacy transceiver, i.e. (less than) 271 kHz (assuming symbol rate sampling for a legacy transceiver), and the interference to adjacent channels is minimized.

To maximise the fraction of the installed legacy BTS hardware where the feature can be implemented, different levels of MS/NW support are motivated. Nevertheless, implementation of the full feature may require hardware enhancements on BSS, but the compatibility objective of coexistence with existing legacy frequency planning is still met.

To further enhance the uplink radio performance of the GERAN with minimal impact to higher layers of the existing EGPRS by means of:

- 1.2 times higher symbol rate (325 ksymbols/s);

- 16-ary modulation;

- 32-ary modulation;

- turbo codes.

To facilitate different levels of MS/NW support, the following levels are defined:

- 16-ary modulation with 271 (legacy) ksymbols/s symbol rate

- 16-ary modulation and 32-ary modulation with 325 ksymbols/s symbol rate

- 32-ary modulation with 325 ksymbols/s symbol rate, and possibly turbo coding (see Note)

NOTE:	Turbo coding is included if the achievable gains (already shown by simulations) justify the cost of its introduction; if so, the Turbo coding scheme defined in 3GPP TS 25.212 will be reused.

It has to be ensured that the different levels of MS and NW support can interoperate. For this reason, it will be studied how the levels above have to be supported by a HUGE MS.

- If it is agreed that different levels of MS support exist, MS support for a higher level (e.g. C) will imply support for all lower levels (e.g. A, B).

- If it is agreed that there is only one level of MS support, it will imply MS support of A, B and C.

The number of options needs to be kept as low as possible in order to reduce complexity. If agreed by TSG GERAN during the work item, level A (16-ary modulation with legacy symbol rate) will be removed.

Different transmit filters were considered. In this work, three prerequisites are that the transmitted signal bandwidth will be small enough to be received by a single legacy transceiver (i.e. less than 271 kHz), that the coverage is maximised and that the interference to adjacent channels will be minimised.

Performance evaluations and optimisations focused on asynchronous networks with uplink diversity but other scenarios were also considered.

Status:	Specifications completed except for conformance testing.

## 6.10	REduced symbol Duration, Higher Order modulation and Turbo coding for downlink (REDHOT)  UID_50121

Responsibility:	GP

References

| Document | Title/Contents |
| --- | --- |
| WID(s) |
| GP-071080 | WID on REduced symbol Duration, Higher Order modulation and Turbo coding (REDHOT) for downlink |
| Impacted Specifications |
| TS 24.008 | Mobile radio interface Layer 3 specification; Core network protocols; Stage 3 |
| TS 45.001 | Physical layer on the radio path; General description |
| TS 45.002 | Multiplexing and multiple access on the radio path |
| TS 45.003 | Channel coding |
| TS 45.004 | Modulation |
| TS 45.005 | Radio transmission and reception |
| TS 45.008 | Radio subsystem link control |
| TS 45.010 | Radio subsystem synchronization |
| TS 43.055 | Dual Transfer Mode (DTM); Stage 2 |
| TS 43.064 | General Packet Radio Service (GPRS); Overall description of the GPRS radio interface; Stage 2 |
| TS 44.018 | Mobile radio interface layer 3 specification; Radio Resource Control (RRC) protocol |
| TS 44.060 | General Packet Radio Service (GPRS); Mobile Station (MS) - Base Station System (BSS) interface; Radio Link Control / Medium Access Control (RLC/MAC) protocol |
| TS 51.010-1 | Mobile Station (MS) conformance specification; Part 1: Conformance specification |
| TS 51.021 | Base Station System (BSS) equipment specification; Radio aspects |
| New Dedicated Specifications/Reports |
| - | None |

In TR 45.912 on evolved GSM/EDGE Radio Access Network (FGE) UID_50568, the benefits of higher order modulation, higher symbol rates and Turbo codes have been demonstrated. Increased data throughput in the entire cell, improved sensitivity and improved spectral efficiency in GERAN networks, have been shown.

Complexity analysis indicates the feasibility of higher order modulations and turbo codes in the downlink. Some features will put higher requirements on the NW/MS. This justifies different levels of MS support. Implementation of the full feature may require hardware enhancements on BSS, but the compatibility objective of coexistence with existing legacy frequency planning is still met.

This work further enhances data rates, sensitivity and spectral efficiency of the GERAN network in typical network layouts through new modulation and coding schemes using:

- QPSK modulation;

- 16-QAM modulation;

- 32-QAM modulation;

- Turbo coding based on independent encoding of RLC/MAC blocks;

- Higher symbol rate (325 ksymbols/s).

To facilitate different levels of MS support, the following approach is taken:

- Level A: 8-PSK, 16-QAM and 32-QAM combined with Turbo coding;

- Level B: QPSK, 16-QAM and 32-QAM combined with Turbo coding and Higher symbol rate.

All MS supporting the REDHOT feature are required to support either level A or level A+B.

The Turbo coding scheme defined in TS 25.212 is reused.

At higher symbol rate, legacy services received by legacy terminals are not worsened: this may imply having more than one solution depending on the interference situation in the network.

REDHOT is compatible with Mobile Station Receive Diversity (MSRD), Dual Carrier Downlink (DCDL), latency reductions (LATRED) and Higher Uplink performance for GERAN Evolution (HUGE). 
REDHOT can be used simultaneously with any of these and compatibility was maintained between these WIs on e.g. mutual aligned signalling.

Status:	Specifications completed except for conformance testing.

# 10	Feasibility Studies

## 10.1	Study on Multimedia Telephony Capabilities for IMS (MITE)  UID_31082

Responsibility:	S1

References

| Document | Title/Contents |
| --- | --- |
| WID(s) |
| SP-050387 | WID on Multimedia Telephony Capabilities for IMS |
| Impacted Specifications |
| - | - |
| New Dedicated Specifications/Reports |
| TR 22.973 | IMS Multimedia Telephony service; and supplementary services |
| TS 22.173 | IP Multimedia Core Network Subsystem (IMS) Multimedia Telephony Service and supplementary services; Stage 1 |

In addition to reusing the IMS system as defined by 3GPP, TISPAN is defining an IMS based Multimedia Telephony service, which is an evolution of the CS based Telephony service provided by traditional ISDN and PSTN. A similar service, defined by 3GPP, is needed for wireless access to IMS, in order to be able to define services to the end-users, and to support interoperability in multi-vendor and multi-operator environment and to provide the user with the same experience across the different IP based accesses and domains.

Define in close cooperation with TISPAN a minimum set of capabilities required to secure multi-vendor and multi-operator inter-operability for Multimedia Telephony and related Supplementary Services.

Conclusion:	Recommendation to standardize a service with the name IMS Multimedia Telephony service endorsing the TISPAN service definition for supplementary services applicable to 3GPP Systems as follows:

- Originating Identification Presentation (OIP);

- Originating Identification Restriction (OIR);

- Terminating Identification Presentation (TIP);

- Terminating Identification Restriction (TIR);

- Communication Diversion (CDIV);

- Communication Hold (HOLD);

- Communication Barring (CB) with the addition that the ICB service extension with a roaming condition (the roaming condition is set to true when the served user is roaming);

- Message Waiting Indication (MWI);

- Conference (CONF);

- Explicit Communication Transfer (ECT);

The study has found one supplementary service not covered by TISPAN but applicable to a 3GPP specified IMS Multimedia Telephony service and that is:

- Communication Diversion: Communication Forwarding on Mobile Subscriber Not Reachable.

TS 22.173 defines the IMS Multimedia Telephony service and the minimum set of capabilities required to secure multi-vendor and multi-operator inter-operability for Multimedia Telephony and related Supplementary Services.

Result:	Spin-off Feature Multimedia Telephony Service for IMS (MTSI) UID_7038

## 10.2	Study on Behaviour of Multi system UEs (BMSU)  UID_31050

Responsibility:	S1

References

| Document | Title/Contents |
| --- | --- |
| WID(s) |
| SP-050502 | WID on Behaviour of multi system terminals |
| Impacted Specifications |
| - | - |
| New Dedicated Specifications/Reports |
| TR 22.936 | Multi-system terminals |

There is a need to standardize how a multi system terminal should perform system selection. TR 22.936 keeps clearly visible the distinction between 3GPP internal PLMN selection requirements and multi system selection requirements.

TR 22.936 clearly identifies which requirements are mandatory and which can be left implementation specific, taking into account interoperability and network protection. The intention is to ensure that the multi system operation does not lead to non 3GPP-compliant behaviour by the terminal.

Particular issues handled included, but was not restricted to:

- Whether the system selection or PLMN selection should take higher priority in a multi system terminal. Related to this, the criteria for system change would need to be defined. This could take the form of a background scan of higher priority systems. If this is supported the interaction between the user's and the operator's preferences should be studied. The existing PLMN selector lists and HPLMN information could be re-used in system selection.

- Whether automatic or manual system selection mode, or both, needs to be supported. The study should identify different methods of system selection and their impact on 3GPP specifications.

- If any priority lists for user's preferences, supported systems or network operators are needed, it should be studied if these should reside in the terminal memory or in the smartcard. When dealing with the 3GPP-compliant part of the terminal, available of the UICC can be assumed.

- Testing of multi-mode terminals, in particular the mechanisms for system selection should be considered. The study should consider what needs to be tested and by whom.

Conclusion:	The method of system selection must provide means for the operator to set system preferences. It may also allow user to set system preferences but more consideration is needed in this area. Also, system of selection must, having switched to a different system, be capable of switching back to the original system and should allow manual system selection as this is likely to be a regulatory requirement in some regions.

## 10.3	Study on IMS with real time services deployment (IRTSD)  UID_31054

Responsibility:	S1

References

| Document | Title/Contents |
| --- | --- |
| WID(s) |
| SP-040465 | WID on Feasibility Study on IMS with real time services deployments |
| SP-040467 | WID on Feasibility Study on Combining CS calls and IMS sessions |
| Impacted Specifications |
| - | - |
| New Dedicated Specifications/Reports |
| TR 22.979 | Feasibility study on combined Circuit Switched (CS) calls and IP Multimedia Subsystem (IMS) sessions |

Operators regard IMS as a key feature. However, there remain issues with the efficiency of transferring Voice over IP over the radio interface, and, with the capability of the GSM radio interface to handle VoIP.  Additionally, operators are interested in techniques that may provide the ability to smooth the rollout and accelerate the take-up of IMS.

In order to use the existing CS infrastructure to transport the voice traffic for multimedia services, there are many different techniques for combining the CS and IMS parts together. However, leaving vendors and operators to develop these different techniques in isolation would lead to interoperability problems and fragmented/small markets.

The objective was to study the different options for combining CS and IMS capabilities. It covers requirements, possible solutions and their trade-offs. Two possible solutions have been identified:

- use CS real time bearers with IMS sessions to better satisfy the existing requirements in TS 22.228;

- add an IMS session to a CS call for exchanging media (e.g. picture, video clip, file) and vice versa;

As the two solutions are related on the architectural level, the stage 2 feasibility studies are documented in a single TR.  TR 22.979 is addressing migration and interoperability issues.

From an end-user point of view, one of the possible fast deployment scenarios for IMS services is to build on existing service such as CS calls and enhance by adding IMS sessions. As an example, the user may want to send a picture while on a voice call. Or alternatively, the user may want to add a voice call to a chat session, e.g. to speak to a member of the chat room. It is desired to make such adding of media simple from user point of view and manageable from an operator point of view. There is a need to assure a single, interoperable solution for adding media to CS calls and IMS sessions including terminals, infrastructure and services from various vendors. The proposed solution should have no or very minor impact on existing CS and IMS services and infrastructure.

TR 22.979 studies solutions for adding IMS sessions to a CS call or a CS call to an IMS session.

Conclusion: 	The requirements captured in TR 22.979, clause 9 should be reflected in 3GPP Stage 1 specifications. 
It recommends developing a new TS for combinational services, to be referenced via the existing appropriate specifications.

## 10.4	Study on Videotelephony teleservice (VidTel)  UID_31075

Responsibility:	S1

References

| Document | Title/Contents |
| --- | --- |
| WID(s) |
| SP-050506 | WID on Study on Videotelephony teleservice |
| Impacted Specifications |
| - | - |
| New Dedicated Specifications/Reports |
| TR 22.903 | Study on Videotelephony teleservice |

The study should provide a full definition of videotelephony as a teleservice, provided that backward compatibility with existing services (e.g. videotelephony services based on the CS Multimedia call Bearer Service) can be assured. 
The requirements for enhancing videotelephony should build on the CS Multimedia call Bearer Service.
In call modifications (rate adaptation) and modifications at call establishment should be investigated.

TR 22.903 concludes that enhancements were needed including:

- Call setup time improvements

- Additional support of supplementary services

- Charging improvements

- Improved in call modification

- More efficient emergency videotelephony call support

- User notification

These enhancements can be provided by either:

  - standardising a new videotelephony teleservice

  - improving the existing videotelephony service that is based on BS30

For both alternatives backwards compatibility with existing videotelephony services using the BS30 Multimedia Call Bearer Service is essential.

Some of the possible advantages for defining a videotelephony teleservice are:

- ability to negotiate the codecs used in the VT call using already standardised mechanisms available today for teleservices

- ability to differentiate the charging between videotelephony and data transfers using BS30

- simplification of handling of call modification for network operators compared to videotelephony services provided using the BS30 Multimedia Call Bearer Service

- simplification of downgrading the service to speech in case of changing from 3G to 2G and vice versa compared to videotelephony services provided using the BS30 Multimedia Call Bearer Service

- the same handling of supplementary services as other teleservices

- unique subscription for videotelephony services including unique definition within roaming agreements which may improve interoperator charging

- possible definition of a unique emergency videotelephony teleservice (if required)

These need to be balanced against possible disadvantages of defining two alternative solutions for providing videotelephony services.

It is thought that videotelephony will be a telecommunication service that provides the complete capability, including terminal equipment functions, for communication between users according to standardized protocols and transmission capabilities established by agreement between operators.

Conclusion:	In light of these considerations it might be beneficial to fully specify a videotelephony teleservice.

## 10.5	Study on Network Selection Principles (NetSel)  UID_31073

Responsibility:	S1

References

| Document | Title/Contents |
| --- | --- |
| WID(s) |
| SP-050227 | SID on Review of Network Selection Principles |
| SP-060220 | WID on Network selection enhancements |
| Impacted Specifications |
| - | - |
| New Dedicated Specifications/Reports |
| TS 22.811 | Review of network selection principles |

The study should review the network selection mechanisms in TS 22.011 and requirements from other work areas, by considering new methods of access and new operator types and ensuring appropriate access is chosen based on:

- Network selection algorithm used by mobile devices

- End user inter-action & interface

- Network operation

- Multiple Access System scenarios

- User & network operator lists

- National roaming

- International roaming

- RAN evolution

- Radio Planning

- Backwards compatibility

Conclusion:	 it would be beneficial to consider enhancements to the current specifications in a number of areas:

1)	The time the network selection process takes, especially in the cases where UEs support multiple bands and multiple modes.

- Ideal performance targets were identified as: less than 20 seconds to select a PLMN in the case where the RPLMN is not available and less than 5 seconds in the case where the RPLMN is available.

- Methods to improve the time taken for a UE to regain service and hence avoid time consuming searches of all the bands in which a UE can operate were considered.

2)	There is a requirement to provide the tools to a network operator to allow them to offer their customers the best possible experience when roaming into other networks. This includes the ability of the home operator to control their user’s selection of visited network from the perspective of service provisioning, access technology, terminal capability, and so on. Such tools include

- The ability for the HPLMN to dynamically direct a UE to select a different VPLMN.

- The ability to prevent users from selecting specific PLMNs.

- Enhancements to Manual Network Selection to provide the user with additional information to assist their choice.

3)	Network Operators need to dynamically distribute their roaming customers across multiple VPLMNs in a given country.

4)	Practical experience from the implementation of National Roaming has highlighted a number of areas where enhancements to the 3GPP specifications could be considered.

- In the case where a UE is registered to a national roaming partner and loses coverage, the UE will attempt to select the RPLMN (the national roaming partner). In some cases, but not all, it is desirable to register to the HPLMN if it has become available.

- In the case where a UE may oscillate between two PLMNs.

5)	The performance of PLMN selection in border areas needs to be improved, as it has been noted that network operators are advising their customers to manually select the HPLMN to avoid accidental roaming.

6)	In the course of the development of the TR some additional areas for enhancements to the 3GPP specifications have been identified. These are:

- It may be beneficial to standardise a minimum size of list to be supported by the ME and any conclusion should support the normal operational requirements of operators

- The use of the Refresh command should be reviewed to allow the subscriber’s operator to update information, used by the UE, in the most optimum manner possible.

- At power on, in manual mode, if the RPLMN is not found, but the HPLMN is available then the UE should automatically register with it.

- It should be possible for the user to set a preference for either manual or automatic network selection on power-up

Some of the proposed enhancements are feasible for Release 7 completion, while other more complex features should be developed in future releases (see Network selection enhancements (NSP-CR)  UID_7041).

## 10.6	Study on Multimedia Priority Service (PRIOR-MM)  UID_31041

Responsibility:	S1

References

| Document | Title/Contents |
| --- | --- |
| WID(s) |
| SP-060329 | WID on Study Item on Multimedia Priority Service |
| Impacted Specifications |
| - | - |
| New Dedicated Specifications/Reports |
| TR 22.953 | Multimedia priority service feasibility study |

The response to emergency situations (e.g. floods, hurricanes, earthquakes, terrorist attacks) depends on the communication capabilities of public networks. In most cases, emergency responders use private radio systems to aid in the logistics of providing critically needed restoration services.  However, certain government and emergency management officials may have to rely on public network services when the communication capability of the serving network may be impaired, for example due to congestion or partial network infrastructure outages, perhaps due to a direct or indirect result of the emergency situation.

Work is underway to provide standardized Priority Service for authorized persons in the context of CS speech communications (e.g. TR 22.950). Similar prioritized service provision is needed for packet (e.g. IP) based multimedia services including data, video, audio, and text transmission capabilities. There is a need to study concepts, features, and requirements for the support of packet based Multimedia Priority Services.

The following high-level requirements were identified to support Multimedia Priority Service:

- Priority Session Origination,

- Priority Session Establishment,

- Priority Session Progression,

- Priority Radio Resource Queuing,

- Priority Levels,

- Invocation on Demand,

- Applicability to Telecommunications Services,

- Multimedia Priority Service Code/Identifier,

- Roaming,

- Handover,

- Charging Data Record,

- Queuing Requests for Bearer Resources,

- Revision from UTRAN to RAN.

The following primary capabilities were identified to support Multimedia Priority Service:

- IMS

- IETF Resource Priority Header

Conclusion:	Recommendation to add the IETF Resource Priority Header to 3GPP IMS specifications.

## 10.7	Study on Transferring of emergency Call data (eCALL)  UID_31083

Responsibility:	S1

References

| Document | Title/Contents |
| --- | --- |
| WID(s) |
| SP-050388 | Study Item on Transferring of emergency Call data |
| Impacted Specifications |
| - | - |
| New Dedicated Specifications/Reports |
| TR 22.967 | Transferring of emergency call data |

During 2004 a number of discussions were between the Commission for the European Communities (CEC), the automotive industry, the telecommunication industry and ETSI standards groups regarding the provision of in-vehicle emergency calls. Based on initial discussions, a joint initiative of the CEC (DG Enterp and DG InfoSo), industry and other stakeholders was defined with aims to accelerate the development, deployment and use of Intelligent Integrated Safety Systems that use information and communication technologies in intelligent solutions, in order to increase road safety and reduce the number of accidents on Europe's roads. This initiative was called eSafety.

As part of this initiative, eCall was defined as a specific item in the scope of the eSafety initiative. It is intended to extend the current E112 capabilities to enable the Transferring of eCall data between the Vehicle and the Public Safety Answering Points (PSAP). This should rely on existing GSM/UMTS infrastructure.

As a result, the CEC has published Commission Recommendation on the processing of caller location information for the purpose of location-enhanced emergency call services (adopted by the Commission in June 2003). At the time of writing this document, there was no directive, but this has not been ruled out.

This work studies the feasibility of data transmission associated with an emergency communication to the PSAP. 
It consisted in collection of regional requirements, matching these with existing capability within 3GPP specifications and, if essential gaps are identified, to work towards an efficient 3GPP solution.

Part of this work was to collect the minimum data set required by emergency services and identify the most appropriate means to supply this data to the PSAPs.

The work involved co-operation in the short term with European initiatives and groups such as E-MERGE, TRANSPORT PROJECT in ETSI RCC, ETSI MSG, EMTEL, ERM TG 37 and the eCall Driving Group.  
The work also involved co-operation with similar initiatives in other regions.

Conclusion:	with the availability of the report from GSME on the Operators' preferred method of implementation, Work Items can be established in the appropriate Working Groups to complete any standardization work required.

## 10.8	Study on Enhancement of E2E QoS  UID_32073

Responsibility:	S2

References

| Document | Title/Contents |
| --- | --- |
| WID(s) |
| SP-040326 | WID on Study on Enhancement of E2E QoS |
| Impacted Specifications |
| - | - |
| New Dedicated Specifications/Reports |
| TR 23.802 | Architectural enhancements for end-to-end Quality of Service (QoS) |

The mechanisms described in the QoS related 3GPP specifications, especially TS 23.207, are insufficient to achieve fully end-to-end QoS guarantees in case of an interworking with different IP network domains or backbone networks. So the ways to interwork QoS policies and control between different IP network domains are needed.

Current solutions that guarantee QoS end-to-end rely on existing IP QoS models and networks that are controlled by the PLMN operators. Consequently, it will not be easy to achieve fully end-to-end QoS guarantees in case of interworking with different IP network domains or backbone networks.

For some important services with strict end-to-end QoS requirements, such as conversational speech or streaming video, the requirements may not be fully satisfied with existing models in case of an interworking with IP network domains or backbone networks that are not under the control of PLMN operators.

Mechanisms which are scalable and can take into account the overall end-to-end networks performance should be considered to enhance the current architecture, especially when the service traffic goes through different IP network domains or backbone networks.

This work studies different possible solutions to enhance the end-to-end QoS architecture specified in TS 23.207 to achieve improved end-to-end QoS also in case of an interworking with IP network domains or backbone networks that are not under the control of PLMN operators.

Interaction with emerging Next Generation Networks (NGN) standards and work in ITU-T and IETF NSIS were considered.

Conclusion:	The current interconnection model for 3GPP networks is described in GSMA PRD IR.34 and this model takes a pragmatic approach to QoS, relying simply on over-provisioning and marking of User Plane IP packets (using DiffServ) to exchange QoS information (i.e. as per Release 99). According to GSMA, IMS deployment in the near term will rely on this approach, together with SLAs, to deliver QoS on inter-PLMN networks. Such solution is described in Annex A.2.1 and A.2.2 of TS 23.207 and in TR 23.802 clause 5.2.3.

It is generally recognized that in the future new interconnection models may be needed, e.g., to accommodate increased adoption of IP based services and/or support interfacing to other Next Generation Networks and/or when the committed SLAs cannot be met, although the timing and the details of such need is not currently well understood.

Recommendation:	The current interconnection model required by GSMA for 3GPP networks does not require the enhancement of TS 23.207, which may require to be enhanced as a result of other ongoing specification work in 3GPP related to IMS and QoS issues. This work should be frozen until timing and details on the need of new interconnection models become clear.

## 10.9		Study on Bandwidth Saving at Nb Interface with IP transport  UID_7034

Responsibility:	C3

References

| Document | Title/Contents |
| --- | --- |
| WID(s) |
| CP-060168 | WID on Study a Multiplexing at Nb Interface with IP transport |
| Impacted Specifications |
| - | None |
| New Dedicated Specifications/Reports |
| TR 29.814 | Bandwidth Saving at Nb Inteface with IP transport |

For typical payload transported over the Nb interface, the /IP/UDP/RTP header overhead (40 byte for IPv4, 60 byte for IPv6) and the layer 2 header/trailer header overhead (e.g. 38 bytes for Ethernet v2, 7 bytes for POS) are much larger than the transported payload NbFP/codec (e.g. 35 byte for AMR 12.2 kHz and 9 byte for SID frames). It is desirable to reduce the /IP/UDP/RTP header and the layer 2 header/trailer overheads to save bandwidth.

The objective of this work item is to study possible solutions for a simple, optional multiplexing mechanism for the Nb interface and IP transport that allows transporting several NbFP/codec payload PDUs of different bearers. The solution shall minimise impacts to existing network characteristics, in particular jitter and packet delay. The solution shall be suitable for any type of payload transported within NbFP. Though primarily intended and possibly optimised for NbFP transport within 3GPP circuit-switched core networks, the multiplexing design should be generic & future proof by not precluding support of non-NbFP payload types, e.g. standard VoIP bearers or other interfaces such as Iu. The solution shall not modify the standard IP header.

TR 29.814 defines a solution allowing to achieve significant bandwidth reductions in an IP network by multiplexing packets with the same destination address and DiffServ class, while taking care to preserve the optional capability to avoid RTPXtalk situations. Extra bandwidth reduction can further be obtained by supporting RTP header compression. A format of compressed RTP headers has been defined for NbFP transport and the transport formats specified in subclause 9.1.1 and 9.1.2.1 are agreed to be added as options for the Nb interface within the scope of 3GPP Rel-7 work.

## 10.12		Study on Routeing of MT-SMs via the HPLMN  UID_14019

Written by K. Kymalainen

Acronym:		SMS7

UID_14019

Main Responsibility:	C4

References for "Study of a SMS Centre for MT SMS "

| Document | Title/Contents |
| --- | --- |
| WID(s) |
| CP-060701 | Study into Routeing of MT-SMs via the HPLMN |
| Impacted Specifications |
|  | None |
| New Dedicated Specifications/Reports |
| TR 23.840 | Study into Routeing of MT-SMs via the HPLMN |

The purpose of this study WI was:

- To determine the most efficient solution for the implementation of the T-SMSC in the MT-SMS transfer procedure. Such a solution should avoid, wherever possible, negatively affecting existing 3GPP defined functionality.

- To determine the most appropriate way to specify such functionality in 3GPP documentation.

## 10.13		Study on the TCAPsec Gateway concept  UID_7025

Written by K. Kymalainen

Acronym:		SEC7-TCAP

UID_7025

Main Responsibility:	C4

References for "TCAPsec Gateway concept "

| Document | Title/Contents |
| --- | --- |
| WID(s) |
| CP-050687 | Feasibility Study regarding the TCAPsec Gateway Concept |
| CP-060170 | TCAPsec Gateway Function |
| Impacted Specifications |
| TS 29.002 | MAP stage 3 |
| New Dedicated Specifications/Reports |
| TR 29.800 | SS7 Security Gateway |
| TS 29.204 | TCAPsec Gateway Function |

The objective of WI was to create a Technical Report that outlines the feasibility of an SS7 Security Gateway concept. The TR was produced as a temporary container for the functional description of the SS7 Security Gateway.

Study covered network architecture, routeing considerations, and protocol details. The contents of the TR was moved into a new TS 29.204. At the same time specific material related to MAPsec was removed from 3GPP TS 29.002 Rel-7.

The Technical Report on TCAPsec Gateway concept

The Technical Report analyzed the impact of the TCAPsec gateway concept on the stage 3 work, and it gives guidance or proposal for the most efficient solution for the implementation. This analysis was based among others on the following necessary changes to the MAPsec concept, which were identified in SA WG3 to be done to support the new concept:

- The gateway concept includes two ‘protection profiles’: ‘Integrity only' and ’integrity and confidentiality’.

- The security mechanism applies by the gateway above the TCAP layer. The target was to apply protection in a way which is agnostic to the application protocol, so that it can protect other protocols in addition to MAP. It was also planned that the message format, security header, etc. from the MAPsec Rel-4 specification can be re-used.

- Explicit verification of SCCP and MAP-payload addresses against MAPsec SPI was studied.

- The MAPsec gateway concept and the MAPsec Rel-4 NE-based solution need not coexist. A solution was found, in co-operation with the specification manager, e.g. to ‘delete’ the MAPsec Rel-4 NE-based solution from the 3GPP specs, or to make it clear in the gateway specifications that interworking with the MAPsec Rel-4 NE-based solution is not supported.

The Technical Specification on TCAPsec Gateway concept

The objective was to create a Technical Specification that covers network architecture, routeing considerations, and protocol details with regard to the SS7 Security Gateway. The TS replaced TR 29.800 which was the result of the study item on the TCAPsec Gateway Concept.

An identified security weakness in 2G and 3G systems is the absence of security in SS7 networks. The work on MAPsec Rel-4 within 3GPP, would allow network operators to secure SS7 connections for all MAP messages passing between them. However, automatic key management was not finalised, and without this feature, MAPsec was difficult to set up and operate in a large scale. Furthermore, with changes needed in every MAP NE, the Rel-4 MAPsec suffered from low acceptance from vendors and operators.

GSMA IREG requested to complete the work on MAPsec and to a support the use of gateways.

SA WG3 re-initiated the work for Rel-7, where further steps were suggested.

Rather than protecting only MAP messages at the MAP-Network Entity (HLR, VLR, MSC, EIR, gsmSCF, SGSN, GGSN,…) it is envisaged to protect all TCAP user messages (including MAP, CAP and possibly others) at an SS7 Security Gateway which is located at the PLMN's border.

Note that this item was first registerred as a Feasibility Study but ended up being an actual Feature.

## 10.14		Study on using M2PA in 3GPP network  UID_7050

Written by K. Kymalainen

Acronym:		FS-M2PA

UID_7050

Main Responsibility:	C4

References for "FS of using M2PA in 3GPP network "

| Document | Title/Contents |
| --- | --- |
| WID(s) |
| CP-060698 | Feasibility study of using M2PA in 3GPP network |
| Impacted Specifications |
|  | None |
| New Dedicated Specifications/Reports |
| TR 29.801 | Feasibility study of using M2PA in 3GPP networks |

The objective of study WI was to study the advantage and disadvantage of M2PA comparing with the M3UA and the possibility of introducing M2PA in 3GPP and specify the functionalities required on the protocol level to meet the requirements of BICC, MAP and CAP.

After study it was proposed that solution 1 "introducing M2PA"is a recommended option that can be used in 3GPP IP based signalling networks for interface B. For solution 2 "introducing enhanced M3UA", this depends on the progress of IETF.

CR to 3GPP TS 29.202 may be considered in the future to add use of M2PA in 3GPP IP based signalling networks for interface B.

## 10.15		Study on Support of (G)MSC-S - (G)MSC-S Nc Interface based on the SIP-I protocol  UID_320018

Written by K. Kymalainen

Acronym:		NcSIP

UID_320018

Main Responsibility:	C4

References for "FS WID on Support of (G)MSC-S - (G)MSC-S Nc Interface based on the SIP-I protocol"

| Document | Title/Contents |
| --- | --- |
| WID(s) |
| CP-070034 | Support of (G)MSC-S – (G)MSC-S Nc Interface based on the SIP-I protocol |
| Impacted Specifications |
| New Dedicated Specifications/Reports |
| TR 29.802 | (G)MSC-S – (G)MSC-S Nc Interface based on the SIP-I protocol |

As the industry trend moves from Voice over TDM to Voice over IP, it is clear that the majority of the networks (fixed telephony, enterprise, IMS) are moving towards SIP-based signalling.  Currently, 3GPP does not define an interworking scenario for SIP-I interworking into the bearer independent circuit switched network, although it is clear that this is a valid interworking scenario.

In order to avoid the use of a heavyweight interworking function and to provide commonality of products between wireless and wireline networks, this work item provided a feasibility study to investigate the implementation of SIP-I on the Nc Interface as an alternative protocol to BICC. This implementation provides the additional benefits of:

- Providing a standardised SIP-I based Nc Interface which improves network interconnections by removing potential signalling interworking to external SIP-I networks.

- Eases interworking issues for IP-Interconnect and converges SIP-I signalling across the industry, wireless and wireline.

- Standardizing end to end service between mobile subscribers that may be located in different networks, e.g. support of codec negotiation over IP transit network to enable TrFO, SCUDIF etc.

- Provides migration of PLMN to common NGN based SIP signalling.

- Reduces CAPEX for Operators and inter-operator agreements regarding interworking functionality.

The objective of this work item was to create a Technical Report which studies the implementation of the feasibility of SIP-I on the Nc Interface as an alternative to the existing BICC definition. The feasibility study incorporated the following:

- The primary objective was the definition of scenario for providing SIP-I on the Nc Interface interworking with an external SIP-I based signalling network.

- Identify impacts and provide support for interworking SIP-I on the Nc interface with a BICC-based Nc interface.

- Identify impacts and provide support for interworking SIP-I on the Nc Interface with the 3GPP IMS.

- Definition of SIP-I on the Nc Interface in order to provide the interworking as specified above.

- Identification and resolution of the impacts related to the effects on the user plane by providing SIP-I on the Nc Interface.

- Identification and resolution of the impacts related to the effects on existing functional capabilities provided by the existing 3GPP BICC implementation (OoBTC, SCUDIF, CSD, etc.) by providing SIP-I on the Nc Interface.

## 10.16	Study on SOAP/HTTP IRP Solution Sets  UID_35066

Responsibility:	S5

References

| Document | Title/Contents |
| --- | --- |
| WID(s) |
| SP-050610 | WID on Study of SOAP/HTTP IRP Solution Sets |
| Impacted Specifications |
| - | - |
| New Dedicated Specifications/Reports |
| TR 32.809 | Feasibility study of XML-based (SOAP/HTTP) IRP solution sets |

Integration Reference Points (IRPs) need to be extended with the introduction of SOAP/HTTP Solution Sets in order to respond to the growing market and industry demand for such lightweight solutions over the Itf-N.

This TR studies the need to specify a new Solution Set for all Interface, Network Resource Model and Data Definition IRPs based on SOAP/HTTP technology, as additional choice to e.g. CORBA.

This study concludes that SA5 should go ahead with the use of XML-Based Solution Sets beyond Release 7. For a start, a particular focus should be set on Service Management but this shouldn't be restrictive. 
Starting with Service Management implementation should allow a smooth transition and to gain experience.

## 10.17	Study on Itf-N Implementation Conformance Statement (ICS) template  UID_35067

Responsibility:	S5

References

| Document | Title/Contents |
| --- | --- |
| WID(s) |
| SP-050609 | WID on Study of Itf-N Implementation Conformance Statement (ICS) template |
| Impacted Specifications |
| - | - |
| New Dedicated Specifications/Reports |
| TR 32.812 | Itf-N Implementation Conformance Statement (ICS) template |

Interface-N (Itf-N) is the interface between the Network and the Network Manager (NM).
3GPP has produced several IRP specifications for 3G networks' OAM&P. Vendors have developed products in compliance with different versions of these specifications. However, there is currently no 3GPP Implementation Conformance Statement (ICS) specification available for testing a vendor’s Itf-N product.

The study provides a template for Itf-N implementation conformance test. It defines the structure and table format for the ICS on the Information Service (IS) and CORBA solution set level.

A few SA5 studies had been moved from Release 7 to Release 8 as follows:

- Study of Element Operations Systems Function (EOSF) definition  UID_35065

- Study of SA5 MTOSI XML Harmonization  UID_35074

- Study of Common Profile Storage (CPS) Framework of User Data for network services and management  UID_320006

## 10.18	Study on IRP Information Mode  UID_35068

Responsibility:	S5

References

| Document | Title/Contents |
| --- | --- |
| WID(s) |
| SP-050611 | WID on Study of IRP Information Model |
| Impacted Specifications |
| - | - |
| New Dedicated Specifications/Reports |
| TR 32.810 | Information model Integration Reference Point (IRP) Study |

Currently there is no standard interface specified for how the Network Manager Centre (NMC) may access details of Network Element Manager (NEM) IM. Currently this type of information is just specified in Configuration Management (CM) IRP Network Resource Models (NRM) specifications for standard NRMs. Details of vendor specific extensions are not included. The same applies to Performance Management (PM) NRMs.

Typically an NMC will be required to interface to several NEMs from different vendors, each of which may support variants and vendor specific extensions to the standard NRMs for CM and PM. To simplify NM operations, it would be advantageous if a standard interface is specified for an NEM to be able to access an NEM’s Information Model (IM) realization.

The TR studies the possibility of specifying an IM IRP enabling an IRPManager to read an IRPAgent's vendor-specific IM view over Itf-N.

The IM should provide the type of information currently specified in IRP and NRMs IS level specifications, e.g. NRM Information Object Classes (IOC), containment, naming, attributes, attribute valid values, RO/RW access support, notifications supported etc.

The scope of the IM covers 3GPP generic and vendor-specific objects/data.

The IM IRP service needs to cover all IRP views.

This study concludes that there are diverging views on being able to provide the IM at run-time. 
Also applying IM and getting the benefits from legacy Network Elements, is questioned by some. 
It is recommended that IM discovery should be further studied in Release 8 as part of the SA5 LTE feasibility study. 
Application and implementation of IM is feasible. More work is needed and other approaches might be better (e.g. UML Profile). Immediate benefit could be to apply the IM IRP to some of the existing 32.xyz NRM specifications, so that the standard models and capabilities can be expressed in formal and machine readable way.

How IM Discovery might be able to address the challenges of OAM&P for an LTE enabled network could be further studied in Release 8 as part of the SA5 LTE feasibility study.

## 10.19	Study on Evolved UTRA and UTRAN  UID_20023

Responsibility:	RP

References

| Document | Title/Contents |
| --- | --- |
| WID(s) |
| RP-040461 | WID on Study on Evolved UTRA and UTRAN |
| Impacted Specifications |
| - | - |
| New Dedicated Specifications/Reports |
| TR 25.912 | Feasibility study for evolved Universal Terrestrial Radio Access (UTRA) and Universal Terrestrial Radio Access Network (UTRAN) |

With enhancements such as HSDPA and Enhanced Uplink, the 3GPP radio-access technology will be highly competitive for several years. However, to ensure competitiveness in an even longer time frame, i.e. for the next 10 years and beyond, a long-term evolution of the 3GPP radio-access technology needs to be considered.

Important parts of such a long-term evolution include reduced latency, higher user data rates, improved system capacity and coverage, and reduced cost for the operator. In order to achieve this, an evolution of the radio interface as well as the radio network architecture should be considered.

Considering a desire for even higher data rates and also taking into account future additional 3G spectrum allocations the long-term 3GPP evolution should include an evolution towards support for wider transmission bandwidth than 5 MHz. At the same time, support for transmission bandwidths of 5MHz and less than 5MHz should be investigated in order to allow for more flexibility in whichever frequency bands the system may be deployed in.

The study gives a framework for the evolution of the 3GPP radio-access technology towards a high-data-rate, low-latency and packet-optimized radio-access technology. It focuses on supporting services provided from the PS-domain. Studied areas:

- Related to the radio-interface physical layer (downlink and uplink): e.g. means to support flexible transmission bandwidth up to 20 MHz, introduction of new transmission schemes and advanced multi-antenna technologies

- Related to the radio interface layer 2 and 3: e.g. signalling optimization

- Related to the UTRAN architecture: identify the most optimum UTRAN network architecture and functional split between RAN network nodes, not precluding considerations on the functional split between UTRAN and CN (SA2 experts should be invited to the latter topic)

- RF-related issues

Targets for the evolution of the radio-interface and radio-access network architecture:

- Significantly increased peak data rate e.g. 100 Mbps (downlink) and 50 Mbps (uplink)

- Increase “cell edge bitrate” whilst maintaining same site locations as deployed today

- Significantly improved spectrum efficiency ( e.g. 2-4 x Rel6)

- Possibility for a Radio-access network latency (user-plane UE – RNC (or corresponding node above Node B) - UE) below 10 ms

- Significantly reduced C-plane latency (e.g. including the possibility to exchange user-plane data starting from camped-state with a transition time of less than 100 ms (excluding downlink paging delay))

- Scaleable bandwidth: a) 5, 10, 20 and possibly 15 MHz; b) [1.25,] 2.5 MHz: to allow flexibility in narrow spectral allocations where the system may be deployed

- Support for inter-working with existing 3G systems and non-3GPP specified systems

- Further enhanced MBMS

- Reduced CAPEX and OPEX including backhaul

- Cost effective migration from Rel-6 UTRA radio interface and architecture

- Reasonable system and terminal complexity, cost, and power consumption.

- Support of further enhanced IMS and core network

- Backwards compatibility is highly desirable, but the trade off versus performance and/or capability enhancements should be carefully considered.

- Efficient support of the various types of services, especially from the PS domain (e.g. Voice over IP, Presence)

- System should be optimized for low mobile speed but also support high mobile speed

- Operation in paired and unpaired spectrum should not be precluded

- Possibility for simplified co-existence between operators in adjacent bands as well as cross-border co-existence

Conclusion: Rel-8 implementation WI to be started

RAN#33 (Sep 2006) completed. Status Report in RP-060472

## 10.20	Study on Performance Evaluation of the UE behaviour in high speed trains with speeds up to 350 kmph  UID_20034

Responsibility:	R4

References

| Document | Title/Contents |
| --- | --- |
| WID(s) |
| RP-050146 | WID on Performance Evaluation of the UE behaviour in high speed trains with speeds up to 350 kmph |
| Impacted Specifications |
| - | - |
| New Dedicated Specifications/Reports |
| - | - |

UE behaviour in high mobility environments is described in the current specifications up 250 km/h and 120 km/h for HSDPA. In order to ensure a certain level of performance in terms of appropriate data rates (throughput) and QoS for the user in mobility environments with higher speeds. The aim of the study was to:

- identify realistic propagation conditions and multipath models for high speed train environments

- decide on the need to perform simulations of the UE behaviour for speeds up to 350 km/h in high speed train environments including HSDPA

- decide on the need to define minimum performance requirements for the UE and the network assuming high speed train environments with speeds up to 350 km/h

- Identify impact to other groups

Completed items:

- Deployment scenarios agreed

- Simulation results presented for ideal receivers

- Agreed that same performance can be achieved by ideal HSDPA UEs at 350 km/h vs. 120 km/h

- Agreed that there is an issue with Doppler shift variation relating to channel estimation that needs to be considered further as part of the TEI work item.

RAN#32 (Jun 2006) completed. Status Report in RP-060412

## 10.21	Study on UTRA Tower Mounted Amplifier (FDD)  UID_20041

Responsibility:	R4

References

| Document | Title/Contents |
| --- | --- |
| WID(s) |
| RP-0????? | WID on UTRA Tower Mounted Amplifier (FDD) |
| Impacted Specifications |
| - | - |
| New Dedicated Specifications/Reports |
| TR 25.818 | UTRA tower mounted amplifier (FDD) study item technical report |

Objectives of the study:

- Identification of the radio requirements, which need to be standardized for external low noise Tower Mounted Amplifier (TMA) in Rx for UTRA FDD.

- The feasibility of splitting the radio requirements between base station and UTRA FDD TMA.

- Alternatives how UTRA FDD TMA radio requirements could be standardized.

- How to structure UTRA FDD TMA radio requirements (e.g. a single set of UTRA FDD TMA requirements supporting all BS configurations or multiple sets of requirements)

- Impact on current specifications TS 25.104, TS 25.141, and TR 25.942.

- Impact on RRM measurements.

- Impact on conformance testing and overall system responsibility.

The feasibility of standardizing the BS – TMA interface was studied in TR 25.818 regarding the following key aspects:

1)	Feasibility of splitting the radio requirements between BS and TMA

2)	Feasibility of standardization alternatives, including conformance testing and system responsibilities

3)	Impact on Radio Resource Management requirements.

Regarding aspect 1) it was observed that a number of radio performance related parameters would need to be split between BS and TMA. No meaningful TMA specification can be developed without such a radio parameter split, as otherwise there would be no defined performance for the BS+TMA chain. However, this parameter split is non-trivial and would need to be reconsidered for each operating band and for each TMA gain alternative. This would require detailed investigations for the TMA+BS receive / transmit chain in a possible WI.

In particular, for deriving the TMA IMD requirements a set of interference scenarios would need to be considered and their respective IMD levels would need to be agreed and split between the BS and TMA. Furthermore, there seems to be no other way in setting TMA IMD requirements than specifying either the details of the TMA receiver implementation (RX filters, IP3) or having a number of IMD test cases.

There exist different options for the split of the performance between the BS and the TMA. That is true not only for the TMA gain but also for linearity in the TMA amplifier as well as the filtering in the TMA. In order to cope with all different solutions the TMA would have to fulfill the worst case scenario or the base station requirements would have to be tightened for some vendors to be compatible with all TMAs. This would either drive the cost for the TMA or the base stations or it would be a solution with a lot of options which would not guarantee interoperability.

The feeder loss between BS and TMA also needs to be taken into account when defining the radio requirements for BS and TMA. Then any minimum performance requirements defined for the BS+TMA chain can only be ensured for the assumed range of feeder losses.

Regarding aspect 2), it was generally noted that the BS-TMA interface needs to be specified for both, the BS and TMA if the inter-working of BS and TMA of different vendors should be facilitated by 3GPP standards. Three standardization alternatives were considered and as a summary the following can be stated:

-	Alternative 1: Not a standardized solution at all, meaning that it does not allow nor guarantee interoperability and therefore does not make sense for vendors or operators.

-	Alternative 2: Jeopardizes overall system performance and might even violate regulatory requirements and is therefore not acceptable.

-	Alternative 3: A multiple set  of radio parameters has to be split between different  BS and TMA implementations, for all considered frequency bands. That means a non-trivial work which requires a considerable amount of standardization work, which seems difficult to handle within a reasonable WI time plan.  This would either be a solution with a number of non-interoperable options or drive the cost for the TMA or the base stations.

It should be noted that the impact on TMA radio requirements related to antenna feeder sharing with other systems (e.g. GSM in Band VIII) was outside the scope of the SI. This configuration is even more complex and would require further analysis, but the conclusions drawn in this study still apply.

Tower Mounted Amplifiers (TMA) are external low noise RX amplifier and are an important part of the radio network, reducing the system noise figure and improving the sensitivity of the Node B.

The TMA has currently a vendor specific performance and characteristic, whereas the overall system performance is covered by requirements and tests according to the concept of different test ports (TS 25.104, TS 25.141). Radio characteristics are specified at the BS antenna connector. If any external apparatus such as RX amplifier, a filter or the combination of such devices is used, requirements apply at the far end antenna connector.

TMA solutions as to the current date are either vendor specific delivered as a whole site solution or are proprietary from different suppliers and hence a mix of TMA and base stations of different supplier is not possible without loosing flexibility for the operator.

This study proposes different alternatives how external low noise RX amplifier radio requirements for UTRA FDD could be standardized.

RAN#31 (Mar 2006) completed. Status Report in RP-060035

## 10.22	Study on Continuous connectivity for packet data users  UID_20044

Responsibility:	R1

References

| Document | Title/Contents |
| --- | --- |
| WID(s) |
| RP-050391 | WID on Continuous connectivity for packet data users |
| Impacted Specifications |
| - | - |
| New Dedicated Specifications/Reports |
| - | - |

Packet-oriented features like HSDPA and E-DCH in WCDMA/UMTS systems promotes the subscribers’ desire for continuous connectivity, where the user stays connected over a long time span with only occasional active periods of data transmission, and avoiding frequent connection termination and re-establishment with its inherent overhead and delay.

To support a high number of HSDPA users in the code limited downlink the feature F-DPCH was introduced in Rel-6. In the uplink, the limiting factor for supporting a similarly high number of E-DCH users is the noise rise. For such a high number of users in the cell it can be assumed that many users are not transmitting any user data for some time (e.g. for reading during web browsing). So the corresponding overhead in the noise rise caused by maintained control channels significantly limits the number of users that can be efficiently supported. As completely releasing dedicated channels during periods of traffic inactivity would cause considerable delays for re-establishing data transmission and a corresponding bad user perception. This study proposes to reduce the impact of control channels on uplink noise rise while maintaining the connections and allowing a much faster reactivation for temporarily inactive users.

It proposes RAN1 to start an implementation WI.

RAN#29 (Sep 2006) completed. Status report in RP-050427

## 10.23	Study on Improvement of Multimedia Broadcast Multicast Service (MBMS) in UTRAN  UID_20051

Responsibility:	R2

References

| Document | Title/Contents |
| --- | --- |
| WID(s) |
| RP-050746 | WID on Improvement of the Multimedia Broadcast Multicast Service (MBMS) in UTRAN |
| Impacted Specifications |
| - | - |
| New Dedicated Specifications/Reports |
| TR 25.905 | Feasibility study on improvement of the Multimedia Broadcast / Multicast Service (MBMS) in UTRAN |

The study recommends considering the following principles in any new WI for improvement of MBMS in UTRAN. Simultaneous reception on different carriers is possible, but not mandated from the UEs. 
Further RAN4 study is expected to better understand issues relating to simultaneous reception on different carriers.
Full mobility/paging etc. support should be provided by all UEs without mandating 2 LO, including operation on SFN.
This covers the following cases:

- Additional DL carrier without SFN;

- Additional DL-only carrier with or without SFN;

- Non DL-only carrier with SFN (TDD only);

- Additional binded DL-only carriers with or without SFN (LCR TDD only);

- Additional DL-only carriers with or without SFN binded with Non DL-only carrier (LCR TDD only).

RAN#34 (Dec 2006) completed. Status Report in RP-060692

## 10.24	Study on Performance Improvements in Small Cells using HSDPA/EDCH  UID_20052

Responsibility:	R4

References

| Document | Title/Contents |
| --- | --- |
| WID(s) |
| RP-050782 | WID on Performance Improvements in Small Cells using HSDPA/EDCH |
| Impacted Specifications |
| - | - |
| New Dedicated Specifications/Reports |
| - | - |

There is a need to investigate the possibilities to further enhance the ability of HSDPA/HSUPA in certain deployed environments beyond the macro cellular case.

HSDPA and HSUPA are very important capabilities for operators. It is critical that performance of these channels especially in environments and deployment scenarios that are not macro cell based be maximized for a wide range of data services, rates, and throughputs.  This is especially important in smaller cells with lower mobility and “contained” environments, most notably outdoor micro-cells (with at least some users indoor and in building pico-cells.

This is especially relevant when 3GPP technologies compete against technologies deployed specifically to serve contained environments. The UE in these situations may not be the typical hand held terminal but could be embedded implementations inside computers, or a PCMCIA type data card (or other diverse form factors) which may be more amenable to embodiment of the improvements.

The objective was to establish and characterize the small cell and/or contained environments that are of greatest operator interest. The selected environment should be sufficiently characterized to enable accurate simulation of advanced W-CDMA technologies in the environment, most notably those using multiple antennas at the UE and/or Node B.  The number of environments and use cases should be limited in order to allow expeditious completion.

RAN#32 (Jun 2006) closed (no progress). Status Report in RP-060263

## 10.25	Study on Further Improved Performance Requirements for UMTS/HSDPA UE (FDD)  UID_20053

Responsibility:	R4

References

| Document | Title/Contents |
| --- | --- |
| WID(s) |
| RP-050880 | WID on Further Improved Performance Requirements for UMTS/HSDPA UE (FDD) |
| Impacted Specifications |
| - | - |
| New Dedicated Specifications/Reports |
| TR 25.963 | Feasibility study on interference cancellation for UTRA FDD User Equipment (UE) |

For UTRA FDD performance specifications have been developed for UE receivers on the basis of equalization and, for HSDPA, 2-branch receive diversity. Equalization is primarily useful in case of high geometry. Diversity is useful in both low- and high-geometry cases, but UE design issues may affect deployment. So performance improvement in low-geometry is still an important priority, particularly for single-antenna UE.

The improvements specified so far have been for thermal noise and noise-like inter-cell interference, and intra-cell interference caused by multipath. Improvements based on cancellation or rejection of other-cell interference have not been included yet.  Such methods are both better understood and more practical than they have been in the past. For GSM radio access, interference cancellation performance has been specified for single branch receivers. Joint detection methods have been developed for UTRA FDD uplink receivers and UTRA TDD receivers. Contributions have been made showing the link-level performance benefit of single-branch interference cancellation for UTRA FDD UE receivers. It is well-known that 2-antenna receivers using algorithms such as space-temporal equalization can reject other-cell interference, but this aspect has not been included to date in the work item based on 2-branch equalization. So there is an opportunity for significant gain, based on well-known and widely accepted techniques, if the interference rejection aspect can be evaluated and specified.

Since the basic performance improvements from diversity and equalization have been addressed in previous work, and there is now work showing substantial potential gains from other-cell interference cancellation, study of both single-branch and two-branch interference mitigation for UTRA FDD had been started, with two goals:

- to evaluate the feasibility and potential gains  at link and system level

- to investigate the metrics and other aspects of specifying UE performance

Objectives:

- Develop realistic network scenarios and interference models and investigate practical metrics that could be used to specify performance based on interference mitigation.

- Evaluate the feasibility, link performance, and system capacity potential of 2 branch interference mitigation with realistic network scenarios and interference models.

- Evaluate feasibility, link performance, and system capacity potential of 1 branch interference mitigation with realistic network scenarios and interference models.

The network scenarios and interference models have much in common for 1-branch and 2-branch methods.

Conclusion: Small gain was noted on Single Branch Receivers

RAN#36 (May 2007) completed. Status Report in RP-070499

## 10.26	Study on Scope of future FDD HSPA Evolution  UID_20065

Responsibility:	RP

References

| Document | Title/Contents |
| --- | --- |
| WID(s) |
| RP-060217 | WID on Scope of future FDD HSPA Evolution |
| Impacted Specifications |
| - | - |
| New Dedicated Specifications/Reports |
| TR 25.999 | High Speed Packet Access (HSPA) evolution; Frequency Division Duplex (FDD) |

The importance to enhance the capabilities and performance of HSPA-based radio networks is widely recognised. HSPA networks form an integral part of 3G systems and must provide a smooth path towards LTE. HSPA operators are just as interested in the potential performance and cost savings which may be achieved through HSPA evolution in a 5MHz bandwidth as they are in the future LTE system.

Guiding principles considered:

- HSPA spectrum efficiency, peak data rate and latency should continue to evolve. The tradeoffs necessary to achieve performance comparable to LTE in 5 MHz should be analyzed;

- The interworking between HSPA Evolution and LTE should be as smooth as possible from one technology to the next and should facilitate joint technology operation;

- Evolved HSPA should be able to operate as a packet-only network based on utilization of Shared Channels only;

- HSPA Evolution shall be backward compatible in the sense that legacy terminals (R99-DCH and HSPA mobiles) are able to share the same carrier with terminals implementing the latest features of the HSPA Evolution track without any performance degradation;

- Ideally, existing infrastructure should only need a simple upgrade to support the features defined as part of the HSPA Evolution.

A number of Work Items listed in section 15 are already open to define potential enhancements to the HSPA standard and these need to be taken into consideration.

Objectives of the study:

a)	Define a broad framework for HSPA Evolution

b)	Define a set of requirements for HSPA Evolution covering:

- Targets for improvements in latency, throughput and spectrum efficiency utilising the existing 5MHz bandwidth

- Define constraints in terms of acceptable hardware and software changes to current elements {UE, Node, RNC, SGSN and GGSN};

- Define constraints in terms of acceptable network architecture changes.

c)	Determine what performance benefit is achieved by the existing WIs

d)  HSPA Evolution shall be backward compatible in the sense that legacy terminals (R99-DCH and HSPA mobiles) are able to share the same carrier with terminals implementing the latest features of the HSPA Evolution track without any performance degradation;

e)	Identify potential solutions to improve HSPA performance towards the agreed targets within the defined constraints;

f)	Make recommendations for future and possible revisions of ongoing WIs related to HSPA;

Results:

- Defined a broad framework for HSPA evolution

- Identified potential solutions to improve HSPA performance towards the agreed targets within the defined constraints;

RAN#37 (Sep 2007) completed. Status Report in RP-070533

## 10.27	Study on Dynamically reconfiguring a FDD UE receiver to reduce power consumption when desired Quality of Service is met  UID_330013

Responsibility:	R4

References

| Document | Title/Contents |
| --- | --- |
| WID(s) |
| RP-060641 | WID on Dynamically reconfiguring a FDD UE receiver to reduce power consumption when desired Quality of Service is met |
| Impacted Specifications |
| - | - |
| New Dedicated Specifications/Reports |
| TR 25.906 | Dynamically reconfiguring a Frequency Division Duplex (FDD) User Equipment (UE) receiver to reduce power consumption when desired Quality of Service (QoS) is met |

In certain conditions, it may be desirable to allow UEs supporting enhanced performance requirements to reduce their performance to TS25.101 minimum performance requirements, for example to reduce receiver power consumption. The purpose of this study item is to investigate how and whether it is this kind of performance reductions could be done in a controlled way, so that the overall UTRAN system benefits of enhanced receiver performance requirements are not lost.

The objectives of this study item are:

a) RAN4 to identify whether there are situations in which individual UE receiver performance reduction has no, or minimal impact to the overall UTRAN system level performance or user experience. RAN4 should also identify scenarios in which UE receiver performance reduction cannot safely be performed.

b) RAN4 to investigate scenarios for the identified situations where the UE could reduce its performance. The purpose of these scenarios is to ensure that UE performance is not degraded when conditions are not suitable.

c) RAN2 to investigate additional signalling which may be beneficial to support UEs in the decision making process for reducing their performance, for example quality thresholds which assist the UE in determining that conditions are suitable to reduce receiver performance.

Conclusion:

Under certain reception conditions benefits could be achieved with negligible impact on system level performance in non-MBMS scenarios. However, procedures related to receiver reconfiguration for non-MBMS channels should not be specified in 3GPP.

RAN#37 (Sep 2007) completed. Status Report in RP-070534

## 10.28	Study on GAN Enhancements (EGAN)  UID_50120

Responsibility:	GP

References

| Document | Title/Contents |
| --- | --- |
| WID(s) |
| GP-062298 | WID on GAN Enhancements |
| Impacted Specifications |
| New Dedicated Specifications/Reports |
| TR 43.902 | Enhanced Generic Access Networks Study (EGAN) |

While 3GPP completed GAN specifications in April 2005 and first commercial deployments have emerged (end 2006), a need for enhancements has been identified by LS from SA1 in terms of architectural and performance in order to:

- Offer both full services for 2G and 3G subscribers

- Offer seamless handovers with full service continuity between 2G/3G networks and GAN

- Reduce protocol overhead and latency for PS services, etc.

- Reduce the cost of delivery of packet data services to enable profitable launches of new high volume data services.

TR 43.902 evaluates enhancement topics for GAN architecture and performance, and recommends the specification of GAN Iu mode in Release 8.

## 10.29	Study on Future GERAN Evolution (FGE)  UID_50568

Main Responsibility:	GP

References

| Document | Title/Contents |
| --- | --- |
| WID(s) |
| GP-051052 | WID on Future GERAN Evolution |
| Impacted Specifications |
|  | - |
| New Dedicated Specifications/Reports |
| TR 45.912 | Feasibility study for evolved GSM/EDGE Radio Access Network (GERAN) |

TR 45.912 studied the means for GERAN to:

- Increase spectral efficiency;

- Increase capacity and coverage;

- Increase average data rates;

- Reduce latency between a mobile station and the GERAN;

- Enhance service continuity with other RAT.

This study resulted in independent GERAN features.

GERAN is a result of over a decade of radio interface evolution that is still ongoing. While GERAN is being deployed worldwide also in emerging markets, evolving further the GERAN radio interface needs to be studied to ensure not only that the same services are available regardless of the underlying radio technology UTRAN or GERAN, but essentially that service continuity exists across these radio technologies supported by core network evolution e.g. IMS. 
Such an evolution is also needed to maintain GERAN competitiveness as well as UTRAN competitiveness.

In order to leverage the investments made in GERAN infrastructure, it was felt a priority to minimize the impacts on it.

Some examples of services that were considered are given below.

- Interactive and Best-effort services (like web browsing, file download and image or video clip upload) typically gain from increased mean bit rates, but also gain from reduced latency, e.g. throughput is limited by the TCP window size divided by the round trip time.

- Conversational services like Voice over IP (VoIP) and enhanced Push-to-talk over Cellular (PoC), as well as, e.g. on-line gaming services typically have high requirements on latency and fast access.

- All services may gain from improved coverage, e.g. video-telephony is a service that needs (better) coverage for higher bit rates for both uplink and downlink.

- All services may gain from a Mobile Station (MS) always being connected to the most appropriate Base Station, i.e. as seen from a radio performance perspective, as this may yield higher capacity, reduce latency, etc. due to improved interference conditions.

- Particular requirements may be set by services like broadcast TV over MBMS bearers. Typically, high bit rates are required at the same time as robustness is important to fulfil coverage and latency requirements as well as providing interactivity.

A GSM/EDGE network may interoperate with WCDMA RAT, either within an operator's network or with different operators. There are also stand-alone GSM/EDGE networks. Both the GSM/WCDMA networks and the GSM only networks may benefit from the increased GSM/EDGE service portfolio. A combined WCDMA & GSM/EDGE network may benefit from better service continuity between the accesses resulting in an easier resource utilization and service provisioning. GSM/EDGE only networks can give their users an increased range of end-user services/applications and possibly make use of applications/services that do not require adaptations to access specific capabilities. This could potentially lead to reduce cost of provisioning and create a wider use of services.

As a general guideline, the performance requirements and design constraints that the proposed features/candidates should take into account are provided by this study. Taking those into consideration would enable easy network evolution and be able to efficiently use existing network equipment and support legacy Mobile Stations.

Each new candidate feature was requested to describe the compliance to the following relevant assumptions and pre-requisites. If non-compliant the reasons and consequences had to be detailed.

TR 45.912 conclusions and recommendations for Downlink:

Mobile Station Receive Diversity (MSRD) is a downlink feature, which improves the receiver performance of the MS by means of an additional antenna. The introduction of Single Antenna Interference Cancellation (SAIC) characterised by the Downlink Advanced Receiver Performance (DARP) requirements has already shown that receiver enhancements in the MS can provide significant gains in terms of spectral efficiency. MS receive diversity offers the possibility of enhanced channel diversity and the potential for further improved interference cancellation performance for GMSK modulated signals. Also, as opposed to SAIC, receive diversity enables significant gains for 8PSK-modulated signals. 
It has been noted that MSRD has significant impact on the MS hardware, and may impact both terminal power consumption and size.

Simulations and literature surveys have shown that considerable gains are achievable for both 8-PSK and GMSK modulated signals, although it is recognized that factors such as antenna performance and terminal design may impact the performance in a live network. To study the performance in more detail a simple channel model was derived, which includes antenna correlation and gain imbalance between the receiver antennas.

The impact of these parameters using the MSRD channel models has been assessed as well as a small literature survey of publications related to the achievable performance MS receive diversity has been provided. Several contributions have shown the impact in terms of receiver performance for different architectures and in general it seems that the diversity receivers are relatively insensitive to parameter variations. That is, large gains are achieved even for high values of correlation and antenna gain imbalance. Link- and system level simulations have been provided for speech services (AMR) and data services (EGPRS).

Based on the results, GERAN#27 has approved a work item on MSRD characterised by DARP Phase II.

Multi-carrier is a performance-enhancing feature whereby data to a single user can be transmitted on multiple carriers. The feature is aimed at enabling higher data rates in GERAN with minimal impacts to infrastructure. Currently, the theoretical peak data rate of EGPRS is 473.6 kbps for a single user. In a real network, average bit rates in the order of 100 kbps to 200 kbps are feasible on four timeslots. With multi-carrier, both peak and average user throughput are increased proportionally to the number of carriers. With a dual-carrier configuration, the peak data rate would be close to 1 Mbps. With this feature, peak and average bit rates can be increased in a very flexible and backwards-compatible manner.

Given the current technical and implementation limitations, it is considered acceptable in an initial phase to restrict the number of carriers to two. The need for higher bit rates could make it desirable to support more than two carriers in future releases of the GERAN standards.

Dual Carrier in the Downlink has been shown to meet some of the performance objectives of GERAN Evolution (in particular it enables an increase in the peak downlink data rate) without impairing any of the other performance metrics. Also, it satisfies all the compatibility objectives for candidate features; in particular, it is expected that it will have no impact on BSS hardware, given that there are no changes to the modulation and to the coding schemes. It is also anticipated that implementation in the MS is feasible.

Dual Carrier in the Downlink can optionally be combined with MS Receive Diversity. Provided that the MS supports this capability, it could be possible for a dual antenna terminal to switch between dual carrier reception and MS receive diversity.

Based on the results of this study, GERAN has approved a work item on Dual Carrier in the Downlink.

Higher Order Modulation and Turbo Codes: the impact of introducing higher order modulation based on QAM and Turbo coding in EGPRS has been analyzed. Simulations to evaluate link performance have taken reasonable practical impairments in the receiver and transmit implementations into consideration.

Based on the results of this study, GERAN has approved a work item on REduced symbol Duration, Higher Order modulation and Turbo coding (REDHOT) for downlink (see work item UID_50121).

Dual symbol rate and modified dual symbol rate: this study proposed two alternative uplink concepts: Dual Symbol Rate (DSR) and Modified Dual Symbol Rate (MDSR) for future GERAN evolution to double bitrates in uplink. 
DSR doubles the modulation rate in the transmitter of the MS and MDSR combines higher symbol rate (3/2) with 16QAM and optionally with QPSK. Both options offer about similar bit rates and performance in uplink e.g. 1.8 to 1.9 times higher average bit rates at coverage and 1.7 to 1.9 times higher bit rates at interference limited scenarios.

The main benefit of MDSR is the narrower signal bandwidth of two 200 kHz GSM channels instead of three in the case of DSR. This could simplify dual transceiver implementation compared to DSR e.g. narrower channel filter may be applied and oscillators are not needed to tune out of 200 kHz channel raster.

It was found earlier that DSR and MDSR with 2.0 and 1.5 times higher symbol rates clearly exceed the given performance objectives on coverage and spectral efficiency but that two legacy TRX implementation option was not favoured. Optimization of MDSR concept for single legacy TRX implementation may be done by removing the 100 kHz offset and reducing the symbol rate further e.g. to 1.2 (6/5) or 1.33 (4/3) times higher than the legacy symbol rate, to produce High Symbol Rate schemes (HSR). To meet peak throughput objectives, e.g. 32QAM modulation would then be needed.

The BTS receiver needs to cope with wider transmission bandwidth and could beneficially utilise the gain of interference rejection combining (IRC) for reception of dual symbol rate. The receiver complexity for DSR is about up to 50% more complex per bit than for 8PSK. The dual symbol rate applies to normal GSM frequency planning for all re-uses up to 1/1. Evolution in uplink bit rates is needed to support uploading of images or video from camera phones and also to maintain a balance in bit rates and in coverage with downlink enhancements e.g. with dual carrier.

Latency enhancements: four different enhancements were evaluated:

- Improved ACK/NACK reporting;

- Reduced Transmission Time Interval (TTI);

- Variable sized Radio Blocks;

- Hybrid ARQ.

The enhancements reduce overall latency and have a second order effect on mean/average and peak bit rates as reduced latency (i.e. lowering the round trip time) may provide better throughput if the bit rate on the link becomes so high that the maximum buffer window size limits the transmission rate.

The improved ACK/NACK reporting and hybrid ARQ mainly provide reduced latency in non-ideal radio conditions, as the number of re-transmissions is almost zero in ideal conditions. The reduced TTI and Variable sized radio blocks takes effect in both non-ideal radio conditions and ideal radio conditions.

Based on the results of this study, GERAN has approved a work item on LATency REDuction (LATRED) UID_50582.

Other aspects in TR 45.912 are: New burst structures and new slot formats, Adaptation between MS receiver diversity and dual-carrier, Enhancements to resource allocation, Modified MBMS Service, Uplink throughput enhancements with low standard impact.

Based on the results of this study, GERAN has approved a work item on Higher Uplink performance for GERAN Evolution (HUGE) UID_50584.

# 11	Deleted items

| Unique_ID | Name | Outline | WG | Acronym | Impacted Spec | WID |
| --- | --- | --- | --- | --- | --- | --- |
| 732028 | deleted - covered by UID33027 - IMS security extensions | 1 | S3 | IMS-SE |  | SP-050395 |
| 32029 | Deleted: FS on applicability of GALILEO for LCS | 1 | S2 | Galileo |  | SP-020541 |
| 32058 | Deleted - TR on Stage 2 | 2 | S2 |  |  |  |
| 50095 | deleted - GERAN review of the TR | 2 | GP |  |  |  |
| 32005 | Deleted - IMS Local services | 1 | S2 | IMSLocal | 23.228 |  |
| 32019 | Deleted - Stage 2 | 2 | S2 |  |  |  |
| 11035 | Delete - Stage 3 for IMS Local services | 2 | C1 |  |  |  |
| 32078 | Deleted - IMS Phase 3 | 1 | S2 |  |  |  |
| 701216 | Deleted - Improvements of Radio Interface | 1 | RP | RInImp |  | RAN_Work_Items |
| 14018 | Deleted: Generic User Profile Phase 2 | 1 | C4 |  |  |  |
| 42003 | Deleted - Stage 3 - Common objects | 2 | C4 |  | 24.241 | TP-020275 |
| 31087 | Delete was duplicated- Study of Customised Alerting Tone (CAT) Requirements | 1 | S1 | CAT |  | SP-050607 |
| 31086 | Delete - was duplicated - Facilitating Machine to Machine Communication in GSM and UMTS (M2M) | 1 | S1 | M2M | 22.868 | SP-050527 |
| 50552 | Deleted - FS of enhanced support of Video Telephony | 1 | GP | VIDGER |  | GP-042221 |
| 32113 | Deleted - PS domain and IMS support for IMS Emergency sessions | 1 | S2 | IMS-EMER | 23.867, TS 23.abc, 23.060, 23.002, 23.271 | SP-050604 |
| 32114 | Deleted - IMS aspects to support IMS Emergency sessions | 2 | S2 |  | 23.867, TS 23.abc, 23.060, 23.002, 23.271 | SP-050604 |
| 32115 | Deleted - PS domain aspects to support IMS Emergency sessions | 2 | S2 |  | 23.867, TS 23.abc, 23.060, 23.002, 23.271 | SP-050604 |
| 31077 | Deleted - Covered by SI - Personal Network (PN) and Personal Area Network (PAN) | 1 | S1 | PNPAN |  | SP-050386 |
| 31078 | Deleted - Covered by SI - Multimedia Telephony Capabilities for IMS | 1 | S1 | MITE |  | SP-050387 |
| 31079 | Deleted - Covered by SI - Transferring of emergency Call data | 1 | S1 | eCALL |  | SP-050388 |
| 31080 | Deleted - Covered by SI - MBMS Enhancements | 1 | S1 | MBMSE |  | SP-050389 |

Moved to Rel-8:

SI on AS-MRFC media server control protocol

FS on Transferring of emergency call data – in-band modem solution

Annex A:
Change history

| Change history |
| --- |
| Date | TSG # | TSG Doc. | CR | Rev | Subject/Comment | Old | New |
| 2008-04 | -- | -- | -- | -- | MCC coordination handover from Alain Sultan to Adrian Zoicas |  | 0.0.1 |
| 2008-05 | -- | -- | -- | -- | Inclusion of leftover material | 0.6.0 | 0.7.0 |
| 2008-06 | -- | -- | -- | -- | Skeleton despatched to MCC for input by 14 July 2008 | 0.8.0 | 0.8.1 |

# Footnotes

Open Platform

An Open Platform is a computing platform with an architectues that allows users to upgrade their hardware and/or update the software running on that platform.  This open architecture makes the platform vulnerable to an increasingly-sophisticated number of hardware and software attacks on the platform.