## Slide 1: On bandwidth parts and “RF” requirements
3GPP TSG RAN1 NR Ad-Hoc#2
Qingdao, P.R. China June 27th – 30th, 2017
Agenda Item: 5.1.7
R1-1711795
Ericsson

## Slide 2: Bandwidth parts – Usage scenarios
Usage scenario #1: Supporting reduced UE BW capability
Usage scenario #2: Supporting reduced UE energy consumption by means of bandwidth adaptation
Usage scenario #3: Supporting FDM of different numerologies
Usage scenario #4: Supporting non-contiguous spectrum
Usage scenario #5: Supporting forward compatibility
….

## Slide 3: Usage scenario #1
No specific requirements on UE reception/transmission outside of active BWP
  Network should not assume that UE can receive/transmit anything outside of active BWP
  No need for additional UE suppression of received/transmitted signals outside of active BWP (but within the overall carrier)
Supporting reduced UE BW capability
BWP
Overall carrier

## Slide 4: Usage scenario #2
Supporting reduced UE energy consumption by mean of bandwidth adaptation
BWP2
Overall carrier
BWP1
Same as scenario #1
  Network should not assume that UE can receive/transmit anything outside of active BWP(s)
  No need for additional UE suppression of received/transmitted signals outside of active BWP (but within the overall carrier)

## Slide 5: Usage scenario #3
Potentially additional suppression of received/transmitted signals outside of active BWP(s)
  To reduce intra-carrier guardbands between numerologies
  RAN4 decision (“spectrum confinement on a subband basis”)
  Relaxed requirements compared to suppression of out-of-carrier signals
Supporting FDM of different numerologies
BWP1 (numerology 1)
Overall carrier
BWP2 (numerology 2)

## Slide 6: Usage scenario #4
Similar requirements on suppression of received/transmitted signals outside of active BWP as out-of-carrier suppression
Supporting non-contiguous spectrum
BWP1
Overall carrier
BWP2
Something completely unknown

## Slide 7: Usage scenario #5
Supporting forward compatibility
Need for additional suppression of received/transmitted signals outside of active BWP
  Probably more relaxed requirements compared to suppression of out-of-carrier signals
Overall carrier
BWP
Something new and not yet defined
?

## Slide 8: Question
What is assumed regarding suppression of UE reception/transmission outside of an active bandwidth part?
Alternative 1:
  No additional suppression beyond “normal” UE suppression of transmission/reception in unassigned resource elements?
Alternative 2:
  Additional suppression up to the level of UE suppression of out-of-carrier transmission/reception?
Alternative 3: A combination of these
  Sometimes associated suppression requirements, sometimes not
  Essentially leading to two different bandwidth-part concepts

## Slide 9: Summary
The different usage scenarios implies different characteristics for the bandwidth parts, for example in terms of suppression of transmission/reception of signals outside of an active bandwidth part
If all these usage scenarios are to be handled by the same concept of bandwidth part it is essential that these differences are fully understood and taking care of
  Otherwise 3GPP may end up with a solution that does not support all the relevant usage scenarios or is unnecessarily (and unacceptably) complex for certain usage scenarios
Alternatively 3GPP limits the concept of bandwidth parts to a subset of these usage scenarios and address the other scenarios with other tools