## Slide 1: Way forward on power headroom reporting for NB-IOT
Ericsson, Nokia, Intel,
3GPP TSG-RAN WG4 Meeting #79AH
Hong Kong, China 28-30 June, 2016
R4-79AH-0260

## Slide 2: Background
According to RAN1 agreements, the NB-PHR is reported in Msg3 of random access procedure using 2 bits for the lowest configured NB-PRACH repetition level. This means that only 4 different values can be reported.

## Slide 3: Agreements on PHR: 1
PHR estimation interval is FFS.
Two PHR report mapping tables are specified. UE will use one of the 2 tables for transmitting PHR. The selection is based on UE coverage level:
  One table (Table#1) is associated with PRACH CE level # 0
  Second table (Table#2) is associated with other PRACH CE levels (i.e. #1 and #2)
  Resolution in table 1 and table 2 are different
Note: Table # 3 associated with CE level 2 is not precluded if second NRSRP threshold is configured

## Slide 4: Agreements on PHR: 2
Mapping based on subcarrier spacing:
  Baseline assumption: same set of table 1 and table 2 are applicable for 3.75 KHz and 15 KHz
  It is FFS if separate set of table 1 and table 2 are required for 3.75 KHz and for 15 KHz