3GPP TSG-SA WG3 Meeting #94Ad-Hoc	S3-190945

Stockholm (Sweden), 11-15 March 2019	revision of S3-190826

# Source:	Ericsson

# Title:	KI#3 in TR 33.809 – updates to requirements

# Document for:	Approval

Agenda Item:	5.9

# 1	Decision/action requested

It is requested that proposed changes are approved.

# 2	References

[1]	N/A

# 3	Rationale

The present pCR proposes following changes to the requirements clause of Key Issue #3 in TR 33.809 for the reasons mentioned below.

- There was an artificial restriction that base station does the detection. In reality, vendors may have the detection logic in the core. Correction has been done.

- There was also another artificial restriction that "nearby" false base stations are detected. In reality, vendors may detect even "far away" false base stations. Correction has been done.

# 4	Detailed proposal

*** BEGIN CHANGES ***

### 5.3.3	Potential security requirements

5G system should be able to detect false base stations.

5G system should be able to employ methods to prevent UEs from connecting to false base stations.

*** END OF CHANGES ***