3GPP TR 33.819 V0.3.0 (2019-03)

Technical Report

3rd Generation Partnership Project;

Technical Specification Group Services and System Aspects;

Study on security for 5GS enhanced support of Vertical and LAN Services;

(Release 16)

The present document has been developed within the 3rd Generation Partnership Project (3GPP TM) and may be further elaborated for the purposes of 3GPP.
The present document has not been subject to any approval process by the 3GPP Organizational Partners and shall not be implemented.
This Report is provided for future development work within 3GPP only. The Organizational Partners accept no liability for any use of this Specification.
Specifications and Reports for implementation of the 3GPP TM system should be obtained via the 3GPP Organizational Partners' Publications Offices.

Keywords

<keyword[, keyword]>

3GPP

Postal address

3GPP support office address

650 Route des Lucioles - Sophia Antipolis

Valbonne - FRANCE

Tel.: +33 4 92 94 42 00 Fax: +33 4 93 65 47 16

Internet

http://www.3gpp.org

Copyright Notification

No part may be reproduced except as authorized by written permission.
The copyright and the foregoing restriction extend to reproduction in all media.

© 2018, 3GPP Organizational Partners (ARIB, ATIS, CCSA, ETSI, TSDSI, TTA, TTC).

All rights reserved.

UMTS™ is a Trade Mark of ETSI registered for the benefit of its members

3GPP™ is a Trade Mark of ETSI registered for the benefit of its Members and of the 3GPP Organizational Partners
LTE™ is a Trade Mark of ETSI registered for the benefit of its Members and of the 3GPP Organizational Partners

GSM® and the GSM logo are registered and owned by the GSM Association

Contents

Foreword	5

Introduction	5

1	Scope	6

2	References	6

3	Definitions, symbols and abbreviations	6

3.1	Definitions	6

3.2	Abbreviations	7

4	Security aspects in the 5G System to enable enhanced support of Vertical and LAN Services	7

5	Key issues	7

5.1	Key Issues related to security for standalone Non-Public Networks	7

5.1.1	Key Issue #1.1: Calculating KSEAF for standalone non-public networks	7

5.1.1.1	Key issue details	7

5.1.1.2	Security threats	7

5.1.1.3	Potential security requirements	7

5.2	Key Issues related to Security aspects on interworking between NPN and PLMN	8

5.2.1	Key Issue #2.1: Authentication and Authorization for Interworking, Roaming between NPN and PLMN	8

5.2.1.1	Key issue details	8

5.2.1.2	Security threats	8

5.2.1.3	Potential security requirements	8

5.2.2	Key Issue #2.2: Security and privacy aspects of service continuity and session continuity	9

5.2.2.1	Key issue details	9

5.2.2.2	Security threats	10

5.2.2.3	Potential security requirements	10

5.2.3	Key Issue #2.3: Independent credentials for authentication and authorization with NPN and PLMN	10

5.2.3.1	Key issue details	10

5.2.3.2	Security threats	10

5.2.3.3	Potential security requirements	10

5.3	Key Issues related to Security for 5G LAN services	11

5.3.1	Key Issue #3.1: Authentication and Authorization of UE in 5GLAN communication	11

5.3.1.1	Key issue details	11

5.3.1.2	Security threats	11

5.3.1.3	Potential security requirements	11

5.3.2	Key Issue #3.2: UP security policy for the 5GLAN Group	11

5.3.2.1	Key issue details	11

5.3.2.2	Security threats	11

5.3.2.3	Potential security requirements	12

5.4	Key Issues related to Security for TSN and 5GS interaction	12

5.4.1	Key Issue #4.1: Protection of interfaces that 5GS interact with TSN	12

5.4.1.1	Key issue details	12

5.4.1.2	Security threats	12

5.3.1.3	Potential security requirements	12

5.5	Key Issues related to authentication on Non-Public Networks	12

5.5.1	Key Issue #5.1: Key hierarchy for non-public networks	12

5.5.1.1	Key issue details	12

5.5.1.2	Security threats	12

5.5.1.3	Potential security requirements	12

6	Solutions	13

6.1	Solution #1: Solution for NPN network access via PLMN	13

6.1.1	Introduction	13

6.1.2	Solution details	13

6.1.2.1 	Registration to NPN via PLMN	13

6.1.2.2 	Registration to PLMN via NPN	14

6.1.3	Evaluation	14

6.2	Solution #2: Security solution for handling UP security policy for a 5GLAN Group	14

6.2.1	Introduction	14

6.2.2	Solution details	15

6.2.3	Evaluation	16

Annex <X>: Change history	17

# Foreword

This Technical Report has been produced by the 3rd Generation Partnership Project (3GPP).

The contents of the present document are subject to continuing work within the TSG and may change following formal TSG approval. Should the TSG modify the contents of the present document, it will be re-released by the TSG with an identifying change of release date and an increase in version number as follows:

Version x.y.z

where:

x	the first digit:

1	presented to TSG for information;

2	presented to TSG for approval;

3	or greater indicates TSG approved document under change control.

y	the second digit is incremented for all changes of substance, i.e. technical enhancements, corrections, updates, etc.

z	the third digit is incremented when editorial only changes have been incorporated in the document.

# Introduction

Editor’s Note: This clause contains some background information for the study.

# 1	Scope

The present document studies security enhancements to 5GS that are required to fulfil Stage-1 service requirements in vertical domains defined in TS 22.261 [1] and TS 22.104 [2] and addresses the solutions described by TR 23.734 [3] and TR 23.725 [4] studies.

Potential security requirements are provided and possible security architecture enhancements to 5GS in vertical domains are proposed that support these security requirements.

# 2	References

The following documents contain provisions which, through reference in this text, constitute provisions of the present document.

-	References are either specific (identified by date of publication, edition number, version number, etc.) or non-specific.

-	For a specific reference, subsequent revisions do not apply.

-	For a non-specific reference, the latest version applies. In the case of a reference to a 3GPP document (including a GSM document), a non-specific reference implicitly refers to the latest version of that document in the same Release as the present document.

[0]	3GPP TR 21.905: "Vocabulary for 3GPP Specifications".

[1]	3GPP TS 22.261: "Service requirements for next generation new services and markets".

[2]	3GPP TS 22.104: "Service requirements for cyber-physical control applications in vertical domains".

[3]	3GPP TR 23.734: "Study on enhancement of 5GS for Vertical and LAN Services".

[4]		3GPP TR 23.725: "Study on enhancement of Ultra-Reliable Low-Latency Communication (URLLC) support in the 5G Core network (5GC)".

[5]	3GPP TS 33.501: "Security architecture and procedures for 5G system".

[6]		3GPP TS 23.502: "Procedures for the 5G System".

[7]	3GPP TS 23.501: "System architecture for the 5G System (5GS) ".

[8]	3GPP TR 23.740: "Study on Enhancement of Network Slicing".

# 3	Definitions, symbols and abbreviations

Delete from the above heading those words which are not applicable.

Clause numbering depends on applicability and should be renumbered accordingly.

## 3.1	Definitions

For the purposes of the present document, the terms and definitions given in 3GPP TR 21.905 [0] and the following apply. A term defined in the present document takes precedence over the definition of the same term, if any, in 3GPP TR 21.905 [0].

Service Continuity: Uninterrupted user experience of a service, including the cases where the IP address and/or anchoring point change (as defined in 3GPP TS 23.501 [7]).

Session Continuity: Continuity of a PDU Session (as defined in 3GPP TS 23.501 [7]).

NOTE: For PDU Session of IPv4 or IPv6 or IPv4v6 type "session continuity" implies that the IP address is preserved for the lifetime of the PDU Session.

## 3.2	Abbreviations

For the purposes of the present document, the abbreviations given in 3GPP TR 21.905 [0] and the following apply. An abbreviation defined in the present document takes precedence over the definition of the same abbreviation, if any, in 3GPP TR 21.905 [0].

Abbreviation format (EW)

<ACRONYM>	<Explanation>

# 4	Security aspects in the 5G System to enable enhanced support of Vertical and LAN Services

Editor’s Note: This clause contains a high-level overview of the Vertical and LAN Services features, the security aspects and the potential impacts on the current Rel-15 security mechanisms.

# 5	Key issues

Editor’s Note: This clause contains all the key issues identified during the study.

## 5.1	Key Issues related to security for standalone Non-Public Networks

### 5.1.1	Key Issue #1.1: Completing AKA based authentication and calculating KSEAF for standalone non-public networks

#### 5.1.1.1	Key issue details

Binding the key to the serving network identity is a requirement for 5G security [1]. For standalone non-public networks, the network identity used (see solution #1 in TR 23.734 [3]) is changed and may not even contain a complete PLMN ID. Hence the standard needs to clearly define the input parameters used to calculate KSEAF as well as KAUSF, RES* and XRES* for 5G AKA and IK’ and CK’ for EAP-AKA' in both the network and UE. Without such a clear definition the security set-up will fail.

When introducing standalone non-public networks, it should also be ensured that the standalone non-public network cannot masquerade as a public network, i.e., the keys derived for a public network and standalone non-public network are different.

#### 5.1.1.2	Security threats

If using the same credentials for more than one network, the UE may be connected to a different standalone public network than the one it tried to connect to.

The UE may be connected to a standalone non-public network when it tried to connect to a public network.

#### 5.1.1.3	Potential security requirements

### The UE shall authenticate the serving standalone non-public network identifier.

#### 5.1.1.4	Potential architectural requirements

The system shall support well-defined key derivations to enable the establishment of security for standalone non-public networks.

### 5.1.2	Key Issue #1.2: (D)DoS attack in Non-standalone Non-Public Networks

#### 5.1.2.1	Key issue details

To enable non-public networks deployed as part of a PLMN, SA2 has concluded (in TR 23.734 [3]) Solution #2 (Closed Access Group) as the basis for normative work, to address the Key Issues (key Issue #1: Network discovery, selection and access control for non-public networks and Key Issue #2: Network Identification for non-public networks in TR 23.734 [3]).

SA2 endorsed [S2-1901391] that Non-standalone Non-Public Networks are Non-Public Networks (NPNs) which are deployed with the support of public PLMNs using Closed Access Group (CAG) and/or network slicing. When an NPN is made available via a PLMN, then the UE has a subscription for the PLMN to access the network and obtain the services provided by the network. A CAG identifies a group of subscribers who are permitted to access one or more CAG cells. When an UE accesses a CAG cell, the network need to verify whether the UE is allowed to access the CAG cell. For state transition and during mobility, it is endorsed that "The AMF shall verify whether the CAG identifier received from NG-RAN is part of the UE’s Allowed CAG list as received from the UDM".

However, for the network to verify a UE’s access to CAG cell, network needs to know the UE’s SUPI. As per TS 33.501 [5], during initial NAS procedure (Registration Procedure), UE sends the Subscription concealed identifier (SUCI) to the network. The serving network receives the UE’s SUPI from the AUSF, only after successful primary authentication. Therefore, if the serving network needs to perform the access control on the UE during initial Registration procedure, then AMF will have to wait until completion of successful primary authentication procedure.

It is likely that, large number of malicious UEs, with or without valid subscription, performing Registration procedures, to access the network via CAG cells. In this scenario, if these malicious UEs are not allowed to access the CAG cell, then there is an overhead (signalling and also computational) on the network and especially in the UDM, AMF and gNB, as the network needs to de-conceal the SUCI and performs authentication procedure and then checks whether the UEs are allowed to access the CAG cell. If such attempts are done on a particular CAG cell or distributed at different CAG cells, then it leads to (Distributed) Denial of Service ((D)DoS) attack on the 5G system.

This key issue needs to be investigated, to minimize the (D)Dos attack on the Non-Stand-alone NPNs.

#### 5.1.2.2	Security threats

The Non-standalone Non-Public Networks should provide a mechanism for verification of UE’s access to CAG cell. When a large number of malicious UEs, which are not allowed to access a CAG cell, perform Registration procedures with the network, then there is an overhead on the network, to perform primary authentication and then do CAG cell access check. Such attempts, when done on a particular cell or distributed at different cells, leads to (Distributed) Denial of Service ((D)DoS) attack on the 5G system. Signalling attack on the core network (like UDM, to generate AVs) has a bigger effect than the access network and will impact larger number of UEs.

This threat is also mentioned in the TS 22.261[1], clause 6.25.1.

#### 5.1.2.3	Potential security requirements

The 5G system should mitigate the (D)DoS attack on Non-standalone NPNs, resulting from large number of Registrations requests from UEs which are not allowed to access a CAG cell.

## 5.2	Key Issues related to Security aspects on interworking between NPN and PLMN

### 5.2.1	Key Issue #2.1: Authentication and Authorization for Interworking, Roaming between NPN and PLMN

#### 5.2.1.1	Key issue details

There is a need for 5GS to support non-public operations for an enterprise using Non Public Networks (NPN) deployed in plants or factories. The envisioned deployment options for NPN are: standalone, hosted by a PLMN or a slice from a PLMN.

The purpose of this key issue is to identify specific issues for authentication and authorization when a UE needs to access and obtain services offered from a PLMN via a NPN and vice versa. Where a roaming agreement between a PLMN operator and an NPN operator allow, it need to be studied what security model could be adopted with authentication in both networks or authentication in only one of the networks, e.g. if a PLMN need to authenticate a UE for network access and to grant service over PLMN network.

In this key issue, a UE authentication with a PLMN (using credentials needed for PLMN) is called "PLMN Authentication" and with NPN (using credentials needed for NPN) is called "NPN Authentication".

This key issue assumes that:

-	Authentication methods, identities, credentials for PLMN access are 3GPP only.

-	NPN may or may not be considered trusted by PLMN.

-	PLMN is considered trusted by NPN.

- 	PLMN Authentication is mandatory to access PLMN offered services via NPN.

The security aspects of authentication and authorization for PLMN and NPN interworking and roaming (including simultaneous access) are as follows:

-	The UE identifier used for NPN Authentication.

- 	The NPN Authentication may use 3GPP or non 3GPP based credentials (e.g. using the EAP framework).

- 	When a UE is already authenticated/registered with the PLMN, an additional NPN authentication may or may not be performed to access and obtain NPN services via the PLMN.

#### 5.2.1.2	Security threats

Access of UEs to NPN offered services via PLMN unauthorized by NPN and/or PLMN.

Access of UEs to PLMN offered services via NPN unauthorized by NPN and/or PLMN.

5.2.1.3	Potential security requirements

FFS

### 5.2.2	Key Issue #2.2: Security and privacy aspects of service continuity and session continuity

#### 5.2.2.1	Key issue details

Background

Clause 3.1 of the present document contains definition of service continuity and session continuity, as specified in 3GPP TS 23.501 [7].

Service continuity and session continuity do not mean transfer of service and session from PLMN to NPN and vice-versa. The continuity is in the sense of transfer from native connective to tunnelled connection, and vice-versa. In other words, there is no "roaming" (in the same sense that we use across PLMNs) between PLMN and NPN.

3GPP TS 23.734 uses the term service continuity in its key issues and solutions. That is fine because support for service continuity would cater session continuity as well. Regarding the key issue #6, i.e., access to PLMN services via NPN and vice-versa, 3GPP TS 23.734 [3] has concluded that solution #20 is chosen as baseline for normative work. Further, it has also concluded (according to solution #21) that seamless service continuity between PLMN and NPN is achieved by dual radio support and there no protocol changes.

In short, the chosen solution #20 works in the following way - one network (PLMN or NPN) treats another network (NPN or PLMN) as a non-3GPP access and tunnels communication using another network's N3IWF. See Figure 5.2.2.1-1.

Figure 5.2.2.1-1: Baseline architecture for accessing PLMN via NPN (left) and NPN via PLMN (right)

Description

This key issue is about investigating security aspects of service and session continuity when accessing PLMN services via NPN and vice-versa. In other words, this key issue is for analysing IF and WHAT "new" security mechanisms would be required for the solution #20 in 3GPP TS 23.734 [3].

There are several aspects that are worth investigating for security and privacy impacts, e.g., because of:

-	Nwu interfaces (NwuPLMN and NwuNPN) between UEs and PLMN/NPN N3IWFs;

-	both the PLMN and the NPN having own security contexts for UEs even though a single radio is used;

-	UEs discovering one network's N3IWF via another network's radio;

-	UEs performing PDU Session(s) handover from NPN N3IWF to NPN 3GPP RAN, and PLMN 3GPP RAN to PLMN N3IWF;

-	UEs performing PDU Session(s) handover from PLMN N3IWF to PLMN 3GPP RAN, and NPN 3GPP RAN to NPN N3IWF;

-	etc.

#### 5.2.2.2	Security threats

FFS

#### 5.2.2.3	Potential security requirements

FFS

### 5.2.3	Key Issue #2.3: Independent credentials for authentication and authorization with NPN and PLMN

#### 5.2.3.1	Key issue details

As per TR 23.734 [3], the possible deployment options for Non-Public Networks are: standalone, hosted by a PLMN or a slice from a PLMN. For standalone deployment option, study concludes solution #20 ("Supporting service continuity between Public PLMN a non-public network via an N3IWF-like gateway") for key issue #6 related to service continuity ("Accessing PLMN service via non-public networks and vice versa").

This key issue is related to support of credentials, for authentication and authorization when a UE needs to access and obtain services offered from a PLMN via a NPN and vice versa.

As per the concluded solution in SA2 TR 23.734 [3], to access PLMN services via non-public network, UE obtains IP connectivity via the non-public network, discovers a N3IWF provided by PLMN, and establishes connectivity to the PLMN via the N3IWF.  Similar procedure to be followed by UE vice versa, to access non-public network services via PLMN. PLMN and non-public networks are different networks that UE will be connected to simultaneously.

For PLMN networks, 5G AKA and EAP-AKA' are supported authentication methods. For Non-public networks (Private networks) using 5G system, supported authentication methods are 5G AKA, EAP-AKA' and additional methods within EAP framework TS 33.501. UE and Non-public network need to be in possession of the security credentials corresponding to the authentication method (over EAP framework) used for primary authentication, based on the NPN operator policy.

#### 5.2.3.2	Security threats

The PLMN and Non-public networks should provide mutual authentication mechanism to ensure that the network services are provided only to the UEs with valid subscription. If same credential is shared for the PLMN network access and also for the NPN network(s) access, then compromise of the security credential at the UE or at any network entity, can lead to compromise of all other network, which shares the same credential.

#### 5.2.3.3	Potential security requirements

The 5G system should support subscription credentials for the NPN network access authentication and authorization that are independent of the credentials used to access the PLMN.

The system shall support (but not mandate) the use of independent subscription credentials for access to different NPN networks.

## 5.3	Key Issues related to Security for 5G LAN services

### 5.3.1	Key Issue #3.1: Authentication and Authorization of UE in 5GLAN communication

#### 5.3.1.1	Key issue details

TR 23.734, Clause 5.4.1 [3] describes a key issue #5: 5GLAN Group Management, which raises an issue on “how to authorize a UE for 5GLAN communication”. Also Figure 6.14.2-2 [3] depicts the procedure for 5GLAN group discovery and configuration through registration.

Therefore, this new key issue is proposed to provide necessary detailed security procedures in order to support authentication and authorization for 5GLAN group communication. If this issue is not addressed, it may lead any illegitimate UE to gain access to the 5GLAN type services without any authentication and authorization.

Editor Note’s: This key issue needs to be aligned after SA2 has concluded on this topic.

#### 5.3.1.2	Security threats

The 5GLAN services are different from the public network services, the system should provide a mutual authentication and authorization mechanism to ensure that these 5GLAN services will be provided to only the UE’s subscribed to the 5GLAN group. If the 5GLAN UE is not authenticated and authorized, then any illegitimate UE may get the 5GLAN-type services provided by 5GLAN group which were not subscribed to these services. It can also lead to risk of theft of service and Denial of Service against the 5GLAN group communication.

#### 5.3.1.3	Potential security requirements

Mutual authentication mechanism between 5GLAN UE and 5GLAN group shall be supported.

Authorization of 5GLAN UE’s for 5GLAN-type services in 5GLAN group shall be supported.

### 5.3.2	Key Issue #3.2: UP security policy for the 5GLAN Group

#### 5.3.2.1	Key issue details

This key issue addresses the security aspects of key issue #4.1: 5GLAN Group Management in TR 23.734 [3].

TR 23.734 [3] has recommended solution #29 "Unified architecture for 5G LAN-type service" for the normative work for 5GLAN group communication.

PDU sessions established by different UE’s belonging to one and the same 5GLAN group will be handled by the same SMF. The SMF is responsible for managing the PDU sessions belonging to the 5GLAN group, for example it includes the management of the total number of established and activated PDU Sessions.

During the PDU session establishment, the 5G Core Network shall determine and provide the UP security policy for a PDU session to the gNB connected to 5GC according to TS 23.501 [7] and TS 23.502 [6]. This key issue investigates whether there is a problem if the 5G Core Network enforce different configurations of UP security (encryption and integrity protection) in the UP security policy for multiple PDU sessions established with different UE’s belonging to one and the same 5GLAN Group.

#### 5.3.2.2	Security threats

If the user plane traffic sent between the UE and the gNB for one PDU session is using lower security then the other PDU sessions for the other UE’s belonging to the same 5GLAN group, then this would imply that the security for the weakest link applies to the whole 5GLAN group. In summary, the security properties of the group communication are determined by the security properties of the weakest communication path.

For example: if encryption is switched off between the UE and the gNB for one PDU session over one path, while all other communication paths between all other UE’s and RAN nodes within the same 5GLAN group are encrypted, then the effect is that all the information exchanged within the 5GLAN group will be eavesdropped. Or if the attacker knows that integrity protection is enabled on one path between the UE and the gNB but not on a second path between a second UE and a gNB, then the attacker could insert or modify user plane data for group communication within the 5GLAN group sent over the second path.

#### 5.3.2.3	Potential security requirements

The system shall support a single security user plane policy for a 5GLAN group.

## 5.4	Key Issues related to Security for TSN and 5GS interaction

### 5.4.1	Key Issue #4.1: Protection of interfaces that 5GS interact with TSN

#### 5.4.1.1	Key issue details

According to TR 23.734 [3], 5GS may integrate with Time Sensitive Networking (TSN). The 5GS may provide multiple interfaces to external services/networks that can be used for TSN integration, such as N5, N6, N33 and N60. The interfaces interact with TSN need to be properly protected.

#### 5.4.1.2	Security threats

In case the interfaces interact with TSN lack confidentiality, integrity and replay protection, it will be possible for an attacker to eavesdrop, modify data and replay packets.

#### 5.3.1.3	Potential security requirements

The interfaces interacting with TSN shall support confidentiality, integrity and replay protection.

## 5.5	Key Issues related to authentication on Non-Public Networks

### 5.5.1	Key Issue #5.1: Key hierarchy for non-public networks

#### 5.5.1.1	Key issue details

The current key hierarchy in TS 33.501 [5] assumes that an AKA method is used to authenticate the UE. This will not necessarily be true for non-public networks. In particular, non-AKA methods do not require the long-term key K to be stored in UE and network and derivation of KAUSF from an EAP-based authentication other than EAP-AKA' is not described.

#### 5.5.1.2	Security threats

With a lack of clarity on how general EAP based authentication methods (i.e. ones other than EAP-AKA') result in the creation of the 5G key hierarchy, it is possible that incompatible UE and network implementation may occur.

#### 5.5.1.3	Potential security requirements

From the above security threats, the following requirements can be drawn:

- The key hierarchy shall support EAP-based authentication methods other than EAP-AKA'.

NOTE 1: This requirement takes no stance on whether this support is described normatively or informatively.

NOTE 2: This requirement will not change the key hierarchy for primary authentication in public networks.

### 5.5.2	Key Issue #5.2: Authentication and authorization of NPN subscribers by an AAA

#### 5.5.2.1	Key issue details

Editor’s note: It is FFS whether the use-case described in this key issue is in the scope of NPN as per SA1 and SA2 agreed scenarios, requirements and architecture.

In the 5G System, the authentication credentials are stored and processed in the UDM/ARP as described in TS 33.501 [5]. For standalone NPNs, it is understood that it is recommended not to have any restriction on the credentials and the authentication methods. This is since the NPN operators might already have their own identity and credential management systems, typically legacy AAA infrastructures for authentication and authorization of the devices or the users.

Now in order to allow the use of any authentication credentials and methods, the common practise was to support an interaction with a AAA entity. This is for example what has been done for the Secondary Authentication where the SMF interacts with an external AAA entity in the DN. This is also what was adopted in the slicing enhancement study captured in TR 23.740 [8] and where it is assumed that the AUSF interacts with AAA entity for the slice specific authentication procedure.

Introducing such a feature in the 5G System for the Primary Authentication would have considerable impact on the UE. In fact, if the AUSF is to interact with AAA entity, and endorse an authenticator role instead of the server role in the EAP framework, then the key hierarchy needs to be revised for this use case so that the KAUSF is derived from the MSK instead of the EMSK key.

For that, the focus of this key issue is to whether it is possible and if yes how to allow such an interaction with AAA while preserving the current role of the AUSF and the UDM in the Primary Authentication framework as described in TS 33.501 [5].

#### 5.5.2.2	Security threats

FFS

#### 5.5.2.3	Potential security requirements

FFS

# 6	Solutions

Editor’s Note: This clause contains the proposed solutions addressing the identified key issues.

## 6.1	Solution #1: Solution for NPN network access via PLMN

### 6.1.1	Introduction

This solution addresses the security requirement for the Authentication and Authorization for Interworking between NPN and PLMN in key issue #2.

From the security point of view, three security requirements shall be specified for the access of UE to NPN via PLMN (and vice versa), i.e.

- Requirement 1: Authentication between UE and PLMN network while UE access to the PLMN network.

- Requirement 2: Authorization for the PLMN PDU session establishment to ensure that UE is authorized to access to NPN services.

- Requirement 3: Authentication between UE and NPN network via PLMN network.

If the Requirement 2 is specified by the secondary authentication in the PLMN network, two authentication procedures between UE and NPN will be introduced, i.e. one is used for PDU session establishment authorization, the other one is used for UE registration to NPN. Therefore, duplicate authentications between UE and NPN will consume the computation and communication resource between them.

This solution proposes a new procedure for the above security requirements and reuses the secondary authentication for the Authorization of the PLMN PDU session establishment. Meanwhile, protection between UE and NPN can be based on the output of secondary authentication.

Editor’s Note: The use of the secondary authentication requires more justification.

### 6.1.2	Solution details

#### 6.1.2.1 	Registration to NPN via PLMN

Figure 6.1.2.1-1 Registration to NPN via PLMN

The procedure assumes that the UE has separate credentials for the PLMN and the NPN.

1. The UE firstly registers into the PLMN network based on the PLMN credential.

2. The UE sends the PDU session establishment request to the AMF, to setup the PDU session for the services provided by the NPN.

The UE initiates the PDU session establishment procedure as in step 4 of Fig 11.1.2-1 in TS 33.501 [5].

The following steps 3a, 3b, 4 are the same as steps 5a-13 in clause 11.1.2 of TS 33.501 [5].

5. After the successful completion of the authentication procedure, NPN-AUSF shall send EAP Success message to the NPN-AMF, including the NPN SEAF key.

6. After receiving the EAP-success and NPN SEAF key from the NPN-AUSF, NPN-AMF generates the NPN AMF key, and NPN-GUTI for the UE, and sends EAP success, NPN-GUTI, NPN-ngKSI, and NPN-ABBA to the PLMN SMF via NPN-N3IWF and PLMN-UPF, where the NPN-ngKSI and NPN-ABBA are determined during the secondary authentication procedure.

7. The PLMN SMF sends a Namf_Communication_N1N2MessageTransfer to the AMF as in step 11 of Figure 4.3.2.2.1-1 in TS 23.502 [6]. This message shall include EAP success, NPN-GUTI, NPN-ngKSI, and NPN-ABBA to be sent to the UE within the NAS SM PDU Session Establishment Accept message.

If the authorization is successful, PDU Session Establishment proceeds further starting at step 9a of Figure 4.3.2.2.1-1 in TS 23.502 [6]. The SMF initiates a N4 Session Modification procedure with the selected UPF as in steps 9.a and 9.b of Fig 4.3.2.2.1-1 in TS 23.502 [6].

8. PLMN AMF forwards NAS SM PDU Session Establishment Accept message along with EAP Success, NPN-GUTI, NPN-ngKSI, and NPN-ABBA to the UE as described in steps 12 and step 13 of Figure 4.3.2.2.1-1 in TS 23.502 [6].

The UE-requested PDU Session Establishment proceeds further as described in sub-clause 4.3.2.3 in TS 23.502 [6].

9. The UE sends the registration request message to the NPN-AMF, including the NPN-GUTI, NPN-ngKSI, NPN-UE security capability.

10. Based on the received NPN-GUTI, NPN-ngKSI, and NPN-UE capability, NPN-AMF firstly determines the NPN-AMF key, then proceeds the NPN-NAS SMC procedure with UE.

The UE-requested registration procedure proceeds further as described in clause 4.2.2.2.2 in TS 23.502 [6].

#### 6.1.2.2 	Registration to PLMN via NPN

This procedure can refer to the clause 6.1.2.1.

### 6.1.3	Evaluation

Editor’s Note: Each solution should motivate how the potential security requirements of the key issues being addressed are fulfilled.

## 6.2	Solution #2: Security solution for handling UP security policy for a 5GLAN Group

### 6.2.1	Introduction

This solution addresses key issue #3.2: UP security policy for the 5GLAN group.

TR 23.734 [2] has recommended solution #29 "Unified architecture for 5G LAN-type service" for the normative work for 5GLAN group communication. In this solution a single SMF and a single PSA UPF is responsible for all the PDU Sessions for 5GLAN group communication within a single 5GLAN group. The same SMF is responsible for managing the PDU sessions belonging to the same 5GLAN group.​

According to TS 23.501 [7] and TS 23.502 [6], the SMF determines and provide the UP security policy for a PDU session to the gNB connected to 5GC during the PDU session establishment procedure.

The UP security policy indicates whether UP confidentiality and/or UP integrity protection are activated or not for all DRBs belonging to that PDU session. The gNB uses UP security policy to activate UP confidentiality and/or UP integrity for all DRBs belonging to the PDU session.

According to TS 23.501 [7], the User Plane Security Policy provides the same level of information as the User Plane Security Enforcement information. Once the User Plane Security Enforcement information is determined at the establishment of the PDU Session, it is provided to the NG-RAN and applies for the life time of the PDU Session. The User Plane Security Enforcement information provides the NG-RAN with User Plane security policies for a PDU session. It indicates:

-	whether UP integrity protection is:

-	Required: for all the traffic on the PDU Session UP integrity protection shall apply.

-	Preferred: for all the traffic on the PDU Session UP integrity protection should apply.

-	Not Needed: UP integrity protection shall not apply on the PDU Session.

-	whether UP confidentiality protection is:

-	Required: for all the traffic on the PDU Session UP confidentiality protection shall apply.

-	Preferred: for all the traffic on the PDU Session UP confidentiality protection should apply.

-	Not Needed: UP confidentiality shall not apply on the PDU Session.

### 6.2.2	Solution details

This solution requires the same security activation status in the UP security policy for all UE’s belonging to the same 5GLAN group. If gNB decides the security activation on its own, the user plane traffic sent between the UE and the gNB for one PDU session could use different security compared to the other PDU sessions for the other UE’s belonging to the same 5GLAN group. In such case, the security for the whole 5GLAN group is indeterministic. In summary, the security properties of the group communication will inadvertently be determined by the security properties of the weakest communication path.

This solution requires that the ciphering and integrity protection activation status of DRBs of all UEs belonging to the same 5GLAN Group shall be the same. For that reason, the SMF shall send the same security activation status in the User Plane Security Policy to the gNBs for establishing PDU sessions with UEs belonging to the same 5GLAN Group.

This solution further requires that the gNBs shall not override the UP Security Policy received from the SMF. For that reason, the SMF shall not send the "Preferred" option in User Plane Security Policy to the gNBs for establishing PDU sessions with UEs belonging to the same 5GLAN Group. In other words, the setting defined in clause 5.10.3 TS 23.501 [7] shall apply with the following modifications:

- Encryption:

- "Required" or "Not Needed" may be used;

- "Preferred" shall not be used.

- Integrity protection:

-	"Required" or "Not Needed" may be used;

-	"Preferred" shall not be used

NOTE: If 5GLAN group communication is taking place over E-UTRA (connected to 5GC), then the setting of "Required" for Integrity protection is not supported.

### 6.2.3	Evaluation

The proposed solution meets all the requirements of key issue #3.2.

## 6.3	Solution #3: Security solution for mitigation of (D)DoS attack in Non-standalone Non-Public Networks

### 6.3.1	Introduction

This solution addresses key issue #1.2 (D)DoS attack in Non-standalone Non-Public Networks.

As mentioned in the security threat of the key issue #1.2 during initial NAS Attach procedures (Registration procedures) from NPN UEs, that are accessing via CAG cell, network has to wait until completion of primary authentication to verify whether the UEs are allowed to access a CAG cell, which is an overhead on the network, if the requesting UE’s are not allowed to access the CAG cell.

This solution details on, checking an UE’s access to a CAG cell during initial NAS procedure (Registration procedure) and reject initial NAS (Registration) request from the UE, if the network identified UE is not allowed to access the CAG cell. Doing this avoids overhead on network (gNB, AMF, AUSF, UDM) and minimises (D)DoS attack on Non-Standalone NPNs.

### 6.3.2	Solution details

During initial NAS (Registration) procedure, the network to verify whether a NPN UE is allowed to access the CAG cell, as early as possible, in order to avoid unnecessary signalling overhead. The steps below detail on how this verification can be done:

- NPN UE sends initial NAS (Registration) request to the network. In this request procedure, NG-RAN sends the CAG identifier (Identifier of the CAG cell which the UE accesses) to the serving network’s AMF.

- As per TS 33.501 [5] AMF/SEAF initiates primary authentication by sending in Nausf_UEAuthentication_Authenticate request message to the AUSF and includes in this request the CAG identifier received from NG-RAN.

- If there is CAG identifier in the Nausf_UEAuthentication_Authenticate request received from SEAF, AUSF includes the CAG identifier in Nudm_UEAuthentication_Get Request message to the UDM.

- UDM de-conceals SUCI, and if the CAG Identifier is included in the Nudm_UEAuthentication_Get Request message, then it verifies whether the UE (SUPI) is allowed to access the CAG cell. If the UE is allowed to access the CAG cell, then the UDM shall proceed further with the procedures as specified in TS 33.501 [5]. Additionally the UDM includes the “Allowed CAG list” of the UE to the AMF, to perform the check for the subsequent procedure when needed, as specified in the SA2 procedures.

- If the UE is not allowed to access the CAG cell, then the UDM includes “CAG cell Reject” in Nudm_UEAuthentication_Get Response message to AUSF, and doesn’t proceed further in authentication procedure, for example, selection of authentication method and generation of authentication vector, like so.

- If there is “CAG Cell Reject” in Nudm_UEAuthentication_Get Response message from UDM, then the AUSF forwards the same to the AMF/SEAF in Nausf_UEAuthentication_Authenticate response message.

- If there is “CAG Cell Reject” in the Nausf_UEAuthentication_Authenticate response message from the AUSF, then the AMF rejects the UE’s registration request by sending the Registration Reject message with an appropriate cause value, to the UE.

This method avoids overhead on UDM of generating Authentication Vector and the network to perform authentication, for the UEs that access via unauthorized CAG cell.

Editor’s Note: It is FFS, how this mechanism protects against DDoS attack and the entities that are protected from DDoS attack.

Editor’s Note: It is FFS, to analyse any privacy impact introduced by this solution on sending CAG Identifier over the air.

Figure 6.X.2-1: Access control during Registration Procedure

### 6.3.3	Evaluation

TBD

## 6.4	Solution #4: Security solution for key derivation in standalone non-public networks

### 6.4.1	Introduction

This solution addresses key issue #1.1 on the derivation of keys in standalone non-public networks.

### 6.4.2	Solution details

For standalone non-public networks, the serving network name that is used as an input to the calculation of KAUSF, RES* and XRES* for 5G AKA, CK’ and IK’ for EAP_AKA’ and KSEAF for all authentication methods should be defined differently from that of the public networks as

a) the input should not be the same as a public network as this would allow a standalone non-public network to masquerade as a public network

b) the input should prevent one standalone public network masquerading as another.

Hence, it is proposed that for standalone non-public networks, the serving network name used in the input to the above key derivation is as follows:

serving network name = 5G:PLMN*:NPN ID

with PLMN* equal to either a PLMN ID or a shortened one based on the conclusion on what to broadcast for standalone non-public networks and NPN ID as defined in TR 23.734 [3].

### The final decision on PLMN* and the exact coding format will need to be taken as the definition of these is completed.

### 6.4.3	Evaluation

TBD

## 6.5	Solution #5: Key hierarchy for authentication using non-AKA EAP methods in non-public network

### 6.5.1	Introduction

This solution addresses key issue #5.1: Key hierarchy for non-public networks.

### 6.5.2	Solution details

NOTE 1: The key hierarchy (subclause 6.2.1 of TS 33.501[x]) and the key derivation and distribution (clause 6.2.2 of TS 33.501 [x]) clauses cannot apply to generic non-AKA EAP methods of authentication as they are written on the assumption that an AKA method is used for authentication.

For the purposes of this solution to describe the key hierarchy modifications, it is assumed that the EAP authentication terminates in the AUSF in the network.

The major change needed is on the derivation of KAUSF. It is proposed that this derivation is as follows:

- KAUSF is derived from the EMSK created by the EAP authentication as for EAP-AKA’.

The following figure captures a visual representation of that change:

Figure 6.X.2.1-1: KAUSF derivation for generic non-AKA EAP methods

Other text from clauses 6.2.1 and 6.2.2 cannot be directly used for generic non-AKA EAP methods (e.g. where the text is specific to the key hierarchy and derivation and distribution for the AKA authentication methods).

### 6.5.3	Evaluation

The proposed solution meets all the requirements of key issue #5.1.

# Annex A:	Deployment options for authentication in SNPNs considering different types of NPN credentials

These deployment options are given as example only to ease the understanding of NPN.

Depending on whether a standalone NPN (SNPN) involves a AAA server (or simply the AAA server thereafter) in UE authentication, two options of deploying authentication schemes for 5G Core (5GC) for NPN should be considered:

- SNPN fully uses 5GC with authentication by AUSF/UDM/ARPF (referred to as NPN-without-AAA)

- SNPN involves a AAA server in authentication, which interworks with 5GC NFs (referred to as NPN-with-AAA)

NOTE: The reason of considering for SNPN an AAA server is that most enterprises deploying NPNs may already have AAA servers for authenticating their users. Thus, it may be desirable to allow a NPN to interwork with the AAA server. Further, it allows to illustrate how 5G core can function as an EAP pass-through authenticator without the need of implementing any specific authentication method. The involvement of an AAA server in an SNPN has impact on the role assignment in EAP framework.

SNPN-without-AAA

The SNPN fully uses 5GC without involving any AAA server to authenticate UEs. This case is equivalent to PLMN in terms of EAP role assignment. More specifically, UE acts as EAP peer, SEAF acts as pass-through authenticator, and AUSF acts as the EAP server (see figure below). Thus, authentication methods supported by this option are implemented by UE and AUSF.  Note that each supported authentication method needs to be selectable by UDM.

SNPN-with-AAA

The SNPN uses the AAA server to authenticate UE. In this case, UE and SEAF continue to take the role of EAP peer and pass-through authenticator respectively. However, the role of AUSF is subject to discussion, depending on how it is designed to interwork with the AAA server. More specifically, AUSF may continue to take the role of EAP server, take the role of pass-through authenticator (see figure below), or may not take any role at all. In the case that AUSF does not take the role of EAP server, the AAA server can take such role (see figure below).

Thus, authentication methods supported by this option are implemented by UE and either by AUSF or the AAA server. In the latter case, the 5G core becomes transparent. However, interfaces must be defined between 5G Core and the AAA server to transport EAP messages, as well as keying materials (e.g., MSK) that might be transported back from the AAA server.

Types of UE Credentials in SNPN

The types of UE credentials also play important role in both UE authentication and key hierarchy. More specifically, different types of UE credentials often require different authentication methods, which in turn have impact on EAP peer (UE) and EAP server (AUSF or AAA server). Further, different authentication methods also have impact on the key hierarchy. More specifically, it is distinguished between the following 2 credential types.

- a public key-based credential (e.g., certificate-based) allows to establish a root key, and

- a shared secret-based credential often serves as the root key itself, i.e., allowing to derive all subsequent keys from a shared secret.

Based on the requirement from SA1, both 3GPP credentials and non-3GPP credentials should be supported for NPNs. 3GPP credentials are clearly defined in 33.501, which we will refrain from further discussion here. Non-3GPP credentials can be classified as certificate-based and non-certificate-based (see Table below).

| Credential Types in NPNs | UE credentials in NPNs |
| --- | --- |
| 3GPP UE Credentials | Shared Symmetric Keys |
| Non-3GPP UE Credentials | Certificate-based | Non-certificate-based |

Table 1 Classification of UE Credentials in SNPNs

Combination options of deployment and credential type

The combinations of two deployment options and two credentials types result in four authentication options for SNPNs (see table below).

|  | NPN-without-AAA | NPN-with-AAA |
| --- | --- | --- |
| Certificate-based UE Credentials | Option A.1 (EAP-TLS) | Option B.1 |
| Non-certificate-based UE Credentials | Option A.2 | Option B.2 |

Table 2 Authentication Options in SNPN

Remarks to the authentication options in SNPNs

Among them, only Option A.1 is covered by 33.501, Annex B, which provides EAP-TLS as an example authentication method. The root of the key hierarchy is the EMSK established by TLS.

Option B.1 is suggested to not follow up, since AUSF needs to implement EAP-TLS to support Option A.1 anyway. Thus, this option appears to have only drawbacks without clear benefit as discussed in tdoc S3-190845.

For non-certificate-based UE credentials (Option A.2. and B.2), there are a number of authentication methods that can be considered. Once the authentication methods supported by NPNs are decided, the key hierarchy can be defined accordingly.

Annex <X>:
Change history

| Change history |
| --- |
| Date | Meeting | TDoc | CR | Rev | Cat | Subject/Comment | New version |
| 2018-11 | SA3#93 | S3-183311 |  |  |  | TR skeleton | 0.0.0 |
| 2018-11 | SA3#93 | S3-183826 |  |  |  | Version after SA3#93bis incorporating changes from S3-183798, S3-183418, S3-183827, S3-183828, S3-183829 | 0.1.0 |
| 2019-02 | SA3#94 | S3-190492 |  |  |  | S3-180304, S3-190493, S3-190494, S3-190495, S3-190496, S3-190497, S3-190498, S3-190499 | 0.2.0 |
| 2019-03 | S3#94bis | S3-191018 |  |  |  | S3-190857, S3-191001, S3-190995, S3-190994, S3-190790, S3-191000, S3-190992, S3-190993, S3-190991 | 0.3.0 |