## Slide 1: Clarification of SIB1 PDSCH repetition for TN
NTT DOCOMO, INC.
RP-253487
3GPP TSG RAN Meeting #110
Baltimore, US, Dec. 8th - 11th, 2025
Agenda item: 9.9.2.2
Document for: Discussion

## Slide 2: Background
At RAN#108, it was proposed in RP-251857 that common PDCCH repetition should be applicable to TN as well as NTN, and it was endorsed as below:
Corresponding RAN1 agreement below:
RP-251857 Applicability of Rel-19 common PDCCH repetition for terrestrial Huawei, HiSilicon, China
networks telecom, Apple, OPPO,
Lenovo
Replaces
RP-251651
The document was endorsed.
  In RP-251857
  Proposal：Common PDCCH repetition introduced in Rel-19 NR NTN WI is also applicable for TN for FR1 only.
Agreement
Adopt the following TP for TS 38.213
WI Code: TEI19 [Common_PDCCH_Rep_TN] Reason for change: In RAN#108, it was agreed to apply common PDCCH repetition for TN for FR1. Summary of change: Type0-PDCCH repetition introduced in Rel-19 NR NTN WI is also applicable for TN for FR1 only, “NTN” in “For an NTN cell in FR1” is removed. Consequence if not approved: Extension of common PDCCH repetition to TN is not captured in the specifications.
13 UE procedure for monitoring Type0-PDCCH CSS sets *** Unchanged parts are omitted *** - For and for a SS/PBCH block index , the two slots including the associated Type0-PDCCH monitoring occasions are slots and . , , and the index of the first symbol of the CORESET in slots and are provided by Table 13-11 and Table 13-12. For an NTN cell in FR1, if the PBCH payload bit has value 1, the UE assumes that a same PDCCH candidate for a CCE aggregation level in slots and provides same information for DCI format 1_0 with CRC scrambled by the SI-RNTI. *** Unchanged parts are omitted ***

## Slide 3: Issue/View/Proposal
Issue
  There is no explicit text in the RAN plenary decision for SIB1 PDSCH repetition
  Meanwhile, the RAN1 agreement for NTN is that when PDCCH repetition for type 0 CSS is enabled, SIB1 PDSCH repetition is also enabled automatically
  As a result, two interpretations are possible as below and the corresponding RAN1 spec cannot be stable
    Interpretation 1: SIB1 PDSCH repetition is also applicable to TN, as in TN
    Interpretation 2: SIB1 PDSCH repetition is NOT applicable to TN, i.e., it is required to clarify further how to receive SIB1 PDSCH in case of the PDCCH repetition enabled
View
  Interpretation 1 seems to be better as no further RAN1 discussion is necessary
  Interpretation 2 is not aligned with the enabling/disabling mechanism defined for NTN and therefore leads to further RAN1 discussion/spec change
Proposal
  Proposal: RAN to clarify whether SIB1 PDSCH repetition is applicable to TN or not
  Proposal: SIB1 PDSCH repetition introduced in Rel-19 NR NTN WI is also applicable for TN for FR1 only.
  In 5.1 of 38.214:
A UE capable of PDSCH repetitions for broadcast channels, which assumed the DCI format 1_0 in the Type0 PDCCH CSS of searchSpaceZero transmitted with two inter-slot repetitions may assume that PDSCHs scheduled by the DCI format 1_0 have also been transmitted with inter-slot repetitions in the same slots as the Type0 PDCCH CSS, with the same RV as indicated by the DCI format 1_0.