3GPP TSG RAN WG1 #116bis			R1-2403701

Changsha, Hunan Province, China, April 15th – 19th, 2024

Source:		Ad-Hoc Chair (NTT DOCOMO)

Title:			Session Notes for 8.5.2

Agenda Item:		8.5.2

Document for: 	Endorsement

### 8.5.2	UE features for other Rel-18 work items (Topics A)

#### NR_FR1_lessthan_5MHz_BW

R1-2403435	Summary of discussion on UE features for dedicated spectrum less than 5MHz	Moderator (NTT DOCOMO, INC.)

Agreement:

- Update FG 51-1 as follows:

| 51. NR_FR1_lessthan_5MHz_BW | 51-1 | Support for 3 MHz channel bandwidth | 1) Reception of 12 PRB PBCH based on RB-level puncturing 2) Short RACH preamble formats with 15kHz SCS, and long PRACH formats with 1.25kHz SCS 3) Reception of 15 PRB CORESET0 |  | Yes | N/A | UE is not able to support 3 MHz channel bandwidth with 15 PRB CORESET0 | Per Band | FDD only | FR1 only | N/A | This FG is supported for 15 kHz SCS only This FG is applicable only when an associated SS/PBCH block is located according to Table 5.4.3.3-2 in TS 38.101-1 in Rel-18 Note: The UE supporting this FG supports configuration of 15 PRB BWP operation This FG is only applicable to single-carrier operation. This FG is not applicable to UEs indicating supportOfRedCap-r17 (i.e., FG 28-1) or supportOfERedCap-r18 (i.e., FG 48-1). | Optional with capability signalling |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

- Split FG 51-2 into two FGs as follows:

| 51. NR_FR1_lessthan_5MHz_BW | 51-2a | Support 12 PRB CORESET0 | 1) Reception of 12 PRB CORESET0 with an associated SS/PBCH block that is located according to Table 5.4.3.1-2 in TS 38.101-1 | 51-1 | Yes | N/A | UE is not able to support 3 MHz channel bandwidth with 12 PRB CORESET0 when an associated SS/PBCH block is located according to Table 5.4.3.1-2 in TS 38.101-1 | Per Band | FDD only | FR1 only | N/A | This FG is supported for 15 kHz SCS only Note: The UE supporting this FG supports configuration of 12 PRB BWP operation This FG is only applicable to single-carrier operation. This FG is not applicable to UEs indicating supportOfRedCap-r17 (i.e., FG 28-1) or supportOfERedCap-r18 (i.e., FG 48-1). | Optional with capability signalling |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 51. NR_FR1_lessthan_5MHz_BW | 51-2b | Support 12 PRB CORESET0 with an associated SS/PBCH block located at GSCN 41637 | 1) Reception of 12 PRB CORESET0 with an associated SS/PBCH block located at GSCN 41637 | 51-1 | Yes | N/A | UE is not able to support 3 MHz channel bandwidth with 12 PRB CORESET0 when an associated SS/PBCH block is located in band n100 at frequency GSCN 41637 of Table 5.4.3.1-3 in TS 38.101-1 | Per UE | FDD only | FR1 only | N/A | This FG is supported for 15 kHz SCS only This FG is only applicable when an associated SS/PBCH block is located in band n100 at GSCN 41637 of Table 5.4.3.1-3 in TS 38.101-1 in Rel-18. Note: The UE supporting this FG supports configuration of 12 PRB BWP operation This FG is only applicable to single-carrier operation. This FG is not applicable to UEs indicating supportOfRedCap-r17 (i.e., FG 28-1) or supportOfERedCap-r18 (i.e., FG 48-1). | Optional with capability signalling |

#### NR_DSS_enh

R1-2403434	Summary of discussion on UE features for eDSS	Moderator (NTT DOCOMO, INC.)

Agreement:

- The term “legacy” in the Note column of FG52-1/1a is replaced by “Rel-15”.

#### NR_XR_Enh

R1-2403433	Summary of discussion on UE features for XR enhancements	Moderator (NTT DOCOMO, INC.)

Agreement:

- The note in FG 50-1a is updated as “When UE supports both FG 11-9 and 50-1a, the total number which can be configured for legacy CG with single-PUSCH TO in one CG period and multi-PUSCH CG with multi-PUSCH TO in one CG period should not exceed the value reported by FG 11-9”

#### TEI18

R1-2403436	Summary of discussion on UE features for TEIs	Moderator (NTT DOCOMO, INC.)

Agreement:

- Remove ‘Legacy behaviour applies’ from the consequence if not supported column of FG 55-1.

Agreement:

- Update the notes of FGs 55-4a/55-4b/55-4c as follows:

  - UE does not expect to determine a different codebook size in a PUCCH slot from the codebook size determined based on HARQ-ACK information associated with PDSCH reception(s) scheduled before a UL grant that schedules a PUSCH in a slot overlapping with the PUCCH slot unless the UE reports support of FG 55-4e.

  - UE does not expect to determine a different PUCCH time domain resource in a slot from the PUCCH time domain resource determined based on HARQ-ACK information associated with PDSCH reception(s) scheduled before a UL grant that schedules a PUSCH in that slot unless the UE reports support of FG 55-4d.

Agreement:

- Send an LS to RAN2 to reply that the restriction in FG 11-2a/f and FG 11-2c/11-2g is also applicable to FG55-6a/f and 55-6c/g

Agreement:

- Add ‘The minimum of the summation of capability on the number of CCs with Rel-15 PDCCH monitoring capability and the capability on the number of CCs with Rel-16 PDCCH monitoring capability is 3’ for the note column of FG 55-6c.

Agreement:

- Add the following for the note column of FG 55-6d.

  - If the UE reports pdcch-BlindDetectionCA-r16,

    - Candidate values for pdcch-BlindDetectionMCG-UE-r16 is 1 to pdcch-BlindDetectionCA-r16-1

    - Candidate values for pdcch-BlindDetectionSCG-UE-r16 is 1 to pdcch-BlindDetectionCA-r16-1

    - pdcch-BlindDetectionMCG-UE-r16 + pdcch-BlindDetectionSCG-UE-r16 >= pdcch-BlindDetectionCA-r16

  - Otherwise, if N_(NR-DC,max,r16)^(DL,cells) is a maximum total number of downlink cells for which the UE is provided monitoringCapabilityConfig-r16 = r16monitoringcapability and the UE is configured on both the MCG and the SCG for NR-DC as indicated in UE-NR-Capability

    - the value of pdcch-BlindDetectionMCG-UE-r16 or of pdcch-BlindDetectionSCG-UE-r16 is 1,

    - pdcch-BlindDetectionMCG-UE-r16 + pdcch-BlindDetectionSCG-UE-r16 >= N_(NR-DC,max,r16)^(DL,cells)

  - Note: If a UE supports FG 55-6a or FG 55-6f, then the capability defined by FG 55-6a or FG 55-6f is applied to FG 55-6d.

Agreement:

- Add the following for the note column of FG 55-6e.

  - ‘One combination of (pdcch-BlindDetectionMCG-UE-r15, pdcch-BlindDetectionSCG-UE-r15, pdcch-BlindDetectionMCG-UE-r16, pdcch-BlindDetectionSCG-UE-r16) corresponds to one combination of (pdcch-BlindDetectionCA-r15, pdcch-BlindDetectionCA-r16)’

  - If the UE reports pdcch-BlindDetectionCA-r15,

    - Candidate values for pdcch-BlindDetectionMCG-UE-r15 is 0 to pdcch-BlindDetectionCA-r15

    - Candidate values for pdcch-BlindDetectionSCG-UE-r15 is 0 to pdcch-BlindDetectionCA-r15

    - pdcch-BlindDetectionMCG-UE-r15 + pdcch-BlindDetectionSCG-UE-r15>= pdcch-BlindDetectionCA-r15

  - Otherwise, if N_(NR-DC,max,r15)^(DL,cells) is a maximum total number of downlink cells for which the UE is provided monitoringCapabilityConfig-r16 = r15monitoringcapability

    - Candidate values for pdcch-BlindDetectionMCG-UE-r15 is [0, 1, 2]

    - Candidate values for pdcch-BlindDetectionSCG-UE-r15 is [0, 1, 2]

    - pdcch-BlindDetectionMCG-UE-r15 + pdcch-BlindDetectionSCG-UE-r15 >= N_(NR-DC,max,r15)^(DL,cells)

  - If the UE reports pdcch-BlindDetectionCA-r16,

    - Candidate values for pdcch-BlindDetectionMCG-UE-r16 is 0 to pdcch-BlindDetectionCA-r16

    - Candidate values for pdcch-BlindDetectionSCG-UE-r16 is 0 to pdcch-BlindDetectionCA-r16

    - pdcch-BlindDetectionMCG-UE-r16 + pdcch-BlindDetectionSCG-UE-r16>= pdcch-BlindDetectionCA-r16

  - Otherwise, if N_(NR-DC,max,r16)^(DL,cells) is a maximum total number of downlink cells for which the UE is provided monitoringCapabilityConfig-r16 = r16monitoringcapability

    - Candidate values for pdcch-BlindDetectionMCG-UE-r16 is [0, 1]

    - Candidate values for pdcch-BlindDetectionSCG-UE-r16 is [0, 1]

    - pdcch-BlindDetectionMCG-UE-r16 + pdcch-BlindDetectionSCG-UE-r16 >= N_(NR-DC,max,r16)^(DL,cells)

  - Note: If a UE supports FG 55-6c or FG 55-6g, then the capability defined by FG 55-6c or FG 55-6g is applied to FG 55-6e.

Agreement:

- Add ‘The minimum of the summation of capability on the number of CCs with Rel-15 PDCCH monitoring capability and the capability on the number of CCs with Rel-16 PDCCH monitoring capability is 3’ for the note column of FG 55-6g.

Agreement:

- Add ‘This capability is signalled for SCS 15 kHz and 30 kHz.’ for the note column of FG 55-6h.

#### NR_MC_enh

R1-2403431	Summary of discussion on UE features for MC enhancements	Moderator (NTT DOCOMO, INC.)

Agreement:

- Correct the indentation of the bullet for TDD scheduling cell in component 9 for 49-2b: placing it on the same level as the previous bullet for FDD scheduling cell.

Agreement:

For Advanced DCI processing capabilities FG 49-3x/49-3y, clarify that the “unicast DCI” includes the MC-DCI, as shown below, to distinguish from legacy FGs 18-5c and 18-5d:

| 49. NR_MC_enh | 49-3x | Advanced UE capability for larger number of unicast DL DCI | Processing up to X unicast DCI scheduling PDSCH per scheduled cell in a set of cells configured for multi-cell PDSCH scheduling by DCI format 1_3: Up to X DCI formats 1_3 for the set of cells, and Up to X unicast DL DCI formats 1_0/1_1/1_2 (if supported) for each of the cells in the set of cells For each cell in the set of cells, no more than X DCIs scheduling PDSCH for the cell X is based on pair of (scheduling CC SCS, scheduled CC SCS): Candidate value(s) of X X={2,4} for (15,120), (15,60), (30,120) and X={2} for (15,30), (30,60), (60,120 kHz) X applies per slot of scheduling CC | 49-1b | Yes |  |  | Per BC | N/A | N/A | N/A |  | Optional with capability signaling |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 49. NR_MC_enh | 49-3y | Advanced UE capability for larger number of unicast UL DCI | Processing up to X unicast DCI scheduling PUSCH per scheduled cell in a set of cells configured for multi-cell PUSCH scheduling by DCI format 0_3 Up to X DCI formats 0_3 for the set of cells, and Up to X unicast UL DCI formats 0_0/0_1/0_2 (if supported) for each of the cells in the set of cells For a cell in the set of cells, no more than X DCIs scheduling PUSCH for the cell X is based on pair of (scheduling CC SCS, scheduled CC SCS): Candidate value(s) of X X={2,4} for (15,120), (15,60), (30,120) and X={2} for (15,30), (30,60), (60,120 kHz) X applies per slot of scheduling CC | 49-2b | Yes |  |  | Per BC | N/A | N/A | N/A |  | Optional with capability signaling |

Agreement:

- Introduce new FG49-6b for DL priority indication with mixed DCI formats including DCI format 1_3 (based on 11-4b)

  - FG name:

    - DL priority indication in DCI with mixed DCI formats including DCI format 1_3

  - Component:

    - Support of priority indicator field configured in DCI formats 1_3 and (1_1 or 1_2) in a BWP when configured to monitor both DCI formats 1_3 and (1_1 or 1_2) in the BWP

  - Prerequisite:

    - 49-6

  - Type:

    - Per UE without differentiation

  - Note:

    - None

  - Mandatory or Optional:

    - Optional with capability signaling

Agreement:

- Introduce new FG49-6 for Two HARQ-ACK codebooks with up to one sub-slot based HARQ-ACK codebook simultaneously constructed for supporting HARQ-ACK codebooks with different priorities at a UE (based on 11-4)

  - FG name:

    - Two HARQ-ACK codebooks with up to one sub-slot based HARQ-ACK codebook simultaneously constructed for supporting HARQ-ACK codebooks with different priorities by DCI format 1_3

  - Component:

    - 1.	Supports two HARQ-ACK codebooks with different priorities to be simultaneously constructed with the restriction up to one sub-slot based HARQ-ACK codebook.

    - 2.	Supports separate PUCCH configuration for different HARQ-ACK codebooks.

    - 3.	Supports 2-level priority of HARQ-ACK for dynamically scheduled PDSCH and SPS PDSCH.

    - 4.	Supports a DCI format 1_3 scheduling PDSCH with different HARQ-ACK priorities when only DCI format 0_3/1_3 is configured per BWP.

    - 5.	Supports separate configuration of parameters PDSCH-HARQ-ACK-Codebook, UCI-OnPUSCH and 'codeBlockGroupTransmission" for different HARQ-ACK codebooks.

    - 6.	Supported maximum number of actual PUCCH transmissions for HARQ-ACK within a slot

      - Candidate values for the component 6 of this FG is: For NCP, {4, 5, 6, 7} for 2-symbol*7 sub-slot configuration; For ECP, the candidate value is {4,5,6} for 2-symbol*6 sub-slot configuration

    - 7.	Support intra-UE multiplexing/prioritization of UL overlapping channels/signals with two priority levels for HARQ-ACK

  - Prerequisite:

    - At least one of {49-1, 49-1b}

  - Type:

    - Per FS

  - Note:

    - If a UE reports both 11-3 and this FG, it can support two slot-based HARQ-ACK codebooks, and one slot-based and one-sub-slot-based HARQ-ACK codebooks. If a UE reports this FG but not 11-3, it can only support two slot-based HARQ-ACK codebooks.

    - The number of PUCCHs for CSI reporting per slot is not impacted compared with Rel-15 by introducing the new HARQ-ACK CBs

    - Component 6 is applied to the sub-slot HARQ-ACK codebook. It is assumed that only 1 actual PUCCH transmission for HARQ-ACK within a slot for slot-based HARQ-ACK codebook.

      - Component 6 is reported for 2-symbol*7 sub-slot configuration. For 7-symbol*2 sub-slot configuration, the value of component 6 is {2} for both NCP and ECP cases.

    - For component 6, maximum of 1 actual PUCCH transmission for HARQ-ACK within a slot for slot-based HARQ-ACK codebook. Thus value reported for component 6 has no meaning for "slot-based + slot based".

  - Mandatory or Optional:

    - Optional with capability signaling

Agreement:

- Introduce new FG49-6a for Two HARQ-ACK codebooks with two sub-slot based HARQ-ACK codebook simultaneously constructed for supporting HARQ-ACK codebooks with different priorities by DCI format 1_3 (based on 11-4a)

  - FG name:

    - Two HARQ-ACK codebooks with two sub-slot based HARQ-ACK codebook simultaneously constructed for supporting HARQ-ACK codebooks with different priorities by DCI format 1_3

  - Component:

    - 1.	Supports two subslot based HARQ-ACK codebooks with different priorities to be simultaneously constructed.

    - 2.	Supports separate PUCCH configuration for different HARQ-ACK codebooks.

    - 3.	Supports 2-level priority of HARQ-ACK for dynamically scheduled PDSCH and SPS PDSCH.

    - 4.	Supports a DCI format 1_3 scheduling PDSCH with different HARQ-ACK priorities when only DCI format 0_3/1_3 is configured in USS per BWP.

    - 5.	Supports separate configuration of parameters PDSCH-HARQ-ACK-Codebook, UCI-OnPUSCH and "codeBlockGroupTransmission" for different HARQ-ACK codebooks.

    - 6.	Supported maximum number of actual PUCCH transmissions for HARQ-ACK within a slot.

      - Candidate values for the component 6 of this FG is: For NCP, {4, 5, 6, 7} for 2-symbol*7 sub-slot configuration; For ECP, the candidate value is {4,5,6} for 2-symbol*6 sub-slot configuration.

  - Prerequisite:

    - 11-3, 49-6

  - Type:

    - Per FS

  - Note:

    - The number of PUCCHs for CSI reporting per slot is not impacted compared with Rel-15 by introducing the new HARQ-ACK CBs

    - Component 6 is applied to the two sub-slot HARQ-ACK codebooks, respectively.

    - Component 6 is reported for 2-symbol*7 sub-slot configuration. For 7-symbol*2 sub-slot configuration, the value of component 6 is {2} for both NCP and ECP cases.

  - Mandatory or Optional:

    - Optional with capability signaling

Agreement:

- Introduce new FG49-7a for UL priority indication in DCI with mixed DCI formats including DCI format 0_3 (based on 12-1a)

  - FG name:

    - UL priority indication in DCI with mixed DCI formats including DCI format 0_3

  - Component:

    - Support of priority indicator field configured in DCI formats 0_3 and (0_1 or 0_2) in a BWP when configured to monitor both DCI formats 0_3 and (0_1 or 0_2) in the BWP

  - Prerequisite:

    - 49-7

  - Type:

    - Per UE without differentiation

  - Note:

    - None

  - Mandatory or Optional:

    - Optional with capability signaling

Agreement:

- Introduce new FG49-7 for UL intra-UE multiplexing/prioritization of overlapping channel/signals with two priority levels in physical layer for DCI format 1_3/0_3 (based on 12-1)

  - FG name:

    - UL intra-UE multiplexing/prioritization of overlapping channel/signals with two priority levels in physical layer for DCI format 1_3/0_3

  - Component:

    - Support intra-UE multiplexing/prioritization of overlapping PUCCH/PUCCH and PUCCH/PUSCH with two priority levels in physical layer (PHY) for DCI format 1_3/0_3

    - 1)	Configuration of PHY priority level for CG PUSCH and SR, and dynamic indication of priority level for dynamic PUSCH with a single DCI format 0_3

    - 2)	Multiplexing/prioritization between UL channels/signals with the same PHY priority level

    - 3)	Prioritization between UL channels/signals with different PHY priority levels

    - 4)	Additional number of symbols (d1) needed beyond the PUSCH preparation time for cancelling a low priority UL transmission.

    - 5)	Additional number of symbols (d2) of the preparation time needed for the high priority UL transmission that cancels a low priority UL transmission

  - Prerequisite:

    - At least one of {49-1, 49-1b, 49-2, 49-2b}

  - Type:

    - Per FS

  - Note:

    - Candidate value set for component 4: {0, 1, 2}

    - Candidate value set for component 5: {0, 1, 2}

  - Mandatory or Optional:

    - Optional with capability signaling

Agreement:

- Introduce new FG49-8 for HARQ-ACK re-transmission triggered by DCI format 1_3 (based on 25-7)

  - FG name:

    - Triggered HARQ-ACK codebook re-transmission for DCI format 1_3

  - Component:

    - 1. Support HARQ-ACK re-transmission from an earlier PUCCH slot based on the triggering information in DCI format 1_3

    - 2. Support the related PHY priority handling in terms of HARQ-ACK codebook selection and the applicable PUCCH configuration (for a UE supporting two HARQ-ACK codebooks / PUCCH config in 49-6)

    - 3. Supported minimum value M for the HARQ re-tx offset

    - 4. Supported maximum value N for the HARQ re-tx offset

  - Prerequisite:

    - 25-7 and at least one of {49-1, 49-1b}

  - Type:

    - Per band

  - Note:

    - Candidate values for component 3 is: M = {-7, -5, …, 1}

    - Candidate values for component 4 is: N= {4, 6, …, 24}

    - Note: The minimum requirement for Component 3 and Component 4 of this FG is valid for HARQ CBs consisted of HARQ Processes with a single HARQ bit per HARQ Process ID

  - Mandatory or Optional:

    - Optional with capability signaling

Agreement:

- Introduce new FG49-9 for SCell dormancy indication in DCI format 0_3/1_3 (based on 18-4)

  - FG name:

    - SCell dormancy indication within active time in DCI format 0_3/1_3

  - Component:

    - Support for SCell dormancy indication sent within the active time on PCell with DCI format 0_3/1_3

  - Prerequisite:

    - 6-5, at least one of {49-1, 49-1b, 49-2,49-2b}

  - Type:

    - Per BC

  - Note:

    - One dormant BWP and one non-dormant BWP is supported per carrier

    - More than one non-dormant BWP per carrier is supported only if UE feature 6-3/6-4 is also supported

    - One dormant BWP and one non-dormant BWP are UE specific BWPs even for UEs not supporting 6-2 or 6-3

  - Mandatory or Optional:

    - Optional with capability signaling

Agreement:

- Introduce new FG49-10 for dynamic indication of applicable minimum scheduling restriction by DCI format 0_3/1_3 (based on 19-2)

  - FG name:

    - dynamic indication of applicable minimum scheduling restriction by DCI format 0_3/1_3

  - Component:

    - 1)	Dynamic indication of applicable minimum scheduling restriction by DCI format 0_3 and 1_3

    - 2	minimumSchedulingOffset K0 configuration for PDSCH and aperiodic CSI-RS triggering offset

    - 3)	minimumSchedulingOffset K2 configuration for PUSCH

    - 4)	Support of extended value range for aperiodic CSI-RS triggering offset

  - Prerequisite:

    - at least one of {49-1, 49-1b, 49-2,49-2b}

  - Type:

    - Per UE (without differentiation)

  - Note:

    - None

  - Mandatory or Optional:

    - Optional with capability signaling

Proposal 2-3:

Replace “[11-4]” by “49-6” for component 4 of FG49-5b

Proposal 2-8:

- Introduce new FG for PHY priority handling for one-shot HARQ-ACK feedback triggered by DCI format 1_3 (based on 25-5)

  - FG name:

    - PHY priority handling for one-shot HARQ-ACK feedback triggered by DCI format 1_3

  - Component:

    - Support transmission of type 3 HARQ-ACK codebook using the first or second PUCCH configuration based on PHY priority indication in the triggering DCI format 1_3

  - Prerequisite:

    - 49-5a and 49-6

  - Type:

    - Per band

  - Note:

    - None

  - Mandatory or Optional:

    - Optional with capability signaling

#### NR_redcap_enh

R1-2403432	Summary of discussion on UE features for eRedCap	Moderator (NTT DOCOMO, INC.)

Agreement:

- Conclude that FGs 33-1 and 33-2 can be reused by eRedCap UE.

  - FG33-1 and FG33-2 can be reused for eRedCap with the understanding that restrictions on peak rate and/or BW reduction are applied for MBS PDSCH if eRedCap UE report FG33-1/33-2.

Agreement:

- Conclude that FGs 33-2g, 33-2i and 33-2j can be reused by eRedCap UE.

Agreement:

- Conclude that FGs 33-1-2, 33-3-2 and 33-3-3 can be reused by eRedCap UE.

R1-2402007	UE features for other Rel-18 WIs (Topics A)	Huawei, HiSilicon

R1-2402164	Discussion on UE feature topics A	ZTE

R1-2402228	Discussion on UE features for NR multi-carrier enhancement	vivo

R1-2402314	Discussion on UE features for multi-carrier enhancement	OPPO

R1-2402452	UE features for other Rel-18 work items (Topic A)	Samsung

R1-2402592	Rel-18 UE features topics set A	Ericsson

R1-2402598	A joint proposal on UE features for NR support for dedicated spectrum less than 5 MHz for FR1 	Nokia, Ericsson, Huawei, Qualcomm

R1-2402604	Remaining issues of UE Features for Other Topics A (MCenh, eRedCap, NRenh, covEnh2, sub5MHz, eDSS, TEI)	Nokia

R1-2402646	Discussion on UE features for eRedCap	Xiaomi

R1-2403180	UE features for other Rel-18 work items (Topics A)	Qualcomm Incorporated

R1-2403230	Discussion on UE features for other Rel-18 work items (Topics A)	NTT DOCOMO, INC.